## Slide 1: Bridges
Advanced Computer Networks
D12

## Slide 2: Bridges Outline
Repeaters
Bridges
  Backward learning
Bridge Loops
  Spanning trees (transparent bridges)
  Source-routing bridges (e.g., token rings)

## Slide 3
Repeater
S1
S2
S3
LAN1
LAN2
S4
A repeater operates at the physical layer and forwards
everything between the two LANs.
LAN1 and LAN2 are in the same collision domain.
Repeaters

## Slide 4
Bridges
Bridge
Leon-Garcia & Widjaja:
Communication Networks

## Slide 5: Bridges
Operate at the data link layer.
Bridges use backward learning in recording source address on transmissions.
Unlike repeaters, bridges will not forward a frame onto another LAN segment if it knows about the location of the destination node.
Bridge management gets more complicated when loops are possible in the frame route.

## Slide 6
Bridge
Network
Physical
Network
LLC
Physical
Physical
Physical
LLC
MAC
MAC
MAC
MAC
A bridge is a store and forward device that separates collision domains.
Bridge

## Slide 7
B1
S1
S2
B2
S3
S4
S5
Address Port
Address Port
port 1
port 2
port 1
port 2
LAN1
LAN2
LAN3
Bridges
Leon-Garcia & Widjaja:
Communication Networks

## Slide 8
B1
S1
S2
B2
S3
S4
S5
Address Port
Address Port
port 1
port 2
port 1
port 2
LAN1
LAN2
LAN3
S1 S5
S1
1
S1
1
Bridges
Leon-Garcia & Widjaja:
Communication Networks

## Slide 9
B1
S1
S2
B2
S3
S4
S5
Address Port
Address Port
port 1
port 2
port 1
port 2
LAN1
LAN2
LAN3
S1
1
S1
1
S3
2
S3
1
Bridges
Leon-Garcia & Widjaja:
Communication Networks
S3 S2

## Slide 10
B1
S1
S2
B2
S3
S4
S5
Address Port
Address Port
port 1
port 2
port 1
port 2
LAN1
LAN2
LAN3
S1
1
S1
1
S3
2
S3
1
S4
2
S4
2
Bridge 1 does not
forward the
frame to LAN1
Bridges
Leon-Garcia & Widjaja:
Communication Networks
S4 S3

## Slide 11
Bridge1
S1
S2
Bridge 2
S3
S4
S5
Address Port
Address Port
port 1
port 2
port 1
port 2
LAN1
LAN2
LAN3
S1
1
S1
1
S3
2
S3
1
S4
2
S4
2
S2
1
Bridge 1 does not
forward the
frame to LAN2
Bridges
Leon-Garcia & Widjaja:
Communication Networks
S2 S1

## Slide 12
LAN1
LAN2
LAN3
B1
B2
B3
B4
B5
LAN4
(1)
(2)
(1)
(1)
(1)
(1)
(2)
(2)
(2)
(2)
(3)
MAN with Bridge Loops
Leon-Garcia & Widjaja:
Communication Networks

## Slide 13
One solution to
bridge loops
Build a Spanning Tree!
MAN with Bridge Loops
Leon-Garcia & Widjaja:
Communication Networks

## Slide 14: Bridges Summary
Repeaters
Bridges
  Backward learning
Bridge Loops
  Spanning trees (transparent bridges)
  Source-routing bridges (e.g., token rings)