## Slide 1: Transmission Errors Error Detection and Correction
Advanced Computer Networks
D12
Term C10

## Slide 2: Transmission Errors Outline
Error Detection versus Error Correction
Hamming Distances and Codes
Linear Codes - Parity
Internet Checksum
Polynomial Codes
Cyclic Redundancy Checking (CRC)
Properties for Detecting Errors with Generating Polynomials

## Slide 3: Transmission Errors
Transmission errors are caused by:
  thermal noise {Shannon}
  impulse noise (e..g, arcing relays)
  signal distortion during transmission (attenuation)
  crosstalk
  voice amplitude signal compression (companding)
  quantization noise (PCM)
  jitter (variations in signal timings)
  receiver and transmitter out of synch.

## Slide 4: Error Detection and Correction
error detection :: adding enough “extra” bits (redundancy) to deduce that there is an error but not enough bits to correct the error.
If only error detection is employed in a network transmission  a retransmission is necessary to recover the frame (data link layer) or the packet (network layer).
At the data link layer, this is referred to as ARQ (Automatic Repeat reQuest).

## Slide 5: Error Detection and Correction
error correction :: requires enough additional redundant bits to deduce what the correct bits must have been.
Examples
Hamming Codes
FEC = Forward Error Correction found in MPEG-4 for streaming multimedia.

## Slide 6: Hamming Codes
codeword :: a legal dataword consisting of m data bits and r redundant bits.
Error detection involves determining if the received message matches one of the legal codewords.
Hamming distance :: the number of bit positions in which two bit patterns differ.
Starting with a complete list of legal codewords, we need to find the two codewords whose Hamming distance is the smallest. This determines the Hamming distance of the code.

## Slide 7: Error Correcting Codes
Figure 3-7. Use of a Hamming code to correct burst errors.
Note
Check bits occupy
power of 2 slots
Tanenbaum

## Slide 8: Hamming Distance
x = codewords o = non-codewords
x
x
x
x
x
x
x
o
o
o
o
o
o
o
o
o
o
o
o
x
x
x
x
x
x
x
o
o
o
o
o
o
o
o
o
o
o
o
A code with poor distance properties
A code with good distance properties
(a)
(b)
Leon-Garcia & Widjaja:
Communication Networks

## Slide 9: Hamming Codes
To detect d single bit errors, you need a d+1 code distance.
To correct d single bit errors, you need a 2d+1 code distance.
In general, the price for redundant bits is too expensive to do error correction for network messages.
Network protocols normally use error detection and ARQ.

## Slide 10: Error Detection
Note - Errors in network transmissions are bursty.
The percentage of damage due to errors is lower.
It is harder to detect and correct network errors.
Linear codes
  Single parity check code :: take k information bits and appends a single check bit to form a codeword.
  Two-dimensional parity checks
IP Checksum
Polynomial Codes
Example: CRC (Cyclic Redundancy Checking)

## Slide 11: General Error Detection System
Channel
Encoder
User
information
Pattern
Checking
All inputs to channel
satisfy pattern/condition
Channel
output
Deliver user
information
or
set error alarm!
Leon-Garcia & Widjaja:
Communication Networks
Done by the receiver

## Slide 12
Calculate check bits
Channel
Recalculate check bits
Compare
Information bits
Received information bits
Check
bits
Information accepted if check bits match
Received check bits
Error Detection System Using Check Bits
Leon-Garcia & Widjaja:
Communication Networks
sent serially

## Slide 13
1 0 0 1 0 0
0 1 0 0 0 1
1 0 0 1 0 0
1 1 0 1 1 0
1 0 0 1 1 1
Bottom row consists of check bit for each column
Last column consists of check bits for each row
Two-dimensional Parity Check Code
Leon-Garcia & Widjaja:
Communication Networks

## Slide 14
1 0 0 1 0 0
0 0 0 0 0 1
1 0 0 1 0 0
1 1 0 1 1 0
1 0 0 1 1 1
1 0 0 1 0 0
0 0 0 0 0 1
1 0 0 1 0 0
1 0 0 1 1 0
1 0 0 1 1 1
1 0 0 1 0 0
0 0 0 1 0 1
1 0 0 1 0 0
1 0 0 1 1 0
1 0 0 1 1 1
1 0 0 1 0 0
0 0 0 1 0 1
1 0 0 1 0 0
1 0 0 0 1 0
1 0 0 1 1 1
Two errors
One error
Three errors
Four errors
Arrows indicate failed check bits
Multiple Errors
Leon-Garcia & Widjaja:
Communication Networks

## Slide 15
Internet Checksum
Leon-Garcia & Widjaja:
Communication Networks
15

## Slide 16: Polynomial Codes
Used extensively.
Implemented using shift-register circuits for speed advantages.
Also called CRC (cyclic redundancy checking) because these codes generate check bits.
Polynomial codes :: bit strings are treated as representations of polynomials with ONLY binary coefficients (0’s and 1’s).

## Slide 17: Polynomial Codes
The k bits of a message are regarded as the coefficient list for an information polynomial of degree k-1.
I :: i(x) = i xk-1 + i xk-2 + … + i x + i
k-1 k-2 1 0
Example:
i(x) = x6 + x4 + x3
1 0 1 1 0 0 0

## Slide 18: Polynomial Notation
Encoding process takes i(x) produces a codeword polynomial b(x) that contains information bits and additional check bits that satisfy a pattern.
Let the codeword have n bits with k information bits and n-k check bits.
We need a generator polynomial of degree n-k of the form
G = g(x) = xn-k + g xn-k-1 + … + g x + 1
n-k-1 1
Note – the first and last coefficient are always 1.

## Slide 19: CRC Codeword
n bit codeword
k information bits
n-k check bits

## Slide 20: Polynomial Arithmetic
Addition:
Multiplication:
Division:
x3 + x + 1 ) x6 + x5
x3 + x2 + x
x6 + x4 + x3
x5 + x4 + x3
x5 + x3 + x2
x4 + x2
x4 + x2 + x
x
= q(x) quotient
= r(x) remainder
divisor
dividend
Leon-Garcia & Widjaja:
Communication Networks

## Slide 21: CRC Algorithm
CRC Steps:
1) Multiply i(x) by xn-k (puts zeros in (n-k) low order positions)
2) Divide xn-k i(x) by g(x)
3) Add remainder r(x) to xn-k i(x)
(puts check bits in the n-k low order positions):
quotient
remainder
transmitted codeword
b(x) = xn-ki(x) + r(x)
xn-ki(x) = g(x) q(x) + r(x)
Leon-Garcia & Widjaja:
Communication Networks

## Slide 22: CRC Example
Information: (1,1,0,0) i(x) = x3 + x2
Generator polynomial: g(x) = x3 + x + 1
Encoding: x3i(x) = x6 + x5
1011 ) 1100000
1110
1011
1110
1011
1010
1011
x3 + x + 1 ) x6 + x5
x3 + x2 + x
x6 + x4 + x3
x5 + x4 + x3
x5 + x3 + x2
x4 + x2
x4 + x2 + x
x
Transmitted codeword:
      b(x) = x6 + x5 + x
      b = (1,1,0,0,0,1,0)
010
Leon-Garcia & Widjaja:
Communication Networks

## Slide 23: CRC Long Division
Figure 2.15 CRC Calculation using Polynomial Long Division
P&D

## Slide 24: Generator Polynomial Properties for Detecting Errors
GOAL :: minimize the occurrence of an error going undetected.
Undetected means:
E(x) / G(x) has no remainder.
Notes: 24

## Slide 25
1. Single bit errors: e(x) = xi 0  i  n-1
  If g(x) has more than one non-zero term, it cannot divide e(x)
2. Double bit errors: e(x) = xi + xj 0  i < j  n-1
= xi (1 + xj-i )
  If g(x) is primitive polynomial, it will not divide (1 + xj-i )
  for j-i  2n-k  1
3. Odd number of bit errors: e(1) = 1
If number of errors is odd.
  If g(x) has (x+1) as a factor, then g(1) = 0 and all codewords have an even number of 1s.
GP Properties for Detecting Errors
Leon-Garcia & Widjaja:
Communication Networks

## Slide 26
4. Error bursts of length L: 000011 • 0001101100 • • 0
e(x) = xi d(x) where deg(d(x)) = L-1
g(x) has degree n-k;
g(x) cannot divide d(x) if deg(g(x))> deg(d(x))
if L = (n-k) or less: all will be detected
if L = (n-k+1) : deg(d(x)) = deg(g(x))
i.e. d(x) = g(x) is the only undetectable error pattern,
fraction of bursts which are undetectable = 1/2L-2
if L > (n-k+1) : fraction of bursts which are undetectable = 1/2n-k
L
i th
position
error pattern d(x)
GP Properties for Detecting Errors
Leon-Garcia & Widjaja:
Communication Networks

## Slide 27: Standard Generating Polynomials
Six generator polynomials that have become international standards are:
  CRC-8 = x8+x2+x+1
  CRC-10 = x10+x9+x5+x4+x+1
  CRC-12 = x12+x11+x3+x2+x+1
  CRC-16 = x16+x15+x2+1
  CRC-CCITT = x16+x12+x5+1
  CRC-32 = x32+x26+x23+x22+x16+x12+x11
  +x10+x8+x7+x5+x4+x2+x+1

## Slide 28: Basic ARQ with CRC
Packet
sequence
Error-free
packet
sequence
Information
frames
Control frames
Transmitter
Receiver
CRC
Information
packet
Header
Station A
Station B
Information Frame
Control frame
CRC
Header
Leon-Garcia & Widjaja:
Communication Networks

## Slide 29: Transmission Errors Summary
Error Detection versus Error Correction
Hamming Distances and Codes
Parity
Internet Checksum
Polynomial Codes
Cyclic Redundancy Checking (CRC)
Properties for Detecting Errors with Generating Polynomials