## Slide 1: Operating Systems
Input/Output Devices
ENCE 360

## Slide 2: Need for Input and Output
An OS clearly needs input
  How else can it know what services are required?
An OS clearly provides output
  How else are users/clients supposed to benefit from the services?
THE CRUX: HOW TO INTEGRATE I/O INTO OPERATING SYSTEMS?
How should I/O be integrated into OS?
What are the general mechanisms?
How can we make them efficient?

## Slide 3: Outline
Introduction (done)
Device Controllers (next)
Device Software
Hard Disks
Chapter 5
MODERN OPERATING SYSTEMS (MOS)
By Andrew Tanenbaum
Chapter 36, 37
OPERATING SYSTEMS: THREE EASY PIECES By Arpaci-Dusseau and Arpaci-Dusseau

## Slide 4: Prototypical System Architecture
Fast, so must be short.
Also $$
Longer, so slower.
Need many devices
Devices that demand high perf generally closer to CPU
OS must deal with all devices!

## Slide 5: Canonical Device
See any problems?
Hint: remember, devices can be slow!
For OS, device is interface - like API of 3rd party system/library!
Internals can be simple (e.g., USB controller) to complex (e.g., RAID controller)
Canonical Protocol
while (STATUS == BUSY)
; // wait until device is not busy
write data to DATA register
; // device may need to service request
write command to COMMAND register
; // starts device to execute command
while (STATUS == BUSY)
; // wait until device is done

## Slide 6: Canonical Device
THE CRUX:
HOW TO AVOID THE COST OF POLLING?
How can OS check device status without frequent polling?
For OS, device is interface - like API of 3rd party system/library!
Internals can be simple (e.g., USB controller) to complex (e.g., RAID controller)
Canonical Protocol
while (STATUS == BUSY)
; // wait until device is not busy
write data to DATA register
; // device may need to service request
write command to COMMAND register
; // starts device to execute command
while (STATUS == BUSY)
; // wait until device is done

## Slide 7: Solution – the Interrupt (Again)
Instead, CPU switches to new process
Device raises interrupt when done
Invokes interrupt handler
Polling
Interrupt

## Slide 8: Copying Data? Ho, Hum
CPU copying data (write and read) rather trivial
  Could be better spent on other tasks!
Process 1 wants to write data to disk
CPU copies data to device
THE CRUX:
HOW TO LOWER DEVICE OVERHEADS?
  How can OS offload work so CPU can be more efficient?

## Slide 9: Solution – Direct Memory Access (DMA)
CPU provides DMA address
Device performs direct transfer to memory
Device interrupts processor
Processor accesses device data from memory
CPU
1
2
3
4

## Slide 10: The Benefits of DMA
Process 1 wants to write data to disk
CPU copies data to device
Device copies data from mem
CPU can run another process

## Slide 11: Outline
Introduction (done)
Device Controllers (done)
Device Software (next)
Hard Disks

## Slide 12: Integration
Devices interfaces are very specific
  Even for functionally similar devices!
    e.g., SCSI disk vs. IDE disk vs. USB thumb drive …
  Not to mention functionally different devices!
    e.g., keyboard vs. disk vs. network card …
Want system to be (mostly) oblivious to differences
THE CRUX:
HOW TO BUILD DEVICE-NEUTRAL OS?
How to hide details of device interactions from OS interactions?

## Slide 13: Solution – Abstraction
Application oblivious to file system details
File system oblivious layer specific details
Device layer oblivious device specific details
Device driver knows specifics of device hardware
70% of Linux is device driver code!
Hardware

## Slide 14: Generic Device Types
Hardware
block - access is independent of previous
  e.g., hard disk
stream - access is serial
  e.g., keyboard, network
other (e.g., timer/clock (just generate interrupts))

## Slide 15: Interrupt Handler (1 of 2)
Interrupts handled by device in two parts
  Short at first/top (generic)
  Longer next/bottom (device specific)
Hardware
(top)
Interrupt Handler
(bottom)
(Next slide)

## Slide 16: Interrupt Handler (2 of 2)
When handling interrupt, other interrupts disabled
  Incoming ones may be lost
  So, make as small as possible
Solution  Split into two pieces
  First part minimal amount of work
  Defer rest until later
  Effectively, queue up rest
  Re-enable interrupts
  Linux: “top-half” handler
Second part does most of work
  Run device-specific code
  Windows: “deferred procedure call”
  Linux: “bottom-half” handler
Device Driver
Interrupt
Handler
Hardware
request
response
top
bottom

## Slide 17: I/O System Summary
User Level Library
Device Independent
Software
Device Drivers
Interrupt
Handlers
Hardware
I/O request
I/O response
Make I/O call, format request and response
Handle naming, protection, blocking, buffering, allocation
Setup device registers for request, check status upon response
Respond to interrupt when device completes I/O
Perform I/O operation
top
bottom

## Slide 18: Outline
Introduction (done)
Device Controllers (done)
Device Software (done)
Hard Disks (next)

## Slide 19: Hard Drive Overview
Hard disk has series of platters
How do bytes get arranged on disk?
The quick brown fox jumped over the lazy dogs
File
Hard Disk
???

## Slide 20: Reading/Writing Disk Blocks
Time to read/write block:
Seek time – move arm to position
Rotation time – spin disk to right block
Transfer time – data on/off disk
Disk with 1 track
Disk with 3 tracks

## Slide 21: Organizing Disk Block Requests
Rotation fast
Arm movement relatively slower
 Seek time dominates
Because matters so much, OS often organizes requests for efficiency
 But how?
21
2
So, if 2 and 21, then which next?

## Slide 22: First-Come First-Served (FCFS)
Service requests in order that they arrive
  Total time: 14+13+2+6+3+12+3=53
Little done to optimize
How can we make more efficient?
x
x
x
x
x
x
x
1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 17 18 19 20
Time

## Slide 23: Shortest Seek First (SSF)
Service request closest to read arm
  Total time: 1+2+6+9+3+2 = 23
What might happen that is bad?
  Hint: something similar happened with scheduling
x
x
x
x
x
x
x
1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 17 18 19 20
Time

## Slide 24: Shortest Seek First (SSF)
Service request closest to read arm
  Total time: 1+2+6+9+3+2 = 23
What might happen that is bad?
  Continual request near arm  starvation!
x
x
x
x
x
x
x
1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 17 18 19 20
Time

## Slide 25: Elevator (SCAN)
Total time: 1+2+6+3+2+17 = 31
Usually, a little worse average seek time than SSTF
  But more fair, avoids starvation
Alternate C-SCAN has less variance
Note, seek getting faster, rotational not
  Someday, change algorithms
x
x
x
x
x
x
x
1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 17 18 19 20
Time

## Slide 26: State of the Art – a Mixed Bag
Disks evolving (e.g., rotation + seek converging), so OS may not always know best
Instead, issue cluster of requests that are likely to be best
  Send to disk and let disk handle
Linux – no one-size fits all (sys admins tune)
  Complete Fair Queueing (CFQ) – queue per processes, so fair but can optimize within process
    Default for many systems
  Deadline – optimize queries (better perf), but hard limit on latency to avoid starvation
  Noop – no-sorting of requests at all (good for SSD. Why?)

## Slide 27: Outline
Introduction (done)
Device Controllers (done)
Device Software (done)
Hard Disks (done)