## Slide 1: L3 - Live Lightboard Lectures
Mark Claypool

## Slide 2: Live Lightboard Lectures
Glass
Lit from beneath
Neon markers make text “pop”
So what?
  Students see professor (not just slides!)
  Face students - better than whiteboard!
Prof
Camera
Affects student engagement

## Slide 3: Motivation
Time
Space
Asynchronous
Synchronous
Same place
Anywhere

## Slide 4: Overview
Build lightboard
Setup “studio”
Configure software
Lecture!

## Slide 5: Find/Buy Parts
Tools: drill, screwdriver, adjustable wrench
Lightboard
  Acrylic glass (2'x4', 1/4" or 3/8" thick)
  Light strip, basic
  Corner braces (4"-6") and screws
  Board/table to mount on
Software
  Zoom
  PowerPoint
  OBS (with VirtualCam)
  Virtual Audio Cable
Studio
  Lights
  Camera stand/mount
  Black backdrop
  Neon markers
  Micro-fiber cloths
Computer , Webcam

## Slide 6: Build It!
Drill holes in glass (measure twice, drill once)
Screw in brackets to glass
Drill holes in board/table
Tape lightstrip on bottom
Mount to board
Done!
Side view
Glass
Corner
brace
Board

## Slide 7: Light It!
Most challenge part of studio setup!
Light “talent” not screen, not backdrop
Household lights can work, but may need hoods or shutters

## Slide 8: Configure Software
OBS, VoiceMeeter, Zoom, PowerPoint
OBS (to flip video, add ppt)
Virtualcam (OBS “camera” for Zoom)
VB-Cable (Zoom speaker to go to OBS , else audio out of synch)
Mic:
VB-Cable
Mic:
VB-Cable
Virtualcam
Window
Capture
Mic
Filters  +
 Color Key (Black)
Webcam
Speaker

## Slide 9: Lecture Prep
(My Workflow)
Make slides with full text
Before present, copy slides
Delete all text/images to draw by hand
“Full” copy as present
Notes
Original
Presentation

## Slide 10: Slide Template
Black background
Keep space for yourself!
  Don’t write on your face
Neon logo (tell it’s working)
Use blank slides!
  Reminder to pause, question, write
Don’t wear a “busy” shirt
Lecture notes across my face!

## Slide 11: Tips and Tricks
Blackout ceiling
Logitech Capture for adjustments
“Confidence” monitor
  Polarizing lenses
Black pen for reference marks

## Slide 12: L3 - Live Lightboard Lectures
Mark Claypool
Time
Space
Asynchronous
Synchronous
Same place
Anywhere