## Slide 1
Maryam Ataei Kachooei
Advisor: Prof. Mark Claypool
Department of Computer Science
Fixing TCP Slow Start for Slow Fat Links
Satellite networks are an essential part of modern network infrastructures. The critical challenge of these networks is to overcome the inherent high latencies that are detrimental to TCP throughputs. We improve TCP performance by using bandwidth estimation to more quickly increase throughput for links with high latency. We evaluate the proposed slow start algorithm over a commercial geostationary satellite link. Our preliminary results indicate that our proposed slow start adjustments improve start-up performance over satellite links, outperforming the measured alternatives.
Abstract
HyStart on: Exit too early, underutilization
HyStart off: Exit too late, Overshooting, Packet loss
BEST: Shorter download times for 80 MByte objects than HyStart on or HyStart off with more substantial improvements for smaller bottleneck queue sizes
Conclusion
Time to download objects
of different sizes
Introduction
RTT and throughput with HyStart on
ACK
ACK
ACK
Data
Data
Data
Data
Exit closer to here?
Can we avoid this?
150 ms
150 ms
Sender window
Receiver window
Congestion window
Modem
+ Router
Satellite
Client
Internet
Gateway
Servers
WPI
Geo Satellite Measurement Testbed
Evaluate
Use Viasat testbed
Several bulk downloads using Iperf3
Compare BEST, HyStart on, and off
Illustration of packet temporal spacing through a bottleneck link
BDP limitations for the default(6291456) and
Recommended(26214400) maximum Linux buffer sizes
Approach
Estimated bandwidth for each RTT (rounds 1 to 5)
bandwidth = bytes acked / ack-pair Δt
ACK = n+N
ACK=n+4N
SEQ = n
SEQ=n+N
SEQ=n+2N
SEQ=n+3N
Established
Host A
Host B
Disconnected
bytes acked
ack-pair Δt
Making change on TCP in Linux kernel
Use information of log file
Packet pairs for each RTT
Estimate bandwidth
Find the median of estimated bandwidths for each RTT
Determine threshold to set BDP
Result
The shortest download times and about half the packet losses of HyStart
Performance of BEST for different queue sizes
Time to download 80 MB
Number of packet loss:
HyStart on = 88
HyStart off = 9111
BEST = 4328
Near the optimal exit points for different queue sizes
Future Work
Accommodate LEO link characteristic
Evaluation in more networks and system configuration
Consider other approaches including sending-delivery rate method and Ack Space method
Slow
Fat
Links
High Delay
High Bandwidth