## Slide 1: A Credit-based Home Access Point (CHAP) to Improve Application Performance on IEEE 802.11 Networks
Choong-Soo Lee, Mark Claypool and Robert Kinicki
In Proceedings of the First ACM Multimedia Systems Conference (MMSys), Scottsdale, Arizona, USA, February 2010
In Proceedings of the ACM Multimedia Conference, Florence, Italy, October 25-29, 2010

## Slide 2: Introduction
Wide deployment of broadband access at home
Wireless Access Point to connect devices at home over the shared Internet connection
Diverse networked devices
Diverse applications and their needs

## Slide 3: Challenge and Possible Approaches
How to manage throughput, delay and loss with a diversity of applications and their needs
Possible Approaches:
  Applications can claim quality requirements.
    Changes to the end-hosts, applications and protocols
  Middle boxes can figure out quality requirements.
    Port/signature-based classification
  Both approaches require:
    Pre-determined treatment for traffic classes
    Careful configuration

## Slide 4: Outline
Introduction (done)
Credit-based Home Access Point (CHAP)
Performance Evaluation
Conclusion

## Slide 5: Summary of Network Traffic Characteristics
Low
Medium
High
Low
Medium
High

## Slide 6: Credit-based Scheduling
Use of credit as priority
Map application traffic characteristics to credit
Bandwidth
Delay Tolerance
Credit

## Slide 7: Credit-based Home Access Point (CHAP)
Credits in time
Wireless Transmission Time
P

## Slide 8: How CHAP Works
Credits
S
N1
N2
Delay sensitive
Delay insensitive
Wireless
Access Point
The delay insensitive flow runs out of credits.
 Increase credits of all active flows by:
1. halving the current credits
2. increasing by boost parameter (15 bars)
Cost of each transmission = 5 bars

## Slide 9: How CHAP Works
S
N1
N2
Wireless
Access Point
Cost of each transmission to N1 = 5 bars
Cost of each transmission to N2 = 5 bars
Credits
Delay sensitive
Delay insensitive
10

## Slide 10: Outline
Introduction (done)
Credit-based Home Access Point (CHAP) (done)
Performance Evaluation
  Simulation
  Implementation
Conclusion and Future Work

## Slide 11: Simulation Setup
Network Simulator (NS-2)
  Single channel, IEEE 802.11g Infrastructure Network
  Shadowing propagation model
  DropTail / CHAP / Strict Priority Queue (SPQ)

## Slide 12: Simulation Flow Schedule
30
90
150
210
270
330
Time (s)
FTP 2
FTP 1
Application
under test

## Slide 13: FTP Scenario - Throughputs
Chart: DropTail
Chart: CHAP
Chart: SPQ

## Slide 14: Game Scenario – G-Model MOS
Chart: Time (s)
Chart: G-Model MOS
DropTail | 3.6705
SPQ | 4.2699
CHAP | 4.2707

## Slide 15: Summary of Performance
Scn. | App (Unit) | DropTail | CHAP | SPQ | % Impr.
Game | Game (MOS) | 3.67 | 4.27 | 4.27 | +16%
 | FTPs (Mbps) | 26.42 | 26.60 | 26.00 | +1%
VoIP | VoIP (MOS) | 4.37 | 4.42 | 4.42 | +1%
 | FTPs (Mbps) | 26.18 | 26.34 | 26.17 | +1%
Video | Video (fps) | 9.97 | 30.00 | 30.00 | +201%
 | FTPs (Mbps) | 23.03 | 23.12 | 22.95 | +0%
Web | Web (ms) | 109.52 | 39.70 | 33.96 | +64%
 | FTPs (Mbps) | 26.59 | 26.73 | 26.54 | +1%

## Slide 16: Varying Wireless Conditions via Distance (Video)
Simulation runs with varying distances
  d = 1m ~ 30m
d

## Slide 17: Results: Varying Wireless Conditions via Distance (Video)
Chart: FTP Throughput
| 1 | 5 | 10 | 15 | 20 | 25 | 30
FIFO | 23.4023 | 23.077 | 16.8336 | 3.0794 | 0.39978 | 0.20138 | 0.16411
CHAP | 23.3719 | 23.048 | 16.8709 | 5.7821 | 1.902 | 0.64099 | 0.29545
SPQ | 23.3693 | 23.0453 | 16.5502 | 0 | 0 | 0 | 0
Chart: Video Frame Rate
| 1 | 5 | 10 | 15 | 20 | 25 | 30
FIFO | 18.1492 | 18.6464 | 24.2928 | 3.5691 | 1.1381 | 1 | 1
CHAP | 30 | 30 | 23.9558 | 3.6354 | 1.0442 | 1 | 1
SPQ | 30 | 30 | 29.453 | 4.8232 | 1.0442 | 1 | 1
CHAP provides higher throughput than FIFO and SPQ
CHAP provides video application quality higher than FIFO and
close to SPQ, while providing higher FTP throughput than FIFO and SPQ
when video application is placed further away from AP.

## Slide 18: Case Study Setup
Broadband: Verizon 7Mbps/768Kbps DSL Line
Linux bridge provides bottleneck
  Extra 2ms delay  about 5 Mbps
350 packet queue limit
Boost parameter of 25 ms for CHAP
Case Studies
Web Browsing: Firefox 3.6
Online Game: Quake IV
  Moving around
  Shooting a shotgun

## Slide 19: Websites Tested
Yahoo
Google News
CNN
Wall Street Journal

## Slide 20: Webpage Load Times
Chart: Sites Visited
| Yahoo | CNN | Google News | Wall Street Journal
FIFO (web only) | 1.4278 | 3.5372 | 0.5248 | 3.222
FIFO (web + download) | 11.1052 | 20.1746 | 3.8054 | 14.3912
CHAP (web only) | 1.4514 | 3.4014 | 0.514 | 3.3618
CHAP (web + download) | 1.8138 | 5.6894 | 0.5738 | 3.7646
CHAP provides Webpage load times similar to FIFO in absence of
file download, and provides much faster webpage load times than FIFO
with file download.

## Slide 21: Quake IV Servers
Worcester, MA
(qstat to get IP address, geolocate IP address on Google map)

## Slide 22: Quake IV Server Ping Times
Chart: Server Ping (ms)
Chart: Server Ping (ms)
425 ms
Playable
Threshold
CHAP provides server ping times similar to FIFO in absence of
file download, and provides much smaller server ping times than FIFO
in presence of file download.

## Slide 23: Quake IV – Moving Around
FIFO – Quake IV + Debian ISO Download
(477 – 546 ms)
CHAP – Quake IV + Debian ISO Download
(62 – 94 ms)
FIFO – Quake IV alone
(62 – 125 ms)
CHAP allows the player to move around freely as if there is no concurrent
file download while FIFO prevents the player from moving due to the large
roundtrip time to the server.
http://perform.wpi.edu/chap/

## Slide 24: Outline
Introduction (done)
Credit-based Home Access Point (CHAP) (done)
Performance Evaluation (done)
Conclusion and Future Work

## Slide 25: Conclusion
Credit-based Home Access Point (CHAP) improves quality of delay sensitive applications.
  FTP performance preservation
CHAP improves performance over DropTail and provides performance close to SPQ.
  Minimal configuration
  No explicit classification
  No pre-determined treatment
CHAP adjusts to wireless network configuration automatically.
  Overall performance improvement over DropTail and SPQ

## Slide 26: Future Work?

## Slide 27: Future Work
More evaluation of CHAP
Formal analysis of CHAP algorithm for setting the increment
Prototype implementation using a Linux-based access point