## Slide 1: An Empirical Evaluation of VoIP Playout Buffer Dimensioning in Skype, Google Talk, and MSN Messenger
Chen-Chi Wu, Kuan-Ta Chen, Yu-Chun Chang, and Chin-Laung Lei
ACM Workshop on Network and Operating System Support for Digital Audio and Video (NOSSDAV)
Williamsburg, VA, USA
June 2009

## Slide 2: Introduction (1 of 2)
VoIP increasingly important
  Started with inexpensive use at home with friends and family
  Now businesses between corporations
Sound quality can be comparable to traditional telephones
Skype reports: 405 million registered users, 15 million online users [footnote 1]
Reliable service and quality a priority for ISP and VoIP providers

## Slide 3: Introduction (2 of 2)
Many factors impacting quality
(This class talks about a lot of them!)
  Codec, Transport protocol, Redundancy and Error Control, and Playout Buffer
This work focuses on the Playout Buffer

## Slide 4: Buffering Basics
Sacrifice speech conversational interactivity for better sounding quality playout
  “Smoother” sound, plus could repair loss
Typically, transmit packets every 30 ms, but can arrive later than 30 ms from previous (delay jiiter)
  Results is silent periods, noise, unclear speech (depending upon loss concealment)
So, playout buffer holds packet temporarily in order to allow more packets to arrive on time

## Slide 5: Buffering Challenge
How to determine best playout buffer size to use?
Larger buffer leads to better sounding voice quality, but lower interactivity and vice versa
Optimal size affected by network delay, delay jitter, repair and compression (codec) implementations
  And network factors may change over time, so buffer size should too!

## Slide 6: Buffering in Practice
Academics proposed many algorithms [9-11, 13]
Most adjust buffer based on linear combination of network delay and jitter
  Combinations vary with network measurements
But what algorithms are used in practice?
Analyze 3 popular VoIP applications: Skype, Google Talk, MSN Messenger
  Do they differ?
  Do they adjust?
  How close to “optimal”?

## Slide 7: Outline
Introduction
Related Work
Experiments
Results
Optimal
Conclusion

## Slide 8: Related Work (1 of 2)
[11]: Authors use weighted exponential moving average of delay and standard deviation to determine buffer
  weights are hard-coded
[10]: extends [11] by adapting the weights according to magnitude of events
  Both [10] and [11] by simulation
[9,13]: extend by adjusting during talk spurt so can adapt to changes in network more quickly
Above, all academic systems
 What is used in practice?

## Slide 9: Related Work (2 of 2)
To assess, Perceptual Evaluation of Speech Quality (PESQ) [8]
  Compare original to degraded, and map to Mean Opinion Score (MOS), value 1-5.
E-Model has arithmetic sum of impairments of delay, equipment and compression [7]
  R = 94 – i(delay) – i(loss)  R factor, can map to MOS
Neither is sufficient. PESQ does not use delay, E-model not accurate nor combines delay and quality
[5] combines both
   Use their technique (later)

## Slide 10: Outline
Introduction
Related Work
Experiments
Results
Optimal
Conclusion

## Slide 11: Experiment Methodology
Free BSD w/dummynet as router
  Control loss, delay, jitter (stddev of delay)
  Link is 1 Mb/s
2 PCs running Windows XP with Skype, Google Talk, MSN Messenger
  One PC “talker” the other “listener”
Play recording on talker, send to listener
  Recording from Open Speech Repository [3]
Record both talker and listener speech
  Compare to get degradation
Each “call” 240 seconds
10 calls at each setting
degraded voice
voice

## Slide 12: Buffer Size Estimation
Have two audio samples. Compare to determine delay (use cross-correlation coefficient [1])
  (MLC: not validated as a technique?)
Note, not sure of sample interval, compression, etc. (“black box”)
  But, estimate to be 50 msec based on literature
May not be totally accurate, but want to see how commercial VoIP applications adjust

## Slide 13: Outline
Introduction
Related Work
Experiments
Results
Optimal
Conclusion

## Slide 14: Network Delay and Jitter
Delay:
  Skype doesn’t adjust
  MSN doesn’t adjust
  Google may (fig b, trendlines differ).
Jitter:
  Skype flat, so doesn’t adjust
  Google adjusts slightly, lots of variance
  MSN adjusts linearly

## Slide 15: Network Loss Rate
All flat, so no apparent adaptation

## Slide 16: Outline
Introduction
Related Work
Experiments
Results
Optimal
Conclusion

## Slide 17: QoE Measurement Model
Based on [5] …
Given original and degraded clips
Apply PESQ to get MOS
Convert MOS to R score
  Using formula in ITU-T G.107 [7]
Compute delay impairment (Id) from E-model
  Id = 0.024 x d if d < 177.3
  Id = 0.024 x d x (d – 177.3) if d > 177.3
Subtract Id from R score to get R’
Convert R back to MOS

## Slide 18: Determining Optimal Buffer Size
Yields best quality (QoE, previous slide)
Encode audio clips from open speech repository [3] to VoIP using [2]
  Use G.711, popular codec
Simulate any loss (using Gilbert model)
Add delay (Gamma distribution)
  If later than buffer size, drop
    (MLC: what policy is this?)
Decode any resulting stream
Apply QoE to determine quality

## Slide 19: Optimal Buffer Size with Delay and Jitter
As expected, MOS decreases with delay (sanity check)
MOS varies a lot with buffer size
  Important to get buffer size right
Optimal indicated by ‘X’
  As jitter increases, more delay is necessary

## Slide 20: Optimal Buffer Size with Loss
Method: Delay all 100 ms, add loss
Loss degrades MOS (sanity check)
With jitter, optimal point shifts left with higher loss
  May be different with repair (future work)

## Slide 21: Optimal for Skype, Google, MSN
(They don’t adjust for loss, so no further analysis)
All are conservative (~220 ms buffer) with no jitter
MSN adapts best with jitter, others too conservative

## Slide 22: Model for Determining Optimal Buffer Size
Can derive optimal via simulations
  But lot of work, not real-time
Try regression to determine under network scenario
Optimal buffer =
Delay – average network delay, jitter – std of delay, plr - packet loss rate
For G.711, coefficients are below, R2 is 0.885 (good)

## Slide 23: Conclusions
Investigate if gap between academic research and practice exists
  MSN Messenger, Skype, Google Talk
MSN best in terms of buffer dimensioning
Skype, does not adjust much at all
Provide algorithm to compute optimal based on QoE metric and model

## Slide 24: Future Work?

## Slide 25: Future Work
More factors
  Frame size
  Repair
  Codec
Use optimal dimensioning model in system
  Real-life experiments to evaluate