## Slide 1: Introduction to GPGPU CS 525G – Lecture 5
Prof Emmanuel Agu
Computer Science Dept.
Worcester Polytechnic Institute (WPI)
Notes: <number>

## Slide 2: Outline
CUDA memory management and performance strategies:
  CUDA memory types
  Shared memory
  Memory coalescing
  Data prefetching
  Loop unrolling
Notes: <number>

## Slide 3: Why different CUDA Memory Types?
CPU has RAM, GPU has its own device memory
  E.g. T10 processor has up to 4GB DRAM
cudaMalloc allocates global memory on GPU
cudaFree deallocates global memory on GPU
Easy to program using global memory
However, global memory is off-chip on GPU card
Even though global memory much faster than CPU memory, still relatively slow
Too much global memory access = congestion

## Slide 4
Host-Device Connection
Host (CPU)
Device Global Memory
Host Memory
Device (GPU)
PCIe x16
4 GB/s
PCIe x16 Gen2
8 GB/s peak
GPU bus
C2050 1030.4 GB/s
GTX 280 141.7 GB/s
DDR 400
3.2 GB/s
GDDR5
230 GB/s
Memory bus
limited by memory and processor-memory connection bandwidth
Hypertransport and Intel’s Quickpath currently 25.6 GB/s

## Slide 5: Why different CUDA Memory Types?
CUDA has different memory types
Proper use of different CUDA memory types reduces congestion
Defining memory types dictates storage location, access speed of data, and visibility
GPU has faster on-chip memory although data has to be transferred explicitly into shared memory
Main idea: Load frequently accessed data into faster memory types (e.g. shared memory)
Main on-chip memory: shared memory and registers

## Slide 6
Currently can only transfer data from host to global (and constant memory) and not host directly to shared.
Constant memory used for data that does not change (i.e. read-only by GPU)
Shared memory can be up to 15x speed of global memory
Register similar speed to shared memory if reading same address or no bank conflicts.
CUDA Memory Hierarchy

## Slide 7: CUDA Memory Hierarchy
Memory only seen by this thread
Shared Memory seen by
threads within same block
Global memory seen by all
threads in all blocks and grids

## Slide 9: Where to Declare Variables?
Can host access it?
Outside of any Function
In the kernel
yes
no
global
constant
register (automatic)
shared
local
Notes: <number>

## Slide 13
Global Memory
__device__
For data available to all threads in device.
Declared outside function bodies
Scope of Grid and lifetime of application
#include <stdio.h>
#include <stdlib.h>
#include <cuda.h>
#define N 1000
…
__device__ int A[N];
__global__ kernel() {
int tid = blockIdx.x * blockDim.x + threadIdx.x;
A[tid] = …
…
}
main {
…
}

## Slide 14
Issues with using Global memory
Long delays, slow
Access congestion
Cannot synchronize accesses
Need to ensure no conflicts of accesses between threads

## Slide 15
Shared Memory
Shared memory is on the GPU chip and very fast
Separate data available to all threads in one block.
Declared inside function bodies
Scope of block and lifetime of kernel call
So each block would have its own array A[N]
#include <stdio.h>
#include <stdlib.h>
#include <cuda.h>
#define N 1000
…
__global__ kernel() {
__shared__ int A[N];
int tid = threadIdx.x;
A[tid] = …
…
}
main {
…
}

## Slide 16
<number>
Transferring data to shared memory
int A[N][N]; //to be copied into device from host with cudamalloc
__global__ void myKernel (int *A_global) {
__shared__ int A_sh[n][n]; // declare shared memory
int row = …
int col = …
A_sh[i][j] = *A_global[row + col*N]; //copy from global to shared
…
}
main () {
…
cudaMalloc((void**)dev_ A, size); // allocate global memory
cudaMemcpy(dev_A, A, size, cudaMemcpyHostTo Device); //copy to global memory
myKernel<<G,B>>(dev_A)
…
}
Coping from global to
Shared memory

## Slide 17
Issues with Shared Memory
Shared memory is not immediately synchronized after access.
Usually it is the writes that can cause problems.
Use __syncthreads() before you read data that has been altered.
Shared memory is very limited
(Fermi has up to 48KB per GPU core, NOT per block)
Hence may have to divide your data into “chunks”

## Slide 18
Example uses of shared data
Where the data can be divided into independent parts:
Image processing
- Image can be divided into blocks and placed into shared memory for processing
Block matrix multiplication
Sub-matrices can be stored in shared memory

## Slide 19
Registers
Compiler will place variables declared in kernel in registers when possible
Limit to the number of registers
Fermi has 32768 32-bit registers
Registers divided across “warps” and have lifetime of the warps
__global__ kernel() {
int x, y, z;
…
}

## Slide 20
Arrays declared within kernel
(Automatic array variables)
__global__ kernel() {
int A[10];
…
}
Generally stored in global memory but private copy made for each thread.*
Can be as slow access as global memory, except if cached
If array indexed with a constant value, compiler may use registers

## Slide 21
Constant Memory
__constant__
For data not altered by device.
Although stored in global memory, cached and has fast access
Declared outside function bodies
Scope of grid and lifetime of application
Size currently limited to 65536 bytes
#include <stdio.h>
#include <stdlib.h>
#include <cuda.h>
…
__constant__ int n;
__global__ kernel() {
…
}
main {
n = …
…
}

## Slide 22
Local memory
For compute capability 2.x, cached in L1 and L2 caches on-chip
Used to hold arrays if not indexed with a constant value
and
for variables when no more available registers
Resides in device memory space (global memory) and is slow except it’s organized such that consecutive 32-bit words accessed by consecutive threadIDs are optimized for best coalesced accesses when possible

## Slide 23: Thread Cooperation using Shared Memory
Shared memory allows threads in same block to communicate and cooperate on large calculations
First thread calculates, writes to shared memory
Second thread reads from shared memory, does work
Shared memory is on GPU, so very fast access
Use keyword __ shared__ to declare shared memory
__ shared__ float cache[threadsPerBlock];

## Slide 24: Thread Synchronization
If multiple threads reading/writing to same [shared] memory location, synchronization necessary
Synchronization? Thread B cannot start reading before thread A finishes writing
Function __synchthreads( ) forces all threads to complete before executing code section
  Threads wait for each other at __synchthreads( ) before continuing

## Slide 25: Example: Vector Dot Product
Define vectors
Then vector addition:
a
a+b
b

## Slide 26: Vector Dot Product
Dot product,
Example, if a=(2,3,1) and b=(0,4,-1) then

## Slide 27: Study: Vector Dot Product
#include "../common/book.h"
#define imin(a,b) (a<b?a:b)
const int N = 33 * 1024;
const int threadsPerBlock = 256;
const int blocksPerGrid =
imin(32,(N+threadsPerBlock-1)/threadsPerBlock);
Formula yields smallest multiple of threadsPerBlock
that is greater than or equal to N

## Slide 28: Vector Dot Product
__global__ void dot( float *a, float *b, float *c ) {
__shared__ float cache[threadsPerBlock];
int tid = threadIdx.x + blockIdx.x * blockDim.x;
int cacheIndex = threadIdx.x;
Shared memory called cache
Each block of threads sees
different cache
Each block has private copy of shared memory.No need to incorporate blockIdx.

## Slide 29: Vector Dot Product
float temp = 0;
while (tid < N) {
temp += a[tid] * b[tid];
tid += blockDim.x * gridDim.x;
}
// set the cache values
cache[cacheIndex] = temp;
cache is shared memory so all threads sees different cache
temp is a global variable so each thread has a different copy

## Slide 30: Vector Dot Product
So far, have computed elements of dot product
For instance calculated and stored in cache[1]
Now need to sum all elements to get dot product
Dangerous! All threads must finish computing elements before summation starts
Synchronize using __synchthreads( ) before summing

## Slide 31: Summing arrays using Reduction

## Slide 32: Summing arrays using Reduction
0
1
2
3
4
5
7
6
10
9
8
11
0+1
2+3
4+5
6+7
10+11
8+9
0...3
4..7
8..11
0..7
8..15
1
2
3
Array elements
iterations
Thread 0
Thread 8
Thread 2
Thread 4
Thread 6
Thread 10
<number>
Number of iterations = Log2(no. of threads)
Notes: <number>

## Slide 33: Reduction Code
// synchronize threads in this block
__syncthreads();
// for reductions, threadsPerBlock must be power of 2
// because of the following code
int i = blockDim.x/2;
while (i != 0) {
if (cacheIndex < i)
cache[cacheIndex] += cache[cacheIndex + i];
__syncthreads();
i /= 2;
}
Must synch up all threads
after threads add pairs

## Slide 34: Vector Dot Product
if (cacheIndex == 0)
c[blockIdx.x] = cache[0];
int main( void ) {
float *a, *b, c, *partial_c;
float *dev_a, *dev_b, *dev_partial_c;
// allocate memory on the cpu side
a = (float*)malloc( N*sizeof(float) );
b = (float*)malloc( N*sizeof(float) );
partial_c = (float*)malloc( blocksPerGrid*sizeof(float) );
Move result from shared to global memory
Allocate memory on host for
input and output arrays

## Slide 35: Vector Dot Product
// allocate the memory on the GPU
HANDLE_ERROR( cudaMalloc( (void**)&dev_a,
N*sizeof(float) ) );
HANDLE_ERROR( cudaMalloc( (void**)&dev_b,
N*sizeof(float) ) );
HANDLE_ERROR( cudaMalloc( (void**)&dev_partial_c,
blocksPerGrid*sizeof(float) ) );
// fill in the host memory with data
for (int i=0; i<N; i++) {
a[i] = i;
b[i] = i*2;
}
Fill arrays a[ ] and b[ ]

## Slide 36: Vector Dot Product
// copy the arrays 'a' and 'b' to the GPU
HANDLE_ERROR( cudaMemcpy( dev_a, a, N*sizeof(float),
cudaMemcpyHostToDevice) );
HANDLE_ERROR( cudaMemcpy( dev_b, b, N*sizeof(float),
cudaMemcpyHostToDevice ) );
dot<<<blocksPerGrid,threadsPerBlock>>>( dev_a, dev_b,dev_partial_c );
Launch kernel
Pre-defined number of blocks and threads

## Slide 37: Vector Dot Product
// copy array 'c' back from the GPU to the CPU
HANDLE_ERROR( cudaMemcpy( partial_c, dev_partial_c,
blocksPerGrid*sizeof(float),
cudaMemcpyDeviceToHost ) );
// add up per-block results on CPU side
c = 0;
for (int i=0; i<blocksPerGrid; i++) {
c += partial_c[i];
}
Move result from shared to global memory

## Slide 38: Vector Dot Product
#define sum_squares(x) (x*(x+1)*(2*x+1)/6)
printf( "Does GPU value %.6g = %.6g?\n", c,
2 * sum_squares( (float)(N - 1) ) );
// free memory on the gpu side
HANDLE_ERROR( cudaFree( dev_a ) );
HANDLE_ERROR( cudaFree( dev_b ) );
HANDLE_ERROR( cudaFree( dev_partial_c ) );
// free memory on the cpu side
free( a );
free( b );
free( partial_c );
}
Free memory on CPU
Free memory on GPU

## Slide 39: Fun Example: Shared Memory Bitmap
#include "cuda.h"
#include "../common/book.h"
#include "../common/cpu_bitmap.h"
#define DIM 1024
#define PI 3.1415926535897932f
__global__ void kernel( unsigned char *ptr ) {
// map from threadIdx/BlockIdx to pixel position
int x = threadIdx.x + blockIdx.x * blockDim.x;
int y = threadIdx.y + blockIdx.y * blockDim.y;
int offset = x + y * blockDim.x * gridDim.x;
Compute global location this thread will work on

## Slide 40: Fun Example: Shared Memory Bitmap
__shared__ float shared[16][16];
// now calculate the value at that position
const float period = 128.0f;
shared[threadIdx.x][threadIdx.y] =
255 * (sinf(x*2.0f*PI/ period) + 1.0f) *
(sinf(y*2.0f*PI/ period) + 1.0f) / 4.0f;
Calculations done on a per-thread basis

## Slide 41: Fun Example: Shared Memory Bitmap
// removing this syncthreads shows graphically
// what happens when it doesn't exist.
// this is an example of why we need it.
__syncthreads();
ptr[offset*4 + 0] = 0;
ptr[offset*4 + 1] = shared[15-threadIdx.x][15- threadIdx.y];
ptr[offset*4 + 2] = 0;
ptr[offset*4 + 3] = 255;
}
Make sure all threads have finished writing to
shared memory before copying to global memory

## Slide 42: Fun Example: Shared Memory Bitmap
// globals needed by the update routine
struct DataBlock {
unsigned char *dev_bitmap;
};
int main( void ) {
DataBlock data;
CPUBitmap bitmap( DIM, DIM, &data );
unsigned char *dev_bitmap;
HANDLE_ERROR( cudaMalloc( (void**)&dev_bitmap,
bitmap.image_size() ) );

## Slide 43: Fun Example: Shared Memory Bitmap
data.dev_bitmap = dev_bitmap;
dim3 grids(DIM/16,DIM/16);
dim3 threads(16,16);
kernel<<<grids,threads>>>( dev_bitmap );
HANDLE_ERROR( cudaMemcpy( bitmap.get_ptr(), dev_bitmap,
bitmap.image_size(),
cudaMemcpyDeviceToHost ) );

## Slide 44: Fun Example: Shared Memory Bitmap
HANDLE_ERROR( cudaFree( dev_bitmap ) );
bitmap.display_and_exit();
}

## Slide 45: Fun Example: Shared Memory Bitmap

## Slide 46: A Common Programming Strategy
© David Kirk/NVIDIA and Wen-mei W. Hwu, 2007-2009
ECE498AL, University of Illinois, Urbana Champaign
<number>
Global memory resides in device memory (DRAM) - much slower access than shared memory
So, a profitable way of performing computation on the device is to tile data to take advantage of fast shared memory:
  Partition data into subsets that fit into shared memory
  Handle each data subset with one thread block by:
    Loading the subset from global memory to shared memory, using multiple threads to exploit memory-level parallelism
    Performing the computation on the subset from shared memory; each thread can efficiently multi-pass over any data element
    Copying results from shared memory to global memory

## Slide 47: Tiling Size Effects
© David Kirk/NVIDIA and Wen-mei W. Hwu, 2007-2009
ECE498AL, University of Illinois, Urbana Champaign
<number>
Notes: <number>
Mention that we’re limited from large tile sizes by thread context maximums.

## Slide 48: Memory Coalescing
© David Kirk/NVIDIA and Wen-mei W. Hwu, 2007-2009
ECE 498AL, University of Illinois, Urbana-Champaign
<number>
When accessing global memory, peak performance utilization occurs when all threads in a half warp access continuous memory locations.
Md
Nd
W
I
D
T
H
WIDTH
Thread 1
Thread 2
Not coalesced
coalesced

## Slide 49: Memory Coalescing
Given a matrix stored row-major in global memory, what is a thread’s desirable access pattern?
Image from: http://bps10.idav.ucdavis.edu/talks/03-fatahalian_gpuArchTeraflop_BPS_SIGGRAPH2010.pdf
M2,0
M1,1
M1,0
M0,0
M0,1
M3,0
M2,1
M3,1
M2,0
M1,0
M0,0
M3,0
M1,1
M0,1
M2,1
M3,1
M1,2
M0,2
M2,2
M3,2
M1,2
M0,2
M2,2
M3,2
M1,3
M0,3
M2,3
M3,3
M1,3
M0,3
M2,3
M3,3
M

## Slide 50: Memory Coalescing
Given a matrix stored row-major in global memory, what is a thread’s desirable access pattern?
Image from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter5-CudaPerformance.pdf
Md
Nd
W
I
D
T
H
WIDTH
Thread 0
Thread 1
Thread
0
Thread
1
a) column after column?
b) row after row?
Notes: <number>

## Slide 51: Memory Coalescing
Given a matrix stored row-major in global memory, what is a thread’s desirable access pattern?
  a) column after column
    Individual threads read increasing, consecutive memory address
  b) row after row
    Adjacent threads read increasing, consecutive memory addresses
Notes: <number>

## Slide 52: Memory Coalescing
Image from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter5-CudaPerformance.pdf
a) column after column
Notes: <number>

## Slide 53: Memory Coalescing
Image from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter5-CudaPerformance.pdf
b) row after row
Notes: <number>

## Slide 54: Memory Coalescing
Image from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter5-CudaPerformance.pdf
Recall warp partitioning; if these threads are in the same warp, global memory addresses are increasing and consecutive across warps.
Notes: <number>

## Slide 55: Memory Coalescing
Global memory bandwidth (DRAM)
  G80 – 86.4 GB/s
  GT200 – 150 GB/s
Achieve peak bandwidth by requesting large, consecutive locations from DRAM
  Accessing random location results in much lower bandwidth

## Slide 56: Memory Coalescing
Memory coalescing – rearrange access patterns to improve performance
Useful today but will be less useful with large on-chip caches

## Slide 57: Memory Coalescing
The GPU coalesce consecutive reads in a half-warp into a single read
  What makes this possible?
Strategy: read global memory in a coalesce-able fashion into shared memory
  Then access shared memory randomly at maximum bandwidth
    Ignoring bank conflicts
See Appendix G in the NVIDIA CUDA C Programming Guide for coalescing alignment requirements
Notes: Because each thread executes the same instruction
<number>

## Slide 58: 2 More Performance Strategies
Data prefetching
Loop unrolling

## Slide 59: Data Prefetching
Independent instructions between a global memory read and its use can hide memory latency
float m = Md[i];
float f = a * b + c * d;
float f2 = m *f;

## Slide 60: Data Prefetching
Independent instructions between a global memory read and its use can hide memory latency
float m = Md[i];
float f = a * b + c * d;
float f2 = m *f;
Read global memory

## Slide 61: Data Prefetching
Independent instructions between a global memory read and its use can hide memory latency
float m = Md[i];
float f = a * b + c * d;
float f2 = m *f;
Execute instructions that are not dependent on memory read

## Slide 62: Data Prefetching
Independent instructions between a global memory read and its use can hide memory latency
float m = Md[i];
float f = a * b + c * d;
float f2 = m *f;
Use global memory after the above line from enough warps hide the memory latency

## Slide 63: Data Prefetching
Prefetching data from global memory can effectively increase the number of independent instructions between global memory read and use

## Slide 64: Data Prefetching
Recall tiled matrix multiply:
for (/* ... */)
{
// Load current tile into shared memory
__syncthreads();
// Accumulate dot product
__syncthreads();
}

## Slide 65: Data Prefetching
Tiled matrix multiply with prefect:
// Load first tile into registers
for (/* ... */)
{
// Deposit registers into shared memory
__syncthreads();
// Load next tile into registers
// Accumulate dot product
__syncthreads();
}

## Slide 66: Data Prefetching
Tiled matrix multiply with prefetch:
// Load first tile into registers
for (/* ... */)
{
// Deposit registers into shared memory
__syncthreads();
// Load next tile into registers
// Accumulate dot product
__syncthreads();
}

## Slide 67: Data Prefetching
Tiled matrix multiply with prefetch:
// Load first tile into registers
for (/* ... */)
{
// Deposit registers into shared memory
__syncthreads();
// Load next tile into registers
// Accumulate dot product
__syncthreads();
}
Prefetch for next iteration of the loop

## Slide 68: Data Prefetching
Tiled matrix multiply with prefetch:
// Load first tile into registers
for (/* ... */)
{
// Deposit registers into shared memory
__syncthreads();
// Load next tile into registers
// Accumulate dot product
__syncthreads();
}
These instructions executed by enough threads will hide the memory latency of the prefetch

## Slide 69: Loop Unrolling
for (int k = 0; k < BLOCK_SIZE; ++k)
{
Pvalue += Ms[ty][k] * Ns[k][tx];
}
Instructions per iteration
  One floating-point multiple
  One floating-point add
  What else?

## Slide 70: Loop Unrolling
for (int k = 0; k < BLOCK_SIZE; ++k)
{
Pvalue += Ms[ty][k] * Ns[k][tx];
}
Other instructions per iteration
  Update loop counter

## Slide 71: Loop Unrolling
for (int k = 0; k < BLOCK_SIZE; ++k)
{
Pvalue += Ms[ty][k] * Ns[k][tx];
}
Other instructions per iteration
  Update loop counter
  Branch

## Slide 72: Loop Unrolling
for (int k = 0; k < BLOCK_SIZE; ++k)
{
Pvalue += Ms[ty][k] * Ns[k][tx];
}
Other instructions per iteration
  Update loop counter
  Branch
  Address arithmetic

## Slide 73: Loop Unrolling
for (int k = 0; k < BLOCK_SIZE; ++k)
{
Pvalue += Ms[ty][k] * Ns[k][tx];
}
Instruction Mix
  2 floating-point arithmetic instructions
  1 loop branch instruction
  2 address arithmetic instructions
  1 loop counter increment instruction

## Slide 74: Loop Unrolling
Only 1/3 are floating-point calculations
  But I want my full theoretical 346.5 GFLOPs (G80)
  Consider loop unrolling

## Slide 75: Loop Unrolling
Pvalue +=
Ms[ty][0] * Ns[0][tx] +
Ms[ty][1] * Ns[1][tx] +
...
Ms[ty][15] * Ns[15][tx]; // BLOCK_SIZE = 16
No more loop
  No loop count update
  No branch
  Constant indices – no address arithmetic instructions
Notes: Compilers are getting better at unrolling, but many programmers still do it by hand.
<number>

## Slide 76
Measuring Performance
These notes will introduce:
Timing Program Execution
How to measure time of execution of CUDA programs
CUDA “events”
Synchronous and asynchronous CUDA routines
Bandwidth measures
Computation measures – floating point operations/sec

## Slide 77
Ways to measure time of execution
Generally instrument code
Measure time at two places and get difference
Ways to measure time:
C clock() or time() routines
CUDA “events” (seems the best way)
CUDA SDK timer

## Slide 78
If program uses cudaMemcpy, which is synchronous and waits for previous operations to complete and returns when it is complete, could use clock():
#include <time.h> // needed for clock()
int main() {
float start, stop; // actually return types are clock_t
…
start = clock();
cudaMemcpy
mykernel<<<B,T>>>(); // kernel call
cudaMemcpy
stop = clock();
…
printf(“Execution time is %f seconds\n",
(stop-start)/(float)CLOCKS_PER_SEC);
return 0;
}
Timing with clock()

## Slide 79
<number>
If just measuring time of asynchronous kernel with clock()
Important to remember that kernel calls asynchronous and return immediately and before kernels have fully executed.
Hence need to wait for kernel to complete.
Can be achieved using cudaThreadSynchronize():
start = clock();
mykernel<<<B,T>>>(); // kernel call
cudaThreadSynchronize();
stop = clock();
(We will discuss synchronization within a computation later.)

## Slide 80
<number>
CUDA event timer
In general, better to use CUDA event timer.
First need to create event objects.
cudaEvent_t event1;
cudaEventCreate(&event1);
cudaEvent_t event1;
cudaEventCreate(&event1);
creates two “event” objects, event1 and event1.

## Slide 81
<number>
Recording Events
cudaEventRecord(event1, 0) record an “event” into default “stream” (0).
Device will record a timestamp for the event when it reaches that event in the stream, that is, after all preceding operations have completed.
NOTE: This operation is asynchronous and may return before recording event!

## Slide 82
<number>
Making event actually recorded
cudaEventSynchronize(event) -- waits until named event actually recorded.
Event recorded when all work done by threads to complete prior to specified event
(Not strictly necessary if synchronous CUDA call in code.)

## Slide 83
<number>
Measuring time between two events
cudaEventElapsedTime(&time, event1, event2) will return (pointer argument) the time elapsed between two events, in milliseconds.
Resolution approx ½ millisecond.
Timing measured using GPU clock.

## Slide 84
<number>
Timing GPU Execution with CUDA events
Code
cudaEvent_t start, stop;
float elapsedTime;
cudaEventCreate(&start); // create event objects
cudaEventCreate(&stop);
cudaEventRecord(start, 0); // Record start event
.
.
.
cudaEventRecord(stop, 0); // record end event
cudaEventSynchronize(stop); // wait for all device work to complete
cudaEventElapsedTime(&elapsedTime, start, stop); //time between events
cudaEventDestroy(start); //destroy start event
cudaEventDestroy(stop);); //destroy stop event
Timed period

## Slide 85
<number>
http://developer.download.nvidia.com/
compute/cuda/3_0/toolkit/docs/online/index.html
http://developer.download.nvidia.com/
compute/cuda/2_3/toolkit/docs/online/index.html
CUDA on-line documentation

## Slide 86
<number>
Avoid including time of first kernel launch which will be more timing consuming than subsequent launches because of initialization – applies if re-calling same kernel:
for (i=0; i < N; i++) {
myKernel<<B,T>>>();
}
Asynchronous CUDA routines returning before they are complete – a big issue.
Issues to watch for

## Slide 87
<number>
Asynchronous and synchronous calls
Kernels
Kernel starts after all previous CUDA calls completed
Control returned to CPU immediately (asynchronous, non-blocking)
cudaMemcpy
Copy starts after all previous CUDA calls completed
Returns after copy complete (synchronous)

## Slide 88
<number>
Bandwidth
Bandwidth is the rate at which data is transferred.
Physical connection will define the maximum system bandwidth.
S2050 (4 GPUs) 4121.6 GB/sec
C2050 Telsa (coit-grid06) 1030.4 GB/sec
GTX 280 141.6 GB/sec
GT 320M/330M (in Mac pro laptops) 25.6 GB/sec
Pentium Core i7 with Quickpath 25.6 GB/sec
Xbox 6.4 GB/sec
Effective bandwidth is the actual bandwidth achieved by a program. Hence if we measure the effective bandwidth of a program, we can compare that to the maximum possible.
Wikipedia: Comparison of Nvidia graphics processing units http://en.wikipedia.org/wiki/Comparison_of_Nvidia_graphics_processing_units#Tesla

## Slide 89
<number>
Effective Bandwidth
Effective bandwidth, the actual bandwidth achieved by a program/kernel given by
Effective Bandwidth = (number_Bytes/time) * 10-9 GB/s
where:
number_Bytes is total number of bytes read or written
time is the time period in seconds
GB/s = Gigabytes per second = 1,000,000,000 Bytes/s
Use effective bandwidth as a metric for measuring performance/optimization benefits*
* from NVIDIA CUDA C Best Practices Guide, Version 3.2, 8/20/2010

## Slide 90
<number>
Bandwidth of Matrix Copy Operation
From NVIDIA CUDA C Best Practices Guide, Version 3.2, 8/20/2010
Copying an N x N matrix:
((N2 x b x 2)/time) x 10-9 GB/sec
where there are b bytes in each number
Integers b = 4 (4 bytes)
Floating point b = 4(4 bytes)
Read plus write, 2 transfers.
Need to know size of variables.

## Slide 91
<number>
Computational Measures
The classical measure in high performance computing (HPC) to measure performance is the number of floating point operations. Systems have peak GFLOPs
Tianhe-1 2.5 PFLOPS*
Cray Jaguar 1.75 PFLOPS
S2050 (4 GPUs) 5152 GFLOPS
C2050 Telsa (coit-grid06) 1288 GFLOPS
GTX 280 933 GFLOPS
GT 330M (in Mac pro laptops) 182 GFLOPS
Pentium Core i7 40-55 GFLOPS
Peak single precision GFLOPs
Petaflops, 1015 FLOPS, Gflops = 109 FLOPS)
These numbers need checking

## Slide 92
<number>
Actual FLOPS
Measured using standard benchmark programs such as LINPACK
If measure it on your program, can see how close it get to the peak (which presumably is doing only floating point operations).

## Slide 93
#define N 1000 // a big number up to INT_MAX, 2,147,483,647
__global__ void gpu_compute(float *result) {
int i, j;
float a = 0.0;
int tid = blockIdx.x * blockDim.x + threadIdx.x;
for (i = 0; i < N; i++)
for (j = 0; j < N; j++) a = a + 0.0001; // do something, N x N floating pt operations
result[tid] = a; // store result
return;
}
int main(int argc, char *argv[]) {
int T = 1, B = 1; // threads per block and blocks per grid
float cpu_result, *gpu_result, ans[T * B]; // result from gpu, to make sure computation is being done
cudaEvent_t start, end; // using cuda events to measure time
float time; // which is applicable for asynchronous code also
cudaEventCreate(&start); // instrument code to measure start time
cudaEventCreate(&end);
Sample partial code to measure performance on GPU

## Slide 94
cudaEventRecord(start, 0 );
cudaMalloc((void**) &gpu_result, T * B * sizeof(float));
gpu_compute<<<B,T>>>(gpu_result);
cudaMemcpy(ans,gpu_result, T * B * sizeof(float),cudaMemcpyDeviceToHost);
cudaEventRecord(end, 0 ); // instrument code to measure end time
cudaEventSynchronize(end);
cudaEventElapsedTime(&time, start, end);
printf("GPU Number of floating pt operations done %e\n", (double) N * N * T * B);
printf("GPU Time using CUDA events: %f ms\n", time); // time is in ms
cudaEventDestroy(start);
cudaEventDestroy(end);
return 0;
}
Sample partial code to measure performance on GPU (contd)