## Slide 1: Introduction to GPGPU (CS 525G) Lecture 7 - Graphics Interoperability, Atomics, Page Locked Memory
Prof Emmanuel Agu
Computer Science Dept.
Worcester Polytechnic Institute (WPI)
Notes: <number>

## Slide 2: Outline
Graphics interoperability
Atomics
Concurrent execution between host and device
Pagelocked memory
Notes: <number>

## Slide 3: CUDA graphics Interoperability
Remember: G in GPU stands for Graphics
GPUs first good at graphics,
  Then General Purpose GPGPU (non-graphics)
Sometimes want:
  complex calculations + graphics rendering

## Slide 4: CUDA Graphics Interoperability
Example: Image processing applications may do complex calculations (per pixel) then display image
Original Image
Sobel Filter

## Slide 5: CUDA graphics Interoperability
Yes!
Combine CUDA with popular graphics libraries OpenGL and DirectX
  CUDA: Do calculations
  OpenGL, DirectX: Display resulting images
Approach: Share common buffers
Shared
Buffer
CUDA calculates,
Writes to shared buffer
OpenGL, DirectX reads shared buffer, displays!

## Slide 6: OpenGL and GLUT
OpenGL
    Runs on many window systems (Apple, Windows, etc)
    Concerned only with drawing
    No window management (create, resize, etc), very portable
GLUT (GL Utility Toolkit):
    Minimal window management
    Interfaces with different native windowing systems
    Easy porting between windowing systems. Fast prototyping
GLUT
OpenGL

## Slide 7: Graphics Interoperability
Graphics Interop: Map GL (OpenGL) resource into CUDA address space
  Buffers (Off screen buffers)
  Textures
  Renderbuffers

## Slide 8: Graphics Interoperability
OpenGL Buffer Interop
  Assign device with GL interop
    cudaGLSetGLDevice()
  Register GL resource with CUDA
    cudaGraphicsGLRegisterBuffer()
  Map it
    cudaGraphicsMapResources()
  Get mapped pointer
    cudaGraphicsResourceGetMappedPointer()

## Slide 9: CUDA graphics Interoperability
Consider a program that
  performs image processing calculations
  Passes data to OpenGL to render
First include header files
  CUDA interop header, cuda_gl_interop.h
  Graphics header, GL/glut.h

## Slide 10: CUDA Graphics Interoperability
First, declare two global variables to store handles to data we share between OpenGL and CUDA
Declared 2 handles to the same data
Shared
Buffer
CUDA
OpenGL
*resource
bufferObj

## Slide 11: CUDA Graphics Interoperability
Next we select a CUDA device on which to run our application
Most systems will have just one CUDA device
Some systems have multiple CUDA devices. Need to choose one

## Slide 12: CUDA Graphics Interoperability
Use cudaDeviceProp to select CUDA device
Code below tells runtime to select any GPU that has compute capability of version 1.0 or better
Clear structure
Choose Device for
CUDA + GL
ID of device satisfying constraints
Specified in &prop, returned in dev
Want CUDA 1.0 or more recent

## Slide 13: CUDA Graphics Interoperability
Then set device with returned ID as CUDA + GL device
Then make GLUT calls to initialize GLUT and create drawing window (that we have called “bitmap”)
Double buffering,
color set as RGB
Window dimensions (Width x Height)
Create window, call it “bitmap”

## Slide 14: CUDA Graphics Interoperability
Then comes the actual interoperation
Shared buffers are key for CUDA graphics interoperation
pixel buffer object (PBO) is off-screen buffer for storing pixels
First,
  Create a pixel buffer object (PBO) in OpenGL
  Store the handle in global variable Gluint bufferObj;
Shared
Buffer
CUDA
OpenGL
*resource
bufferObj
Allocate DIM x DIM
32-bit values for PBO

## Slide 15: CUDA Graphics Interoperability
Finally we notify CUDA runtime we intend to share the OpenGL buffer called bufferObj
To accomplish this we register bufferObj as a graphics resource
Graphics handle to shared buffer
CUDA handle to shared buffer
Specifies we do NOT care to make
this read-or write-only

## Slide 16: CUDA Graphics Interoperability
Instead of cudaGraphicsMapFlagsNone, we could use
cudaGraphicsMapFlagsReadOnly: buffer is read-only
cudaGraphicsMapFlagsWriteOnly: buffer is write-only
To read and write to shared buffer, we need its address
So we
  Tell CUDA runtime to map [addresses of] shared resource
  Request a pointer to mapped resource
Can use devPtr as any device pointer
OpenGL can also use data as pixel source
Size in bytes of mapped resource
Notes: <number>

## Slide 17: CUDA Graphics Interoperability
The rest of main( ) is as follows:
  Launch our kernel, passing it the pointer to our shared buffer
  (Kernel generates image to be rendered)
  Unmap our shared resource (Done with buffer!)
Last, we register keyboard and display callback functions then get into glutMainLoop( ) which does rendering
Draw_func is GLUT function where drawing is done
Key_func is GLUT function, accepts/responds to keystrokes

## Slide 18: CUDA Graphics Interoperability
Kernel takes device pointer and generates image data (similar to ripple example)

## Slide 19: CUDA Graphics Interoperability
How to draw the CUDA-generated buffer using OpenGL?
Recall the following call when we created PBO in main( )
glBindBuffer(GL_PIXEL_UNPACK_BUFFER_ARB, bufferObj);
Above call bounds shared buffer as pixel source for OpenGL driver to use in subsequent calls to glDrawPixels( )
Any glDrawPixels( ) calls renders image rendered by CUDA
Our draw_func looks like this
Double buffering: Swap front and back buffer
Draws from PBO

## Slide 20: CUDA Graphics Interoperability
Our GLUT keyboard callback function key_func
If user hits Esc key
  Cleans up (Unmaps resource, deletes buffers)
  exits program

## Slide 21: Graphics Interoperability (Full Program)
#include "../common/book.h"
#include "../common/cpu_bitmap.h"
#include "cuda.h"
#include "cuda_gl_interop.h"
PFNGLBINDBUFFERARBPROC glBindBuffer = NULL;
PFNGLDELETEBUFFERSARBPROC glDeleteBuffers = NULL;
PFNGLGENBUFFERSARBPROC glGenBuffers = NULL;
PFNGLBUFFERDATAARBPROC glBufferData = NULL;

## Slide 22: Graphics Interoperability (Full Program)
#define DIM 512
GLuint bufferObj;
cudaGraphicsResource *resource;
__global__ void kernel( uchar4 *ptr ) {
// map from threadIdx/BlockIdx to pixel position
int x = threadIdx.x + blockIdx.x * blockDim.x;
int y = threadIdx.y + blockIdx.y * blockDim.y;
int offset = x + y * blockDim.x * gridDim.x;

## Slide 23: Graphics Interoperability (Full Program)
// now calculate the value at that position
float fx = x/(float)DIM - 0.5f;
float fy = y/(float)DIM - 0.5f;
unsigned char green = 128 + 127 *
sin( abs(fx*100) - abs(fy*100) );
// accessing uchar4 vs unsigned char*
ptr[offset].x = 0;
ptr[offset].y = green;
ptr[offset].z = 0;
ptr[offset].w = 255;
}

## Slide 24: Graphics Interoperability (Full Program)
static void key_func( unsigned char key, int x, int y ) {
switch (key) {
case 27:
// clean up OpenGL and CUDA
HANDLE_ERROR( cudaGraphicsUnregisterResource( resource ) );
glBindBuffer( GL_PIXEL_UNPACK_BUFFER_ARB, 0 );
glDeleteBuffers( 1, &bufferObj );
exit(0);
}
}

## Slide 25: Graphics Interoperability (Full Program)
static void draw_func( void ) {
glDrawPixels( DIM, DIM, GL_RGBA,GL_UNSIGNED_BYTE, 0 );
glutSwapBuffers();
}
Width
Height
Format of pixel data
Type of pixel data

## Slide 26: Graphics Interoperability (Full Program)
int main( int argc, char **argv ) {
cudaDeviceProp prop;
int dev;
memset( &prop, 0, sizeof( cudaDeviceProp ) );
prop.major = 1;
prop.minor = 0;
HANDLE_ERROR( cudaChooseDevice( &dev, &prop ) );
Specifies constraints (CUDA 1.0)
ID of device meeting constraint specified in prop

## Slide 27: Graphics Interoperability (Full Program)
// tell CUDA dev we will be using for graphic interop
// from CUDA programming guide: Interoperability with
// OpenGL requires the CUDA device be specified by
// cudaGLSetGLDevice() before any other //runtime calls.
HANDLE_ERROR( cudaGLSetGLDevice( dev ) );
ID of device returned by cudaChooseDevice( ), meets constraint specified in prop

## Slide 28: Graphics Interoperability (Full Program)
// these GLUT calls need to be made before OpenGL
// calls, else we get a seg fault
glutInit( &argc, argv );
glutInitDisplayMode( GLUT_DOUBLE | GLUT_RGBA );
glutInitWindowSize( DIM, DIM );
glutCreateWindow( "bitmap" );
glBindBuffer = (PFNGLBINDBUFFERARBPROC)
GET_PROC_ADDRESS("glBindBuffer");
glDeleteBuffers = (PFNGLDELETEBUFFERSARBPROC)
GET_PROC_ADDRESS("glDeleteBuffers");

## Slide 29: Graphics Interoperability (Full Program)
glGenBuffers = (PFNGLGENBUFFERSARBPROC)
GET_PROC_ADDRESS("glGenBuffers");
glBufferData = (PFNGLBUFFERDATAARBPROC)
GET_PROC_ADDRESS("glBufferData");
glGenBuffers( 1, &bufferObj );
glBindBuffer( GL_PIXEL_UNPACK_BUFFER_ARB, bufferObj );
glBufferData( GL_PIXEL_UNPACK_BUFFER_ARB, DIM * DIM * 4, NULL, GL_DYNAMIC_DRAW_ARB );

## Slide 30: Graphics Interoperability (Full Program)
// Tell CUDA want to use buffer for CUDA + graphics
HANDLE_ERROR( cudaGraphicsGLRegisterBuffer( &resource,
bufferObj, cudaGraphicsMapFlagsNone ) );
// map the shared buffer addresses
HANDLE_ERROR( cudaGraphicsMapResources( 1, &resource, NULL ) );
uchar4* devPtr;
size_t size;

## Slide 31: Graphics Interoperability (Full Program)
// Get ptr to mapped buffer addresses
HANDLE_ERROR(
cudaGraphicsResourceGetMappedPointer( (void**)&devPtr, &size, resource) );
dim3 grids(DIM/16,DIM/16);
dim3 threads(16,16);
kernel<<<grids,threads>>>( devPtr );
// done with calculation, unmap resource
HANDLE_ERROR( cudaGraphicsUnmapResources( 1, &resource, NULL ) );

## Slide 32: Graphics Interoperability (Full Program)
// set up GLUT keyboard and draw functions,
// then sit in GLUT main loop
glutKeyboardFunc( key_func );
glutDisplayFunc( draw_func );
glutMainLoop();
}

## Slide 33: CUDA graphics Interoperability
Resulting image

## Slide 34
Atomics and Critical Sections
Now introduce:
Accessing shared data by multiple threads
Atomics
Critical sections
Compare and swap instruction and usage
Memory fence instruction and usage

## Slide 35: Atomic Functions
__device__ unsigned int count = 0;
// ...
++count;
What is value of count if 8 threads execute ++count?
Can cause problems if multiple threads modify the same variable
Notes: 1 to 8. Maybe 1 if all threads are in the same warp and issued at the same time.
<number>

## Slide 36: Atomic Functions
__device__ unsigned int count = 0;
// ...
++count;
What is value of count if 8 threads execute ++count?
Can cause problems if multiple threads modify the same variable
Ans: 1 to 8 Maybe 1 if all threads are in the
same warp and issued at the same time.
Notes: 1 to 8. Maybe 1 if all threads are in the same warp and issued at the same time.
<number>

## Slide 37
Accessing shared data needs careful control.
Consider two threads each of which is to add one to a shared data item, x.
Location x is read, x + 1 computed, and result written back to the same location:
Accessing Shared Data
Instruction
x = x + 1;
Thread 2
Thread 1
Read x
Compute x + 1
Write to x
Read x
Compute x + 1
Write to x
Time
Thread 1 and 2 instructions may occur in any order: Race condition!!!

## Slide 38
Conflict in accessing shared variable
Thread 1
Thread 2

## Slide 39
One possible interleaving
Thread 1 Read x
Thread 1 Compute x + 1
Thread 1 Write to x
Time
Thread 2 Read x
Thread 2 Compute x + 1
Thread 2 Write to x
Suppose initial value of x is 10.
What is the final value?

## Slide 40
Need to ensure each thread is allowed exclusive access to shared variable to complete its operation (if a write operation is involved)
Atomic functions perform a read-modify-write operation on a word in shared memory without interference by other threads
Access to the memory location with specified address is blocked until atomic completed.
Atomic Functions

## Slide 41
CUDA Atomic Operations
Performs read-modify-write atomic operation on one word residing in global or shared GPU memory.
  - Guaranteed no interference from other threads
  - No guarantee on order
Defined operations on signed/unsigned integers, add, sub, min, max, and, or, xor, increment, decrement, exchange, compare and swap.
Requires GPU with compute capability 1.1+ (> G80)
(Shared memory operations and 64-bit words require higher capability)

## Slide 42
Example CUDA atomics*
int atomicAdd(int* address, int val);
Adds val to memory location given by address, atomically (atomic read-modify-write operation)
int atomicSub(int* address, int val);
Subtracts val from memory location given by address, atomically (atomic read-modify-write operation)
Functions returns original value in address.
* See CUDA C Programming Guide for full list

## Slide 43: Atomic Functions
__device__ unsigned int count = 0;
// ...
// atomic ++count
atomicInc(&count, 1);
What is the value of count if 8 threads execute atomicInc below?
Notes: 8 – no race condition
<number>

## Slide 44: Atomic Functions
__device__ unsigned int count = 0;
// ...
// atomic ++count
atomicInc(&count, 1);
What is the value of count if 8 threads execute atomicInc below?
Ans: Always 8 – no race condition!
Notes: 8 – no race condition
<number>

## Slide 45
#include <stdio.h>
#include <cuda.h>
#include <stdlib.h>
__device__ int gpu_Count=0; //global variable in device
__global__ void gpu_Counter() {
atomicAdd(&gpu_Count,1);
}
int main(void) {
int cpu_Count;
…
gpu_Counter<<<B,T>>>();
cudaMemcpyFromSymbol(&cpu_Count, "gpu_Count",
sizeof(int), 0, cudaMemcpyDeviceToHost);
printf("Count = %d\n",cpu_Count);
…
return 0;
}
Example code
Synchronous, so cudaThreadSynchronize() not needed

## Slide 46
Another Example
Computing Histogram
// globally accessible on gpu
__device__ int gpu_hist[10]; // histogram computed on gpu
__global__ void gpu_histogram(int *a, int N) {
int *ptr;
int tid = blockIdx.x * blockDim.x + threadIdx.x;
int numberThreads = blockDim.x * gridDim.x;
while (tid < N) {
ptr = &gpu_hist[a[tid]];
atomicAdd(ptr,1);
tid += numberThreads; // if no of threads less than N, threads reused
}
}

## Slide 47
int main(int argc, char *argv[]) {
int T = 10, B = 10; // threads per block and blocks per grid
int N = 10; // Number of numbers
int *a; // ptr to array holding numbers on host
int *dev_a; // ptr to array holding numbers on device
int hist[10]; // final results from gpu
printf("Enter number of numbers, currently %d\n",N);
scanf("%d",&N);
input_thread_values(&B,&T); // keyboard input for no of threads and blocks
if (N > B * T) printf("Note; number of threads less than number of numbers\n");
int size = N * sizeof(int); // number of bytes in total in list of numbers
a = (int*) malloc(size);
srand(1); // set rand() seed to 1 for repeatability
for(int i=0;i<N;i++) // load arrays with digits
a[i] = rand() % 10;

## Slide 48
cudaMalloc((void**)&dev_a, size);
cudaMemcpy(dev_a, a , size ,cudaMemcpyHostToDevice); // copy numbers to device
gpu_histogram<<<B,T>>>(dev_a,N);
cudaThreadSynchronize(); // wait for all threads to complete, needed?
cudaMemcpyFromSymbol(&hist, "gpu_hist", sizeof(hist), 0, cudaMemcpyDeviceToHost);
printf("Histogram, as computed on GPU\n");
for(int i = 0;i < 10;i++)
printf("Number of %d's = %d\n",i,hist[i]);
free(a); // clean up
cudaFree(dev_a);
return 0;
}

## Slide 49
Other atomic operations
int atomicSub(int* address, int val);
int atomicExch(int* address, int val);
int atomicMin(int* address, int val);
int atomicMax(int* address, int val);
unsigned int atomicInc(unsigned int* address, unsigned int val);
unsigned int atomicDec(unsigned int* address, unsigned int val);
int atomicCAS(int* address, int compare, int val); //compare and swap
int atomicAnd(int* address, int val);
int atomicOr(int* address, int val);
int atomicXor(int* address, int val);
Source: NVIDIA CUDA C Programming Guide, version 3.2, 11/9/2010

## Slide 50
A mechanism for ensuring that only one process (or in this context, thread) accesses a particular resource at a time.
critical section – a section of code for accessing resource
Arrange that only one such critical section is executed at a time.
This mechanism is known as mutual exclusion.
Concept also appears in an operating systems.
Critical Sections

## Slide 51
Simplest mechanism for ensuring mutual exclusion of critical sections.
A lock: 1-bit variable
- set to 1 to indicates a process in critical section (occupied)
- set to 0 to indicates no process in critical section (vacant)
Operates much like that of a door lock (bathroom?):
A process coming to “door” of a critical section and finding it open may enter critical section, locking the door behind it to prevent other processes from entering.
Once process has finished the critical section, it unlocks the door and leaves
Locks

## Slide 52
<number>
Control of critical sections through busy waiting

## Slide 53
Implementing Locks
Checking lock and setting it if not set at the entrance to a critical section must be done indivisibly and atomically
Usual way to achieve this is for the processor to have special atomic machine instruction notably one of:
Test and set
Fetch and add
Compare and Swap CAS (or compare and exchange)

## Slide 54
Compare and Swap CAS
  CAS -- compares contents of a memory location to a given value and only if the same, modifies contents of the memory location to a specified value, i.e.:
  if (x == compare_value ) x = new_val; (else x = x;)
  For a critical section lock:
  x = lock variable
  compare_value = 0 (FALSE)
  new_value = 1 (TRUE)
  i.e if (x == 0) x = 1; (else x = x;)

## Slide 55
__device__ int lock=0; // unlocked
__global__ void kernel(...) {
...
do {} while (atomicCAS(&lock,0,1) ); // if lock = 0 set to1
// and enter
... // critical section
lock = 0; // free lock
…
}
Coding Critical Sections with “Spin” Locks

## Slide 56
Critical Sections Serializing Code
High performance programs should have as few as possible critical sections as their use can serialize the code.
Suppose, all processes happen to come to their critical section together.
They will execute their critical sections one after the other
(parallel becomes sequential execution)
Performance becomes almost that of a single processor

## Slide 57
Illustration

## Slide 58
Results from Histogram program

## Slide 59
<number>
3.1 seems max because of accesses to shared histogram array
More threads than numbers obviously will not help
Less threads than numbers causes threads to be reused in counting, so slower
Varying N, T and B

## Slide 60
Memory Fences
Threads may see effects of a series of writes to memory executed by another thread in different orders. To enforce ordering:
void __threadfence_block();
waits until all global and shared memory accesses made by calling thread prior to __threadfence_block() are visible to all threads in thread block.
Other routines:
void __threadfence();
void __threadfence_system();

## Slide 61
<number>
Writes to device memory not guaranteed in any order, so global writes may not have completed by the time the lock is unlocked
__global__ void kernel(...) {
...
do {} while(atomicCAS(&lock,0,1));
... // critical section
__threadfence(); // wait for writes to finish
lock = 0;
}
Critical sections with memory operations

## Slide 62: Atomic Functions
How do you implement atomicInc?
__device__ int atomicAdd(
int *address, int val);
Notes: <number>

## Slide 63: Atomic Functions
How do you implement atomicInc?
__device__ int atomicAdd(
int *address, int val)
{ // Made up keyword:
__lock (address) {
*address += value;
}
}
Notes: <number>

## Slide 64: Atomic Functions
Lots of atomics:
// Arithmetic // Bitwise
atomicAdd() atomicAnd()
atomicSub() atomicOr()
atomicExch() atomicXor()
atomicMin()
atomicMax()
atomicInc()
atomicDec()
atomicCAS()
See B.10 in the NVIDIA CUDA C Programming Guide
Notes: <number>

## Slide 65: Concurrent Execution between Host and Device
In order to facilitate concurrent execution between host and device, some function calls are asynchronous
  Control is returned to the host thread before the device has completed the requested task
Examples of asynchronous calls
  Kernel launches
  Device $ device memory copies
  Host $ device memory copies of a memory block of 64 KB or less
  Memory copies performed by functions that are suffixed with Async
NOTE: When an application is run via a CUDA debugger or profiler (cuda-gdb, CUDA Visual Profiler, Parallel Nsight), all launches are synchronous
<number>

## Slide 66: Concurrent Kernel Execution [CUDA 3.2]
Feature allows up to 16 kernels to be run on the device at the same time
When is this useful?
  Devices of compute capability 2.x are pretty wide (large number of SMs)
  Sometimes you launch kernels whose execution configuration is smaller than the GPU’s “width”
  Then, two or three independent kernels can be “squeezed” on the GPU at the same time
Represents one of GPU’s attempts to look like a MIMD architecture
<number>

## Slide 67: Host-Device Data Transfer Issues
In general, host $ device data transfers using cudaMemcpy() are blocking
  Control is returned to the host thread only after the data transfer is complete
There is a non-blocking variant, cudaMemcpyAsync()
  The host does not wait on the device to finish the mem copy and the kernel call for it to start execution of cpuFunction() call
  The launch of “kernel” only happens after the mem copy call finishes
NOTE: the asynchronous transfer version requires pinned host memory (More later)
<number>

## Slide 68: Overlapping Host $ Device Data Transfer with Device Execution
When is this overlapping useful?
  Imagine a kernel executes on the device and only works with the lower half of the device memory
  Then, you can copy data from host to device in the upper half of the device memory?
  These two operations can take place simultaneously
Note that there is a issue with this idea:
  The device execution stack is FIFO, one function call on the device is not serviced until all the previous device function calls completed
  This would prevent overlapping execution with data transfer
This issue was addressed by the use of CUDA “streams” (More later)
<number>

## Slide 69: Page-Locked Host Memory
Page-locked Memory
  Host memory that is essentially removed from virtual memory
  Also called Pinned Memory

## Slide 70: Page-Locked Host Memory
Benefits
  Overlap kernel execution and data transfers
See G.1 in the NVIDIA CUDA C Programming Guide for full compute capability requirements
Time
Data Transfer
Kernel Execution
Data Transfer
Kernel Execution
Normally:
Paged-locked:

## Slide 71: Page-Locked Host Memory
Benefits
  Increased memory bandwidth for systems with a front-side bus (carries data from CPU to north bridge)
    Up to ~2x throughput
Image from http://arstechnica.com/hardware/news/2009/10/day-of-nvidia-chipset-reckoning-arrives.ars
Notes: <number>

## Slide 72: Page-Locked Host Memory
Benefits
  Paged-locked host memory can be mapped into the address space of the device on some systems
  Does your system support this?
    Call cudaGetDeviceProperties() and check canMapHostMemory
Notes: Hybrid CPU/GPU, mobile?, consoles
Eliminates the need to copy to and from host memory.
Enables applications where the memory transfer (bus bandwidth) was the bottleneck such as simple image processing.
<number>

## Slide 73: Page-Locked Host Memory
Previously allocated memory on host using malloc( )
Another mechanism for CUDA programs to allocate memory on host using command cudaHostAlloc( )
Key difference between between malloc and cudaHostAlloc:
  OS can page memory allocated by malloc out to disk
  OS cannot page memory allocated by cudaHostAlloc out to disk: page-Locked!!
Since address of page-locked host memory never changes,
  OS can let application access physical address
  GPU can use DMA to copy data to host
  GPU-CPU Copy speed over 2x over pageable memory on most systems

## Slide 74: Page-Locked Host Memory
Disadvantage of page-locked memory:
  Application needs physical memory for every page-locked buffer
  Memory on host runs out quicker
  Other programs running on system can be affected
Next, we create an example program
  Compares speed of pageable vs page-locked memory for copying
  Allocates equal size memory on GPU and CPU
  Copies data either GPU-to-host (up) or from host-to-GPU (down)
  Uses pageable or page-locked memory and compares speed

## Slide 75: Page-Locked Host Memory
Disadvantage of page-locked memory:
  Application needs physical memory for every page-locked buffer
  Memory on host runs out quicker
  Other programs running on system can be affected
Next, we create an example program
  Compares speed of pageable vs page-locked memory for copying
  Allocates equal size memory on GPU and CPU
  Copies data either GPU-to-host (up) or from host-to-GPU (down)
  Uses pageable or page-locked memory and compares speed

## Slide 76: Page-Locked Host Memory
Performance shall be timed using CUDA events as before:
Allocate host and GPU buffers of size integers
This version uses standard malloc( ) to allocate pageable host memory

## Slide 77: Page-Locked Host Memory
Perform 100 copies in direction specified by variable up
Stop timer after copying

## Slide 78: Page-Locked Host Memory
Clean up by
  Freeing host and GPU buffers
  Destroying timer events

## Slide 79: Page-Locked Host Memory
Consider version of cuda_malloc_test using cudaHostAlloc( )

## Slide 80: Page-Locked Host Memory

## Slide 81: Page-Locked Host Memory

## Slide 82: Page-Locked Host Memory
The main function
Since up argument is true, host to device performance is tested

## Slide 83: Page-Locked Host Memory
Now measure device to host copy speed by repeating calls with up argument set to false
Since up argument is false, device to host performance is tested

## Slide 84: Page-Locked Host Memory
Perform same tests using cudaHostAlloc( ) once with up argument set to true and once set to false

## Slide 85: Page-Locked Host Memory
Usage:
cudaHostAlloc() / cudaMallocHost()
cudaHostFree()
cudaMemcpyAsync()
See 3.2.5 in the NVIDIA CUDA C Programming Guide
Notes: <number>

## Slide 86: Page-Locked Host Memory
What’s the catch?
  Page-locked memory is scarce
    Allocations will start failing before allocation of in pageable memory
  Reduces amount of physical memory available to the OS for paging
    Allocating too much will hurt overall system performance
Notes: <number>