## Slide 1: Introduction to GPGPU CS 525G – Lecture 2 Introduction to GPU Hardware, Setting up and Programming
Prof Emmanuel Agu
Computer Science Dept.
Worcester Polytechnic Institute (WPI)
Notes: <number>

## Slide 2: Outline
Introduction to GPU Hardware
Setting up (Hardware and Software)
CUDA program structure
CUDA Hello World program
Compiling and debugging CUDA programs
Notes: <number>

## Slide 3: Choosing CUDA Hardware
  CUDA-capable GPUS
    Graphics cards: do graphics + CUDA (Nvidia, Intel, AMD, etc)
    Nvidia Tesla cards: Does only GPGPU
  Recall: Where to find CUDA versions supported by hardware:
    Go to http://developer.nvidia.com/cuda-gpus
  Recall: Which cards are in machines?
    Check Control panel->system->Device Manager

## Slide 4: Choosing GPU Hardware
  GPU card considerations
    Graphics only or also GPGPU
    Form factor: Half vs full height
    CPU memory
    Bus: PCI express (GPU cards usually need 16 lanes)
    Power supply:
      Is machine power supply big enough? Some tesla cards need 1000W power supply
  Physical installation: open machine, insert GPU card

## Slide 5: GPU Server?
Using Nvidia SLI, may install multiple cards

## Slide 6: Why Study Hardware?
Before installing software, let’s study hardware
Why? To understand major factors that dictate performance when using GPU for GPGPU
  The feeds (interconnects) and speeds of traditional CPU world
  The feeds and speeds when employing a GPU
  Leverage knowledge for performance programming in GPU

## Slide 7: Bandwidth : Gravity of Modern Computer Systems
Recall GPU Computation Model:
  Copy data to GPU
  Compute
  Copy back
The Bandwidth between key (CPU and GPU) components ultimately dictates system performance
  Especially for massively parallel systems processing massive amount of data
CPU
GPU
Bottleneck
Notes: <number>

## Slide 8: Classic PC architecture
Northbridge connects 3 components that need high speed communication
  CPU, DRAM, video
  Previous NVIDIA cards connected to AGP (2 GB/s)
Southbridge is a concentrator for slower I/O devices
CPU
Core Logic Chipset

## Slide 9: Bandwidth in a CPU-GPU System
Robert Strzodka, Max Plank Institute, Germany
<number>
Notes: <number>

## Slide 10: (Original) PCI Bus Specification
Connected to southBridge
  Originally 33 MHz, 32-bit wide, 132 MB/sec peak transfer rate
  More recently 66 MHz, 64-bit, 512 MB/sec peak
  Upstream bandwidth remain slow for device (256MB/sec peak)
  Shared bus with arbitration
    Winner of arbitration becomes bus master and can connect to CPU or DRAM through southbridge and northbridge

## Slide 11: PCI Express (PCIe)
Switched, point-to-point connection
  Each card has a dedicated “link” to the central switch, no bus arbitration.
  Prioritized packets for QoS
    E.g., real-time video streaming

## Slide 12: PCIe Links and Lanes
Each link: 1 or more lanes
  Each lane = 1-bit (2.5Gb/s upstream and downstream)
    Bi-directional, symmetric
  Each Link may have 1, 2, 4, 8, 12, 16 lanes- x1, x2, etc.
  Data bytes 8b/10b encoded
  1 data byte = 10 encoded bits
  Thus, net data rates each way
    2500/10 = 250 MBytes/s (x1)
    500 MB/s (x2)
    1GB/s (x4)
    2 GB/s (x8)
    4 GB/s (x16)
Best for GPGPU

## Slide 13: PCIe Connectors
On motherboard

## Slide 14: PCIe PC Architecture
PCIe forms the interconnect backbone
  Northbridge/Southbridge are both PCIe switches
Source: Jon Stokes, PCI Express: An Overview
  http://arstechnica.com/articles/paedia/hardware/pcie.ars

## Slide 15: Today’s Intel PC Architecture: Single Core System
FSB connection between processor and Northbridge (82925X)
  Memory Control Hub
Northbridge handles “primary” PCIe to video/GPU and DRAM.
  PCIe x16 bandwidth at 8 GB/s (4 GB each direction)
Southbridge (ICH6RW) handles other peripherals

## Slide 16: Nvidia GPU Generations: G80, GT200, and Fermi
November 2006: G80 (GeForce 8 series, 8400M, 8700, 8800)
June 2008: GT200 (GTX 260, 280)
March 2011: Fermi (GF100) (GTX 470, 480, 495)
Image from: http://stanford-cs193g-sp2010.googlecode.com/svn/trunk/lectures/lecture_11/the_fermi_architecture.pdf
Notes: Fermi design started around 2005.
<number>

## Slide 17: GeForce 7800 GTX Board Details
256MB/256-bit DDR3
  600 MHz
  8 pieces of 8Mx32
16x PCI-Express
SLI Connector
DVI x 2
sVideo
TV Out
Single slot cooling

## Slide 18: GeForce-8 Series HW Overview
TPC
TPC
TPC
TPC
TPC
TPC
TEX
SM
SP
SP
SP
SP
SFU
SP
SP
SP
SP
SFU
Instruction Fetch/Dispatch
Instruction L1
Data L1
Texture Processor Cluster
Streaming Multiprocessor
SM
Shared Memory
Streaming Processor Array
…

## Slide 19: NVIDIA TESLA C1060 [Newton’s GPU cards]
<number>
240 Scalar Processors
4 GB device memory
Memory Bandwidth: 102 GB/s
Clock Rate: 1.3GHz
Approx. $1,250
Notes: <number>

## Slide 20: Streaming Multiprocessor (SM)
Streaming Multiprocessor (SM)
  8 Streaming Processors (SP)
  2 Super Function Units (SFU)
Multi-threaded instruction dispatch
  1 to 512 threads active
20+ GFLOPS
16 KB shared memory
texture and global memory access
SP
SP
SP
SP
SFU
SP
SP
SP
SP
SFU
Instruction Fetch/Dispatch
Instruction L1
Data L1
Streaming Multiprocessor
Shared Memory

## Slide 21: Fermi: What’s More?
More total cores (SPs) – not SMs though
More registers: 32K per SM
More shared memory: up to 48K per SM
More Super Functional Units (SFUs)

## Slide 22: Fermi: What’s Faster?
Faster double precision – 8x over GT200
Faster atomic operations - 5-20x
Faster context switches
  Between applications – 10x
  Between graphics and compute, e.g., OpenGL and CUDA
Notes: Double precision runs at half speed, on GT200 it was 1/8 speed
Atomics are faster due to L1/L2 caches and more atomic hardware units.
Faster atomics allow more CPU-like applications like ray tracing and random scatter.
Application context switches are below 25 microseconds
<number>

## Slide 23: Fermi: What’s New?
L1 and L2 caches.
  For compute or graphics?
Dual warp scheduling
Concurrent kernel execution
C++ support
Unified address space
Error Correcting Code (ECC) memory support
Fixed function tessellation for graphics
Notes: Previous L1/L2 was for textures only
Motivation for cache is more for compute than graphics. Graphics is streaming; all data is brought on-chip each frameC++ support includes virtual functions, new/delete, and try/catch
C++: virtual functions, new/delete, try/catch
IEEE support includes denorms, so it doesn’t flush to zero. It is a pain to do in hardware; CPUs would use a trap and do it in software – thousands of cycles
Previous GPUs used IEEE 754-198
<number>

## Slide 24: G80, GT200, and Fermi
Image from: http://stanford-cs193g-sp2010.googlecode.com/svn/trunk/lectures/lecture_11/the_fermi_architecture.pdf
Notes: Number of cores have basically increased at the same rate as the number of transistors, following Moore’s Law. Granted, double precision support was added as well as L1 and L2 caches and more complex dispatch (dual warp scheduling).
<number>

## Slide 25: Fermi Block Diagram
Image from: http://www.nvidia.com/content/PDF/fermi_white_papers/NVIDIA_Fermi_Compute_Architecture_Whitepaper.pdf
GF100
16 SMs
Each with 32 cores
  512 total cores
Each SM hosts up to
  48 warps, or
  1,536 threads
In flight, up to
  24,576 threads

## Slide 26: Fermi: 32 Cores Per SM
G80 – 8 cores
GT200 – 8 cores
GF100 – 32 cores
Notes: Enables dual-warp scheduling. 2 cycles per warp now, instead of 4.
<number>

## Slide 27
Slide from: http://gpgpu.org/wp/wp-content/uploads/2009/11/SC09_CUDA_luebke_Intro.pdf
Notes: Kernels from same application execute in parallel
<number>

## Slide 28: Fermi Caches
Slide from: http://stanford-cs193g-sp2010.googlecode.com/svn/trunk/lectures/lecture_11/the_fermi_architecture.pdf
Notes: Registers spill to L1 cache instead of directly to DRAM
<number>

## Slide 29: Fermi: Unified Address Space
Image from: http://www.nvidia.com/content/PDF/fermi_white_papers/NVIDIA_Fermi_Compute_Architecture_Whitepaper.pdf
Notes: Useful for developers implementing libraries since one pointer can point to any memory type.
<number>

## Slide 30: Fermi: Unified Address Space
64-bit virtual addresses
40-bit physical addresses (currently)
CUDA 4: Shared address space with CPU. Why?
  No explicit CPU/GPU copies
  Direct GPU-GPU copies
  Direct I/O device to GPU copies
Notes: Useful for developers implementing libraries since one pointer can point to any memory type.
<number>

## Slide 31: Fermi Tessellation
Image from: http://stanford-cs193g-sp2010.googlecode.com/svn/trunk/lectures/lecture_11/the_fermi_architecture.pdf
Notes: 1.6 billion triangles per second for water
Hair include physics simulation and rendering
<number>

## Slide 32: Setting up: Nvidia GPGPU software tools
  After setting up GPU hardware
  Set up software tools
    Nvidia device driver
    CUDA development tookit
    A standard C compiler (e.g. Visual Studio)
    [Optional] GPU Computing SDK (CUDA examples)

## Slide 33: 1. Update Nvidia Device Driver
  Drivers allow your programs communicate with CUDA hardware
  Check for latest drivers for your hardware:
    Go to www.nvidia.com/page/drivers.html , specify OS, GPU card, etc
    Download latest drivers (if necessary)

## Slide 34: 2. CUDA Development Toolkit
  Includes CUDA GPU compiler (nvcc)
  Go to http://developer.nvidia.com/cuda-toolkit
  Download latest Nvidia toolkit (Currently at 4.0)

## Slide 35: 3. Standard C Compiler
CUDA toolkit (nvcc compiler) is for GPU
Need Standard C compiler for host (CPU) code
Windows: Visual Studio (2005, 2008, 2010)
  Visual Studio Express (2008, 2010) free
Linux: ships with gcc compiler
  Fedora 13, Redhat Enterprise (4.8, 5.5, 6.0), Ubuntu Linux 10.10, OpenSUSE 11.2, SUSE Linux Enterprise Server

## Slide 36: 3. Standard C Compiler (Contd)
Macintosh OS X
  CUDA 4.0 Need at least version 10.6.7 of Mac OS X
  Download gcc by downloading Apple’s Xcode
  Xcode is apple’s IDE for developing Mac, iPhone programs
  Xcode available for free at http://developer.apple.com/xcode/

## Slide 37: 4. Get Nvidia GPU Computing SDK
Contains dozens of sample GPU computing applications
  Code, white papers
Optional since you can write your own programs without it
Various categories of applications including
  CUDA basic topics
  CUDA advanced topics
  CUDA systems integration
  Data-parallel algorithms
  Graphics interoperability
  Performance strategies
  Linear algebra
  Image/Video Processing

## Slide 38: Nvidia GPU SDK
More categories sample applications
  Computational finance
  Data Compression
  Physically-Based Simulation

## Slide 39: Hello World
#include "../common/book.h"
int main( void ) {
printf( "Hello, World!\n" );
return 0;
}

## Slide 40: GPU Hello World
#include "../common/book.h"
__global__ void kernel( void ) {
}
int main( void ) {
kernel<<<1,1>>>();
printf( "Hello, World!\n" );
return 0;
}
Note: printf possible on CPU
On old CUDA hardware,
Cannot do printf on device
Fermi can now do printf on device

## Slide 41: Single-Program Multiple-Data (SPMD)
CUDA integrated CPU + GPU application C program
  Serial C code executes on CPU
  Parallel Kernel C code executes on GPU thread blocks
CPU Serial Code
Grid 0
. . .
. . .
GPU Parallel Kernel
KernelA<<< nBlk, nTid >>>(args);
Grid 1
CPU Serial Code
GPU Parallel Kernel
KernelB<<< nBlk, nTid >>>(args);

## Slide 42
Compiling a CUDA Program
NVCC
  C/C++ CUDA
  Application
PTX to Target
Compiler
  G80
  …
GPU
Target code
  PTX Code
Virtual
Physical
  CPU Code
Compilation of NVCC
.cu file compiled by nvcc
Produce PTX assembly code
Produce cubin file for specific hardware
Produce host C code
•PTX(Parallel Thread Execution) code
Can be ported to different GPUs
PTX 2.0 for Fermi architecture
cubin binary code
For a particular GPU
Generate by recompiling PTX
float4 me = gx[gtid];
me.x += me.y * me.z;
ld.global.v4.f32 {$f1,$f3,$f5,$f7}, [$r9+0];
mad.f32 $f1, $f5, $f3, $f1;
Notes: <number>

## Slide 43
Compilation
Any source file containing CUDA language extensions must be compiled with NVCC
NVCC is a compiler driver
  Works by invoking all the necessary tools and compilers like cudacc, g++, cl, ...
NVCC outputs:
  C code (host CPU Code)
    Must then be compiled with the rest of the application using another tool
  PTX
    Object code directly
    Or, PTX source, interpreted at runtime
Notes: <number>

## Slide 44: Linking
Any executable with CUDA code requires two dynamic libraries:
  The CUDA runtime library (cudart)‏
  The CUDA core library (cuda)‏
Notes: <number>

## Slide 45: Debugging Using the Device Emulation Mode
An executable compiled in device emulation mode
(nvcc -deviceemu) runs completely on host using CUDA runtime
  No need of any device and CUDA driver
  Each device thread is emulated with a host thread
Running in device emulation mode, one can:
  Use host native debug support (breakpoints, inspection, etc.)‏
  Access any device-specific data from host code and vice-versa
  Call any host function from device code (e.g. printf) and vice-versa
  Detect deadlock situations caused by improper usage of __syncthreads
Notes: <number>

## Slide 46: Device Emulation Mode Pitfalls
Emulated device threads execute sequentially
Simultaneous accesses of the same memory location by multiple threads could produce different results.
Dereferencing device pointers on host or host pointers on the device can produce correct results in device emulation mode, but will generate an error in device execution mode
Notes: <number>
What are the options that the students can use?

## Slide 47: Debugging CUDA Programs
CUDA-GDB (On Linux)
Nvidia extended open source gdb debugger to support GPUs
Familiar gdb interface maintained
Programmers can debug CUDA kernels (functions) right on GPU
Highlights
  View CUDA state: installed GPUs and their capabilities, etc
  Set breakpoints in CUDA code
  Inspecting GPU memory (global, shared, etc)
  Breaking into hung or deadlocked running applications
Also includes cuda-memcheck tool that allows insights into memory violations, misaligned memory accesses, etc

## Slide 48: Nvidia Parallel Nsight
Windows-based debugger
Introduced end of 2009
Integrated CPU/GPU debugger for Microsoft Visual Studio
Currently available in Windows 7 or Vista
Not available in Windows XP (not available in this class)
Uses can
  Debug CUDA code with thousands of threads
  Place breakpoints
  Inspect memory directly, detect out-of-bounds memory accesses

## Slide 49: Nvidia Parallel Nsight: Debugger

## Slide 50: Nvidia Parallel Nsight: Performance Analysis
View CPU+GPU events to isolate performance bottlenecks

## Slide 51: Nvidia Visual Profiler
Visually identify why some CUDA code isn’t performing well
Example: compare two implementations of matrix transpose

## Slide 52: Passing Parameters to Kernels
#include "../common/book.h“
__global__ void add( int a, int b, int *c ) {
*c = a + b;
}
int main( void ) {
int c;
int *dev_c;
HANDLE_ERROR( cudaMalloc( (void**)&dev_c, sizeof(int) ) );

## Slide 53: Passing Parameters to Kernels
add<<<1,1>>>( 2, 7, dev_c );
HANDLE_ERROR( cudaMemcpy( &c, dev_c, sizeof(int),
cudaMemcpyDeviceToHost) );
printf( "2 + 7 = %d\n", c );
HANDLE_ERROR( cudaFree( dev_c ) );
return 0;
}

## Slide 54: Application Programming Interface
CUDA C API is extension to C prog. language
It consists of:
  Language extensions
    To target portions of code for execution on the device
  A runtime library split into:
    A common component providing built-in vector types and subset of C runtime library in both host and device codes
    A host component to control and access one or more devices from the host
    A device component providing device-specific functions

## Slide 57: Common Runtime Component: Mathematical Functions
pow, sqrt, cbrt, hypot
exp, exp2, expm1
log, log2, log10, log1p
sin, cos, tan, asin, acos, atan, atan2
sinh, cosh, tanh, asinh, acosh, atanh
ceil, floor, trunc, round, etc
  When executed on the host, a given function uses the C runtime implementation if available
  These functions are only supported for scalar types, not vector types

## Slide 58: Device Runtime Component: Mathematical Functions
Some mathematical functions (e.g. sin(x)) have a less accurate, but faster device-only version (e.g. __sin(x))
  __pow
  __log, __log2, __log10
  __exp
  __sin, __cos, __tan

## Slide 59: Host Runtime Component
Provides functions to deal with:
  Device management (including multi-device systems)
  Memory management
  Error handling
Initializes the first time a runtime function is called
A host thread can invoke device code on only one device
  Multiple host threads required to run on multiple devices