## Slide 1: Networking for Games
IMGD 4000

## Slide 2: Introduction (1 of 2)
Games are increasingly networked
  Multi-player, connecting PCs and Game consoles (e.g., Counter-strike, Halo)
  Single-player, pulling and pushing content to Web service (e.g., Lumosity)
Emerging services play game in “cloud”, sending rendered game down as video
  (However, will not talk about this approach much)
All require an understanding of networking (conversant), with enough knowledge to design and build network game (develop)

## Slide 3: Introduction (2 of 2)
For now, “networking” mostly means “Internet networking”, so that will be our reference
Other networking aspects that can be relevant for games includes:
  Ad Hoc / Mesh networking
  Short-range wireless (e.g., Bluetooth)
  Network security (including cheating)
  Mobile application (game) development (often networked)
These, and other topics available in-depth from your friendly, neighborhood WPI course
(next slide)

## Slide 4: Networking at WPI
General, core networks:
  CS 3516 – Computer Networks
  Broad view of computer networks, top-down
  CS 4516 – Advanced Computer Networks
  In-depth computer networks, more “under the hood”
Networks applied to specific domains
  CS 4513 – Distributed Systems
  CS 4518 – Mobile and Ubiquitous Computing
  CS 4241 – Webware: Computational Technology for Network Information Systems
  CS 4404 – Tools and Techniques in Computer Network Security
Also grad courses
  CS 513 – Introduction to Local and Wide Area Networks
  CS 528 – Mobile and Ubiquitous Computing
  CS 529 – Multimedia Networking
  CS 530 – High-Performance Networks
  CS 533 – Modeling and Performance Evaluation of Network and Computer Systems
  CS 558 – Computer Network Security
  CS 577 – Advanced Computer and Communications Networks
This deck  core networking applied to computer games.

## Slide 5: The Internet from the Edge (1 of 2)
Reasonable analogy  Postal Service
  Letter in envelope
  Find address of business in phonebook
  Address on envelope
  Put in Mailbox  trust that will reach destination
  Don’t know how envelope gets there
  Delivery takes different amounts of time for each
    Generally, further away longer (but not always)
  Use external ways to confirm
    (ex: Use phone, or resend letter until confirmation)

## Slide 6: The Internet from the Edge (2 of 2)
Reasonable analogy  Postal Service
Users view the Internet similarly  An opaque cloud
  User application content is like letter
  Putting content into packet for sending is like envelope
  IP address is like address on envelope
  Internet name service (DNS) to find address is like phonebook
  Internet routing is like mail carrier delivery route
  If don’t get return letter, resend (packet) to make sure message is received
    There are other ways to ensure delivery (e.g., repair) that we will not discuss

## Slide 7: Outline
Introduction (done)
Basic Internet Architecture (next)
Loss and Latency
Latency Compensation Techniques
Client-Server Synchronization

## Slide 8: The Internet
Many design decisions and end-user experiences for multi-player networked games derive from nature of Internet
  “Best Effort” service
  Internet naming and addressing
  Transport protocols (TCP/UDP)
Layered
Applications (Half-Life, WoW, Mario…)
Services (DNS, HTTP, Overlay…)
Transport (TCP,UDP)
Network (IP)

## Slide 9: Internet Provides “Best Effort” Service
Few guarantees on timeliness
  Can take milliseconds, 100’s of milliseconds, or even seconds to deliver packet
Few guarantees on arrival certainty
  Sometimes packet doesn’t arrive (loss)
  Or arrives out of order (e.g., packet #3 arrives before packet #2)
  Or can arrive twice (duplicates, uncommon but possible)
Time to reach destination called latency
  Lag typically latency + end-host (server and client) time
    Often, players have hard time distinguishing
(More on loss and latency later)

## Slide 10: Endpoints and Addressing
IPv4 numerical 32-bit (4 byte) values
  Dotted quad form: 192.168.1.5 or 130.215.36.142
  In theory, 232 (about 4 billion) addresses, but practically fewer since allocated in blocks
Each Internet host has IP address
  Client running game client
  Server running game host
Some have 2
  Client with wireless and wired network (multi-homed)
  Router with multiple connections
IPv6 has 2128 addresses (enough for 100 addresses for each atom on the earth surface), but not widely deployed in U.S.
Packet has: source, destination
Payload is upper layer (transport, application)
Network worries about arrival
IP address related to, but not same as domain name (later)
“Flow” determined by port, too
 Transport layer (next)

## Slide 11: Transmission Control Protocol (TCP)
Many applications sensitive to loss, not time
  e.g., File transfer (.exe), email
  Need reliable, ordered transfer of bytes
Frames data  send as IP packets
Provides connection
Uses window for outstanding packets
  Provides flow control and congestion control
  Window grows with success, shrinks with loss
  Lost packets retransmitted
Some games more sensitive to time
Don’t use TCP
But many games do use TCP
RTS, MMO
Generally, easier to use TCP for games!
Notes: Section 4.1.2.1

## Slide 12: User Datagram Protocol (UDP)
Some applications sensitive to time
  e.g., Voice over IP (VoIP)
  Some games (e.g., First Person Shooter)
Unreliable, connectionless
No flow control (sender can go faster than receiver)
No congestion control (sender can go faster than network)
  Note: IP does ensure there are no bit errors (via Cyclic Redundancy Check, CRC)
Lightweight, but application must handle loss!
Only use UDP if you know your application is sensitive to latency!
Otherwise, use TCP (see previous slide)
Notes: Section 4.1.2.2

## Slide 13: Unicast, Multicast, Broadcast
(a) Unicast, one send and one receive
  Wastes capacity when path shared
(c) Broadcast, one send and all receive
  Perhaps ok for LAN, but cannot do on Internet
  Wastes capacity when most don’t need
(b) Multicast, one send and only subscribed receive
  Current Internet does not support
  Multicast can work for overlay networks (separate topic)
Note, UE4 provides a multicast networking feature. However, this is not true IP multicast, but rather replicated unicast to all clients.
Notes: Section 4.1.3

## Slide 14: Connectivity
Often edge most important
  Game developer does not see internals
But some aspects important for understanding network performance
  Hierarchy
  Routing
  Link-layer
Independent choice for packet route based solely on destination address
Not based on sender
Not based on QoS
Notes: Section 4.2

## Slide 15: Connectivity – Hierarchy
Routers designed for speed
  Get packet to outgoing link asap
Value + Prefix size
  128.80.0.0/16  all w/128.80 go to R1
  R1 forwards more precisely to subnet
  WPI has 130.215 with
    130.215.28 CS subnet
    130.215.36 CCC subnet (CCC1, …)
    130.215.16 ECE subnet…

## Slide 16: Connectivity – Routing
Routers use dynamic routing
  Discover topology
  Pick “best” routes (want tree)
    Typically shortest path (# hops, latency…)
Note: Local (internal to ISP) routing protocol different than among ISPs (ASes). The “cost” between ASes different than simply distance.
Notes: Section 4.2.2

## Slide 17: Connectivity – Link Layer
Link layer conveys packets across LAN
  Medium Access Control (MAC)
IP address mapped to data link layer
  Ethernet (IEEE 802.3), Wi-Fi (IEEE 802.11)
  MAC address 48-bit. E.g., 00:0F:1F:81:41:6C
  MAC address specified by vendor on card
IP to MAC assignment:
  Fixed (e.g., register computer with netops)
  Dynamic (assigned when boot)
Typically, network game won’t care about link layer since usually fast. But …. wireless, particularly wide-area wireless (e.g, 4G) can have 10s or 100s and even 1000s of millseconds of latency!
Notes: Section 4.2.3

## Slide 18: Miscellaneous
Time-to-Live
  Prevent loops (routers may have different shortest-path trees)
  8-bit value (0 to 255)
  Decrement by one each hop
  If zero, then discard
Maximum Transmission Unit (MTU)
  IP packet could be 64 KBytes
  In practice, bound by Ethernet (prevalent standard)
   1500 byte payload, so 1460 bytes for application payload
  If larger, then fragment into multiple IP packets
    Re-assemble at end
    If one lost, all lost!
First Hop
  Only know egress (e.g., first router)
ifconfig (Linux)
ipconfig /all (Windows)
For network games using UDP, keep data payloads smaller than MTU!

## Slide 19: Address Management Mini-Outline
Network Address Translation
Dynamic Host Configuration Protocol
Dynamic Name Service

## Slide 20: Network Address Translation (NAT) (1 of 2)
Used at boundary of ISP
  Where internal private addresses use external publicly routable address
Good if internal address not allocated
  Ex: private networks
    10/8, 172.16/12, 192.168/16
Also, may help keep internal network secure (but not sufficient)
Notes: Section 4.3.2

## Slide 21: Network Address Translation (NAT) (2 of 2)
Source hosts use private IP
Forward to NAT router
Swap private source address with public address (could be range)
  1-to-1 mapping between source hosts and public addresses
Send to ISP for Internet routing
Remember process so can do reverse on return

## Slide 22: Network Address Port Translation (NAPT) (1 of 2)
Have only 1 public address for multiple private addresses

## Slide 23: Network Address Port Translation (NAPT) (2 of 2)
Good:
  Easy to renumber (one number)
  Only need one public address
Bad: Breaks transparency (need to add functionality for each new protocol)
Hard for outside hosts to access inside
  Ex: what if two different Unreal Tournament servers inside?
  Need non-standard ports that clients know about
    Typically, local server register w/master server
      Gives IP adress + Port where server is
  Need to configure NAT box to forward ports
For network game, cannot rely upon reaching server behind NAT!

## Slide 24: Dynamic Host Configuration Protocol (DHCP)
Hosts need: IP address, subnet mask, IP address of at least one router
  Use DHCP to get from LAN device
    Typical with WLAN router, cable modem, …
Client broadcasts DHCP discovery to port 67
  Identifies its MAC address (e.g., 00:0a:95:9d:68:16)
DHCP server responds w/IP + Mask + Router IP
Client confirms, may request additional information (could be more than one DHCP server)
Server ACKs
For network game, host may not have same IP address each time!

## Slide 25: Domain Name System
Map text names to IP address
  Ex: www.wpi.edu mapped to 130.215.36.26
  Names more human-readable
Minimal <name>.tld (top-level-domain)
  tld: .com, .gov, .edu
  tld: .au, .fr, .uk
Hierarchy
  Distributed name servers
  Know first one, it knows upper level
  Local responses cached
    Local DNS, and at host
nslookup, dig, host
Initial latency may be high for first query (then cached by host)

## Slide 26: Outline
Introduction (done)
Basic Internet Architecture (done)
Loss and Latency (next)
Latency Compensation Techniques
Client-Server Synchronization

## Slide 27: Loss and Latency
Characteristics most identified with IP networks
  Note, in other cases capacity, but not usually for network games
Loss – packet does not arrive
  Usually, fraction #recv/#sent, p  [0:1]
  Note, often assumed independent but can be bursty (several lost in row)
Latency – time to get from source to destination
  Round trip time (RTT) often important since server response to game action
  Often assumed (2 x latency), but network path can be asymmetric
  Also jitter (or latency jitter) variation in latency (not discussed more here)
How much does each matter? (later)
Right now, sources for each

## Slide 28: Sources of Loss
Note, here we are considering only IP packet loss
  Above IP, TCP will retransmit lost packets
  Below IP, data link often retransmits or does repair (forward error correction)
IP packet loss predominantly from congestion
  Causes queue overflow (incoming packets dropped)
Bit errors
  More common on wireless
Loss during route change (link/host unavailable)
Often bursty!
Router
Routing
Table
Packet
queue
10 Mbps
10 Mbps
5 Mbps

## Slide 29: Sources of Latency
Serialization – Time to transmit packet on link 1 bit at a time
Propagation – Time for bits to travel from one host to another
Queueing delay – Time spent in router queue waiting to be transmitted
Typically
  Propagation time fast (about speed of light)
  Serialization time usually fast for high capacity links
  Queuing delay can dominate, and exacerbated by long serialization times

## Slide 30: Latency Compensation Mini-Outline
Motivation
Prediction
Time delay and Time warp
Data compression
Visual tricks
Cheating

## Slide 31: Need for Latency Compensation
Capacities are growing, but cannot solve all problems
Still bursty, transient congestion (queues)
Capacities uneven across all clients
  And often asymmetric in downlink/uplink.
Wireless Wide Area Networks (WWANs) growing (low, variable capacities, high latency)
Propagation delays (~25 msec min across U.S.)
“There is an old network saying: ‘Bandwidth problems can be cured with money. Latency problems are harder because the speed of light is fixed – you can’t bribe
God.’ ” —David Clark, MIT

## Slide 32: Is It Latency or Do You Just Suck?
http://www.youtube.com/watch?v=Bn1nBR5jOx8
http://www.youtube.com/watch?v=r6PwHkhEAkU
Notes: Video taken from YouTube, indicated by URL

## Slide 33: Is It Latency or Do You Just Suck?
http://www.youtube.com/watch?v=Bn1nBR5jOx8
http://www.youtube.com/watch?v=r6PwHkhEAkU
Delayed response
“Magic” bullets
Server matters
Notes: Video taken from YouTube, indicated by URL

## Slide 34: Latency and Playability (1 of 2)
Affects player – subjective and objective (below)
But depends upon type of game!
Notes: Grenville Armitage, Mark Claypool, and Philip Branch. Networking and Online Games: Understanding and Engineering Multiplayer Internet Games, John Wiley and Sons, Ltd., June 2006. Chapter 7.

## Slide 35: Latency and Playability (2 of 2)
Notes: Mark Claypool and Kajal Claypool. Latency and Player Actions in Online Games,Communications of the ACM, Volume 49, Issue 11, November 2006. Online at:http://www.cs.wpi.edu/~claypool/papers/precision-deadline/

## Slide 36: What is Network Latency for Games?
Internet
Game
client
Game
server
Latency - time to get from source to destination
  There and back (round-trip time)

## Slide 37: Basic Client-Server Game Architecture
“Dumb” client
Server keeps all state
Validates all moves
Client only updates when server says “ok”
Algorithm
Sample user input
Pack up data and send to server
Receive updates from server and unpack
Determine visible objects and game state
Render scene
Repeat
Time
User
Input
Render
Input
Process and Validate
Input
Message:
User Input
Message:
Ok User Input
Latency affects responsiveness

## Slide 38: Latency Example (1 of 2)
Player is pressing left
Player is pressing up
Running back goes out of bounds
Notes: James Nichols and Mark Claypool. The Effects of Latency on Online Madden NFL Football, In Proceedings of the 14th ACM International Workshop on Network and Operating Systems Support for Digital Audio and Video (NOSSDAV), Kinsale, County Cork, Ireland, June 16-18, 2004. Online at: http://www.cs.wpi.edu/~claypool/papers/madden/

## Slide 39: Latency Example (2 of 2)
Player is pressing “pass”
Pass starts rendering
Interception
Notes: James Nichols and Mark Claypool. The Effects of Latency on Online Madden NFL Football, In Proceedings of the 14th ACM International Workshop on Network and Operating Systems Support for Digital Audio and Video (NOSSDAV), Kinsale, County Cork, Ireland, June 16-18, 2004. Online at: http://www.cs.wpi.edu/~claypool/papers/madden/

## Slide 40: Outline
Introduction (done)
Basic Internet Architecture (done)
Loss and Latency (done)
Latency Compensation Techniques (next)
Examples – Dragonfly and UE4

## Slide 41: Compensating for Latency – Prediction
Broadly, two kinds of latency compensation:
  Player prediction
  Opponent prediction (often called “dead reckoning” but that name does little to help remember)

## Slide 42: Compensating for Latency – Player Prediction
Prediction Algorithm
Sample user input
Pack up data and send to server
Determine visible objects and game state
Render scene
Receive updates from server and unpack
Fix up any discrepancies
Repeat
Time
User
Input
Render
Input
Process and Validate
Input
Message:
User Input
Message:
Ok with Update
Fix Up
Potentially, tremendous benefit. Render as if local, no latency.
But, note, “fix up” step additional. Needed since
server has master copy.

## Slide 43: Example of State Inconsistency
Predicted state differs from actual state
Notes: James Nichols and Mark Claypool. The Effects of Latency on Online Madden NFL Football, In Proceedings of the 14th ACM International Workshop on Network and Operating Systems Support for Digital Audio and Video (NOSSDAV), Kinsale, County Cork, Ireland, June 16-18, 2004. Online at: http://www.cs.wpi.edu/~claypool/papers/madden/

## Slide 44: Prediction Tradeoffs
Tension between responsiveness (latency compensation) and consistency
More responsive,
Less consistent
Less responsive,
More consistent
Client uses prediction
Client waits for server ok

## Slide 45: Compensating for Latency – Opponent Prediction
Opponent sends position, velocity (maybe acceleration)
Player predicts where opponent is
t0
t1
t2
t3
send initial
position
send
update
send
update
send
update
Unit Owner
Actual Path
Opponent
Predicted Path
(User can see “Warp” or “Rubber band”.)

## Slide 46: Opponent Prediction Algorithms
Unit Owner
Sample user input
Update {location | velocity | acceleration} on basis of new input
Compute predicted location on the basis of previous {location | velocity | acceleration}
If (current location – predicted location) < threshold then
  Pack up {location | velocity | acceleration} data
  Send to each other opponent
Repeat
Opponent
Receive new packet
Extract state update information {location | velocity | acceleration}
If seen unit before then
  Update unit information
else
  Add unit information to list
For each unit in list
  Update predicted location
Render frame
Repeat

## Slide 47: Opponent Prediction Notes
Some predictions easy
  Ex: falling object
Other predictions harder
  Ex: pixie that can teleport
Some predictions game specific
  Ex: Can predict “return to base” with pre-defined notion of what “return to base” is.
Cost is having each host runs prediction algorithm for each opponent.
Also, although is latency compensation method, can greatly reduce bitrate.
  Predict self. Don’t send updates unless needed.
  Especially when objects relatively static.

## Slide 48: Why Else Does Latency Matter?
Time
User
Input
Message:
Treasure!
Message:
Treasure!
User
Input
Message:
Get treasure
Message:
Get treasure
Message:
Ok
Message:
Tough luck!
Latency affects fairness
Solution? Manipulate time
  Time Delay
  Time Warp

## Slide 49: Compensating for Latency – Time Delay
Server delays processing of events
  Wait until all messages from clients arrive
Server sends messages to more distant client first, delays messages to closer
  Needs accurate estimate of RTT
  (Note, game plays at highest round trip time (RTT))
Time
Client 1
command arrives
Client 2
command arrives
Server processes
both client commands
Time Delay

## Slide 50: Compensating for Latency – Time Warp
In older FPS (e.g., Quake 3), player had to “lead” opponent to hit
  Otherwise, opponent had moved
  Even with “instant” weapon!
Knowing latency roll-back (warp) to when action taken place
  Usually assume ½ RTT
Time Warp Algorithm
Receive packet from client
Extract information (user input)
elapsed time = current time – latency to client
Rollback all events in reverse order to current time – elapsed time
Execute user command
Repeat all events in order, updating any clients affected
Repeat

## Slide 51: Time Warp Example
Client 100 ms behind Server
Shots still hits (note blood)

## Slide 52: Time Warp Notes
Inconsistency
  Opponent targets player
  Player moves around corner to hide
  Time warps backward  hit
  Bullets seem to “bend” around corner!
Fortunately, player often does not notice
  Doesn’t see opponent
  May be just wounded

## Slide 53: Compensating for Latency – Data Compression (1 of 2)
Idea  less data, means less latency to get it there
  So, reduce # or size of messages  reduce latency (serialization)
Use lossless compression (like zip)
Opponent prediction
  Don’t send unless need update
Delta compression (like opponent, but more general)
  Don’t send all data, just updates
Interest management
  Only send data to units that need to see it (next slide)

## Slide 54: Interest Management
Hider’s
Nimbus
Seeker’s
Nimbus
Hider’s
Focus
Seeker’s
Focus
Where are
you?

## Slide 55: Compensating for Latency – Data Compression (2 of 2)
Peer-to-Peer (P2P)
  Limit server congestion
  Also, client1serverclient2 higher latency than client1client2
  But scales with slowest computer
  But cheating especially problematic in P2P systems
Update aggregation
  Message Move A  Send C, Move B  Send C
  Instead, Move A + Move B  Send C
  Avoid packet overhead (if less than MTU)
  Works well w/time delay

## Slide 56: Compensating for Latency – Visual Tricks
Latency present, but hide from user
  Give feeling of local response
Ex: player pulls trigger, make sound and puff of smoke while waiting for confirmation of hit
Ex: player tells boat to move, while waiting for confirmation raise sails, pull anchor
Ex: player tells tank to move, while waiting, batten hatches, start engine

## Slide 57: Outline
Introduction (done)
Basic Internet Architecture (done)
Loss and Latency (done)
Latency Compensation Techniques (done)
Client Server Synchronization (next)
  By Example – Dragonfly and UE4

## Slide 58: Network Game Case Study – Saucer Shoot 2
Saucer Shoot for two players

## Slide 59: Dragonfly – Network Manager
class NetworkManager : public Manager {
private:
NetworkManager();.
NetworkManager(NetworkManager const&);
void operator=(NetworkManager const&);
int sock;
public:
// Get the one and only instance of the NetworkManager.
static NetworkManager &getInstance();
// Start up NetworkManager.
int startUp();
// Shut down NetworkManager.
void shutDown();
// Accept only network events.
// Returns false for other engine events.
bool isValid(string event_type);
…
// Block, waiting to accept network connection.
int accept(string port = DRAGONFLY_PORT);
// Make network connection.
int connect(string host,
string port = DRAGONFLY_PORT);
// Close network connection.
int close();
// Send buffer to connected network.
int send(void *buffer, int bytes);
// Receive from connected network (no more than bytes).
int receive(void *buffer, int bytes);
// Check if network data.
int isData();
// Return true if network connected, else false.
bool isConnected();
// Return socket.
int getSocket();
};
Basic manager stuff
Network specific stuff

## Slide 60: Dragonfly – Network Events
#include "Event.h"
#define NETWORK_EVENT "__network__"
class EventNetwork : public Event {
private:
int bytes; // Number of bytes available
public:
// Default constructor.
EventNetwork();
// Create object with initial bytes.
EventNetwork(int initial_bytes);
// Set number of bytes available.
void setBytes(int new_bytes);
// Get number of bytes available.
int getBytes();
};
Indicate network data is available
And how much
Bytes are actually still with network manager

## Slide 61: Client and Host Objects
Host object (derived from Object) runs on server
Client object (derived from Object) runs on client
Host game started first, whereupon Host (using NetworkManager) readies computer for connection
Client (also using NetworkManager) starts after and connects to Host
Client gathers input normally, but also sends data to Host
Host receives keystrokes sent by Client, generating network events to game objects (e.g., the Client Hero) to handle
Each game loop, Host checks all game objects to see which ones are new and/or updated
  Need to synchronize Objects between Host and Client … but how?

## Slide 62: How to Synchronize Client and Host (Server)?
Many decisions for multiplayer game
  How are player actions transmitted to server?
  What Objects are synchronized and how often?
  How are inconsistencies between client and server game states resolved?
Key aspect – how to “send” Object from one computer to another

## Slide 63: Serializing (Marshalling) Objects
Convert Object attributes to byte stream for storage or transmission
http://www.techrepublic.com/article/application-development-an-introduction-to-serialization-in-net/
Network
Also known as “marshalling”

## Slide 64: Serializing Objects
// Serialize Object attributes to single string (json-like).
// e.g., "id:110,is_active:true, ...
// Only modified attributes are serialized (unless all is true).
virtual string serialize(bool all = false);
// Deserialize string to become Object attributes.
virtual int deserialize(string s);
// Return true if attribute modified since last serialize.
bool isModified(enum ObjectAttribute attribute);
Object class extensions to support marshalling
id:0,is_active:true,is_visible:true,event_count:0,box-corner-x:0,
box-corner-y:0,box-horizontal:1,box-vertical:1,pos-x:0,pos-y:0,
type:Object,sprite_name:,sprite_center:true,sprite_transparency:0,
sprite_index:0,sprite_slowdown:1,sprite_slowdown_count:0,altitude:2,
solidness:0,no_soft:false,x_velocity:0,x_velocity_countdown:0,
y_velocity:0, y_velocity_countdown:0,
e.g.,

## Slide 65: Synchronizing Objects (1 of 2)
Only synchronize important objects and events (e.g., Hero destruction vs. Stars moving)

## Slide 66: Synchronizing Objects (2 of 2)
Have configuration for game (host | client)
  Can keep same codebase for Hero, Bullet, Points…
Generally, only Host creates/destroys
  Except for Explosion
Generally, Host and Client move and animate
  Except for Client Hero (see below)
Client Player input
  Could update Hero location and synchronize
    But if not allowed, need to “roll back” state
  Instead, send keystrokes to server
    Let server move all Objects and send to client

## Slide 67: Multi-player Networking
Client-Server (no P2P support)
  Authoritative server, makes all decisions
Replicate objects, variables, functions
  Replicated Actors are main “workhorse” server uses to synchronize
  Server gathers attributes that change, send to client
Not all objects, variables, functions need to be replicated
  E.g., objects that compute AI behavior on server  only when move Actor
  E.g., only replicate functions that result in client seeing/hearing

## Slide 68: Replication
When replicated object created/modified/destroyed on server, sent to clients
When replicated object created/modified on client, not sent
  Can be used for “cosmetic” objects that don’t effect gameplay
Client sends information via “run on server” functionality
  Remote Procedure Call (RPC)

## Slide 69: Remote Procedure Calls (RPC)
RPCs are functions called locally (they look like “normal” functions), but are executed on server
  Client invokes via “run on server” function
Allow client/server to send messages to each other
Used for playing sounds, spawning particles

## Slide 70: Reliability
Any replicated event can be reliable or unreliable
Reliable
  Guaranteed to be called, resent if error, delayed when bandwidth saturated
    E.g., use for starting game
Unreliable
  Attempt to call, but not resent if error, dropped if bandwidth saturated
    E.g., use for player movement
NetMulticast – send to all clients (not true multicast)
  E.g., send notice of player death

## Slide 71: Summary
Networking increasingly important for games
  The network is the computer
  Many games come with multi-player, online play, downloads, player communities
Internet influences design of game architecture
  Need to live with “best effort” service
Choice of solution depends upon action within game
  Transport protocol
  Latency compensation
  Client-server architectures dominate
Game developers need to carefully consider design of object synchronization