## Slide 1: Wireless Network Dynamic Rate Adaptation and SS and DS mode in MIMO
Advanced Computer Networks

## Slide 2: Rate Adaptation Algorithms
1997 ARF
1998
1999
2000
2001 RBAR
2002 MPDU OAR PER
2003 LA MiSer SwissRA
2004 AARF AMRR HRC MultiRateRetry
2005 Fast-LA LD-ARF RFT SampleRate
2006 CARA CROAR DOFRA RRAA
2007

## Slide 3: Sample Rate
Sample Rate [Bickett] is based on transmission statistics over a sliding window.
It adjusts to the bit rate that would achieve the smallest average transmission time in the last sampling period.
Transmission time for a frame :: time to send a frame successfully (until ACKed) which includes backoff times and retransmissions.
Sample Rate starts at the highest rate and decreases the rate immediately if it experiences four consecutive transmission failures.

## Slide 4: Sample Rate
Sample Rate calculates the average transmission time per frame for different rates every ten seconds.
It randomly selects one rate from the set of all other rates whose average transmission time is less than the average lossless transmission time of the rate in use for every tenth frame.

## Slide 5: RRAA
Robust Rate Adaptation Algorithm (RRAA) requires the use of RTS/CTS after a frame loss to eliminate further collisions due to hidden terminals.
RRAA has two elements:
  Rate adaptation (loss ratio estimation and rate selection)
  Collision elimination

## Slide 6: RRAA
RRAA measures the loss ratio from recent transmissions statistics over a window.
RRAA begins transmissions at the maximum rate. In each short cycle, RRAA transmits a window of frames at a selected rate.
The window size can vary per rate.

## Slide 7: RRAA
At the end of each window, the frame loss rate p for the corresponding rate is available for rate adjustment.
RRAA uses two thresholds PMTL and PORI .
If p > PMTL , the next lower rate is chosen for the next window transmission.
If p < PORI , the rate is increased.

## Slide 8: RRAA
If PORI <= p <= PMTL , the rate remains unchanged and the window slides forward
Additionally RRAA uses a strategy called Adaptive RTS (A-RTS) to reduce collisions caused by hidden terminals.

## Slide 9: MIMO Modes
Both transmitter and receiver devices allow for diversity single stream (SS).
DS is spatial multiplexing double streams which are independent and separately encoded spatial streams from multiple chains.