## Slide 1: Ultra-Low Duty Cycle MAC with Scheduled Channel Polling
Wei Ye and John Heidemann
CS577
Brett Levasseur

## Slide 2: Outline
Introduction
Scheduled Channel Polling (SCP-MAC)
Energy Performance Analysis
Implementation
Conclusions

## Slide 3: Introduction
Sensor networks need to save power
Controlling the power and duty cycle is critical
Synchronization techniques are power efficient but have complex management
Contention based protocols used more often but must be kept at low duty cycles

## Slide 4: Related Work
Low Power Listening (LPL)
  Low power probe to check channel activity
  No long wake period
  Requires transmission preamble
Scheduled Protocols
  Sleep/Wake schedules
  Only transmit when receiver is listening
  Requires coordination

## Slide 5: Limitations
Scheduling and LPL require 1 -2% duty cycle
Scheduling has long wake time
LPL has long transmit preamble
Authors propose Schedule Channel Polling (SCP)
  Ultra low duty cycles of 0.01 – 0.1%
  Reduce energy consumption by factor of 10-100

## Slide 6: Outline
Introduction
Scheduled Channel Polling (SCP-MAC)
Energy Performance Analysis
Implementation
Conclusions

## Slide 7: SCP-MAC
Combines short channel polling from LPL with scheduling
Periodic channel polling (LPL)
Polling time is synchronized across nodes
  Reduced transmit preamble size
  Requires less energy

## Slide 8: Synchronized Channel Polling
LPL requires long preamble
  Preamble at least as long as channel polling period
SCP synchronizes polling time
  Only short wake up tone is required
  Requires synchronization

## Slide 9: Bursty Traffic
Running SCP-MAC at low duty cycle adds latency during heavy traffic periods
  Low duty cycle means more time between transmission opportunities
Detect bursty traffic and add polling slots
  The new slots allows for more transmissions in less time

## Slide 10: Adaptive Polling
Node B adds n polling slots when it receives from A
Node A can give up transmitting to B so B can transmit to C
  This gets C to add its own n polling slots
Should add one poll per node that needs to send

## Slide 11: Two-Phase Contention
Carrier sense in CW1 before sending tone
If channel idle send wakeup tone
If tone sent successfully node performs carrier sense in CW2
If channel idle then send data

## Slide 12: Overhearing Avoidance
Hearing a packet meant for another node
  Causes overhearing node to waste power
Stop listening to packets not meant for the node
  With RTS/CTS nodes can see when the channel is busy
  Without RTS/CTS nodes examine MAC headers and goes back to sleep if receiving address is not for them

## Slide 13: Outline
Introduction
Scheduled Channel Polling (SCP-MAC)
Energy Performance Analysis
Implementation
Conclusions

## Slide 14: Energy Performance Analysis

## Slide 15: Energy Consumption
Sum of energy used for each state
  Carrier Sense
  Transmit
  Receive
  Poll
  Sleep

## Slide 16: Asynchronous Channel Polling
What is the energy cost to poll using asynchronous channel polling in LPL?
  Length of preamble
  Time for carrier sense
  Time for polling
  Time spent sleeping
  Transmission/Reception rate

## Slide 17: LPL Preamble
Preamble must be as long as the polling interval Tp
tb is the time to transmit a byte
Lpreamble is the length of the preamble in bytes

## Slide 18: LPL Carrier Sense
Nodes perform carrier sense before preamble
tcs1 is the average carrier sense time
rdata is the rate of sending data

## Slide 19: Time Transmitting/Receiving
Transmit is sending preamble and data
Receive is sum across all nodes
  n is the number of nodes

## Slide 20: Polling and Sleeping
Normalized time for polling and sleeping
The node is asleep when not in carrier sense, transmission, reception or polling

## Slide 21: Random Channel Polling LPL
Power consumed determined by
  Neighborhood size
  Data rate
  Channel polling
Small Tp reduces cost of polling but increases transmit and reception cost

## Slide 22: Optimize Polling Time LPL

## Slide 23: Synchronization
Nodes broadcast scheduling information
  Occurs every synchronization period
  Required every 10 – 60 minutes
Piggyback synchronization with data when possible
Clock drift requires guard time

## Slide 24: Clock Drift
Tsync – Synchronization period
rclk – Clock drift rate
Tsyncrclk
Time
tdiff
Current Time

## Slide 25: Guard Time 2 Nodes
Tsyncrclk
Time
tguard
Tsyncrclk
tdiff
Difference between 2 nodes requires 2tdiff

## Slide 26: Guard Time n + 1 Nodes
Every node sends a SYNC in each Tsync period
For n neighbors this reduces clock drift (n+1) times
Time
(4 * Tsyncrclk) / (n + 1)
4 * Tsyncrclk

## Slide 27: Wake-up Tone
Guard time plus a short fixed time
tmtone is time needed to detect tone
Time
Ttone
Tguard

## Slide 28: SCP with Piggybacking
Perfect piggyback means all synchronization goes out with application data
Carrier Sense
Tx / Rx
Polling
Sleep

## Slide 29: SCP without Piggybacking
More time needed to transmit and receive synchronization packets

## Slide 30: Poll Time (Tp) in LPL and SCP
LPL
Larger poll time adds to transmission and reception cost
SCP
Larger poll time does not add to transmission and reception cost

## Slide 31: With/Without Piggybacking
With piggybacking synchronization sent with data
Without synchronization data sent on its own

## Slide 32: Optimal Tsync

## Slide 33: Optimum Energy Consumption
LPL uses 3-6 times more energy than SCP
Piggybacking reduces energy cost when data is rarely sent
Benefits minimal when data sent frequently
LPL worse on newer radio, SCP better

## Slide 34: Outline
Introduction
Scheduled Channel Polling (SCP-MAC)
Energy Performance Analysis
Implementation
Conclusions

## Slide 35: Implementation
TinyOS on Mica2 (CC1000) and MicaZ (CC2420) motes
Layered approach
LPL used for polling
SCP used for scheduling
TinyOS controls CPU power and timers
[Wei 05]

## Slide 36: Power Consumption
4 mA
Energy required to maintain timers is less than using the radio
Adding timers for scheduling is a low energy impact
1 ms
[Wei 05]
[Wei 05]

## Slide 37: Optimal Setup
Periodic traffic
10 nodes all in range
40B data message
1 message every 5 – 30 seconds
LPL requires 2 – 2.5 times more energy than SCP

## Slide 38: Optimal Setup Cont
LPL needs 3–6 times more power than SCP
  Both optimized for periodic traffic
Experimental results similar to analytical results

## Slide 39: Experiment vs Analysis
[Wei 05]

## Slide 40: Unanticipated Traffic
Long down time and then large amount of traffic
0.3% duty cycle
Poll every second
Busy mode
  20, 100B long messages
LPL uses 8 times more energy than SCP
  Mostly preamble

## Slide 41: Unanticipated Traffic Cont
Heavy traffic load leads to contention
LPL has one congestion window
  32 slots, 10 nodes
  About 1/3 chance of nodes conflicting
SCP has two congestion windows
  Collision rate about 4%

## Slide 42: Mean Energy
LPL uses 20 – 40 times more energy than full (adaptive polling) SCP-MAC
  Long preamble
  Overhearing nodes
False wakeups
  LPL needs to receive full preamble

## Slide 43: Mean Latency
Basic SCP and LPL have similar latency
  Polling interval latency
Adaptive channel polling causes lower latency for SCP full
  All nodes switch to higher duty cycle polling after first packet

## Slide 44: Conclusions
Proposed SCP (LPL with scheduling)
Found best operating points for LPL and SCP
SCP showed less power usage than LPL
  3 – 6 times better under ideal scenario (periodic traffic)
SCP has greater improvements when using newer radios

## Slide 45: Questions

## Slide 46: References
[Wei 06] - Wei Ye, Fabio Silva, and John Heidemann. 2006. Ultra-low duty cycle MAC with scheduled channel polling. In Proceedings of the 4th international conference on Embedded networked sensor systems (SenSys '06). ACM, New York, NY, USA, 321-334. DOI=10.1145/1182807.1182839 http://doi.acm.org/10.1145/1182807.1182839
[Wei 05] - Wei Ye, Fabio Silva, and John Heidemann. 2005. Ultra-low duty cycle MAC with scheduled channel polling. http://www.isi.edu/~johnh/PAPERS/Ye05a.pdf