## Slide 1: TCP Congestion Control

## Slide 2: Principles of Congestion Control
Congestion:
informally: “too many sources sending too much data too fast for the network to handle”
different from flow control!
manifestations:
  lost packets (buffer overflow at routers)
  long delays (queueing in router buffers)
a major problem in networking!

## Slide 3: Causes/Costs of Congestion Scenario 1
two senders, two receivers
one router, infinite buffers
no retransmission
large delays when congested
maximum achievable throughput
unlimited shared output link buffers
Host A
lin : original data
Host B
lout

## Slide 4: Causes/Costs of Congestion Scenario 2
one router, finite buffers
sender retransmits lost packets
finite shared output link buffers
Host A
lin : original data
Host B
lout
l'in : original data, plus retransmitted data
offered load

## Slide 5: Causes/Costs of Congestion Scenario 2
always: (goodput)
“perfect” retransmission only when loss:
retransmission of delayed (not lost) packet makes larger (than perfect case) for same
l
in
l
out
=
l
in
l
out
>
l
in
l
out
“costs” of congestion:
more work (retransmissions) for a given “goodput”
unneeded retransmissions: link carries multiple copies of packet
R/2
R/2
lin
lout
b.
R/2
R/2
lin
lout
a.
R/2
R/2
lin
lout
c.
R/4
R/3

## Slide 6: Approaches towards Congestion Control
end-end congestion control:
no explicit feedback from network
congestion inferred from end-system observed loss, delay
approach taken by TCP
network-assisted congestion control:
routers provide feedback to end systems
  single bit indicating congestion (SNA, DECbit, TCP/IP ECN, ATM)
  explicit rate sender should use for sending.
Two broad approaches towards congestion control:

## Slide 7: TCP Congestion Control
Lecture material taken from
“Computer Networks A Systems Approach”, Fourth Edition,Peterson and Davie,
Morgan Kaufmann, 2007.

## Slide 8: TCP Congestion Control
Essential strategy :: The TCP host sends packets into the network without a reservation and then the host reacts to observable events.
Originally TCP assumed FIFO queuing.
Basic idea :: each source determines how much capacity is available to a given flow in the network.
ACKs are used to ‘pace’ the transmission of packets such that TCP is “self-clocking”.

## Slide 9: TCP Congestion Control
Goal: TCP sender should transmit as fast as possible, but without congesting network.
  issue - how to find rate just below congestion level?
Each TCP sender sets its window size, based on implicit feedback:
  ACK segment received  network is not congested, so increase sending rate.
  lost segment - assume loss due to congestion, so decrease sending rate.
K & R

## Slide 10: TCP Congestion Control
“probing for bandwidth”: increase transmission rate on receipt of ACK, until eventually loss occurs, then decrease transmission rate
  continue to increase on ACK, decrease on loss (since available bandwidth is changing, depending on other connections in network).
ACKs being received,
so increase rate
X
X
X
X
X
loss, so decrease rate
sending rate
time
Q: how fast to increase/decrease?
TCP’s
“sawtooth”
behavior
K & R

## Slide 11: AIMD (Additive Increase / Multiplicative Decrease)
CongestionWindow (cwnd) is a variable held by the TCP source for each connection.
cwnd is set based on the perceived level of congestion. The Host receives implicit (packet drop) or explicit (packet mark) indications of internal congestion.
MaxWindow :: min (CongestionWindow , AdvertisedWindow)
EffectiveWindow = MaxWindow – (LastByteSent -LastByteAcked)

## Slide 12: Additive Increase (AI)
Additive Increase is a reaction to perceived available capacity (referred to as congestion avoidance stage).
Frequently in the literature, additive increase is defined by parameter α (where the default is α = 1).
Linear Increase :: For each “cwnd’s worth” of packets sent, increase cwnd by 1 packet.
In practice, cwnd is incremented fractionally for each arriving ACK.
increment = MSS x (MSS /cwnd)
cwnd = cwnd + increment

## Slide 13: Figure 6.8 Additive Increase
Source
Destination
Add one packet
each RTT

## Slide 14: Multiplicative Decrease (MD)
Key assumption :: a dropped packet and resultant timeout are due to congestion at a router.
Frequently in the literature, multiplicative decrease is defined by parameter β (where the default is β = 0.5)
Multiplicate Decrease:: TCP reacts to a timeout by halving cwnd.
Although defined in bytes, the literature often discusses cwnd in terms of packets (or more formally in MSS == Maximum Segment Size).
cwnd is not allowed below the size of a single packet.

## Slide 15: AIMD (Additive Increase / Multiplicative Decrease)
It has been shown that AIMD is a necessary condition for TCP congestion control to be stable.
Because the simple CC mechanism involves timeouts that cause retransmissions, it is important that hosts have an accurate timeout mechanism.
Timeouts set as a function of average RTT and standard deviation of RTT.
However, TCP hosts only sample round-trip time once per RTT using coarse-grained clock.

## Slide 16: Figure 6.9 Typical TCP Sawtooth Pattern

## Slide 17: Slow Start
Linear additive increase takes too long to ramp up a new TCP connection from cold start.
Beginning with TCP Tahoe, the slow start mechanism was added to provide an initial exponential increase in the size of cwnd.
Remember mechanism by: slow start prevents a slow start. Moreover, slow start is slower than sending a full advertised window’s worth of packets all at once.

## Slide 18: Slow Start
The source starts with cwnd = 1.
Every time an ACK arrives, cwnd is incremented.
cwnd is effectively doubled per RTT “epoch”.
Two slow start situations:
  At the very beginning of a connection {cold start}.
  When the connection goes dead waiting for a timeout to occur (i.e, when the advertized window goes to zero!)

## Slide 19: Figure 6.10 Slow Start
Source
Destination
Slow Start
Add one packet
per ACK

## Slide 20: Slow Start
However, in the second case the source has more information. The current value of cwnd can be saved as a congestion threshold.
This is also known as the “slow start threshold” ssthresh.

## Slide 21
ssthresh

## Slide 22: Figure 6.11 Behavior of TCP Congestion Control

## Slide 23: Fast Retransmit
Coarse timeouts remained a problem, and Fast retransmit was added with TCP Tahoe.
Since the receiver responds every time a packet arrives, this implies the sender will see duplicate ACKs.
Basic Idea:: use duplicate ACKs to signal lost packet.
Fast Retransmit
Upon receipt of three duplicate ACKs, the TCP Sender
retransmits the lost packet.

## Slide 24: Fast Retransmit
Generally, fast retransmit eliminates about half the coarse-grain timeouts.
This yields roughly a 20% improvement in throughput.
Note – fast retransmit does not eliminate all the timeouts due to small window sizes at the source.

## Slide 25: Figure 6.12 Fast Retransmit
Fast Retransmit
Based on three
duplicate ACKs

## Slide 26: Figure 6.13 TCP Fast Retransmit Trace

## Slide 27: Fast Recovery
Fast recovery was added with TCP Reno.
Basic idea:: When fast retransmit detects three duplicate ACKs, start the recovery process from congestion avoidance region and use ACKs in the pipe to pace the sending of packets.
Fast Recovery
After Fast Retransmit, half cwnd and commence
recovery from this point using linear additive increase
‘primed’ by left over ACKs in pipe.

## Slide 28: Modified Slow Start
With fast recovery, slow start only occurs:
  At cold start
  After a coarse-grain timeout
This is the difference between TCP Tahoe and TCP Reno!!

## Slide 29: Many TCP ‘flavors’
TCP New Reno
TCP SACK
  requires sender and receiver both to support TCP SACK.
  possible state machine is complex.
TCP Vegas
  adjusts window size based on difference between expected and actual RTT.
TCP BIC  TCP Cubic {used by Linux}
TCP Compound {used by Windows}

## Slide 30: TCP New Reno
Two problem scenarios with TCP Reno
  bursty losses, Reno cannot recover from bursts of 3+ losses.
  Packets arriving out-of-order can yield duplicate acks when in fact there is no loss.
New Reno solution – try to determine the end of a burst loss.

## Slide 31: TCP New Reno
When duplicate ACKs trigger a retransmission for a lost packet, remember the highest packet sent from window in recover.
Upon receiving an ACK,
  if ACK < recover => partial ACK
  If ACK ≥ recover => new ACK

## Slide 32: TCP New Reno
Partial ACK implies another lost packet: retransmit next packet, inflate window and stay in fast recovery.
New ACK implies fast recovery is over: starting from 0.5 x cwnd proceed with congestion avoidance (linear increase).
New Reno recovers from n losses in n round trips.

## Slide 33: Figure 5.6 Three-way TCP Handshake

## Slide 34: Adaptive Retransmissions
RTT:: Round Trip Time between a pair of hosts on the Internet.
How to set the TimeOut value (RTO)?
  The timeout value is set as a function of the expected RTT.
  Consequences of a bad choice?

## Slide 35: Original Algorithm
Keep a running average of RTT and compute TimeOut as a function of this RTT.
  Send packet and keep timestamp ts .
  When ACK arrives, record timestamp ta .
  SampleRTT = ta - ts

## Slide 36: Original Algorithm
Compute a weighted average:
EstimatedRTT = α x EstimatedRTT + (1- α) x SampleRTT
Original TCP spec: α in range (0.8,0.9)
TimeOut = 2 x EstimatedRTT

## Slide 37: Karn/Partidge Algorithm
An obvious flaw in the original algorithm:
Whenever there is a retransmission it is impossible to know whether to associate the ACK with the original packet or the retransmitted packet.

## Slide 38: Figure 5.10 Associating the ACK?

## Slide 39: Karn/Partidge Algorithm
Do not measure SampleRTT when sending packet more than once.
For each retransmission, set TimeOut to double the last TimeOut.
{ Note – this is a form of exponential backoff based on the believe that the lost packet is due to congestion.}

## Slide 40: Jacobson/Karels Algorithm
The problem with the original algorithm is that it did not take into account the variance of SampleRTT.
Difference = SampleRTT – EstimatedRTT
EstimatedRTT = EstimatedRTT +
(δ x Difference)
Deviation = δ (|Difference| - Deviation)
where δ is a fraction between 0 and 1.

## Slide 41: Jacobson/Karels Algorithm
TCP computes timeout using both the mean and variance of RTT
TimeOut = µ x EstimatedRTT
+ Φ x Deviation
where based on experience µ = 1 and Φ = 4.

## Slide 42: TCP Congestion Control Summary
Congestion occurs due to a variety of circumstance.
TCP interacts with routers in the subnet and reacts to implicit congestion notification (packet drop) by reducing the TCP sender’s congestion window (MD).
TCP increases congestion window using slow start or congestion avoidance (AI).

## Slide 43: TCP Congestion Control Summary
Important TCP Congestion Control ideas include: AIMD, Slow Start, Fast Retransmit and Fast Recovery.
Currently, the two most common versions of TCP are Compound (Windows) and Cubic (Linux).
TCP needs rules and an algorithm to determine RIO and RTO.