## Slide 1: Congestion Control and Resource Allocation
Lecture material taken from
“Computer Networks A Systems Approach”, Third Edition,Peterson and Davie,
Morgan Kaufmann, 2007.

## Slide 2: Congestion Control Outline
Congestion Control
Flows
CC Taxonomy
Evaluation Criteria
Introduction to Queueing
  FIFO (FCFS drop tail)
  Priority
  FQ (Fair Queueing)
  WFQ (Weighted Fair Queueing)

## Slide 3: Definitions
Flow control:: keep a fast sender from overrunning a slow receiver.
Congestion control:: the efforts made by network nodes to prevent or respond to overload conditions.
Congestion control is intended to keep a fast sender from sending data into the network due to a lack of resources in the network {e.g., available link capacity, router buffers}.

## Slide 4: Congestion Control
Congestion control is concerned with the bottleneck routers in a packet switched network.
Congestion control can be distinguished from routing in that sometimes there is no way to ‘route around’ a congested router.

## Slide 5
4
8
6
3
2
1
5
7
Congestion
Figure 7.50b
Leon-Garcia & Widjaja: Communication Networks
Leon-Garcia & Widjaja: Communication Networks
Leon-Garcia & Widjaja: Communication Networks
Copyright ©2000 The McGraw Hill Companies
Copyright ©2000 The McGraw Hill Companies
Leon-Garcia & Widjaja: Communication Networks

## Slide 6: Figure 6.1 Congestion in a packet-switched network

## Slide 7: Flows
flow :: a sequence of packets sent between a source/destination pair and following the same route through the network.
Connectionless flows within the TCP/IP model:: The connection-oriented abstraction, TCP, is implemented at the transport layer while IP provides a connectionless datagram delivery service.
With connectionless flows, there exists no state at the routers.

## Slide 8: Flows
Connection-oriented flows (e.g., X.25) – connection-oriented networks maintain hard state at the routers.
Soft state :: represents a middle ground where soft state is not always explicitly created and removed by signaling.
Correct operation of the network does not depend on the presence of soft state, but soft state can permit the router to better handle packets.

## Slide 9: Figure 6.2 Multiple Flows passing through a set of routers

## Slide 10: Service
Best-effort service :: The hosts are given no opportunity to ask for guarantees on a flow’s service.
QoS (Quality of Service) :: is a service model that supports some type of guarantee for a flow’s service.

## Slide 11
Offered load
Throughput
Controlled
Uncontrolled
Figure 7.51
Leon-Garcia & Widjaja: Communication Networks
Copyright ©2000 The McGraw Hill Companies
Lack of Congestion Control

## Slide 12: Congestion Control Taxonomy
Router-Centric
  The internal network routers take responsibility for:
    Which packets to forward
    Which packets to drop or mark
    The nature of congestion notification to the hosts.
  This includes the Queuing Algorithm to manage the buffers at the router.
Host-Centric
  The end hosts adjust their behavior based on observations of network conditions.
  (e.g., TCP Congestion Control Mechanisms)

## Slide 13: Congestion Control Taxonomy
Reservation-Based – the hosts attempt to reserve network capacity when the flow is established.
  The routers allocate resources to satisfy reservations or the flow is rejected.
  The reservation can be receiver-based (e.g., RSVP) or sender-based.

## Slide 14: Congestion Control Taxonomy
Feedback-Based - The transmission rate is adjusted (via window size) according to feedback received from the sub network.
  Explicit feedback – FECN, BECN, ECN
  Implicit feedback – router packet drops.
Window-Based - The receiver sends an advertised window to the sender or a window advertisement can be used to reserve buffer space in routers.
Rate-Based – The sender’s rate is controlled by the receiver indicating the bits per second it can absorb.

## Slide 15: Evaluation Criteria
Evaluation criteria are needed to decide how well a network effectively and fairly allocates resources.
Effective measures – throughput, utilization, efficiency, delay, queue length, goodput and power.
throughputα
Power = --------------
delay

## Slide 16: Fairness
Jain’s fairness index
For any given set of user throughputs (x1, x2,…xn ), the fairness index to the set is defined:
f(x1, x2, …, xn) =
Max-min fairness
Essentially ‘borrow’ from the rich-in-performance to help the poor-in-performance.
For example, CSFQ (Core Stateless Fair Queueing)

## Slide 17: Congestion Control (at the router)
Queuing algorithms determine:
  How packets are buffered.
  Which packets get transmitted.
  Which packets get marked or dropped.
  Indirectly determine the delay at the router.
Queues at outgoing links drop/mark packets to implicitly signal congestion to TCP sources.
Remember to separate queuing policy from queuing mechanism.

## Slide 18: Congestion Control (at the router)
Some of the possible choices in queuing algorithms:
  FIFO (FCFS) also called Drop-Tail
  Fair Queuing (FQ)
  Weighted Fair Queuing (WFQ)
  Random Early Detection (RED)
  Explicit Congestion Notification (ECN).

## Slide 19: Drop Tail Router [FIFO]
First packet to arrive is first to be transmitted.
FIFO queuing mechanism that drops packets from the tail of the queue when the queue overflows.
Introduces global synchronization when packets are dropped from several connections.
FIFO is the scheduling mechanism, Drop Tail is the policy

## Slide 20: Priority Queuing
Mark each packet with a priority (e.g., in TOS (Type of Service field in IP)
Implement multiple FIFO queues, one for each priority class.
Always transmit out of the highest priority non-empty queue.
Still no guarantees for a given priority class.

## Slide 21: Priority Queuing
Problem:: high priority packets can ‘starve’ lower priority class packets.
Priority queuing is a simple case of “differentiated services” [DiffServ].
One practical use in the Internet is to protect routing update packets by giving them a higher priority and a special queue at the router.

## Slide 22: Fair Queuing [FQ]
The basic problem with FIFO is that it does not separate packets by flow.
Another problem with FIFO is an “ill-behaved” flow can capture an arbitrarily large share of the network’s capacity.
Idea:: maintain a separate queue for each flow, and Fair Queuing (FQ) services these queues in a round-robin fashion.

## Slide 23: Figure 6.6 Fair Queuing

## Slide 24: Fair Queuing [FQ]
“Ill-behaved” flows are segregated into their own queue.
There are many implementation details for FQ, but the main problem is that packets are of different lengths  simple FQ is not fair!!
Ideal FQ:: do bit-by-bit round-robin.

## Slide 25: Fair Queuing [FQ]
FQ simulates bit-by-bit behavior by using timestamps (too many details for here!).
One can think of FQ as providing a guaranteed minimum share of bandwidth to each flow.
FQ is work-conserving in that the server is never idle as long as there is a customer in the queue.
Note: The per-flow state information kept at the router is expensive (it does not scale).

## Slide 26: Weighted Fair Queuing [WFQ]
WFQ idea:: Assign a weight to each flow (queue) such that the weight logically specifies the number of bits to transmit each time the router services that queue.
This controls the percentage of the link capacity that the flow will receive.
The queues can represent “classes” of service and this becomes DiffServ.
An issue – how does the router learn of the weight assignments?
  Manual configuration
  Signaling from sources or receivers.

## Slide 27: Congestion Control Summary
Congestion Control (definition)
Flows
CC Taxonomy
Evaluation Criteria
  Jain’s fairness
Introduction to Queueing
  FIFO (FCFS drop tail)
  Priority
  FQ (Fair Queueing)
  WFQ (Weighted Fair Queueing)