## Slide 1: Network Layer
Computer Networks

## Slide 2: Network Layer Topics
4.1 Introduction
4.2 Virtual circuit and datagram networks
4.3 What is inside a router?
4.4 IP: Internet Protocol
  Datagram Format
  IPv4 addressing
  Subnets
  CIDR
  ARP & DHCP
  NAT
4.5 Routing algorithms
  Algorithm Classification
  Link State
  Distance Vector
  Hierarchical Routing
4.6 Routing in the Internet
  RIP
  OSPF
  BGP
4.7 ICMP
K & R

## Slide 3: Network Layer Introduction
Concerned with getting packets from source to destination.
The network layer must know the topology of the subnet and choose appropriate paths through it.
When source and destination hosts are in different networks, the network layer (IP) must deal with these differences.
Key issue: What service does the network layer provide to the transport layer?
connection-oriented or connectionless

## Slide 4: Network Layer Design Goals
1. The services provided by the network layer should be independent of the subnet topology.
2. The transport layer should be shielded from the number, type and topology of the subnets present.
3. The network addresses available to the transport layer should use a uniform numbering plan (even across LANs, WANs and WLANs).

## Slide 5
Physical
layer
Data link
layer
Physical
layer
Data link
layer
End system
a
Network
layer
Physical
layer
Data link
layer
Physical
layer
Data link
layer
Transport
layer
Transport
layer
Messages
Messages
Segments
End system
b
Network
service
Network
service
Network
layer
Network
layer
Network Layer
Leon-Garcia & Widjaja:
Communication Networks
Network
layer

## Slide 6
Application
Transport
Internet
Network Interface
Application
Transport
Internet
Internet
Network 1
Network 2
Machine A
Machine B
Router/Gateway
Network Interface
Network Interface
Leon-Garcia & Widjaja:
Communication Networks
Network Layer

## Slide 7: Metropolitan Area Network (MAN)
R
R
R
R
S
S
S
s
s
s
s
s
s
s
s
s
s
R
s
R
Backbone
To the Internet or wide area network
Organization Servers
Gateway
Departmental Server
Leon-Garcia & Widjaja:
Communication Networks

## Slide 8: Wide Area Network (WAN)
Interdomain level
Intradomain level
LAN level
Autonomous system
or domain
Border routers
Border routers
Internet Service Provider (ISP)
Leon-Garcia & Widjaja:
Communication Networks

## Slide 9: Modern Internet Backbone
National service provider A
National service provider B
National service provider C
NAP
NAP
National Internet Service Providers
Network Access
Point
Leon-Garcia & Widjaja:
Communication Networks

## Slide 10: Network Access Point
Leon-Garcia & Widjaja:
Communication Networks
RA
RB
RC
Route server
NAP
LAN
often called
the default router

## Slide 11: Network Layer Topics
4.1 Introduction
4.2 Virtual circuit and datagram networks
4.3 What is inside a router?
4.4 IP: Internet Protocol
  Datagram Format
  IPv4 addressing
  Subnets
  CIDR
  ARP & DHCP
  NAT
4.5 Routing algorithms
  Algorithm Classification
  Link State
  Distance Vector
  Hierarchical Routing
4.6 Routing in the Internet
  RIP
  OSPF
  BGP
4.7 Broadcast and multicast routing
K & R

## Slide 12: Datagram Packet Switching
Packet 2
Packet 1
Packet 1
Packet 2
Packet 2
Leon-Garcia & Widjaja:
Communication Networks

## Slide 13: Datagram Routing Table
Destination
address
Output
port
1345
12
2458
7
0785
6
12
1566
IP addresses
Leon-Garcia & Widjaja:
Communication Networks

## Slide 14: Virtual Circuit Packet Switching
Packet
Packet
Leon-Garcia & Widjaja:
Communication Networks

## Slide 15: Virtual Circuit Routing Table
Identifier
Output
port
15
9
58
13
13
7
27
12
Next
identifier
44
23
16
34
Entry for packets
with identifier 15
Leon-Garcia & Widjaja:
Communication Networks
Packet leaves with
new identifier 23

## Slide 16: Network Layer
transports segment from sending to receiving host.
encapsulates segments on sending side into datagram packets.
delivers segments on receiving side to the transport layer.
network layer protocols exist in every host, router.
router examines header fields in all IP datagrams passing through it.
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
K & R

## Slide 17: Network Layer Topics
4.1 Introduction
4.2 Virtual circuit and datagram networks
4.3 What is inside a router?
4.4 IP: Internet Protocol
  Datagram Format
  IPv4 addressing
  Subnets
  CIDR
  ARP & DHCP
  NAT
4.5 Routing algorithms
  Algorithm Classification
  Link State
  Distance Vector
  Hierarchical Routing
4.6 Routing in the Internet
  RIP
  OSPF
  BGP
4.7 ICMP
K & R

## Slide 18: Two Key Network Layer Functions
forwarding: move packets from router’s input to appropriate router output.
routing: determine route taken by packets from source to destination.
analogy:
forwarding: process of getting through single interchange
routing: process of planning trip from source to destination
K & R

## Slide 19: Interplay between Routing and Forwarding
1
2
3
0111
value in arriving
packet’s header
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
K & R
Routing creates the tables.
Forwarding uses the tables.

## Slide 20: Router Node Forwarding
packet
node 15
17
Outgoing Link
Router Link Buffer
Server
packet
Incoming Link
Routing table
lookup
134 17

## Slide 21: Routing in an internet
  Figure 3.14 A Simple internetwork with Three Routers

## Slide 22: Protocol Layers along the Route
IP runs on all the nodes in a collection of networks and defines the infrastructure that allows these nodes and networks to function as a single logical internetwork.
  Figure 3.15 Protocol Layers used for a Simple internet

## Slide 23: Forwarding Table Example
Network Number | Next Hop
1 | R1
2 | Interface 1
3 | Interface 0
4 | R3
  Table 3.6 Complete Forwarding
  Table for Router R2 in Figure 3.14
  Note – As R2 is on Network 2 and Network 3, this table shows packets headed for H1, H2 and H3 are not forwarded by R2 to another router.

## Slide 24: The Internet Network Layer
forwarding
table
Host, router network layer functions:
Routing protocols
path selection
RIP, OSPF, BGP
IP protocol
addressing conventions
datagram format
packet handling conventions
ICMP protocol
error reporting
router “signaling”
Transport Layer: TCP, UDP
Data Link Layer
Physical Layer
Network
Layer
K & R

## Slide 25: Network Layer Topics
4.1 Introduction
4.2 Virtual circuit and datagram networks
4.3 What is inside a router?
4.4 IP: Internet Protocol
  Datagram Format
  IPv4 addressing
  Subnets
  CIDR
  ARP & DHCP
  NAT
4.5 Routing algorithms
  Algorithm Classification
  Link State
  Distance Vector
  Hierarchical Routing
4.6 Routing in the Internet
  RIP
  OSPF
  BGP
4.7 ICMP
K & R

## Slide 26: IPv4 Datagram Format
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
IP protocol version
number
header length
(bytes)
TTL:: max hops
remaining (each
router decrements)
Three fields
for
fragmentation/
reassembly
total datagram
length (bytes)
upper layer protocol
to deliver payload to
head.
len
type of
service
TOS:: data type
flgs
fragment
offset
upper
layer
32 bit destination IP address
Options (if any)
E.g. timestamp,
record route
taken, specify
list of routers
to visit.
how much overhead with TCP?
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead
K & R

## Slide 27: IP Fragmentation & Reassembly
network links have MTU (max.transfer size) - largest possible link-level frame.
  different link types, different MTUs
large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams.
  “reassembled” only at final destination.
  IP header bits used to identify, order related fragments.
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly
K & R

## Slide 28: IP Fragmentation & Reassembly
Specified in
8 byte units
Figure 3.18 Header fields used in IP fragmentation: (a) unfragmented packet; (b) fragmented packets.

## Slide 29
Figure 3.17 IP datagrams traversing the sequence of physical networks graphed in Figure 3.14.
IP Fragmentation for Figure 3.14

## Slide 30: Network Layer Topics
4.1 Introduction
4.2 Virtual circuit and datagram networks
4.3 What is inside a router?
4.4 IP: Internet Protocol
  Datagram Format
  IPv4 addressing
  Subnets
  CIDR
  ARP & DHCP
  NAT
4.5 Routing algorithms
  Algorithm Classification
  Link State
  Distance Vector
  Hierarchical Routing
4.6 Routing in the Internet
  RIP
  OSPF
  BGP
4.7 Broadcast and multicast routing
K & R

## Slide 31: Figure 4.1 The tree structure of the Internet in 1990
NSFNET backbone
Stanford
BARRNET
regional
Berkeley
PARC
NCAR
UA
UNM
Westnet
regional
UNL
KU
ISU
MidNet
regional
■ ■ ■
Global Internet

## Slide 32: Global Internet
Each provider network is regional and a single autonomous system (AS)
Major issues are:
  Scalability of routing
  Address utilization
    Now out of IPv4 addresses
Hierarchy is used to improve scalability.
  Namely, utilize subnets with masks.

## Slide 33
Figure 3.19 IP addresses: (a) class A; (b) class B; (c) class C.
IPv4 Network Classes

## Slide 34: Network Number Problems
Assigning one network number per physical network uses up IP address too fast!
Adding more network numbers also increases forwarding table size.
Subnet solution ::
The idea is to take a single IP network number and allocate the IP addresses with that network number to several physical networks which are referred to as subnets.
The subnets need to be physically close to each other for routing purposes.

## Slide 35: Subnetting
The mechanism by which a single network number can be shared among multiple networks involves configuring all the nodes on each subnet with a subnet mask.
The subnet mask enables introduction of a single subnet number which provides for another level of hierarchy into the IP address.
All hosts on a given subnet are configured with the same mask, i.e., there is one subnet mask per subnet.

## Slide 36: IP Addressing: Introduction
IP address:: 32-bit identifier for host, router interface.
interface:: connection between host/router and physical link
  router’s typically have multiple interfaces.
  host typically has one interface.
  IP addresses are associated with each interface.
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1
K & R

## Slide 37: Subnets
IP address:
  subnet part (high order bits)
  host part (low order bits)
What is a subnet ?
  device interfaces with same subnet part of IP address.
  can physically reach each other without an intervening router.
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
network consisting of three subnets
subnet
K & R

## Slide 38
Figure 3.20 Subnet Addressing
Subnet Masks

## Slide 39: Subnetting Example
Figure 3.21
An Example of Subnetting
Table 3.7
Forwarding Table at Router R1

## Slide 40: Subnets
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
Subnet Concepts
To determine the subnets, detach each interface from its host or router, creating islands of isolated networks. Each isolated network is called a subnet.
Sending host does bitwise AND between subnet mask and destination address to determine whether packet needs to be routed or not.
Subnet mask: /24 :: defined
by the leftmost 24 bits.
K & R

## Slide 41: Subnets
How many subnets
in the figure?
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.1
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2
K & R

## Slide 42: IP Addressing: CIDR
CIDR: Classless InterDomain Routing
  Allows a subnet portion of address of arbitrary length.
  address format: a.b.c.d/x, where x is number of bits in subnet portion of address.
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23
K & R

## Slide 43: Classless Routing (CIDR)
CIDR helps aggregate routes by breaking up rigid boundaries between classes.
Handing out Class C addresses in contiguous blocks by address makes it possible for addresses to share a common prefix.
  allocate Class C networks as a power of 2.
We need a protocol that understands these rules, e.g., BGP
Network numbers are represented by (length,value) where length is the length of the prefix {similar to a mask}.

## Slide 44: Classless Routing (CIDR)
Figure 4.27 Route Aggregation
with CIDR
P&D 4th

## Slide 45
Figure 3.22 Route Aggregation with CIDR
CIDR Route Aggregation
Eight ISP customers
share a 21-bit
common prefix.

## Slide 46: Network Layer Topics
4.1 Introduction
4.2 Virtual circuit and datagram networks
4.3 What is inside a router?
4.4 IP: Internet Protocol
  Datagram Format
  IPv4 addressing
  Subnets
  CIDR
  ARP & DHCP
  NAT
4.5 Routing algorithms
  Algorithm Classification
  Link State
  Distance Vector
  Hierarchical Routing
4.6 Routing in the Internet
  RIP
  OSPF
  BGP
4.7 ICMP
K & R

## Slide 47: Routing Algorithm Classification
Computer Networks
Network Layer

## Slide 48: Routing
Routing algorithm:: that part of the Network Layer responsible for deciding on which output line to transmit an incoming packet.
Remember: For virtual circuit subnets the routing decision is made ONLY at set up.
Algorithm properties:: correctness, simplicity, robustness, stability, fairness, optimality, and scalability.

## Slide 49: Routing Classification
Adaptive Routing
based on current measurements
of traffic and/or topology.
1. centralized
2. isolated
3. distributed
Non-Adaptive Routing
routing computed in advance and off-line
1. flooding
2. static routing using shortest path algorithms

## Slide 50: Flooding
Pure flooding :: every incoming packet to a node is sent out on every outgoing line.
  Obvious adjustment – do not send out on arriving link (assuming full-duplex links).
  The routing algorithm can use a hop counter (e.g., TTL) to dampen the flooding.
  Selective flooding :: only send on those lines going “approximately” in the right direction.

## Slide 51
Figure 3.28 Network represented as a graph.
Routing is Graph Theory Problem
edges have costs

## Slide 52: Shortest Path Routing
1. Bellman-Ford Algorithm [Distance Vector]
2. Dijkstra’s Algorithm [Link State]
What does it mean to be the shortest (or optimal) route?
We need a cost metric (edges in graph):
a. Minimize the number of hops along the path.
b. Minimize the mean packet delay.
c. Maximize the network throughput.

## Slide 53: Internetwork Routing [Halsall]
Adaptive Routing
Centralized
Distributed
Intradomain routing
Interdomain routing
Distance Vector routing
Link State routing
[IGP]
[EGP]
[BGP,IDRP]
[OSPF,IS-IS,PNNI]
[RIP]
[RCC]
Interior
Gateway Protocols
Exterior
Gateway Protocols
Isolated

## Slide 54: Adaptive Routing Design
Design Issues:
How much overhead is incurred due to gathering the routing information and sending routing packets?
What is the time frame (i.e, the frequency) for sending routing packets in support of adaptive routing?
What is the complexity of the routing strategy?

## Slide 55: Adaptive Routing
Basic functions:
1. Measurement of pertinent network data {e.g. the cost metric}.
2. Forwarding of information to where the routing computation will be done.
3. Compute the routing tables.
4. Convert the routing table information into a routing decision and then dispatch the data packet.

## Slide 56: Centralized Routing
RCC
A
Z
W
B

## Slide 57: Network Layer Topics
4.1 Introduction
4.2 Virtual circuit and datagram networks
4.3 What is inside a router?
4.4 IP: Internet Protocol
  Datagram Format
  IPv4 addressing
  Subnets
  CIDR
  ARP & DHCP
  NAT
4.5 Routing algorithms
  Algorithm Classification
  Link State
  Distance Vector
  Hierarchical Routing
4.6 Routing in the Internet
  RIP
  OSPF
  BGP
4.7 ICMP
K & R

## Slide 58: Distance Vector Routing {Tanenbaum & Perlman version}
Computer Networks
Network Layer

## Slide 59: Distance Vector Routing
Historically known as the old ARPANET routing algorithm {or known as Bellman-Ford (BF) algorithm}.
BF Basic idea: each router maintains a Distance Vector table containing the distance between itself and ALL possible destination nodes.
Distances, based on the chosen metric, are computed using information from the neighbors’ distance vectors.
Distance Metric: usually hops or delay

## Slide 60: Distance Vector Routing
Information kept by DV router
each router has an ID
associated with each link connected to a router, there is a link cost (static or dynamic).
Distance Vector Table Initialization
Distance to itself = 0
Distance to ALL other routers = infinity number

## Slide 61: Distance Vector Algorithm [Perlman]
A router transmits its distance vector to each of its neighbors in a routing packet.
Each router receives and saves the most recently received distance vector from each of its neighbors.
A router recalculates its distance vector when:
  It receives a distance vector from a neighbor containing different information than before.
  It discovers that a link to a neighbor has gone down (i.e., a topology change).
The DV calculation is based on minimizing the cost to each destination.

## Slide 62: Distance Vector Example
Tanenbaum
Figure 5-9.(a) A subnet. (b) Input from A, I, H, K, and the new routing table for J.

## Slide 63: Distance Vector Routing {Kurose & Ross version}
Computer Networks
Distance Vector Routing

## Slide 64: Distance Vector Algorithm
Bellman-Ford Equation (dynamic programming)
Define
dx(y) := cost of least-cost path from x to y
Then
dx(y) = min {c(x,v) + dv (y)}
where min is taken over all neighbors v of x.
v

## Slide 65: Bellman-Ford Example
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
Clearly, dv(z) = 5, dx(z) = 3, dw(z) = 3
du(z) = min { c(u,v) + dv(z),
c(u,x) + dx(z),
c(u,w) + dw(z) }
= min {2 + 5,
1 + 3,
5 + 3} = 4
The node that achieves minimum is next
hop in shortest path ➜ forwarding table.
Namely, packets from u destined for z are
forwarded out link between u and x.
B-F equation says:

## Slide 66: Distance Vector Algorithm (3)
Dx(y) = estimate of least cost from x to y
Node x knows cost to each neighbor v: c(x,v)
Node x maintains distance vector
Dx = [Dx(y): y є N ]
Node x also maintains its neighbors’ distance vectors
  For each neighbor v, x maintains Dv = [Dv(y): y є N ]

## Slide 67: Distance Vector Algorithm (4)
DV Basic idea:
From time-to-time, each node sends its own distance vector estimate to neighbors.
Asynchronous
When a node x receives a new DV estimate from any neighbor v, it saves v’s distance vector and it updates its own DV using B-F equation:
Dx(y) ← minv{c(x,v) + Dv(y)} for each node y ∊ N
Under minor, natural conditions, the estimate Dx(y) converges to the actual least cost dx(y).

## Slide 68: Distance Vector Algorithm (5)
Iterative, asynchronous: each local iteration caused by:
local link cost change
DV update message from neighbor
Distributed:
each node notifies neighbors only when its DV changes
  neighbors then notify their neighbors if necessary.
wait for (change in local link cost or msg from neighbor)
recompute estimates
if DV to any destination has changed, notify neighbors
Each node:

## Slide 69
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0
from
cost to
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
time
x
z
1
2
7
y
node x table
node y table
node z table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
3
2

## Slide 70
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
2 0 1
7 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
time
x
z
1
2
7
y
node x table
node y table
node z table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3

## Slide 71: Distance Vector: Link Cost Changes
Link cost changes:
node detects local link cost change.
updates routing info, recalculates distance vector.
if DV changes, it notifies neighbors .
At time t0, y detects the link-cost change, updates its DV, and informs its neighbors.
“good
news
travels
fast”
At time t1, z receives the update from y and updates its table.
It computes a new least cost to x and sends its neighbors its DV.
At time t2, y receives z’s update and updates its distance table.
y’s least costs do not change and hence y does not send any
message to z.
x
z
1
4
50
y
1

## Slide 72
Link cost changes:
good news travels fast
bad news travels slow - “count to
infinity” problem!
44 iterations before algorithm
stabilizes: see P&D page 248!
Does this solve count to infinity problem?
x
z
1
4
50
y
60
Distance Vector: Link Cost Changes
Possible solutions:
Keep ‘infinity ‘ small {depends on graph diameter}.
Split Horizon: node does not send those routes learned from a neighbor back to that neighbor.
Split Horizon with Poison Reverse:
  If z routes through y to get to x, z tells y its (z’s) distance to x is infinite (so y won’t route to x via z).

## Slide 73: Network Layer Topics
4.1 Introduction
4.2 Virtual circuit and datagram networks
4.3 What is inside a router?
4.4 IP: Internet Protocol
  Datagram Format
  IPv4 addressing
  Subnets
  CIDR
  ARP & DHCP
  NAT
4.5 Routing algorithms
  Algorithm Classification
  Link State
  Distance Vector
  Hierarchical Routing
4.6 Routing in the Internet
  RIP
  OSPF
  BGP
4.7 ICMP
K & R

## Slide 74: Link State Algorithm
Each router is responsible for meeting its neighbors and learning their names.
Each router constructs a link state packet (LSP) which consists of a list of names and cost to reach each of its neighbors.
The LSP is transmitted to ALL other routers. Each router stores the most recently generated LSP from each other router.
Each router uses complete information on the network topology to compute the shortest path route to each destination node.

## Slide 75: Figure 3.32 Reliable LSP Flooding
Reliable Flooding

## Slide 76
Reliable Flooding
The process of making sure all the nodes participating in the routing protocol get a copy of the link-state information from all the other nodes.
LSP contains:
  Sending router’s node ID
  List of connected neighbors with the associated link cost to each neighbor
  Sequence number
  Time-to-live (TTL) {an aging mechanism}

## Slide 77
First two items enable route calculation.
Last two items make process reliable
  ACKs and checking for duplicates is needed.
Periodic Hello packets used to determine the demise of a neighbor.
The sequence numbers are not expected to wrap around.
   this field needs to be large (64 bits) !!
Reliable Flooding

## Slide 78: A Link-State Routing Algorithm
Dijkstra’s algorithm
net topology, link costs known to all nodes
  accomplished via “link state broadcast”.
  all nodes have same info.
computes least cost paths from one node (‘source”) to all other nodes
  gives forwarding table for that node.
iterative: after k iterations, know least cost path to k destinations.
Notation:
c(x,y): link cost from node x to y; = ∞ if not direct neighbors.
D(v): current value of cost of path from source to destination v
p(v): predecessor node along path from source to v
N': set of nodes whose least cost path is definitively known.
K & R

## Slide 79: Dijsktra’s Algorithm [K&R]
1 Initialization:
2 N' = {u}
3 for all nodes v
4 if v adjacent to u
5 then D(v) = c(u,v)
6 else D(v) = ∞
7
8 Loop
9 find w not in N' such that D(w) is a minimum
10 add w to N'
11 update D(v) for all v adjacent to w and not in N' :
12 D(v) = min( D(v), D(w) + c(w,v) )
13 /* new cost to v is either old cost to v or known
14 shortest path cost to w plus cost from w to v */
15 until all nodes in N'
K & R

## Slide 80: Dijkstra’s Algorithm: Example
Step
0
1
2
3
4
5
N'
u
ux
uxy
uxyv
uxyvw
uxyvwz
D(v),p(v)
2,u
2,u
2,u
D(w),p(w)
5,u
4,x
3,y
3,y
D(x),p(x)
1,u
D(y),p(y)
∞
2,x
D(z),p(z)
∞
∞
4,y
4,y
4,y
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
K & R

## Slide 81: Dijkstra’s Algorithm: Example (2)
u
y
x
w
v
z
Resulting shortest-path tree from u:
v
x
y
w
z
(u,v)
(u,x)
(u,x)
(u,x)
(u,x)
destination
link
Resulting forwarding table in u:
K & R

## Slide 82: Dijkstra’s Algorithm, Discussion
Algorithm complexity: n nodes
each iteration: need to check all nodes, w, not in N
n(n+1)/2 comparisons: O(n2)
more efficient implementations possible: O(nlogn)
Oscillations possible:
e.g., link cost = amount of carried traffic
A
D
C
B
1
1+e
e
0
e
1
1
0
0
A
D
C
B
2+e
0
0
0
1+e
1
A
D
C
B
0
2+e
1+e
1
0
0
A
D
C
B
2+e
0
e
0
1+e
1
initially
… recompute
routing
… recompute
… recompute
K & R

## Slide 83: Network Layer Topics
4.1 Introduction
4.2 Virtual circuit and datagram networks
4.3 What’s inside a router
4.4 IP: Internet Protocol
  Datagram Format
  IPv4 addressing
  Subnets
  CIDR
  ARP & DHCP
  NAT
4.5 Routing algorithms
  Algorithm Classification
  Link State
  Distance Vector
  Hierarchical Routing
4.6 Routing in the Internet
  RIP
  OSPF
  BGP
4.7 ICMP
K & R

## Slide 84: Hierarchical Routing
scale: with 200 million destinations:
can’t store all destinations in routing tables!
routing table exchange would swamp links!
administrative autonomy
internet = network of networks
each network admin may want to control routing in its own network.
Our routing study thus far - idealization
all routers identical
network “flat”
… not true in practice

## Slide 85: Hierarchical Routing
aggregate routers into regions, “autonomous systems” (AS)
routers in same AS run same routing protocol
  “intra-AS” routing protocol
  routers in different AS can run different intra-AS routing protocol
Gateway router
Direct link to router in another AS

## Slide 86: Interconnected AS’s
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
Intra-AS
Routing
algorithm
Inter-AS
Routing
algorithm
Forwarding
table
3c
forwarding table configured by both intra- and inter-AS routing algorithm
  intra-AS sets entries for internal destinations.
  inter-AS & intra-AS sets entries for external destinations.

## Slide 87: Inter-AS Tasks
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
suppose router in AS1 receives datagram destined outside of AS1:
  router should forward packet to gateway router, but which one?
AS1 must:
learn which dests are reachable through AS2, which through AS3
propagate this reachability info to all routers in AS1
Job of inter-AS routing!

## Slide 88: Network Layer Topics
4. 1 Introduction
4.2 Virtual circuit and datagram networks
4.3 What is inside a router?
4.4 IP: Internet Protocol
  Datagram format
  IPv4 addressing
  Subnets
  CIDR
  ARP & DHCP
  NAT
4.5 Routing algorithms
  Algorithm Classification
  Link State
  Distance Vector
  Hierarchical Routing
4.6 Routing in the Internet
  RIP
  OSPF
  BGP
4.7 ICMP

## Slide 89: Intra-AS Routing
also known as Interior Gateway Protocols (IGP)
most common Intra-AS routing protocols:
  RIP: Routing Information Protocol
  OSPF: Open Shortest Path First
  IGRP: Interior Gateway Routing Protocol (Cisco proprietary)

## Slide 90: Network Layer Topics
4. 1 Introduction
4.2 Virtual circuit and datagram networks
4.3 What is inside a router?
4.4 IP: Internet Protocol
  Datagram format
  IPv4 addressing
  Subnets
  CIDR
  ARP & DHCP
  NAT
4.5 Routing algorithms
  Algorithm Classification
  Link State
  Distance Vector
  Hierarchical Routing
4.6 Routing in the Internet
  RIP
  OSPF
  BGP
4.7 ICMP

## Slide 91: Routing Information Protocol (RIP)
RIP had widespread use because it was distributed with BSD Unix in “routed”, a router management daemon in 1982.
RIP - most used Distance Vector protocol.
RFC1058 in June 1988
Runs over UDP.
Metric = hop count
Big problem is max. hop count =16
 RIP limited to running on small networks (or AS’s that have a small diameter)!!

## Slide 92: Routing Information Protocol (RIP)
Sends DV packets every 30 seconds (or faster) as Response Messages (also called advertisements).
each advertisement: list of up to 25 destination subnets within AS.
Upgraded to RIPv2
D
C
B
A
u
v
w
x
y
z
destination hops
u 1
v 2
w 2
x 3
y 3
z 2
From router A to subnets:

## Slide 93: Figure 4.17 RIP Packet Format
(network_address,
distance)
pairs
P&D 4th
RIP Packets

## Slide 94: RIPv2
Allows routing on a subnet (subnet masks)
Has an authentication mechanism
Tries to deal with multicast
Uses route tags
Has the ability for router to announce routes on behalf of another router.

## Slide 95
Figure 3.31 RIPv2 Packet Format
RIPv2 Packets
subnet masks

## Slide 96: Network Layer Topics
4.1 Introduction
4.2 Virtual circuit and datagram networks
4.3 What’s inside a router
4.4 IP: Internet Protocol
  Datagram Format
  IPv4 addressing
  Subnets
  CIDR
  ARP & DHCP
  NAT
4.5 Routing algorithms
  Algorithm Classification
  Link State
  Distance Vector
  Hierarchical Routing
4.6 Routing in the Internet
  RIP
  OSPF
  BGP
4.7 ICMP
K & R

## Slide 97: OSPF (Open Shortest Path First)
“open” :: publicly available (due to IETF)
uses Link State algorithm
  LS packet dissemination
  topology map at each node
  route computation uses Dijkstra’s algorithm.
OSPF advertisement carries one entry per neighbor router.
advertisements disseminated to entire AS (via flooding*).
  carried in OSPF messages directly over IP (rather than TCP or UDP).
* However hierarchy (partitioning domains into areas) reduces flooding impact.

## Slide 98
Figure 4.2 A domain divided into areas
Partitioning Domains

## Slide 99: Hierarchical OSPF

## Slide 100: Hierarchical OSPF
Two-level Hierarchy:: local area, backbone.
  Some Link-State Advertisement (LSA) types are only sent into one area.
  Each node has detailed area topology; only knows direction (shortest path) to nets in other areas.
area border routers: “summarize” distances to nets in own area, advertise to other Area Border routers.
backbone routers: run OSPF routing limited to backbone.
boundary routers: connect to other AS’s.

## Slide 101: OSPF LSA Types
1. Router link advertisement [Hello message]
2. Network link advertisement
  identifies connected networks.
3. Network summary link advertisement
4. AS border router’s summary link advertisement
5. AS external link advertisement

## Slide 102
Figure 3.34 OSPF Header Format
OSPF Header

## Slide 103
Type 1 OSPF LSA
Figure 3.3 OSPF Link-State Advertisement (LSA)

## Slide 104: OSPF “Advanced” Features (not in RIP)
security: all OSPF messages authenticated (to prevent malicious intrusion).
multiple same-cost paths means distributed load balancing of traffic over routes (only one path in RIP).
For each link, multiple cost metrics for different TOS (e.g., satellite link cost set “low” for best effort; high for real time).
integrated uni- and multicast support:
  Multicast OSPF (MOSPF) uses same topology data base as OSPF.
hierarchical OSPF is used in large domains.

## Slide 105: OSPF
Figure 5-65.The relation between AS’s, backbones, and areas in OSPF
Tanenbaum

## Slide 106: Network Layer Topics
4.1 Introduction
4.2 Virtual circuit and datagram networks
4.3 What is inside a router?
4.4 IP: Internet Protocol
  Datagram Format
  IPv4 addressing
  Subnets
  CIDR
  ARP &DHCP
  NAT
4.5 Routing algorithms
  Algorithm Classification
  Link State
  Distance Vector
  Hierarchical Routing
4.6 Routing in the Internet
  RIP
  OSPF
  BGP
4.7 ICMP
K & R

## Slide 107: Internet Inter-AS Routing: BGP
BGP (Border Gateway Protocol): de facto standard interdomain routing protocol.
BGP provides each AS a means to:
  Obtain subnet reachability information from neighboring ASs.
  Propagate reachability information to all AS-internal routers.
  Determine “good” loop-free routes to subnets based on reachability information and policy.
allows subnet to advertise its existence to rest of Internet: “I am here!”

## Slide 108
Figure 4.4 A simple multi-provider Internet
BGP Assumes an Arbitrary
Interconnection of AS’s

## Slide 109: BGP Issues/Concerns
Scalability: An Internet backbone router must be able to forward any packet destined anywhere in the Internet.
  Having a routing table that will provide a match for any valid IP address.
Autonomous nature of the domains
  It is impossible to calculate meaningful path costs for a path that crosses multiple ASs.
  A cost of 1000 across one provider might imply a great path but it might mean an unacceptable bad one from another provider.
Issues of trust
  Provider A might be unwilling to believe certain advertisements from provider B.

## Slide 110: BGP-4: Border Gateway Protocol
Define local traffic as traffic that originates at or terminates on nodes within an AS, and transit traffic as traffic that passes through an AS.
Classify AS's into three types:
  Stub AS:: an AS that has only a single connection to one other AS; such an AS will only carry local traffic (small corporation in Figure 4.4 ).
  Multihomed AS:: an AS that has connections to more than one other AS, but refuses to carry transit traffic (large corporation at the top in Figure 4.4).
  Transit AS:: an AS that has connections to more than one other AS, and is designed to carry both transit and local traffic (backbone providers in Figure 4.4).

## Slide 111: BGP
BGP does not belong to either of the two main classes of routing protocols (distance vectors and link-state protocols).
BGP advertises complete paths as an enumerated lists of ASs to reach a particular network. Hence, often referred to as a path-vector protocol.
  BGP paths need to be loop-free!!
   Carried AS numbers need to be unique.

## Slide 112
Figure 4.5 Example of a network running BGP
BGP Interdomain Routing

## Slide 113
Figure 4.6 Example of loop among autonomous systems
Loops in AS Topology

## Slide 114: Network Layer Topics
4.1 Introduction
4.2 Virtual circuit and datagram networks
4.3 What is inside a router?
4.4 IP: Internet Protocol
  Datagram Format
  IPv4 addressing
  Subnets
  CIDR
  ARP & DHCP
  NAT
4.5 Routing algorithms
  Algorithm Classification
  Link State
  Distance Vector
  Hierarchical Routing
4.6 Routing in the Internet
  RIP
  OSPF
  BGP
4.7 ICMP
K & R

## Slide 115: Address Resolution Protocol (ARP)
A mechanism is needed to translate IP addresses into DL layer addresses that make sense on that network (e.g., 48-bit Ethernet addresses on an Ethernet LAN).
Address pair == (hostID, Network Point of Attachment address)
where
hostID == IP address
  NPA address == Ethernet address
This translation is needed by a local interior router (e.g., R1 in Figure 3.14) and by hosts on the LAN (e.g., H1- H3 in Figure 3.14)

## Slide 116: Routing in an internet
  Figure 3.14 A Simple internetwork with Three Routers

## Slide 117: Address Resolution Protocol (ARP)
One solution :: have the router maintain a table of address pairs for all hosts attached to the LAN. Table is then copied to each host on the LAN.
  This will generate lots of extra traffic on the LAN.
* a better solution:: each host dynamically learns the contents of this address pairs table using the LAN.
This is the function performed by ARP (Address Resolution Protocol).

## Slide 118: Address Resolution Protocol (ARP)
Each node maintains an address pairs table in its cache.
If IP address of destination host is NOT found in the cache, it invokes ARP over the LAN.
An ARP query for desired IP address is broadcast on the LAN. The query includes address pair of sending host.
Each IP host receives the query and checks to see if it matches its own IP address.

## Slide 119: Address Translation Protocol (ARP)
The target host sends an ARP reply with its DL layer address and adds sending address pair to its local table.
Query originator updates information in its cached ARP table.
Note - target hosts will ‘refresh’ their cache entry if originator is in local cache, but will not make a new table entry otherwise.
ARP cache entries time out periodically (e.g., every 15 minutes) and non-refreshed entries are discarded.

## Slide 120
Figure 3.23 ARP packet format for mapping
IP addresses into Ethernet addresses
ARP Packet Format
  HardwareType: type of physical network (e.g., Ethernet)
  ProtocolType: type of higher layer protocol (e.g., IP)
  Hlen & Plen: length of link layer and protocol layer addresses
  Operation: request or response

## Slide 121: IP Addresses: How to Get One?
Q: How does a host get IP address?
hard-coded by system admin in a file
  Windows: control-panel->network->configuration->tcp/ip->properties
  UNIX: /etc/rc.config
DHCP: Dynamic Host Configuration Protocol: A host dynamically gets address from a server.
  A “plug-and-play” protocol

## Slide 122: Host Configurations
Ethernet addresses are configured into network by manufacturer and they are unique.
IP addresses must be unique on a given internetwork but also must reflect the structure of the internetwork.
Most host operating systems provide a mechanism to manually configure the host’s IP information.
Manual configuration disadvantages:
  A lot of work to configure all the hosts in a large network.
  Configuration process is error-prone.
Automated configuration process is required.

## Slide 123: DHCP
Relies on the existence of a DHCP Server that provides configuration information.
Uses UDP and ports 67 and 68.
Has widespread use in wireless LANs.
DHCP server maintains a pool of available addresses that are allocated on demand.

## Slide 124: DHCP: Dynamic Host Configuration Protocol
Goal: Allow a host to dynamically obtain its IP address from network server when it joins the network.
  Can renew its lease on address in use.
  Allows reuse of addresses (only hold address while connected and “on”).
  Support for mobile users who want to join network (more shortly). {widely used in WLANs}
DHCP overview:
  host broadcasts “DHCP discover” msg [optional]
  DHCP server responds with “DHCP offer” msg [optional]
  host requests IP address: “DHCP request” msg
  DHCP server sends address: “DHCP ACK” msg

## Slide 125: DHCP Client-Server Scenario
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
DHCP
server
arriving DHCP
client needs
address in this
network
K & R

## Slide 126: DHCP Client-Server Scenario
DHCP server: 223.1.2.5
arriving
client
time
1. DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
2. DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
Lifetime: 3600 secs
3. DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
Lifetime: 3600 secs
4. DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
Lifetime: 3600 secs
K & R

## Slide 127: DHCP: More than IP address
DHCP can return more than just allocated IP address on subnet:
  address of first-hop router for client
  name and IP address of DNS sever
  network mask (indicating network versus host portion of address).

## Slide 128: DHCP Relay Agent
Figure 3.24 DHCP relay agent receives DISCOVER message
To avoid a DHCP server on every network, DHCP relay agent unicasts the message to DHCP server and waits for the response.

## Slide 129: DHCP: Example
connecting laptop needs its IP address, addr of first-hop router, addr of DNS server: use DHCP
router
(runs DHCP)
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.1 Ethernet.
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server.
Ethernet demux’ed to IP demux’ed, UDP demux’ed to DHCP.
168.1.1.1
K & R

## Slide 130: DHCP: Example
DCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
router
(runs DHCP)
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
encapsulation of DHCP server, frame forwarded to client, demux’ing up to DHCP at client.
client now knows its IP address, name and IP address of DNS server, IP address of its first-hop router.
K & R

## Slide 131: DHCP: Wireshark Output (home LAN)
Message type: Boot Reply (2)
Hardware type: Ethernet
Hardware address length: 6
Hops: 0
Transaction ID: 0x6b3a11b7
Seconds elapsed: 0
Bootp flags: 0x0000 (Unicast)
Client IP address: 192.168.1.101 (192.168.1.101)
Your (client) IP address: 0.0.0.0 (0.0.0.0)
Next server IP address: 192.168.1.1 (192.168.1.1)
Relay agent IP address: 0.0.0.0 (0.0.0.0)
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Server host name not given
Boot file name not given
Magic cookie: (OK)
Option: (t=53,l=1) DHCP Message Type = DHCP ACK
Option: (t=54,l=4) Server Identifier = 192.168.1.1
Option: (t=1,l=4) Subnet Mask = 255.255.255.0
Option: (t=3,l=4) Router = 192.168.1.1
Option: (6) Domain Name Server
Length: 12; Value: 445747E2445749F244574092;
IP Address: 68.87.71.226;
IP Address: 68.87.73.242;
IP Address: 68.87.64.146
Option: (t=15,l=20) Domain Name = "hsd1.ma.comcast.net."
reply
Message type: Boot Request (1)
Hardware type: Ethernet
Hardware address length: 6
Hops: 0
Transaction ID: 0x6b3a11b7
Seconds elapsed: 0
Bootp flags: 0x0000 (Unicast)
Client IP address: 0.0.0.0 (0.0.0.0)
Your (client) IP address: 0.0.0.0 (0.0.0.0)
Next server IP address: 0.0.0.0 (0.0.0.0)
Relay agent IP address: 0.0.0.0 (0.0.0.0)
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Server host name not given
Boot file name not given
Magic cookie: (OK)
Option: (t=53,l=1) DHCP Message Type = DHCP Request
Option: (61) Client identifier
Length: 7; Value: 010016D323688A;
Hardware type: Ethernet
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Option: (t=50,l=4) Requested IP Address = 192.168.1.101
Option: (t=12,l=5) Host Name = "nomad"
Option: (55) Parameter Request List
Length: 11; Value: 010F03062C2E2F1F21F92B
1 = Subnet Mask; 15 = Domain Name
3 = Router; 6 = Domain Name Server
44 = NetBIOS over TCP/IP Name Server
……
request
reply
K & R

## Slide 132: Network Layer Topics
4.1 Introduction
4.2 Virtual circuit and datagram networks
4.3 What’s inside a router
4.4 IP: Internet Protocol
  Datagram Format
  IPv4 addressing
  Subnets
  CIDR
  ARP & DHCP
  NAT
4.5 Routing algorithms
  Link State
  Distance Vector
  Hierarchical Routing
4.6 Routing in the Internet
  RIP
  OSPF
  BGP
4.7 ICMP
K & R

## Slide 133: NAT: Network Address Translation
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
138.76.29.7
local network
(e.g., home network)
10.0.0/24
rest of
Internet
Datagrams with source or
destination in this network
have 10.0.0/24 address for
source, destination (as usual).
All datagrams leaving local
network have the same single source NAT IP address: 138.76.29.7,
with different source port numbers
K & R

## Slide 134
Motivation: local network uses just one IP address as far as outside world is concerned:
  range of addresses not needed from ISP: just one IP address for all devices.
  can change addresses of devices in local network without notifying outside world.
  can change ISP without changing addresses of devices in local network.
  devices inside local net not explicitly addressable, visible by outside world (a security plus).
NAT: Network Address Translation

## Slide 135
Implementation: NAT router must:
  outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
    . . . remote clients/servers will respond using (NAT IP address, new port #) as destination address.
  remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair.
  incoming datagrams: replace (NAT IP address, new port #) in dest fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table.
NAT: Network Address Translation

## Slide 136: NAT: Network Address Translation
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to
128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
10.0.0.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: Reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 10.0.0.1, 3345
K & R

## Slide 137: NAT Traversal Problem
client wants to connect to server with address 10.0.0.1
  server address 10.0.0.1 local to LAN (client can’t use it as destination addr)
  only one externally visible NATted address: 138.76.29.7
Solution 1: statically configure NAT to forward incoming connection requests at given port to server
  e.g., (138.76.29.7, port 2500) always forwarded to 10.0.0.1 port 25000
10.0.0.1
10.0.0.4
NAT
router
138.76.29.7
Client
?
K & R

## Slide 138: NAT Traversal Problem
Solution 2: Universal Plug and Play (UPnP) Internet Gateway Device (IGD) Protocol allows NATted host to:
  learn public IP address (138.76.29.7)
  add/remove port mappings (with lease times)
  i.e., automate static NAT port map configuration.
10.0.0.1
10.0.0.4
NAT
router
138.76.29.7
IGD
K & R

## Slide 139: NAT Traversal Problem
Solution 3: relaying (used in Skype)
  NATed client establishes connection to relay node.
  External client connects to relay.
  Relay bridges packets between to connections.
138.76.29.7
Client
10.0.0.1
NAT
router
1. connection to
relay initiated
by NATted host
2. connection to
relay initiated
by client
3. relaying
established
K & R

## Slide 140: Network Layer Topics
4.1 Introduction
4.2 Virtual circuit and datagram networks
4.3 What is inside a router?
4.4 IP: Internet Protocol
  Datagram Format
  IPv4 addressing
  Subnets
  CIDR
  ARP & DHCP
  NAT
4.5 Routing algorithms
  Algorithm Classification
  Link State
  Distance Vector
  Hierarchical Routing
4.6 Routing in the Internet
  RIP
  OSPF
  BGP
ICMP
K & R

## Slide 141: Internet Control Message Protocol (ICMP)
IP is always configured with a companion protocol (ICMP) that defines a collection of error messages that are sent back to the source host whenever a router or host is unable to process an IP datagram successfully, e.g.,
  Destination host unreachable due to link /node failure.
  Reassembly process failed.
  TTL had reached 0 (so datagrams don't cycle forever)
  IP header checksum failed
ICMP includes several control messages that a router can use to send back to a source host.
  ICMP-Redirect
  Sent from router R1 to a source host to inform host there exists a better path through R2 to a particular destination.
  Contains better route information.

## Slide 142: Other ICMP functions
ping uses ICMP echo messages to determine if a node is reachable and alive. Can be used to estimate RTT.
traceroute is used to determine the set of routes along the path to a desintination.
* Note - some routers send ICMP packets through a separate ‘special’ queue.

## Slide 143: Network Layer Summary
4.1 Introduction
4.2 Virtual circuit and datagram networks
4.3 What is inside a router?
4.4 IP: Internet Protocol
  Datagram Format
  IPv4 addressing
  Subnets
  CIDR
  ARP & DHCP
  NAT
4.5 Routing algorithms
  Algorithm Classification
  Link State
  Distance Vector
  Hierarchical Routing
4.6 Routing in the Internet
  RIP
  OSPF
  BGP
ICMP
K & R