## Slide 1: Synchronous Optical Networks (SONET)
Advanced Computer Networks

## Slide 2: SONET Outline
Brief History
SONET Overview
SONET Rates
SONET Ring Architecture
  Add/Drop Multiplexor (ADM)
  Section, Line and Path
  Virtual Tributaries
  Synchronous Payload Envelope (SPE)
Connection to ATM

## Slide 3: Telephone Networks {Brief History}
Digital carrier systems
  The hierarchy of digital signals that the telephone network uses.
  Trunks and access links organized in DS (digital signal) hierarchy
  Problem: rates are not multiples of each other.
In the 1980’s Bellcore developed the Synchronous Optical Network (SONET) standard.
Previous efforts include: ISDN and BISDN.

## Slide 4
North American Digital Hierarchy
Primary
Multiplex
Eg. Digital
Switch
30 chan PCM
4th order
Multiplex
x4
2nd order
Multiplex
x4
3rd order
Multiplex
x4
34.368 Mbps
2.048 Mbps
8.448 Mbps
139.264 Mbps
CEPT 1
CEPT 4
European Digital Hierarchy
28
M13
Multiplex
M23
Multiplex
x7
Primary
Multiplex
Eg. Digital
Switch
24 chan PCM
M12
Multiplex
x4
1
DS3 44.736 Mbps
DS1 1.544 Mbps
DS2 6.312 Mbps
DS3 44.736 Mbps



Leon-Garcia & Widjaja:
Communication Networks

## Slide 6: SONET
SONET:: encodes bit streams into optical signals propagated over optical fiber. SONET defines a technology for carrying many signals of different capacities through a synchronous, flexible, optical hierarchy.
A bit-way implementation providing end-to-end transport of bit streams.
All clocks in the network are locked to a common master clock so that simple TDM can be used.
Multiplexing done by byte interleaving.
SONET is backward compatible to DS-1 and E-1 and forward compatible to ATM cells.
Demultiplexing is easy.

## Slide 7: SONET
Transmission links of the telephone network have been changing to SONET where rates are arranged in STS (Synchronous Transfer Signal) hierarchy.
The hierarchy is called SDH (Synchronous Digital Hierarchy) defined by CCITT.
It is an ITU standard.

## Slide 9: SONET Rates
Figure 2-37. SONET and SDH Multiplex Rates
Tanenbaum
10 Gbps

## Slide 10: SONET Multipexing
Low-Speed
Mapping
Function
Medium
Speed
Mapping
Function
High-
Speed
Mapping
Function
DS3
44.736
DS1
DS2
CEPT-1
CEPT-4
139.264
ATM
150 Mbps
STS-1
STS-1
STS-1
STS-1
STS-1
STS-1
STS-1
STS-1
STS-3c
STS-3c
OC-n
Scrambler
E/O
51.84 Mbps
High-
Speed
Mapping
Function
Mux
STS-n






Leon-Garcia & Widjaja:
Communication Networks

## Slide 11
STS-1
STS-1
STS-1
STS-1
STS-1
STS-1
Map
Map
Map
STS-1
STS-1
STS-1
STS-1
STS-1
STS-1
Byte
Interleave
STS-3
Incoming
STS-1 Frames
Synchronized New
STS-1 Frames
SONET Synchronous Multiplexing
Leon-Garcia & Widjaja:
Communication Networks

## Slide 13: SONET Architecture
SONET topology can be a mesh, but most often it is a dual ring.
Standard component of SONET ring is an ADM (Add/Drop Multiplexer)
  Drop one incoming multiplexed stream and replace it with another stream.
  Used to make up bi-directional line switching rings.

## Slide 14
a
b
c
d
a
b
c
d
(a) Dual ring
(b) Loop-around
in response to fault
ADM
ADM
ADM
ADM
SONET Ring
Leon-Garcia & Widjaja:
Communication Networks

## Slide 15
SONET Ring
Changed from
FDDI

## Slide 16: ADM
MUX
DEMUX
MUX
DEMUX
MUX
DEMUX
(a) pre-SONET multiplexing
remove
tributary
insert
tributary
ADM
remove
tributary
insert
tributary
(b) SONET Add-Drop multiplexing
MUX
Leon-Garcia & Widjaja:
Communication Networks

## Slide 17
Inter-Office
Rings
Metro
Ring
Regional
Ring
SONET Ring
Leon-Garcia & Widjaja:
Communication Networks

## Slide 18: Gigabit ATM Over 10 Gb/s SONET Ring
Washington U. St Louis 1995

## Slide 19: SONET Architecture
STE: Section Terminating Equipment, e.g. a repeater
LTE: Line Terminating Equipment, e.g. a STS-1 to STS-3 multiplexer
PTE: Path Terminating Equipment, e.g. an STS-1 multiplexer
optical
section
optical
section
optical
section
optical
section
line
optical
section
line
optical
section
line
path
optical
section
line
path
(a)
(b)
STS
PTE
LTE
STE
STS-1 Path
STS Line
Section
Section
Mux
Mux
reg
reg
reg
SONET
Terminal
STE
STE
LTE
STS
PTE
SONET
Terminal
Leon-Garcia & Widjaja:
Communication Networks

## Slide 20: SONET Architecture
Sections
Lines
Path
SONET
MPX
SONET
MPX
BIM
BIM
ADM
REG
REG
The main SONET elements
OC-1
OC-1
OC-3
OC-3
OC-3
OC-3

## Slide 21
BIM
= BIM (Byte Interleaved Multiplexer)
= Regenerator
Boosts power of optical signal
Optical signal is converted to electrical signal.
Amplify electrical signal.
Amplified electrical signal converted back to optical signal.
SONET Architecture
REG

## Slide 22
Virtual
Tributaries

## Slide 24
B
B
B
87B
Information
Payload
9 Rows
125 s
Transport
overhead
90 bytes
Section
Overhead
3 rows
6 rows
Line
Overhead
SPE Synchronous Payload Envelope
SONET Frame
Leon-Garcia & Widjaja:
Communication Networks

## Slide 25: Figure 2-36. Two Back-to-Back SONET Frames
SONET Frame
Tanenbaum

## Slide 26
Pointer
87 columns
9
rows
first column is path overhead
Synchronous
Payload
Envelope
frame
k
frame
k+1
Pointer
first octet
last octet
SPE straddling SONET Frame
Leon-Garcia & Widjaja:
Communication Networks

## Slide 27
ATM Cells in an STS-3 Frame
Header
5 Bytes
Payload
48 Bytes
ATM Cell Format

## Slide 28: SONET Summary
Brief History
SONET Definition and Overview
SONET Rates (STS and OC’s)
SONET Ring Architecture
  Add/Drop Multiplexor (ADM)
  Section, Line and Path
  Virtual Tributaries
  Synchronous Payload Envelope (SPE)
Connection to ATM