## Slide 1: Wireless Sensor Networks (WSNs)
Advanced Computer Networks 2009

## Slide 2: Wireless Sensor Networks
A distributed connection of nodes that coordinate to perform a common task.
In many applications, the nodes are battery powered and it is often very difficult to recharge or change the batteries.
Prolonging network lifetime is a critical issue.
Sensors often have long period between transmissions (e.g., in seconds).
Thus, a good WSN MAC protocol needs to be energy efficient.

## Slide 3: Open Experimental Platform
Networking
Small microcontroller 8 kB code 512 B data
Simple, low-power radio 10 kbps ASK
EEPROM (32 KB)
Simple sensors
WeC 99
“Smart Rock”
Mica 1/02
NEST open exp. Platform 128 kB code, 4 kB data 40kbps OOK/ASK radio 512 kB Flash
Rene 11/00
Designed for experimentation
sensor boards
power boards
TinyOS
Services
Dot 9/01
Demonstrate scale
Spec 6/03
“Mote on a chip”
Telos 4/04
Robust
Low Power
250kbps
Easy to use
Mica2 12/02
38.4kbps radio FSK
Commercial Off The Shelf Components (COTS)
Notes: Before we jump in to the technical material, I would like to give you one more bit of context.

## Slide 4: Mote Evolution

## Slide 5: Outline
Introduction, Definition, Pictures
Wireless Sensor Network (WSN) Applications
WSN Details
Types Wireless Sensor Networks (WSNs)
Tiered Architectures
Dynamic Cluster Formation
Power-Aware MAC Protocols
  SMAC, TMAC, WiseMAC, TRAMA, SCP-MAC, AS-MAC, Crankshaft

## Slide 6: Camalie Vineyards
Case Study in Crossbow Mote Deployment
Copyright 2006 Camalie Vineyards, Not to be reproduced without written permission

## Slide 7: Water in the Vineyard

## Slide 8: Vineyard Installation
At each Mote location:
  2 soil moisture sensors
  12” and 24” depth
  1 soil temp sensor to calibrate
  soil moisture sensors

## Slide 9: Power Supply
2 month max battery life now with 10 minute sampling interval
Decided to use solar power, always there when doing irrigation. Solar cell $10 in small quantities and need a $.50 regulator.

## Slide 10: Vineyard Mote Prototype
433MHz Mica2dot
Solar power supply
Up to 6 resistive sensor inputs

## Slide 11: Network Maps
Irrigation Block Map
13 nodes late 2005, 18 nodes in 2006

## Slide 12: Soil Moisture Data
Red = 12” depth soil moisture
Green= 24” depth soil moisture
Note delay deeper
More frequent, shorter watering keeps water shallow

## Slide 13: WSNs for Assisted Living
Berkeley Fall Detection System
Alarm-Net
University of Virginia

## Slide 14: WSNs for Assisted Living

## Slide 15: WSNs for Assisted Living
Two-Tiered
WSN
Architecture

## Slide 16: Berkeley Fall Detection System

## Slide 17: Berkeley Fall Detection System

## Slide 18: Outline
Introduction, Definition, Pictures
Wireless Sensor Network (WSN) Applications
WSN Details
Types Wireless Sensor Networks (WSNs)
Tiered Architectures
Dynamic Cluster Formation
Power-Aware MAC Protocols
  SMAC, TMAC, WiseMAC, TRAMA, SCP-MAC, AS-MAC, Crankshaft

## Slide 19: Wireless Sensor Networks
Another attribute is scalability and adaptability to change in network size, node density and topology.
  In general, nodes can die, join later or be mobile.
Often high bandwidth is not important.
Nodes can take advantage of short-range, mulit-hop communication to conserve energy.

## Slide 20: Wireless Sensor Networks
Sources of energy waste:
  Idle listening, collisions, overhearing and control overhead and overmitting.
  Idle listening dominates (measurements show idle listening consumes between 50-100% of the energy required for receiving.)
Idle listening:: listen to receive possible traffic that is not sent.
Overmitting:: transmission of message when receiver is not ready.

## Slide 21: Power Measurements

## Slide 22: WSN Communication Patterns
Broadcast:: e.g., Base station transmits to all sensor nodes in WSN.
Multicast:: sensor transmit to a subset of sensors (e.g. cluster hear to cluster nodes)
Convergecast:: when a group of sensors communicate to one sensor (BS, cluster head, or data fusion center).
Local Gossip:: sensor sends message to neighbor sensors.

## Slide 23: Wireless Sensor Networks
Duty cycle:: ratio between listen time and the full listen-sleep cycle.
central approach – lower the duty cycle by turning the radio off part of the time.
Three techniques to reduce the duty cycle:
  TDMA
  Schedule contention periods
  LPL (Low Power Listening)

## Slide 24: Techniques to Reduce Idle Listening
TDMA requires cluster-based or centralized control.
Scheduling – ensures short listen period when transmitters and listeners can rendezvous and other periods where nodes sleep (turn off their radios).
LPL – nodes wake up briefly to check for channel activity without receiving data.
  If channel is idle, node goes back to sleep.
  If channel is busy, node stays awake to receive data.
  A long preamble (longer than poll period) is used to assure than preamble intersects with polls.

## Slide 25: Outline
Introduction, Definition, Pictures
Wireless Sensor Network (WSN) Applications
WSN Details
Types Wireless Sensor Networks (WSNs)
Tiered Architectures
Dynamic Cluster Formation
Power-Aware MAC Protocols
  SMAC, TMAC, WiseMAC, TRAMA, SCP-MAC, AS-MAC, Crankshaft

## Slide 26: Tiered WSN Architectures
[ Stathopoulos]

## Slide 27: Dynamic Cluster Formation

## Slide 28: Choosing Cluster Heads/ Forming Clusters
Two-tier scheme:
A fixed number of cluster heads that communicate with BS (base station).
Nodes in cluster communicate with head (normally TDMA).
TDMA allows fixed schedule of slots for
sensor to send to cluster head and receive head transmissions.
BS

## Slide 29
BS
Choosing Cluster Heads/ Forming Clusters
Periodically select new cluster heads to minimize power consumption and maximize WSN lifetime.
More complex problem when size of cluster changes dynamically.
As time goes by, some sensor nodes die!
Not worried about coverage issues!
X
X
X
X
X

## Slide 30: Dynamic Cluster Formation
TDMA cluster algorithms:
  LEACH, Bluetooth, …
Rick Skowyra’s MS thesis:
‘Energy Efficient Dynamic Reclustering Strategy for WSNs’
  ‘Leach-like’ with a fitness function and periodic reclustering.
  He designed a distributed genetic algorithm to speed the recluster time.

## Slide 31: Power-Aware MAC Protocols

## Slide 32: Power Aware MAC Protocols
1997
1998 PAMAS
1999
2000
2001 SMAC
2002 LPL NPSM
2003 TMAC TinyOS EMACs TRAMA Sift
2004 BMAC DMAC DSMAC LMAC WiseMAC
2005 PMAC ZMAC SP
2006 SCP-MAC
2007 Crankshaft
2008 AS-MAC

## Slide 33: Power Aware MAC Protocols
Three approaches to saving power:
1. TDMA: TRAMA, EMACs, LMAC
2. Schedule: PAMAS, SMAC, TMAC, DMAC, PMAC, SCP-MAC , Crankshaft, AS-MAC
3. Low Power Listening: LPL, BMAC, WiseMAC
Cross-Layering: SP, BSD

## Slide 34: Table I from WSN Survey Paper