## Slide 1
Design and Evaluation of a Versatile and Efficient Receiver-Initiated Link Layer for Low-Power Wireless
Prabal Dutta, Stephen Dawson-Haggerty, Yin Chen,
Chieh-Jan (Mike) Liang, and Andreas Terzis
Presented by Lianmu Chen

## Slide 2
Outline
Introduction
A-MAC Design Overview
Implementation Details
Backcast Evaluation
Macrobenchmark Evaluation
Conclusions

## Slide 3
Introduction

## Slide 4: A receiver-initiated MAC
Receiver
Sender
P
Listen
D
P
D

## Slide 5: Benefits
Handle hidden terminals better than sender-initiated ones
Support asynchronous communication w/o long-preambles
Support extremely low duty cycles or high data rates
Support many low-power services
  Wakeup
  Discovery
  Unicast
  Broadcast
  Pollcast
  Anycast

## Slide 6: Drawbacks
Probe (LPP) is more expensive than channel sample (LPL)
  Baseline power is higher
Frequent probe transmissions
  Could congest channel & increase latency
  Could disrupt ongoing communications
  Channel usage scales with node density rather than traffic
Services use incompatible probe semantics
  Makes concurrent use of services difficult
  Supporting multiple, incompatible probes increases power

## Slide 7
Is it possible to design a general-purpose,
yet efficient, receiver-initiated link layer?

## Slide 8
A-MAC Design Overview

## Slide 9: A-MAC communication over 802.15.4
P
A
Sender
Receiver
P
A
DATA
DATA
Max data packet
4.256 ms
ACK transmission time 352 µs
RXTX turnaround time: 192 µs
P
P
Listen

## Slide 10
Node 2
Receiver
Node 3
Sender
Node 1
Sender
P
A
Listen
D
P-CW
P
A
Listen
D
P-CW
P
A
D
P-CW
D
BO
D
frame collision
Backcast
A-MAC’s contention mechanism

## Slide 11: A-MAC Communications
Benefits:
Save energy:
(1)only has to wait marginally longer than the radio’s RX/TX turnaround time;
(2)IEEE 802.15.4 standard, a turnaround occurs in 192 μs, nearly 20 times
faster than the 3.75 ms beacon-data turnaround time that RI-MAC requires
with its software based protocol processing
Distinguish between collisions and interference
Therefore, A-MAC is far less susceptible to interference based false alarms
than either LPL or RI-MAC.

## Slide 12
Implementation Details

## Slide 13
Problems
Overreacting:
-a sender will auto-ack every probe it receives, including probes from neighbors for which the
sender has no pending traffic.
Against Standards
-the IEEE 802.15.4-2006 standard specifically prohibits this behavior, any frame that is
broadcast shall be sent with its Acknowledgment Request subfield set to zero.
Mixed radio support
- because this behavior is prohibited, it enjoys somewhat mixed radio support: while the
CC2420 [34] radio and AT86RF230 [3] radio Rev A silicon both support broadcast auto-acks,
the Rev B silicon “fixes” this standards non-compliance and does not auto-ack broadcast
frames.

## Slide 14: Unicast Communications
P
A
Node 2
(Receiver)
Node 3
(Sender)
P
A
Node 1
(Sender)
Listen
D
DST=0x8002
SRC=0x0002
D
P
P
L
MAC=0x8002
P
A
Listen
D
P-CW
MAC=0x8002
P
A
Listen
D
P-CW
MAC=0x8002
P
A
D
P-CW
D
BO
D
DST=0x8002
SRC=0x0002
ACK=0x0023
FRM=0x0001
DST=0x0002
SRC=0x0001
SEQ=0x23
frame collision
Backcast

## Slide 15
Broadcast Communications
Broadcast Communications
  A-MAC broadcast design is identical to Unicast, with an important diference: sender disables hardware address recognition but keeps hardware auto-acks enabled
  In this way, sender will auto-ack every probe it receives and it will send the data packet like in the unicast case

## Slide 16
Backcast Evaluation

## Slide 17: Methodology
Two important metrics:
Received signal strength indicator (RSSI)
Signal strength, measured by the radio over the first eight symbols of an
acknowledgment (ACK) frame
Signal quality (LQI)
measured by the radio over the first eight symbols and is reported as a
7-bit unsigned integer that can be viewed as the average correlation
value or chip error rate (values near 100 indicate an excellent link).

## Slide 18: Large scale performance
Figure 7. The effect on LQI as the number of concurrent ACKs increases from 0 to 94 in a typical indoor deployment setting. The median value of LQI falls quickly for the first six nodes and then falls slowly. Beyond approximately 30 nodes, the LQI values stabilize at approximately 100. The data suggest that even in the presence of a large number of ACK collisions, the receiver can successfully decode the ACK frame. Note the y-axis ranges from 74 to 106.
Conclusion: The statistical superposition of an increasing number of signals does not lead to destructive interference, making backcast a robust synchronization primitive.

## Slide 19: Robustness to External Interference
Table 1. The effect of interference on idle listening current in an office environment using three different synchronization schemes

## Slide 20: Robustness to External Interference
Figure 10. LPL preamble sampling techniques leave receivers susceptible to noisy wireless environments, such as those caused by 802.11 interference.
Figures (a) and (b) show the macroscopic and microscopic behavior of the TinyOS 2.1sampling algorithm when the channel is clear: the receiver immediately returns to sleep. Figures (c) and (d) show the macroscopic and microscopic behavior while a file transfer is in progress using a nearby 802.11 access point. Of the seven channel samples visible in this trace, five are unnecessarily lengthened due to channel noise.

## Slide 21
Macrobenchmark Evaluation

## Slide 22: Multiple Contending Unicast Flows
Table 2 shows between one and four senders contending to transmit to a single receiver for both RI-MAC and A-MAC.

## Slide 23: Multiple Parallel Unicast Flows
R
S
R
S
R
S
Collision
Domain
Table 3 shows A-MAC throughput and packet delivery ratio as a function of
the number of different whitelisted channels that are available for use,
the number of sender:receiver pairs transferring data concurrently,
and the receivers’ probe interval.

## Slide 24: Asynchronous Network Wakeup
Faster Wakeup
Fewer Packets
A-MAC
LPL (Flash)
A-MAC
LPL (Flash)
Figure 11 shows the wakeup times of 59 nodes in a multihop
testbed across a range of sampling/probing intervals.

## Slide 25: Collection Tree Protocol Performance
N = 59 Tdata = 60 s Tprobe = 500 ms
Table 4. CTP performance over LPL and A-MAC.
(a) CDF of CTP Duty Cycles

## Slide 26
Sampling
Channel 18
Channel 26
Probing
Backcast
Sampling
Probing
Backcast
Inference Vulnerability

## Slide 27
Effect of Density on Packet Delivery
Same collision domain (between 0, 1, 2, 3, 8, 13, and 18) who simply transmit probes with varying probe periods (32 ms, 64 ms, 128 ms,
and 256 ms)

## Slide 28: Conclusion
Backcast provides a new synchronization primitive
  Common abstraction underlying many protocols
  Can be implemented using a DATA/ACK frame exchange
  Works even with a 8, 12, 94 colliding ACK frames
  Faster, more efficient, and more robust than LPL, LPP
A-MAC augments Backcast to implement
  Unicast
  Broadcast
  Network wakeup
  Robust pollcast
Results show
  Higher packet delivery ratios
  Lower duty cycles
  Better throughput (and min/max fairness)
  Faster network wakeup
  Higher channel efficiency

## Slide 29
Thank you
Questions？