## Slide 1: A Performance Comparison of Multi-Hop Wireless Ad Hoc Network Routing Protocols
Josh Broch, David A. Maltz, David B. Johnson, Yih-Chun Hu, Jorjeta Jetcheva
Presented by Qian HE (Steve)
CS 577 – Prof. Bob Kinicki

## Slide 2: Outline
Introduction
Simulation Environment
Ad Hoc Network Routing Protocols
  DSDV
  TORA
  DSR
  AODV
Methodology
Simulation Results & Observations
Conclusions

## Slide 3: Outline
Introduction
Simulation Environment
Ad Hoc Network Routing Protocols
  DSDV
  TORA
  DSR
  AODV
Methodology
Simulation Results & Observations
Conclusions

## Slide 4: Introduction
What is ad hoc?
  Ad hoc is a Latin phrase meaning "for this". It generally signifies a solution designed for a specific problem or task, non-generalizable, and not intended to be able to be adapted to other purpose.

## Slide 5: Introduction
What is ad hoc network?
  each mobile node operates not only as a host but also as a router
  ad hoc routing protocol allows each node to discover “multi-hop” paths through the network to any other node
  infrastructureless networking
  dynamically establish routing

## Slide 6: Outline
Introduction
Simulation Environment
Ad Hoc Network Routing Protocols
  DSDV
  TORA
  DSR
  AODV
Methodology
Simulation Results & Observations
Conclusions

## Slide 7: Simulation Environment
ns
  Node mobility
  A realistic physical layer including:
    a radio propagation model
    supporting propagation delay
    capture effects
    carrier sense
  Radio network interfaces with properties such as:
    transmission power
    antenna gain
    receiver sensitivity
  IEEE 802.11 MAC protocol using DCF

## Slide 8: Some details on simulation
Attenuates the power of a signal:
  1/r2 at short distance
  1/r4 at long distance
Reference distance
  100 meters for outdoor
  low-gain antennas 1.5 m above the ground plane
  operating in the 1–2 GHz band
ARP
50 packets with drop-tail

## Slide 9: Outline
Introduction
Simulation Environment
Ad Hoc Network Routing Protocols
  DSDV
  TORA
  DSR
  AODV
Methodology
Simulation Results & Observations
Conclusions

## Slide 10: Ad Hoc Network Routing Protocols
Improvements to all of the protocols:
  To prevent synchronization, periodic broadcasts and packets sent in ACK were jittered using a random delay uniformly distributed between 0 and 10 milliseconds.
  To insure that routing information propagated in a timely fashion, routing packets were queued for transmission at the head of the network interface.
  Each of the protocols use link breakage detection feedback from the 802.11 MAC (except for DSDV).

## Slide 11: Outline
Introduction
Simulation Environment
Ad Hoc Network Routing Protocols
  DSDV
  TORA
  DSR
  AODV
Methodology
Simulation Results & Observations
Conclusions

## Slide 12: Destination-Sequenced Distance Vector (DSDV)
DSDV is a hop-by-hop distance vector routing protocol requiring:
  each node periodically broadcast routing updates
  it guarantees loop-freedom (traditional DV doesn’t)
Based on the Bellman-Ford algorithm

## Slide 13: DSDV
Each node maintains a routing table listing the “next hop” for each reachable destination.
DSDV tags each route with a sequence number. (the higher, the better)
Each node in the network advertises a monotonically increasing even sequence number for itself.
Each node periodically broadcasts update.

## Slide 14: DSDV Implementation
Does not use link layer breakage detection.
Uses both full and incremental updates.
Trigger an update when:
  receipt of a new sequence number for a destination will cause a triggered update (DSDV-SQ)
  receipt of a new metric (simply DSDV).

## Slide 15: Constants in DSDV

## Slide 16: Outline
Introduction
Simulation Environment
Ad Hoc Network Routing Protocols
  DSDV
  TORA
  DSR
  AODV
Methodology
Simulation Results & Observations
Conclusions

## Slide 17: Temporally-Ordered Routing Algorithm (TORA)
A distributed routing protocol based on a “link reversal” algorithm.
Discovers routes on demand.
Provides multiple routes to a destination.
Minimizes communication overhead by localizing algorithmic reaction to topological changes.
Route optimality is considered of secondary importance.
Longer routes are often used to avoid the overhead of discovering newer routes (what?!).

## Slide 18: TORA
Start: when a node needs a route to a particular destination, it broadcasts a QUERY packet.
Propagate: QUERY packet stops at the destination or an intermediate node having a route to the destination.
Response: the recipient then broadcasts an UPDATE packet listing its height with respect to the destination.
End: each node that receives the UPDATE sets its height to a value greater than it received.

## Slide 19: TORA Example
University of Luxembourg, SECAN-Lab
Node C requires a route, so it broadcasts a QRY

## Slide 20: TORA Example
University of Luxembourg, SECAN-Lab
The QRY propagates until it hits a node which has a route to the destination

## Slide 21: TORA Example
University of Luxembourg, SECAN-Lab
The UPD is also propagated, while node E sends a new UPD

## Slide 22: TORA Example
University of Luxembourg, SECAN-Lab
Finally, every node gets its height

## Slide 23: TORA
TORA can be described in terms of water flowing downhill towards a destination node through a network of tubes that models the routing state of the real network.

## Slide 24: TORA Implementation
TORA is layered on top of IMEP (Internet MANET Encapsulation Protocol).
IMEP attempts to aggregate many TORA and IMEP control together into a single packet.
Each IMEP node periodically transmits a BEACON, which is answered by each node hearing it with a HELLO.
Uses ARP instead of IMEP in network layer address resolution.

## Slide 25: TORA Implementation
Balance overhead and routing protocol convergence:
  aggregate HELLO and ACK packets for a time uniformly chosen between 150 ms and 250 ms.
  Does not delay TORA routing messages for aggregation.
  * transmission delay of TORA routing messages + any queuing delay at the network interface, allows these routing loops to last long enough that significant numbers of data packets are dropped.

## Slide 26: Constants in TORA

## Slide 27: Outline
Introduction
Simulation Environment
Ad Hoc Network Routing Protocols
  DSDV
  TORA
  DSR
  AODV
Methodology
Simulation Results & Observations
Conclusions

## Slide 28: Dynamic Source Routing (DSR)
DSR uses source routing rather than hop-by-hop routing. Each packet carries an ordered list of nodes, which the packet must pass.
  intermediate nodes do not need to maintain up-to-date routing information in order to route the packets.
  periodic route advertisement and neighbor detection packets are not needed.
DSR protocol consists of two mechanisms:
  Route Discovery
  Route Maintenance.

## Slide 29: DSR - Route Discovery
Start: the source node broadcasts a REQUEST packet that is flooded through the network. (same as TORA, except the content of REQUEST).
Propagate: the destination node or another node that knows a route to the destination will answer with a REPLY. (same as TORA, except the content of REPLY).

## Slide 30: DSR – Route Discovery
University of Luxembourg, SECAN-Lab
Request:
(source, request, {hops})

## Slide 31: DSR – Route Discovery
University of Luxembourg, SECAN-Lab
Reply:
(source, request, route)

## Slide 32: DSR - Maintenance
Detects when the topology of the network has changed:
  source node is notified with a ROUTE ERROR packet.
Decides:
  if an alternative route can be used.
  if the Route Discovery protocol must be started to find a new path.

## Slide 33: DSR Implementation
Discovers only routes composed of bidirectional links
  by requiring nodes to return ROUTE REPLY messages to where ROUTE REQUEST packet came.
A node sends a ROUTE REQUEST with TTL=0. If this non-propagating search times out, it will send a propagating ROUTE REQUEST.

## Slide 34: Constants in DSR

## Slide 35: Outline
Introduction
Simulation Environment
Ad Hoc Network Routing Protocols
  DSDV
  TORA
  DSR
  AODV
Methodology
Simulation Results & Observations
Conclusions

## Slide 36: Ad Hoc On-Demand Distance Vector (AODV)
AODV is essentially a combination of both DSR and DSDV.
  It borrows the basic on-demand mechanism of Route Discovery and Route Maintenance from DSR.
  It uses hop-by-hop routing, sequence numbers, and periodic beacons from DSDV.

## Slide 37: AODV
Start & propagate: same as DSR, except the REQUEST contains the last known sequence number for that destination.
Response: when the REQUEST reaches a node with a route to D, it generates a REPLY that contains:
  the number of hops necessary to reach D
  the sequence number for D most recently seen it.
  End: Each node that participates in forwarding this REPLY back toward S, creates a forward route to D by remembering only the next hop (same as DSDV).

## Slide 38: AODV - Maintenance
Each node periodically transmit a HELLO message with a default rate of once per second.
Failure to receive three consecutive HELLO messages from a neighbor ?= the neighbor is down.
  Alternatively, may use physical layer or link layer methods to detect link breakages.
UNSOLICITED REPLY containing an infinite metric for that destination will be sent to any upstream node that has recently forwarded packets to a destination using that link.

## Slide 39: AODV Implementation
also implemented a version of AODV that we call AODV-LL (link layer), using only link layer feedback from 802.11 as in DSR.
Changed AODV implementation to use a shorter timeout of 6 seconds before retrying a REQUEST for which no REPLY has been received (RREP WAIT TIME).

## Slide 40: Constants in AODV

## Slide 41: Outline
Introduction
Simulation Environment
Ad Hoc Network Routing Protocols
  DSDV
  TORA
  DSR
  AODV
Methodology
Simulation Results & Observations
Conclusions

## Slide 42: Methodology
The overall goal of our experiments was to measure the ability of the routing protocols to react to network topology changes while continuing to successfully deliver data packets to their destinations.

## Slide 43: Methodology
50 wireless nodes, moving about over a rectangular (1500m * 300m) flat space, simulated 900 s
210 different scenario files with varying movement patterns and traffic loads
Physical radio characteristics: Lucent WaveLAN direct sequence spread spectrum radio.

## Slide 44: Methodology
Movement Model
Communication Model
Scenario Characteristics
Metrics

## Slide 45: Movement Model
“random waypoint” model
  begins by remaining stationary for a pause time
  selects a random destination
  moves to that destination at a speed distributed uniformly 0~MAX
  upon reaching, pauses again for a pause time
  repeats from 2

## Slide 46: Movement Model
7 different pause times: 0, 30, 60, 120, 300, 600, and 900 s.
70 different movement patterns, 10 for each value of pause time
2 different maximum speeds:
  20 m/s
  1 m/s

## Slide 47: Methodology
Movement Model
Communication Model
Scenario Characteristics
Metrics

## Slide 48: Communication Model
Constant Bit Rate (CBR)
  sending rates of 1, 4, and 8 packets per second
  networks containing 10, 20, and 30 CBR sources
  packet sizes of 64 and 1024 bytes
did not use TCP (because it’s so GOOD!!)

## Slide 49: Methodology
Movement Model
Communication Model
Scenario Characteristics
Metrics

## Slide 50: Scenario Characteristics
An internal mechanism of the simulator calculates the shortest path between the originated packet’s sender and its destination.
The shortest path is calculated based on a range of 250m for each radio without congestion and interference.
The average hops is 2.6, and the farthest is 8.

## Slide 51: Scenario Characteristics

## Slide 52: Scenario Characteristics

## Slide 53: Methodology
Movement Model
Communication Model
Scenario Characteristics
Metrics

## Slide 54: Metrics
Packet Delivery Ratio
  the ratio between the number of packets originated and number of packets received
Routing Overhead
  the total number of routing packets transmitted during the simulation (each hop counts)
Path Optimality
  the difference between the number of hops a packet took and the length of the shortest path

## Slide 55: Outline
Introduction
Simulation Environment
Ad Hoc Network Routing Protocols
  DSDV
  TORA
  DSR
  AODV
Methodology
Simulation Results & Observations
Conclusions

## Slide 56: delivery ratio - pause time
20 sources

## Slide 57: overhead - pause time
20 sources

## Slide 58: delivery ratio - pause time

## Slide 59: overhead – pause time

## Slide 60: difference from shortest
20 sources

## Slide 61: Lower Speed of Node Movement
1 m/s, 20 sources

## Slide 62: Overhead in Source Routing Protocols
measured in bytes
includes the bytes of the source route header that DSR places in each packet

## Slide 63: DSDV vs. DSDV-SQ

## Slide 64: Outline
Introduction
Simulation Environment
Ad Hoc Network Routing Protocols
  DSDV
  TORA
  DSR
  AODV
Methodology
Simulation Results & Observations
Conclusions

## Slide 65: Conclusions
This paper:
  provides an accurate simulation of the MAC and physical-layer behavior of the IEEE 802.11 wireless LAN standard with modifications to the ns network simulator. (a powerful tool)
  detailed packet-level simulation comparing DSDV, TORA, DSR, and AODV
Each of the protocols studied performs well in some cases yet has certain drawbacks in others.

## Slide 66: Conclusions
DSDV
  performs quite predictably, delivering virtually all data packets when node mobility rate and movement speed are low
  failing to converge as node mobility increases.

## Slide 67: Conclusions
TORA
  the worst performer in routing packet overhead.
  still delivered over 90% of the packets in scenarios with 10 or 20 sources.
  at 30 sources, the network was unable to handle all of the traffic generated by the routing protocol and a significant fraction of data packets were dropped.

## Slide 68: Conclusions
DSR
  very good at all mobility rates and movement speeds.
  its use of source routing increases the number of routing overhead bytes required by the protocol.

## Slide 69: Conclusions
AODV
  performs almost as well as DSR at all mobility rates and movement speeds.
  accomplishes its goal of eliminating source routing overhead.
  but still requires the transmission of many routing overhead packets and at high rates of node mobility is actually more expensive than DSR.

## Slide 70: Brief Conclusions
TORA was the worst.
DSR was the best.
DSDV performs well when load and mobility is low, poorly as mobility increases.
AODV performs nearly as well as DSR, but has high overhead at high mobility levels.
Borrowed from MOBICOM 1998 Dallas, Texas

## Slide 71: Q & A
Thanks