## Slide 1: Characterization of 802.11 Wireless Networks in the Home
By Mark yarbis, Konstantina papagiannaki, and w. steven conner
Presented by Chung tran cs 577

## Slide 2: Table of contents
Introduction
Experimental Environment
Results
Related Work
Conclusion

## Slide 3: Introduction
Graphs are presented differently in the Intel Report versus the paper I have. I will uses the graphs and table from the Intel report because I can copy it and put it into this PowerPoint presentation
This experiment is important because of the popular rise of wireless network versus wired network
Even those the paper did not say too much about it the popular rise of mobile devices have made this even more in demand
Experiment used IEEE 802.11a/b cards uses in home 3 to be exact 1 in United Kingdom 2 in the United State

## Slide 4: Experimental Environment
Experiment Setup
  6 wireless nodes in each homes.
  Node deployed in different rooms
Methodology
Validation

## Slide 5: Experimental Environment
Determine the quality of wireless links in home environment
Ad-Hoc network 5 channels away from the next 802.11 frequency
Each nodes are to send series of UDP probe packets
Size 1024 bytes
Duration of 150 seconds
Frequency of 500 ms/packet
Wireless link access independently and no simulation transmissions take place inside the network
Take place at night time to avoid human interference

## Slide 6: Factors this papers investigate
Type of house; size, construction materials
Wireless Technology used 802.11a and 802.11b
Transmission rate = txrate
Transmission power = txpower
Node location
Interference with appliances

## Slide 7: Table 1
  TABLE I
  DESCRIPTION OF HOMES USED IN EXPERIMENTAL TESTBEDS.
  Label Size (ft2) Construction # Floors # Nodes
  ushome1 2,500 Wood 2 6
  ushome2 2,000 Wood 2 6
  ukhome1 1,500 Brick / steel 3 6

## Slide 8: Layout UShome1

## Slide 9: Layout UShome2

## Slide 10: Layout UKHome

## Slide 11: Details of Layouts
Fig. 7. Abstract home floorplans and location of links with greater than 95% loss rate at 1 mW and 11 Mbps under different configurations: (a) ukhome1
for layout1, layout2, and layout3, (b) ushome1, and (c) ushome2 for layout1 and layout2. Dashed lines indicate asymmetric links.
The original layout put Ukhome for layout 1 I decided to switch it up so it lineup with the Table 1. This layout help explain how they deploy the nodes

## Slide 12: Experimental Setup 802.11b
802.11b
  Small form-factor PCs with Netgear MA701
  Compact flash 802.11b wireless cards
  Linux Kernel 2.4.19
  Hostap driver

## Slide 13: Experimental Setup 802.11a
802.11a
  Laptops with NetGear WAG511
  BusCard 802.11a
  Linux Kernel 2.4.26
  MIT madwifi-stripped driver

## Slide 14: Methodology 3 Factors
Here they test 3 factors this is done using the layout I show earlier
  Node Location
  Antenna Orientation
  Obstacles
txrate from 2Mbps to 11Mbps
txpower from 1 mW to 30 mw

## Slide 15: Figure 1 30mW and 2Mbps

## Slide 16: Interesting notes about figure 1
Communication between 5-2 is very low
Communication between 3-4 very low success rate
    But the reverse 4-3 is very high success rate nearly loss-free
We can continue to find this asymmetry link from other studies this seems to be quite common in home environments stated by the authors in the experiment
There other cases these are just the extreme cases the author point out so reader can have a better understanding of the experiment

## Slide 17: Fig 2a. Loss rates for each pair of nodes in two runs at ushome1

## Slide 18: Fig 2b. Loss rates for each pair of nodes in two runs at ushome1
Fig4 uses this one

## Slide 19: Authors comments and my personal thought
There are 2 run on ushome1 so there is fig.2a and fig.2b
The authors suggest that fig.2 where poor or asymmetry in 1 run will be the same in run 2
The graphs seems to support their claim
The next graph fig.3 is to valid weather 150 seconds was long enough to determine if loss-rate is enough to uses as a measurement
This graphs is base on 150 seconds versus 20 minutes

## Slide 20: Fig 3 x-for 150 sec y-for entire 20 min

## Slide 21: Fig 4 entire day
Early in the paper it was stated that this experiment was conducted during night time to avoid human interference
Fig 4 want to explore the effect of lose throughout the day
Since figure 3 determine that 150 was acceptable measurement for testing that what they uses to determine different times of day for fig 4
First bar is from node 4 to node 6
Second bar is from node 6 to node 4
txrate = 11 Mbps txpower = 30mW

## Slide 22: Figure 4

## Slide 23: Figure 5 a ukhome layout1

## Slide 24: Figure 5 ushome1 layout 1

## Slide 25: Figure 5 ushome2 layout 1

## Slide 26: Something very interesting I want to point out
I will show figure 7 again this is the layout where these graphs are presented.
In ukhome layout 1 the most loss happen between nodes 2 to 6 or 6 to 2
However those 2 are actually on the same floor yet their loss-rate in layout 1 show they are have the highest loss-rate
Same with ushome1 2-5 and 5-2 have the same problem in all 4 graphs it show it have the consistence high loss-rate
As for ushome2 I cannot conclude the same because the loss-rate however I can see that 5-6 still have a consistence loss-rate higher then the rest even those it on the same floor

## Slide 27: Ukhome Layout 1 on Figure 7
Strange 2-6

## Slide 28: Ushome 1 layout 1 figure 7
Strange 2-5

## Slide 29: Ushome2 layout 1 figure 7
Strange 5-6

## Slide 30: What does all the line means
The authors pointed out that their black line indicate asymmetry link
I draw in the red line to focus on the loss-rate between these nodes
However figure 7 only show when txrate = 11 Mbps and txpower = 1mW
Layout 2 is to test location of nodes and orientation of antenna
Let take a look at each graph when we show them next to each other, by putting them side-by-side I hope to show the effect of layout 1 versus layout 2

## Slide 31: Ukhome layout 1 versus layout 2

## Slide 32: Ushome1 layout 1 versus layout 2

## Slide 33: Ushome2 layout1 versus layout2

## Slide 34: Result of changing the layout
Ukhome there was a significant changes as we can see with the loss-rate
The drastic loss-rate are shown in all the graph it was just easier to see in ukhome that why I point that out first
These small changes cause big change in the results
This is cause by multi-path fading

## Slide 35: Multi-path fading
This is actually a very simple concept
We have a packet when it get to a node it send multiple copy throughout the network until it reach the final destination
However, this cause it to interfere with itself when it reach the final destination, the following is a simple analogy
I am a boss and I want a message deliver to someone
I give 4 copy of the message to my team(consist of 4) to see who can get it done the fastest
They run to the person I want the message to be deliver to they all uses different route
When they get there the 4 underlings stand and wait and complaint about who should be first to give the message

## Slide 36: Figure 9 loss-rate versus distance ukhome layout2

## Slide 37: Figure 9 loss-rate versus distance ushome1 layout2

## Slide 38: Figure 9 loss-rate versus distance ushome2 layout2

## Slide 39: Result of figure 9
The authors suggest that obstacles is what determine the performance of home wireless link
Instead of what common sense would suggest of physical distance and power
This was pointed out at result III.D where loss-rate is not base on physical distance
I cannot follow these graph because the labeling was not very good
I only put it in because the authors seems to rely on this results and what they indicate very strongly

## Slide 40: Inference source 600w microwave

## Slide 41: What does preview graphs means?
This use a microwave with vary distance to show how it interfere with the receiver side
The blue line show no interference so there almost no loss-rate
While the red line show that it lose rate will be effected by the interference at .25 it loss-rate was over 60 percent
Once it reach the distance of .5 the loss-rate almost become the same as no interference

## Slide 42: Figure 13 802.11a ushome1

## Slide 43: Figure 13 802.11a ushome2

## Slide 44: Result of figure 13
This should have shown us that loss-rate does not correlate with the distance between node pairs
I feel they need to label this better for reader to follows I have a hard time following the graphs so no comment about it.
Asymmetry link are going to occur there no way to prevent it on wireless network
To achieve a no loss-rate it possible but that require exact orientation and location of the nodes

## Slide 45: Figure 14 ushome1

## Slide 46: Figure 14 ushome2

## Slide 47: Figure 14
Graph are base on Cumulative density function of loss rates under 802.11b and 802.11a in ushome1 and ushome2
First thing I notice when I read this part is that 802.11a act very binary
It seems that 802.11a at 6 Mbps seems the most reliable compare to 2 or 11 Mbps of 802.11b
However, when they uses 54 Mbps link encoded it performed very poorly between all pairs those values can be seen in figure 11 and 12
The authors suggest that 802.11a uses 5 GHz band may be a contribute to the performance

## Slide 48: Figure 11a layout1

## Slide 49: Figure 11b Layout2

## Slide 50: Figure 12a Layout1

## Slide 51: Figure 12b

## Slide 52: Conclusion
This research show that wireless link in home are:
  Stable over time
  Highly asymmetric
  Highly variable from 1 node to the next
  In home precise node location is the single most important factor in network communication
  Before I read this paper I thought it was going to be physical distance now I know it have more to do with how everything is oriented and what interfering with it, placement.