## Slide 1: Distributed Denial of Service (DDoS)
Defending against Flooding-Based DDoS Attacks: A Tutorial
Rocky K. C. Chang
Presented by
Adwait Belsare (adwait@wpi.edu)
Suvesh Pratapa (suveshp@wpi.edu)
Modified by Bob Kinicki
18 April 2012

## Slide 2: Outline
Introduction
The DDoS Problems
Solutions to the DDoS Problems
An Internet Firewall?
A Comparison of Four Detect and Filter Approaches
Conclusions

## Slide 3: Introduction
A typical DDoS attack consists of amassing a large number of compromised hosts to send useless packets to jam a victim or its Internet connection or both.
Can be done in following ways:
  To exploit system design weaknesses such as ping to death .
  Impose computationally intensive tasks on the victim such as encryption and decryption.
  Flooding-based DDoS Attack.

## Slide 4: DDoS Attacks
Do not rely on particular network protocols or system design weaknesses.
Consist of sufficient number of compromised hosts amassed to send useless packets toward a victim around the same time.
Have become a major threat due to availability of a number of user-friendly attack tools on one hand and lack of effective solutions to defend against them on the other.

## Slide 5: Attacks Reported
May/June, 1998
First primitive DDoS tools developed in the underground - Small networks, only mildly worse than coordinated point-to-point DoS attacks.
August 17, 1999
Attack on the University of Minnesota reported to UW network operations and security teams.
February 2000
Attack on Yahoo, eBay, Amazon.com and other popular websites.
One study observed more than 12,000 attacks during a three week period.
Reference: http://staff.washington.edu/dittrich/misc/ddos/timeline.html

## Slide 6: The DDoS Problems
The attacks can be classified into:
  Direct Attacks.
  Reflector Attacks.

## Slide 7: Direct Attacks
Consists of sending a large number of attack packets directly towards a victim.
Source addresses are usually spoofed so the response goes elsewhere.
Examples:
  TCP-SYN Flooding: The last message of TCP’s 3 way handshake never arrives from source.
  Congesting a victim’s incoming link using ICMP messages, RST packets or UDP packets.
  Attacks use TCP packets (94%), UDP packets (2%) and ICMP packets(2%).

## Slide 8: Direct Attack
Agent Programs: Trinoo, Tribe Flood Network 2000, and Stacheldraht
Figure 1.

## Slide 9: Reflector Attacks
Uses innocent intermediary nodes (routers and servers) known as reflectors.
An attacker sends packets that require responses to the reflectors with the packets’ inscribed source address set to victim’s address.
Can be done using TCP, UDP, ICMP as well as RST packets.
Examples:
  Smurf Attacks: Attacker sends ICMP echo request to a subnet directed broadcast address with the victim’s address as the source address.
  SYN-ACK flooding: Reflectors respond with SYN-ACK packets to victim’s address.

## Slide 10: Reflector Attack
Cannot be observed by backscatter analysis, because victims do not send back any packets.
Packets cannot be filtered as they are legitimate packets.
Figure 1.

## Slide 11: DDoS Attack Architectures

## Slide 12: Some Reflector Attack Methods

## Slide 13: How many attack packets are needed?
If a victim has resources to admit N half open connections, its capacity of processing incoming SYN packets can be modeled as a G/D/INFINITY/N queue where :
G = General arrival process for the SYN packets.
D = Deterministic lifetime of each half-open connection if not receiving the third handshaking message.

## Slide 14: Minimal rates of SYN packets to stall TCP servers in SYN flooding attacks
WIN system offers better protection against SYN flooding based on maximum lifetimes of half-open connections.
1Mb/s connection is sufficient to stall all three servers with N<= 10,000.

## Slide 15: Solutions to the DDoS Problems
There are three lines of defense against the attack:
  Attack Prevention and Preemption (before the attack)
  Attack Detection and Filtering (during the attack)
  Attack Source Traceback and Identification (during and after the attack)
A comprehensive solution should include all three lines of defense.

## Slide 16: Attack Prevention and Preemption
On the passive side, protect hosts from master and agent implants by using signatures and scanning procedures to detect them {essentially an IDS strategy}.
Monitor network traffic for known attack messages sent between attackers and masters.
On the active side, employ cyber-informants and cyber-spies to intercept attack plans (e.g., a group of cooperating agents).
This line of defense alone is inadequate.

## Slide 17: Attack Source Traceback and Identification
An after-the-fact response.
IP Traceback: Identifying actual source of packet without relying on source information.
  Routers can record information they have seen.
  Routers can send additional information about seen packets to their destinations.
Infeasible to use IP Traceback during ongoing attack. Why?
  Cannot always trace packets’ origins. (NATs and Firewalls!)
  IP Traceback also ineffective in reflector attacks.
Nevertheless, it is at least a good idea and is helpful for post-attack law enforcement.

## Slide 18: Attack Detection and Filtering
Two phases:
  DDoS Attack Detection: Identifying DDoS attack packets.
  Attack Packet Filtering: Classifying those packets and dropping them.
  (Overall performance depends on effectiveness of both phases.)
Effectiveness of Detection
  FPR (False Positive Ratio):
  No. of false positives/Total number of confirmed normal packets
  FNR (False Negative Ratio):
  No. of false negatives/Total number of confirmed attack packets
  Both metrics should be low!

## Slide 19: Attack Detection and Filtering
Effectiveness of Filtering
  *Effective attack detection ≠ Effective packet filtering
  Detection phase uses victim identities (Address or Port No.), so even normal packets with same signatures can be dropped.
  NPSR (Normal Packet Survival Ratio):
  Percentage of normal packets that can survive in the midst of an attack
  NPSR should be high!

## Slide 20: Attack Detection and Filtering

## Slide 21: Attack Detection and Filtering
At Source Networks:
  Can filter packets based on address spoofing.
  Direct attacks can be traced easily, difficult for reflector attacks.
  Need to ensure all ISPs have ingress packet filtering. Very difficult (Impossible?)
At the Victim’s Network:
  DDoS victim can detect attack based on volume of incoming traffic or degraded performance. Commercial solutions available.
  Other mechanisms: IP Hopping (Host frequently changes it’s IP address when attack is detected. DNS tracing can still help the attackers)
  Last Straw: If incoming link is jammed, victim has to shut down and ask the upstream ISP to filter the packets.

## Slide 22: Attack Detection and Filtering
At a Victim’s Upstream ISP Network:
  Victim requests frequently to filter packets.
  Can be automated by designing intrusion alert systems, which should be designed carefully.
  Not a good idea though. Normal packets can still be dropped, and this upstream ISP network can still be jammed under large-scale attacks.
At further Upstream ISP Networks:
  The above approach can be further extended to other upstream networks.
  Effective only if ISP networks are willing to co-operate and install packet filters.

## Slide 23: An Internet Firewall
A bipolar defense scheme cannot achieve both effective packet detection and packet filtering.
Hence a proposal to deploy a global defense infrastructure.
The plan is to detect attacks right at the Internet core!
Two methods, which employ a set of distributed nodes in the Internet to perform attack detection and packet filtering.
  Route-based Packet Filtering Approach (RPF)
  Distributed Attack Detection Approach (DAD)

## Slide 24: Route-Based Packet Filtering (RPF)
Extends the ingress packet filtering approach to the Internet.
  Distributed packet filters examine the packets based on source addresses and BGP routing information.
  A packet is considered an attack packet if it comes from an unexpected link. {Attack packets are then dropped!!}
Major Drawbacks
  Requiring BGP messages to carry the needed source addresses - Overhead inside BGP messages!
  Deployment is still tough! – Filters need to be placed in almost 1800 AS (when there were 10,000 AS’s) and the number of AS is continuously increasing.
  Cannot filter reflected packets because source address is legitimate.

## Slide 25: Distributed Attack Detection (DAD)
Deploys a set of distributed Detection Systems (DSs) to observe network anomalies and misuses.
Anomaly detection:: Observing and detecting traffic patterns that significantly deviate from normal (e.g., unusual traffic intensity for specific packet types).
Misuse detection:: Identifying traffic that matches a known attack signature.
DSs rely mainly on anomaly detection. Various DSs exchange attack information from local observations. This is stateful in respect to the DDoS attacks.
Designing an effective and deployable architecture for the DAD approach is a challenging task.

## Slide 26: DS Design Considerations
Packet processing needs to be high speed.
Attack detection process has two levels: local detection and global detection.
Binary hypothesis - H1 and H0 in Figure 5 is tested on a set of packet flows with the same destination IP address.
If local detection supports H1, DS floods attack alert to all other DS’s. DS’s then consolidate and analyze local detection result with attack alerts to make a global detection decision.

## Slide 27: Distributed Attack Detection
DS Design Considerations
Two Hypotheses:
H1 – Presence of a DDoS attack
H0 – Null Hypothesis
Each attack alert includes a ‘confidence level’
Other considerations:
Filters should be installed only on attack
interfaces when in ‘CONFIRMED’ state
All DSs should be connected ‘always’
Works in Progress:
Intrusion Detection Exchange Protocol
Intrusion Detection Message Exchange
Format

## Slide 28: Distributed Attack Detection
Quickest Detection Problem Formulation
Let ith Sample of instantaneous traffic intensity be Ai
Goal – detect abrupt change in distribution P0  P1 as soon as possible.
Disorder event (arrival of attack packets) triggers distribution change.

## Slide 29: Limitations and Open Problems
Limitations of Mathematical Nature:
Choices of global / local thresholds, traffic modeling, etc.
Performance Aspects:
  Two-level detection not useful for DDoS attacks of short durations.
  Flash crowds can trigger false alarms. Algorithm should adapt to this new ‘normality’.
Other attack patterns:
  DeS (degradation of service attacks) use ‘pulsing agents’ with short bursts.
  Using different sets of attack agents each time.

## Slide 30: Comparison of Four Detect-And-Filter Approaches

## Slide 31: Conclusions
Current defense mechanisms are far from adequate.
One promising direction is to develop a global infrastructure, an Internet Firewall.
Deployment and design considerations should be worked upon.
We see that DDoS Defense is possible through careful planning, and this tutorial covered defense mechanisms which try to discover and slow down bad clients.