## Slide 1: Computer Networks Performance Metrics
Advanced Computer Networks
Fall 2014

## Slide 2: Performance Metrics Outline
Warning: Terminologies can differ!!
Introduction to Queueing Model
Generic Performance Metrics
Components of Hop and End-to-End Packet Delay
Traceroute Tool
Other Performance Measures
Summary

## Slide 3: Terminology Differences
Textbook authors, researchers and companies will have different rules and meanings for network performance terms, specifically:
  Bandwidth versus capacity
  Link versus channel
  Latency versus delay versus RTT
** For this course’s exams, use my definitions!!

## Slide 4: Computer Networks
12
1
11
8
4
7
2
6
9
10
14
5
13
15
3
Host
B
Host
C
Host
L
Host
D
Host
E
Host
G
Host
J
Host
A
Host
H
Host
F
Host
M
16
17
W
T
X
Y
Z
nodes
AP
W1
W2
W3
W4

## Slide 5: How do Loss and Delay occur?
packets queue in router buffers
when the sum of the packet arrival rates at the router exceeds the output link capacity.
14
12
packet being transmitted (delay)
packets queueing (delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers
15
17
K & R

## Slide 6: Simple Queueing Model
Customer
Arrivals
Queue
Server

## Slide 7: Router Node
packet
node 15
17
Outgoing Link
Router Buffer
Server
packet
Incoming Link

## Slide 8
Utilization ::
  the percentage of time a device is busy servicing a “customer”.
Throughput ::
  the number of jobs processed by the “system” per unit time.
Response time ::
  the time required to receive a response to a request (round-trip time (RTT) ).
Delay ::
  the time to traverse from one end to the other of a system.
Generic Performance Metrics

## Slide 9: Network Performance Measures
Channel utilization:: the average fraction of time a channel is busy [e.g. Util = 0.8]
  when overhead is taken into account (i.e., it is excluded from the useful bits sent), channel utilization is often referred to as channel efficiency.
Throughput:: bits/sec. successfully sent {includes retransmissions}
[e.g. Tput = 10 Mbps]

## Slide 10: Throughput
throughput:: rate (bits/time unit) at which bits transferred between sender/receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
pipe that can carry
fluid at rate
Rs bits/sec)
pipe that can carry
fluid at rate
Rc bits/sec)
server sends bits
(fluid) into pipe
K & R

## Slide 11: Throughput (more)
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
link on end-end path that constrains end-end throughput
bottleneck link

## Slide 12: Throughput: Internet Scenario
10 connections (fairly) share backbone bottleneck link R bits/sec
Rs
Rs
Rs
Rc
Rc
Rc
R
per-connection end-end throughput: min(Rc,Rs,R/10)
in practice: Rc or Rs is often the bottleneck
The last mile link has capacity Rc.
K & R

## Slide 13: End-to-End Packet Delay
End-to-end delay includes multiple hop link delays.
Tanenbaum

## Slide 14: Hop Delay Components
K & R

## Slide 15: Four Sources of Packet Delay
1. processing at node:
  Checking for bit errors
  determine output link
  Moving packet from input queue to output queue.
    Table lookup time (see routing algorithms)
A
B
propagation
transmission
nodal
processing
queueing
2. queueing delay
time waiting at output link for transmission
depends on congestion level of router.
K & R

## Slide 16: Delay in packet-switched networks
3. Transmission delay:
R=link bandwidth (bps)
L=packet length (bits)
time to send bits into link = L/R
4. Propagation delay:
d = length of physical link
s = propagation speed in medium (~2x108 m/sec)
propagation delay = d/s
A
B
propagation
transmission
nodal
processing
queueing
Note:
s and R are
very different
quantities!

## Slide 17: End-to-end Packet Delay
End-to-end packet delay :: the time to deliver a packet from source to destination Host (or node).
{Most often, we are interested in the packet delay within the communications subnet.} This delay is the sum of the delays on each subnet link traversed by the packet.
Each link delay consists of four components[B&G Bertsekas and Gallager]:

## Slide 18: Link Packet Delay
1. The processing delay [PROC] between the time the packet is correctly received at the head node of the incoming link and the time the packet is assigned to an outgoing link queue for transmission.
2. The queuing delay [QUEUE] between the time the packet is assigned to a queue for transmission and the time it starts being transmitted. During this time, the packet waits while other packets in the transmission queue are transmitted.

## Slide 19: Link Packet Delay
3. The transmission delay [TRANS] between the times that the first and last bits of the packet are transmitted.
4. The propagation delay [PROP] is between the time the last bit is transmitted at the head node of the link queue and the time the last bit is received at the next router. This is proportional to the physical distance between transmitter and receiver.

## Slide 20: Nodal (Link) Delay
dproc = processing delay
  typically a few microsecs or less
dqueue = queueing delay
  depends on congestion
dtrans = transmission delay
  = L/R, significant for low-speed links
dprop = propagation delay
  a few microsecs to hundreds of msecs
K & R

## Slide 21: End-to-End Packet Delay
end-to-end packet delay = sum of ALL link packet delays.
Be Careful !!
end-to-end can be defined either:
  from Host-to-Host
  or only from end-to-end nodes within the subnetwork.
Link packet delay = PROC + QD
+ TRANS + PROP
B & G

## Slide 22: End-to-End Packet Delay
Tanenbaum
End-to-end delay includes multiple hop link delays.

## Slide 23: Bandwidth Delay Product (BDP)
Amount of data “in flight” or “in the pipe”
Sometimes relative to RTT (i.e., 2 x delay)
Example: 100ms x 40Mbps = 4 M bits
Is this 500 KB?

## Slide 24: Queueing Delay (revisited)
R=link bandwidth (bps)
L=packet length (bits)
a=average packet arrival rate
traffic intensity = La/R
La/R ~ 0: average queueing delay small
La/R -> 1: delays become large
La/R = or > 1: more “work” arriving than can be serviced, average delay infinite!
K & R

## Slide 25: “Real” Internet Delays and Routes
What do “real” Internet delay & loss look like?
Traceroute program: provides delay measurement from source to router along end-to-end Internet path towards destination. For all i:
  sends three packets that will reach router i on path towards destination
  router i will return packets to sender.
  sender times interval between transmission and reply.
3 probes
3 probes
3 probes
K & R

## Slide 26: “Real” Internet delays and routes
1 cs-gw (128.119.240.254) 1 ms 1 ms 2 ms
2 border1-rt-fa5-1-0.gw.umass.edu (128.119.3.145) 1 ms 1 ms 2 ms
3 cht-vbns.gw.umass.edu (128.119.3.130) 6 ms 5 ms 5 ms
4 jn1-at1-0-0-19.wor.vbns.net (204.147.132.129) 16 ms 11 ms 13 ms
5 jn1-so7-0-0-0.wae.vbns.net (204.147.136.136) 21 ms 18 ms 18 ms
6 abilene-vbns.abilene.ucaid.edu (198.32.11.9) 22 ms 18 ms 22 ms
7 nycm-wash.abilene.ucaid.edu (198.32.8.46) 22 ms 22 ms 22 ms
8 62.40.103.253 (62.40.103.253) 104 ms 109 ms 106 ms
9 de2-1.de1.de.geant.net (62.40.96.129) 109 ms 102 ms 104 ms
10 de.fr1.fr.geant.net (62.40.96.50) 113 ms 121 ms 114 ms
11 renater-gw.fr1.fr.geant.net (62.40.103.54) 112 ms 114 ms 112 ms
12 nio-n2.cssi.renater.fr (193.51.206.13) 111 ms 114 ms 116 ms
13 nice.cssi.renater.fr (195.220.98.102) 123 ms 125 ms 124 ms
14 r3t2-nice.cssi.renater.fr (195.220.98.110) 126 ms 126 ms 124 ms
15 eurecom-valbonne.r3t2.ft.net (193.48.50.54) 135 ms 128 ms 133 ms
16 194.214.211.25 (194.214.211.25) 126 ms 128 ms 126 ms
17 * * *
18 * * *
19 fantasia.eurecom.fr (193.55.113.142) 132 ms 128 ms 136 ms
traceroute: gaia.cs.umass.edu to www.eurecom.fr
Three delay measurements from
gaia.cs.umass.edu to cs-gw.cs.umass.edu
* means no response (probe lost, router not replying)
trans-oceanic
link
K & R

## Slide 27: Network Performance Measures
Latency ::
  usually implies the minimum possible delay. Latency assumes no queueing and no contention encountered along the path.
Goodput ::
  {measured at the receiver} the rate in bits per second of useful traffic received. Goodput excludes duplicate packets and packets dropped along the path.
Fairness ::
  either Jain’s fairness or max-min fairness are used to measure fair treatment among competing flows.
Quality of Service (QoS) ::
  a QoS measure accounts for importance of specific metric to one type of application [e.g. jitter and playable frame rate for streaming media].

## Slide 28: Wireless Performance Metrics
WLANs and WSNs are concerned with
packet loss and employ additional metrics:
Delivery ratio::
  the ratio of packets received to packets sent {excluding duplicates and retransmissions}.
Packet loss rate::
  the percentage of packets lost or dropped.
Link layer retransmission rates::
  the percentage of DL layer frames that are retransmitted.

## Slide 29: Packet Loss
queue (aka buffer) preceding link in buffer has finite capacity.
packet arriving to full queue is dropped (aka lost) [FIFO Drop Tail router].
lost packet may be retransmitted by previous node, by source end system, or not at all.
A
B
packet being transmitted
packet arriving to
full buffer is dropped.
buffer
(waiting area)
K & R

## Slide 30: Packet/Frame losses
BDP often used as ‘rule of thumb’ in choosing size of the FIFO buffer at a router.
Other causes of packet/frame loss:
  Collisions on media (both wired and wireless media {e.g., hidden terminal})
  Wireless conditions (SNR, multipath fading)
  Out-of-order arrival.

## Slide 31: Performance Metrics Summary
The three most general performance measures are : utilization, throughput and response time.
In computer networks, end-to-end delay is an important performance metric.
Queueing models are used to analyze and estimate computer network performance.

## Slide 32: Performance Metrics Summary
Other useful metrics include: latency, goodput, fairness and QoS metrics such as jitter or playable frame rate.
In wireless networks, delivery ratio, packet loss rate and link layer retransmission rates are valuable network measures.