## Slide 1: Firewalls and Intrusion Detection Systems
Computer Networks

## Slide 2: Firewalls & IDS Outline
Firewalls
  Stateless packet filtering
  Stateful packet filtering
    Access Control Lists
  Application Gateways
Intrusion Detection Systems (IDS)
  Denial of Service Attacks

## Slide 3: K&R Chapter 8 Outline
8.1 What is network security?
8.2 Principles of cryptography
8.3 Message integrity
8.4 Securing e-mail
8.5 Securing TCP connections: SSL
8.6 Network layer security: IPsec
8.7 Securing wireless LANs
8.8 Operational Security: Firewalls and IDS

## Slide 4: Firewalls
isolates organization’s internal net from larger Internet, allowing some packets to pass, blocking others.
Firewall
administered
network
public
Internet
firewall

## Slide 5: Why Firewalls?
prevent denial of service (DoS) attacks:
SYN flooding: attacker establishes many bogus TCP connections, no resources left for “real” connections.
prevent illegal modification/access of internal data.
e.g., attacker replaces CIA’s homepage with something else.
allow only authorized access to inside network (set of authenticated users/hosts)
three types of firewalls:
stateless packet filters
stateful packet filters
application gateways

## Slide 6: Stateless Packet Filtering
internal network connected to Internet via router firewall.
router filters packet-by-packet, decision to forward/drop packet based on:
  source IP address, destination IP address
  TCP/UDP source and destination port numbers
  ICMP message type
  TCP SYN and ACK bits.
Should arriving packet be allowed in? Departing packet let out?

## Slide 7: Stateless Packet Filtering: Example
Example 1:
Block incoming and outgoing datagrams with IP protocol field = 17 and with either source or dest port = 23.
all incoming, outgoing UDP flows and telnet connections are blocked.
Example 2:
Block inbound TCP segments with ACK=0.
prevents external clients from making TCP connections with internal clients, but allows internal clients to connect to outside.

## Slide 8: Stateless Packet Filtering: More Examples
Policy | Firewall Setting
No outside Web access. | Drop all outgoing packets to any IP address, port 80
No incoming TCP connections, except those for institution’s public Web server only. | Drop all incoming TCP SYN packets to any IP except 130.207.244.203, port 80
Prevent Web-radios from eating up the available bandwidth. | Drop all incoming UDP packets - except DNS and router broadcasts.
Prevent your network from being used for a smurf DoS attack. | Drop all ICMP packets going to a “broadcast” address (eg 130.207.255.255).
Prevent your network from being tracerouted. | Drop all outgoing ICMP TTL expired traffic

## Slide 9: Access Control Lists
action | source address | dest address | protocol | source port | dest port | flag bit
allow | 222.22/16 | outside of 222.22/16 | TCP | > 1023 | 80 | any
allow | outside of 222.22/16 | 222.22/16 | TCP | 80 | > 1023 | ACK
allow | 222.22/16 | outside of 222.22/16 | UDP | > 1023 | 53 | ---
allow | outside of 222.22/16 | 222.22/16 | UDP | 53 | > 1023 | ----
deny | all | all | all | all | all | all
ACL: table of rules, applied top to bottom to incoming packets: (action, condition) pairs.
Computer Networks Firewalls and IDS

## Slide 10: Stateful Packet Filtering
stateless packet filter: heavy handed tool
  admits packets that “make no sense,” e.g., dest port = 80, ACK bit set, even though no TCP connection established:
action | source address | dest address | protocol | source port | dest port | flag bit
allow | outside of 222.22/16 | 222.22/16 | TCP | 80 | > 1023 | ACK
stateful packet filter: track status of every TCP connection.
  track connection setup (SYN), teardown (FIN): to determine whether incoming, outgoing packets “makes sense”.
  timeout inactive connections at firewall: no longer admit packets.

## Slide 11: Stateful Packet Filtering
action | source address | dest address | proto | source port | dest port | flag bit | check conxion
allow | 222.22/16 | outside of 222.22/16 | TCP | > 1023 | 80 | any | 
allow | outside of 222.22/16 | 222.22/16 | TCP | 80 | > 1023 | ACK | x
allow | 222.22/16 | outside of 222.22/16 | UDP | > 1023 | 53 | --- | 
allow | outside of 222.22/16 | 222.22/16 | UDP | 53 | > 1023 | ---- | x
deny | all | all | all | all | all | all | 
ACL augmented to indicate need to check connection state table before admitting packet.
Computer Networks Firewalls and IDS

## Slide 12: Application Gateways
Filters packets on application data as well as on IP/TCP/UDP fields.
Example: Allow select internal users to telnet outside.
host-to-gateway
telnet session
gateway-to-remote
host telnet session
application
gateway
router and filter
1. Require all telnet users to telnet through gateway.
2. For authorized users, gateway sets up telnet connection to dest host. Gateway relays data between two connections.
3. Router filter blocks all telnet connections not originating from gateway.

## Slide 13: Limitations of Firewalls and Gateways
IP Spoofing: router can’t know if data “really” comes from claimed source.
If multiple app’s. need special treatment, each has own app. gateway.
Client software must know how to contact gateway.
  e.g., must set IP address of proxy in Web browser.
Filters often use all or nothing policy for UDP.
Tradeoff: degree of communication with outside world, level of security.
Many highly protected sites still suffer from attacks.

## Slide 14: Intrusion Detection Systems (IDS)
Packet filtering:
  operates on TCP/IP headers only.
  no correlation check among sessions.
IDS: Intrusion Detection System
Deep packet inspection: look at packet contents (e.g., check character strings in packet against database of known virus, attack strings).
Examine correlation among multiple packets:
    port scanning
    network mapping
    DoS attack

## Slide 15: Intrusion Detection Systems
Web
server
FTP
server
DNS
server
application
gateway
Internet
demilitarized
zone
internal
network
firewall
IDS
sensors
Multiple IDS’s: employ different types of checking at different locations.

## Slide 16: Firewalls & IDS Summary
Firewalls
  Stateless packet filtering
  Stateful packet filtering
    Access Control Lists
  Application Gateways
Intrusion Detection Systems (IDS)
  Denial of Service Attacks