## Slide 1: Wireless Sensor Networks (WSNs)
Computer Networks

## Slide 2: WSN Outline
Introduction
Mote Revolution
Wireless Sensor Network (WSN) Applications
WSN Details
Types of Wireless Sensor Networks (WSNs)
  Tiered Architectures
Dynamic Cluster Formation
Power-Aware MAC Protocols
  S-MAC, T-MAC, LPL, X-MAC
The Internet of Things

## Slide 3: Wireless Sensor Networks
A distributed connection of nodes that coordinate to perform a common task.
In many applications, the nodes are battery powered and it is often very difficult to recharge or change the batteries.
Prolonging network lifetime is a critical issue.
Sensors often have long period between transmissions (e.g., in seconds).
Thus, a good WSN MAC protocol needs to be energy efficient.

## Slide 4: WSN Outline
Introduction
Mote Revolution
Wireless Sensor Network (WSN) Applications
WSN Details
Types of Wireless Sensor Networks (WSNs)
  Tiered Architectures
Dynamic Cluster Formation
Power-Aware MAC Protocols
  S-MAC, T-MAC, LPL, X-MAC
The Internet of Things

## Slide 5: WSN Applications
Environmental/ Habitat Monitoring
  Scientific, ecological applications
    Non-intrusiveness
    Real-time, high spatial-temporal resolution
    Remote, hard-to-access areas
  Acoustic detection
  Seismic detection
Surveillance and Tracking
  Military and disaster applications
  Reconnaissance and Perimeter control
  Structural monitoring (e.g., bridges)

## Slide 6: WSN Applications
“Smart” Environments
  Precision Agriculture
  Manufacturing/Industrial processes
    Inventory (RFID)
    Process Control
  Smart Grid
Medical Applications
  Hospital/Clinic settings
  Retirement/Assisted Living settings

## Slide 7: Environment Monitoring
Great Duck Island
150 sensing nodes deployed throughout the island relay data temperature, pressure, and humidity to a central device.
Data was made available on the Internet through a satellite link.

## Slide 8: Habitat Monitoring
The ZebraNet Project
Collar-mounted sensors with GPS
Use peer-to peer info communication
monitor zebra movement in Kenya
Margaret Martonosi
Princeton University

## Slide 9: FireBug
Wildfire Instrumentation System Using Networked Sensors.
Allows predictive analysis of evolving fire behavior.
Firebugs: GPS-enabled, wireless thermal sensor motes based on TinyOS that self-organize into networks for collecting real time data in wild fire environments.
Software architecture: Includes several interacting layers (Sensors, Processing of sensor data, Command center).
A project by University of California, Berkeley CA.
9
Computer Networks Wireless Sensor Networks
[Nuwan Gajaweera]
Notes: Sensors : Thermal, light, pressure, GPS, Accelerometer
More can be done here (overview of the protocol)

## Slide 10: Precision Agriculture
The “Wireless Vineyard”
  Sensors monitor temperature, moisture
  Roger the dog collects the data
  Richard Beckwith
  Intel Corporation

## Slide 11: Camalie Vineyards
Case Study in Crossbow Mote Deployment
Copyright 2006 Camalie Vineyards, Not to be reproduced without written permission

## Slide 12: Water in the Vineyard

## Slide 13: Vineyard Installation
At each Mote location:
  2 soil moisture sensors
  12” and 24” depth
  1 soil temp sensor to calibrate
  soil moisture sensors

## Slide 14: Power Supply
2 month max battery life now with 10 minute sampling interval.
Decided to use solar power, always there when doing irrigation. Solar cell $10 in small quantities and need a $.50 regulator.

## Slide 15: Network Maps
Irrigation Block Map
13 nodes late 2005, 18 nodes in 2006

## Slide 16: A Vision for Wireless MIS
Concept includes smart phone platforms
to streamline continuous monitoring.
16
  [DS-MAC]

## Slide 17: A Vision for Wireless MIS
Health surveillance region provides a multi-hop path
from body sensor networks to central data log and
processing nodes.
17
  [DS-MAC]

## Slide 18: WSNs for Assisted Living
Berkeley Fall Detection System
Alarm-Net
University of Virginia

## Slide 19: WSNs for Assisted Living

## Slide 20: WSNs for Assisted Living
Two-Tiered
WSN
Architecture

## Slide 21: Berkeley Fall Detection System

## Slide 22: Berkeley Fall Detection System

## Slide 23: WSN Outline
Introduction
Mote Revolution
Wireless Sensor Network (WSN) Applications
WSN Details
Types of Wireless Sensor Networks (WSNs)
  Tiered Architectures
Dynamic Cluster Formation
Power-Aware MAC Protocols
  S-MAC, T-MAC, LPL, X-MAC
The Internet of Things

## Slide 24: Wireless Sensor Networks
Another attribute is scalability and adaptability to change in network size, node density and topology.
  In general, nodes can die, join later or be mobile.
Often high bandwidth is not important.
Nodes can take advantage of short-range, multi-hop communication to conserve energy.

## Slide 25: Wireless Sensor Networks
Sources of energy waste:
  Idle listening, collisions, overhearing and control overhead and overmitting.
  Idle listening dominates (measurements show idle listening consumes between 50-100% of the energy required for receiving.)
Idle listening:: listen to receive possible traffic that is not sent.
Overmitting:: transmission of message when receiver is not ready.

## Slide 26: Power Measurements

## Slide 27: WSN Communication Patterns
Broadcast:: e.g., Base station transmits to all sensor nodes in WSN.
Multicast:: sensor transmit to a subset of sensors (e.g. cluster head to cluster nodes)
Convergecast:: when a group of sensors communicate to one sensor (BS, cluster head, or data fusion center).
Local Gossip:: sensor sends message to neighbor sensors.

## Slide 28: Wireless Sensor Networks
Duty cycle:: ratio between listen time and the full listen-sleep cycle.
central approach – lower the duty cycle by turning the radio off part of the time.
Three techniques to reduce the duty cycle:
  TDMA
  Scheduled contention periods
  LPL (Low Power Listening)

## Slide 29: Techniques to Reduce Idle Listening
TDMA requires cluster-based or centralized control.
Scheduling – ensures short listen period when transmitters and listeners can rendezvous and other periods where nodes sleep (turn off their radios).
LPL – nodes wake up briefly to check for channel activity without receiving data.
  If channel is idle, node goes back to sleep.
  If channel is busy, node stays awake to receive data.
  A long preamble (longer than poll period) is used to assure than preamble intersects with polls.

## Slide 30: WSN Outline
Introduction
Mote Revolution
Wireless Sensor Network (WSN) Applications
WSN Details
Types of Wireless Sensor Networks (WSNs)
  Tiered Architectures
Dynamic Cluster Formation
Power-Aware MAC Protocols
  S-MAC, T-MAC, LPL, X-MAC
The Internet of Things

## Slide 31: Tree Routing
[ Cuomo]

## Slide 32: Tiered WSN Architectures
[ Stathopoulos]

## Slide 33: Dynamic Cluster Formation
Wireless Sensor Networks

## Slide 34: Choosing Cluster Heads/ Forming Clusters
Two-tier scheme:
A fixed number of cluster heads that communicate with BS (base station).
Nodes in cluster communicate with head (normally TDMA).
TDMA allows fixed schedule of slots for
sensor to send to cluster head and receive head transmissions.
BS

## Slide 35
BS
Choosing Cluster Heads/ Forming Clusters
Periodically select new cluster heads to minimize power consumption and maximize WSN lifetime.
More complex problem when size of cluster changes dynamically.
As time goes by, some sensor nodes die!
Not worried about coverage issues!
X
X
X
X
X

## Slide 36: Dynamic Cluster Formation
TDMA cluster algorithms:
  LEACH, Bluetooth, …
Rick Skowyra’s MS thesis:
“Energy Efficient Dynamic Reclustering Strategy for WSNs”
  ‘Leach-like’ with a fitness function and periodic re-clustering.
  He designed a distributed genetic algorithm to speed the re-cluster time.

## Slide 37: Power-Aware MAC Protocols
Wireless Sensor Networks

## Slide 38: Power Aware MAC Protocols
1997
1998 PAMAS
1999
2000 SMACS
2001 S-MAC CSMA/ARC
2002 LPL NPSM STEM
2003 DE-MAC EMACs Sift T-MAC
2003 TinyOS-MAC
2004 AI-LMAC B-MAC D-MAC DSMAC
2004 L-MAC MS-MAC TA WiseMAC
2005 Bit-MAC FLAMA M-MAC P-MAC
2005 RateEst-MAC SeeSaw Z-MAC

## Slide 39: Power Aware MAC Protocols
2006 PSM SCP-MAC SS-TDMA TRAMA
2006 X-MAC
2007 C-MAC Crankshaft MH-MAC ML-MAC
2007 RMAC Sea-MAC
2008 AS-MAC DS-MAC DW-MAC Koala
2008 RI-MAC W-MAC
2009 ELE-MAC MD-MAC ME-MAC RA-MAC
2009 Tree-MAC WUR-MAC
2010 A-MAC BuzzBuzz MiX-MAC NPM
2010 PE-MAC VL-MAC
2011 AdaptAS-MAC BAS-MAC Contiki-MAC EM-MAC
2011 MC-LMAC

## Slide 40: Power Aware MAC Protocols
Three approaches to saving power:
1. TDMA: TRAMA, EMACs, L-MAC
2. Schedule: PAMAS, S-MAC, T-MAC, D-MAC, PMAC, SCP-MAC, Crankshaft, AS-MAC
3. Low Power Listening: LPL, B-MAC, WiseMAC, X-MAC
**Newest approaches include
4. Receiver Initiated: RI-MAC, A-MAC

## Slide 41: Sensor-MAC (S-MAC)
All nodes periodically listen, sleep and wakeup. Nodes listen and send during the active period and turn off their radios during the sleep period.
The beginning of the active period is a SYNC period used to accomplish periodic synchronization and remedy clock drift {nodes broadcast SYNC frames}.
Following the SYNC period, data may be transferred for the remainder of the fixed-length active period using RTS/CTS for unicast transmissions.

## Slide 42: Sensor-MAC (S-MAC)
Long frames are fragmented and transmitted as a burst.
SMAC controls the duty cycle by trading off energy for delay.
However, as density of WSN grows, SMAC incurs additional overhead in maintaining neighbors’ schedules.

## Slide 43: S-MAC

## Slide 44: Timeout-MAC (T-MAC)
TMAC employs an adaptive duty cycle by using a very short listening window at the beginning of each active period.
After the SYNC portion of the active period, RTS/CTS is used in a listening window. If no activity occurs within a timeout interval (15 ms), the node goes to sleep.
TMAC saves power at the cost of reduced throughput and additional delay.

## Slide 45: T-MAC
adaptive
active time

## Slide 46: LPL and SCP-MAC
All receivers
synched

## Slide 47: X-MAC
X-MAC is an LPL variant that aims to address:
  Overhearing, excessive preamble and incompatibility with packetizing radios (e.g.,CC2420).
Uses strobed preambles where preambles contain receiver(s) address information.
Addresses multiple transmitters to one receiver by having subsequent transmitters view the ACK, back-off and then send without any preamble.

## Slide 48: X-MAC

## Slide 49: WSN Outline
Introduction
Mote Revolution
Wireless Sensor Network (WSN) Applications
WSN Details
Types of Wireless Sensor Networks (WSNs)
Tiered Architectures
Dynamic Cluster Formation
Power-Aware MAC Protocols
  S-MAC, T-MAC, LPL, X-MAC
The Internet of Things

## Slide 50: (Preview) Internet of Things

## Slide 51: WSN Summary
Introduction
Mote Revolution
Wireless Sensor Network (WSN) Applications
WSN Details
Types of Wireless Sensor Networks (WSNs)
Tiered Architectures
Dynamic Cluster Formation
Power-Aware MAC Protocols
  S-MAC, T-MAC, LPL, X-MAC
The Internet of Things