## Slide 1: Energy Analysis of Four Wireless Sensor Network MAC Protocols
ISWPC 2011
Hong Kong
Brian Bates, Andrew Keating and Robert Kinicki
Worcester Polytechnic Institute
Worcester, Massachusetts
USA

## Slide 2: Wireless Sensor Networks
Small embedded devices with simple hardware measure surroundings and communicate wirelessly via radio.
Used to solve a number of real-world problems:
  Periodic Monitoring
  Event Detection
  Tracking

## Slide 3: Motivation
Mote | Radio (Active) | Radio (Sleep) | CPU (Active) | CPU (Sleep)
TelosB | 23 mA | 1 μA | 1.8 mA | 5.1 μA
MicaZ | 19.7 mA | 1 μA | 8 mA | < 15 μA
Powered by two AA batteries

## Slide 4: Background
Terminology
SCP-MAC
AS-MAC
Crankschaft
MLA

## Slide 5: Terminology Review
Idle Listening:: Listening for a message but not receiving one.
Overhearing:: Receiving a message not intended for that sensor.
Duty Cycle:: Percentage of time the radio is on.
Wakeup Slot:: Interval of time the radio is on (receiver wakeup probe).
Wakeup Interval:: Time between wakeup slots.

## Slide 6: Contention Window (CW)
Slotted, time-divided
Scenario: Two simultaneous senders
1
2
5ms
5ms
5ms
5ms
5ms
5ms

## Slide 7: Contention Window (CW)
Before transmission, a CW slot is selected randomly
1
2

## Slide 8: Contention Window (CW)
Node 1 senses the channel and finds it to be free.
Node 2 is still waiting for its slot to occur.
1
2

## Slide 9: Contention Window (CW)
Node 1 begins transmitting
During Node 2’s slot, it senses the channel is busy.
1
2

## Slide 10: Contention Window (CW)
Node 2 backs off – it has lost contention
It will try to retransmit later.
1
2

## Slide 11: Terminology: Collision
Multiple senders randomly select the same CW slot
1
2

## Slide 12: Sender Collision
Simultaneously sense the channel is free.
They both think they have won contention and send.
1
2

## Slide 13: Sender Collision
Result: Packet loss
1
2

## Slide 14: Early WSN MAC Protocols
First duty cycled MACs:
  S-MAC, T-MAC
  High duty cycles, unable to adapt to variable loads.
Low-Power Listening:
B-MAC, X-MAC
  Long preambles
  B-MAC is the only low-power MAC included in TinyOS.

## Slide 15: SCP-MAC
Goal: Schedule wakeup slots to reduce the duty cycle.
All nodes share a common wakeup time.
Scheduling done through synch messages and piggybacking.
Outperforms previous MAC protocols in energy usage.
Main disadvantage is overhearing.

## Slide 16: SCP-MAC vs. LPL

## Slide 17: AS-MAC
Assigns unique listening time slots.
  To eliminate overhearing and keeps the duty cycle low.

## Slide 18: AS-MAC
Two phases:
  Initialization
  Periodic Listening
Nodes keep track of neighbors’ wakeup schedules in a Neighbor Table.

## Slide 19: AS-MAC
Sender waits until receiver wakes up to transmit (just before).

## Slide 20: AS-MAC Problem: Broadcasting
1
4
3
2
5
BS
3
4
2
5
1

## Slide 21: AS-MAC Problem: Broadcasting
1
4
3
2
5
BS
3
4
2
5
1

## Slide 22: AS-MAC Problem: Broadcasting
1
4
3
2
5
BS
3
4
2
5
1

## Slide 23: AS-MAC Problem: Broadcasting
1
4
3
2
5
BS
3
4
2
5
1

## Slide 24: AS-MAC Problem: Broadcasting
1
4
3
2
5
BS
3
4
2
5
1

## Slide 25: AS-MAC Problem: Broadcasting
1
4
3
2
5
BS
3
4
2
5
1

## Slide 26: Crankshaft
Goal: Reduce energy from overhearing in dense sensor networks.
Two different slot types: broadcast and unicast
  All nodes always wake up for broadcast slots.
  Nodes partitioned into unicast slots (via their address mod number of unicast slots).
Advantages: Eliminates overhearing, efficient broadcast.
Disadvantages: More idle listening with light traffic, no synchronization mechanism.

## Slide 27: Crankshaft

## Slide 28: MAC Layer Architecture (MLA)
A framework for optimized and reusable components to be leveraged across multiple MAC protocols.
Move away from monolithic MAC implementations.
Provides hardware dependent services (e.g., alarming).
Provides hardware-independent reusable components (e.g. channel polling and preamble sending).

## Slide 29: MAC Layer Architecture (MLA)

## Slide 30: Research Statement
Used MLA to implement (SCP-MAC, AS-MAC, Crankshaft and BAS-MAC) on TelosB motes running TinyOS 2.1.0.
Analyzed the energy consumption of each protocol under three WSN traffic patterns (local gossip, convergecast and broadcast).

## Slide 31: Methodology Overview
Hardware Selection
Oscilloscope Measurements
MAC Protocol Implementations and Validation
Parameter Selection and Initial Synchronization
Experiment Design and Data Gathering

## Slide 32: Hardware Selection
Considered the Mica2, MicaZ, iMote2, and TelosB
Chose the TelosB:
  Middle of the line specs and price
  Popular in academic research
  Newer CC2420 radio
  USB Interface

## Slide 33: Measuring Energy

## Slide 34: Measuring Energy

## Slide 35: Measuring Energy
Added hooks into radio device drivers.
Ability to measure amount of time the radio is in each state.
Radio State | Observed Current | CC2420 Datasheet Value
Stopped | 0 mA | 21 μA
Starting | 2.51 mA | N/A
Idle | 20.07 mA | 18.8 mA
Sending | 17.01 mA | 17.4 mA
Receiving | 20.22 mA | 18.8 mA
Stopping | 10.04 mA | N/A

## Slide 36: Protocol Implementations
Implemented using TinyOS version 2.1.0
  More standardized message stack than version 1.x
Leveraged the MAC Layer Architecture (MLA) framework
  Provides common MAC code for WSNs.
All four protocols were rebuilt for this frameworks.

## Slide 37: Broadcastable AS-MAC (BAS-MAC)
Added a broadcast slot to AS-MAC

## Slide 38: BAS-MAC Broadcasting
B
BS
3
4
2
5
1
1
4
3
2
5

## Slide 39: Parameter Selection
Goal: Put four different protocols on a level playing field.
Standardized wakeup intervals.
Kept some parameters constant across protocols
  Contention window size and behavior
  Wakeup slot
Left synchronization out of it
  Synch costs are low compared to overall energy costs.
  Synch can be complex and time consuming (AS-MAC).

## Slide 40: Standardizing Wakeup Intervals

## Slide 41: Initialization Synchronization
Mote oscillates between two states:
  Initialization: Radio always on, awaiting a message.
  Running: Normal experimental operation
Resetting a mote changes the state.
Uses the onboard flash to hold persistent state.
User button sends reset message to all motes.

## Slide 42: Mote Programming

## Slide 43: Experiment Overview
4 MAC protocols
3 traffic patterns: local gossip, convergecast, broadcast
Small and large networks (10 node)
Fast and slow sending rates
3 minute experiments, 5 repetitions each (averages reported)
240 total experiments

## Slide 44: Data Collection
Difficulties in collecting data
  Writing to serial takes time, limited storage.
  Want to get energy data from all motes.
Split experiments into phases
  Initialization
  Experiment specific behavior
  Sending information messages to central node.
Central node hooked up via USB – streams results
  Immediately available and visible on laptop.

## Slide 45: Local Gossip

## Slide 46: Sender Staggering
3
4
2
5
1
Wakeup Interval

## Slide 47: Sender Staggering
3
4
2
5
1
Wakeup Interval

## Slide 48: Local Gossip (Senders)

## Slide 49: Local Gossip (Receivers)

## Slide 50: Fast Local Gossip
SCP-MAC performs poorly
  Not enough wakeup slots to send all of the data.
Wakeup Slot
Sending Motes

## Slide 51: Star Topology Setup

## Slide 52: Convergecast (Leaf Nodes)

## Slide 53: Convergecast (Base Station)

## Slide 54: Broadcast
Arrange nodes in a “star” pattern.
Central mote periodically broadcasts messages to all other motes.
All nodes in radio range of one another.

## Slide 55: Broadcast (Base Station)

## Slide 56: Broadcast (Leaf Nodes)

## Slide 57: Conclusions
Overhearing is a significant source of energy waste.
Although sending costs less energy per unit time, the overall cost of sending a message is greater.
AS-MAC inefficiency of broadcast is an high energy consumer.
AS-MAC can be made more robust with the addition of a broadcast slot.
There is no one MAC protocol that is best in all one hop traffic scenarios.

## Slide 58: Future Work
Multi Hop
Parameter Adjustments
Latency and Throughput
Transmission Power/Topology Control
Multi-channel MAC protocols

## Slide 59: Questions?