## Slide 1
The Internet of Every Thing - steps toward sustainability
David E. Culler
Professor, Computer Science Chair
University of California, Berkeley
CWSN Keynote, Sept. 26 2011

## Slide 2: The Internet … a decade ago

## Slide 3: The Internet … that we envisioned

## Slide 4: Why “Real” Information is so Important
Improve Productivity
Protect Health
High-Confidence Transport
Enhance Safety & Security
Improve Food & H20
Save Resources
Preventing Failures
Increase
Comfort
Enable New Knowledge

## Slide 5: Enabling Technology
Microcontroller
Radio
Communication
Flash
Storage
Sensors
IEEE 802.15.4
Network

## Slide 6: Internet Concepts: Layering…
802.5
Token Ring
802.3
Ethernet
802.11
WiFi
802.3a
Ethernet
10b2
802.3i
Ethernet
10bT
802.3y
Ethernet
100bT
802.3ab
Ethernet
1000bT
802.3an
Ethernet
1G bT
802.11a
WiFi
802.11b
WiFi
802.11g
WiFi
802.11n
WiFi
X3T9.5
FDDI
Serial
Modem
GPRS
ISDN
DSL
Sonet
Transport (UDP/IP, TCP/IP)
Application (Telnet, FTP, SMTP, SNMP, HTTP)
Diverse Object and Data Models (HTML, XML, …, BacNet, …)
802.15.4
???
Network (IP)
Link
2: link
3: net
4: xport
7: app
1: phy

## Slide 7: Leading Internet Research Perspective - a decade ago
“Resource constraints may cause us to give up the layered architecture.”
“Sheer numbers of devices, and their unattended deployment, will preclude reliance on broadcast communication or the configuration currently needed to deploy and operate networked devices.”
“There are significant robustness and scalability advantages to designing applications using localized algorithms.”
“Unlike traditional networks, a sensor node may not need an identity (e.g. address).”
“It is reasonable to assume that sensor networks can be tailored to the application at hand.”
We were wrong...

## Slide 8: The Mote/TinyOS revolution…
SmartDust
WeC
Rene
Intel
rene’
99
98
00
01
03
02
04
06
05
07
SENSIT
Expedition
NEST
NETS/ NOSS
CENS STC
NSF
Cyber-Physical
Mica
Intel/UCB
dot
Intel
iMOTE
XBOW
cc-dot
XBOW
mica2
XBOW
rene2
Intel
cf-mica
Bosch
cc-mica
Dust Inc
blue cc-TI
digital sun
rain-mica
XBOW
mica
zeevo BT
Telos
XBOW
micaZ
Intel
MOTE2
Eyes
BTNode
trio
8 kB rom
½ kB ram
48 kB rom
10 kB ram
802.15.4
LoWPAN/IPv6
Epic
11
IETF RPL
10

## Slide 9: Internet of Every Thing – Realized 2008
Footprint, power, packet size, & bandwidth
Open version 27k / 4.6k
 | ROM | RAM
CC2420 Driver | 3149 | 272
802.15.4 Encryption | 1194 | 101
Media Access Control | 330 | 9
Media Management Control | 1348 | 20
6LoWPAN + IPv6 | 2550 | 0
Checksums | 134 | 0
SLAAC | 216 | 32
DHCPv6 Client | 212 | 3
DHCPv6 Proxy | 104 | 2
ICMPv6 | 522 | 0
Unicast Forwarder | 1158 | 451
Multicast Forwarder | 352 | 4
Message Buffers | 0 | 2048
Router | 2050 | 106
UDP | 450 | 6
TCP | 1674 | 50
(including runtime)
* Production implementation on TI msp430/cc2420
24038 | ROM
3598 | RAM

## Slide 10: Internet of Every Thing – standardized 2010

## Slide 11: Networking in the Physical World
Networking Challenges
Variable communication
  Unknown obstacles
  Variable density and loss
Constrained resources
  Limited routing state
  Limited throughput
  Limited buffering
Low power wireless
  Multihop
  Low SNR
  Small MTU
Application Requirements
Embedding in physical space
Large numbers of nodes
Low total cost of ownership

## Slide 12: Confluence Research, Industry, and Standards
Research
Community

## Slide 13: Key Research Developments
Event-Driven Component-Base Operating System
  Framework for building System & Network abstractions
  Low-Power Protocols
  Hardware and Application Specific
Idle listening
  All the energy is consumed by listening for a packet to receive
  => Turn radio on only when there is something to hear
Reliable routing on Low-Power & Lossy Links
  Power, Range, Obstructions => multi-hop
  Always at edge of SNR => loss is common
  => monitoring, retransmission, and local rerouting
Trickle – don’t flood (tx rate < 1/density, and < info change)
  Connectivity is determined by physical points of interest, not network designer.
  never naively respond to a broadcast
  re-broadcast very very politely

## Slide 14: TinyOS – Framework for Innovation
Storage
Processing
Wireless
Sensors
WSN mote platform
Radio Serial
Flash
ADC, Sensor I/F
MCU, Timers, Bus,…
Link
Network
Protocols
Blocks, Logs, Files
Scheduling, Management
Streaming drivers
Over-the-air
Programming
Applications and Services
Communication Centric
Resource-Constrained
Event-driven Execution

## Slide 15: A worldwide community
Storage
Wireless
Processing
Sensors
SmartDust
NEST
Wireless Sensor Networks

## Slide 16: Low Power Networking in the Real World
Applications
system
Storage
Processing
Wireless
Sensors
Technology
architecture
Network
Notes: Now that we’ve set the context, here’s a picture of the rest of the presentation
I do
Kris does

## Slide 17: A Low-Power Standard Link
 | 802.15.4 | 802.15.1 | 802.15.3 | 802.11 | 802.3
Class | WPAN | WPAN | WPAN | WLAN | LAN
Lifetime (days) | 100-1000+ | 1-7 | Powered | 0.1-5 | Powered
Net Size | 65535 | 7 | 243 | 30 | 1024
BW (kbps) | 20-250 | 720 | 11,000+ | 11,000+ | 100,000+
Range (m) | 1-75+ | 1-10+ | 10 | 1-100 | 185 (wired)
Goals | Low Power, Large Scale, Low Cost | Cable Replacement | Cable Replacement | Throughput | Throughput
Low Transmit power, Low Signal-to-noise Ratio (SNR), modest BW, Little Frames

## Slide 18: Decade of Networking (sans Architecture)
Link
Network
Transport
Application
1999
2002
2003
2004
2005
2006
2007
SPIN
2000
2001
2008
Broadcast Storm
TinyOS 0.6
WooMAC
GAF
S-MAC
Aloha PS
PSFQ
GDI
CODA
MintRoute
T-MAC
RMST
B-MAC
MultihopLQI
Fusion
Deluge
FPS
WiseMAC
SP
Drip
Drain
BVR
Redwoods
North Sea
SCP-MAC
PEDAMACS
X-MAC
Volcano
CTP
Flush
Golden Gate Bridge
S4
Dip

## Slide 19: The “Idle Listening” Problem
The power consumption of “short range” (i.e., low-power) wireless communications is roughly the same when
  transmitting,
  receiving,
  or simply ON, “listening” for potential reception.
  IEEE 802.15.4, Zwave, Bluetooth, …, WiFi
Radio must be ON (listening) in order receive anything.
  Transmission is rare
  Listening happens all the time
Energy consumption dominated by idle listening
Do Nothing Well

## Slide 20: Communication Power – Passive Vigilance
Listen just when there is something to hear …
Sleep
~10 uA
Transmit
~20 mA x 1-5 ms
[20 - 100 uAs]
I
I
Time
Time
Listen
~20 mA x * ???
Receive
~20 mA x 2-6 ms

## Slide 21: 3 Basic Solution Techniques
Scheduled Listening
  Arrange a schedule of communication Time Slots
  Maintain coordinated clocks and schedule
  Listen during specific “slots”
  Many variants:
    Aloha, Token-Ring, TDMA, Beacons, Bluetooth piconets, …
    S-MAC, T-MAC, PEDAMACS, TSMP, FPS, …
Sampled Listening
  Listen for very short intervals to detect eminent transmissions
  On detection, listen actively to receive
  DARPA packet radio, LPL, BMAC, XMAC, …
  Maintain “always on” illusion, Robust
Listen after send (with powered infrastructure)
  After transmit to a receptive device, listen for a short time
  Many variants: 802.11 AMAT, Key fobs, remote modems, …
Many hybrids possible
802.15.3e

## Slide 22: Routing in Low Power Wireless Networks
Classic View
  Network = Graph of routers and links
    Like a street map
  Routing is a (distributed) algorithm for finding good paths in this (slowly changing) graph
  Realized (hop by hop) by tables and addressing
But, … there is no graph
  Discover it by attempting to communicate
  Changes due to environment
PAN

## Slide 23: Self-Organized Routing - nutshell
0
1
1
2
2
2
2
2
Receiver diversity through dynamic rerouting
Retrans. rate < 1/density
Neighbor table exceeds RAM
Dissem. rate < change

## Slide 24: Key IPv6 Contributions
Large simple address
  Network ID + Interface ID
  Plenty of addresses, easy to allocate and manage
Autoconfiguration and Management
  ICMPv6
Integrated bootstrap and discovery
  Neighbors, routers, DHCP
Protocol options framework
  Plan for extensibility
Simplify for speed
  MTU discovery with min
6-to-4 translation for compatibility
Prefix
IID
ICMPv6
IPv6 Base
HbH Opt
Routing
Fragment
Dst Opt
128 bits

## Slide 25: 6LoWPAN – IPv6 over 802.15.4
Large IP Address & Header => 16 bit short address / 64 bit EUID
Minimum Transfer Unit => Fragmentation
Short range & Embedded => Multiple Hops
Link frame
ctrl
src UID
len
chk
dst UID
link payload
cls
flow
len
hops
src IP
dst IP
net payload
Network packet
UDP datagram or
TCP stream segment
transport header
application payload
…, modbus, BacNET/IP, … , HTML, XML, …, ZCL
16 B
128 Bytes MAX
1280 Bytes MIN
16 B
40 B + options
NH
?

## Slide 26: 6LoWPAN adaptation layer
802.5
Token Ring
802.3
Ethernet
802.11
WiFi
802.3a
Ethernet
10b2
802.3i
Ethernet
10bT
802.3y
Ethernet
100bT
802.3ab
Ethernet
1000bT
802.3an
Ethernet
1G bT
802.11a
WiFi
802.11b
WiFi
802.11g
WiFi
802.11n
WiFi
X3T9.5
FDDI
Serial
Modem
GPRS
ISDN
DSL
Sonet
Transport (UDP/IP, TCP/IP)
Application (Telnet, FTP, SMTP, SNMP, HTTP)
Diverse Object and Data Models (HTML, XML, …, BacNet, …)
802.15.4
LoWPAN
Network (IP)
Link
2: link
3: net
4: xport
7: app
1: phy
6LoWPAN

## Slide 27: 6LoWPAN – IP Header Optimization
Eliminate all fields in the IPv6 header that can be derived from the 802.15.4 header in the common case
  Source address : derived from link address
  Destination address : derived from link address
  Length : derived from link frame length
  Traffic Class & Flow Label : zero
  Next header : UDP, TCP, or ICMP
Additional IPv6 options follow as options
Link frame
ctrl
src UID
len
chk
dst UID
Network packet
40 B
6LoWPAN adaptation header
hops
3 B
cls
flow
len
hops
src IP
dst IP
net payload
NH

## Slide 28: IP Routing Everywhere
Conventional IP link is a full broadcast domain
  Routing connects links (i.e, networks)
Many IP links have evolved from a broadcast domain to a “mesh” with emulated broadcast
  ethernet => switched ethernet
  802.11 => 802.11s
Utilize high bandwidth on powered links to maintain the illusion of a broadcast domain
802.15.4 networks are limited in bandwidth and power so the emulation is quite visible.
PAN

## Slide 29: Embedded IPv6 in Concept
IP Link ⇒ Broadcast Domain
Structured Decomposition
IP Link ⇒ Always On
Retain illusion even when always off
Retain strict modularity
Some key cross-layer visibility
IPv6 can support a semi-broadcast
link with few changes
IP Link ⇒ “Reliable”
Retain best-effort reliability over unreliable links

## Slide 30: Example: Autoconfiguration Configuring Large Numbers of Interfaces
Cur Hop Limit
Managed Addr Config
Other Config
Router Lifetime
Reachable Time
Prefix Length
Autonomous Config
Valid Lifetime
Preferred Lifetime
Prefix
ICMPv6 Hdr
Router Adv
Prefix Info
RFC 4861 – Neighbor Discovery
RFC 4862 – Stateless Addr Autoconf
RFC 3315 – DHCPv6
Existing Options
New Options
Network ID
Sequence Number
Router Hops
Flags
MHop Info

## Slide 31: Example: Routing with IPv6 options
Default Routes
Discovering Links
ICMPv6 Hdr
Router Adv
MHop Info
Building a Connectivity Graph
Routing Table
Low Routing Cost
High Routing Cost
Selecting the Next Hop
Routing Table
Forwarding Table
Default route
Hop-by-hop retry
Reroute on loss
Prefix | Next
Default | 
Prefix | Next
Prefix | Next

## Slide 32: Complete Embedded IPv6 Stack
Link
Net
Tran
App
Media Management Control
Remote Media
Link Stats
Neighbor Table |  |  |  |  | 
Addr | Period | Phase | Pending | RSSI | PRR
Local Media
Sample Period
Sample Phase
Router
Routing Protocol
Routing Table
Prefix | Next
Stateless
Autoconf
Autoconf
DHCPv6
UDP
TCP
6LoWPAN Adaptation
ICMPv6
Data
Ack
HTTP
Telnet
SNMP
DNS
…
Forwarder
Multicast
Send Manager
Buffer
Unicast
Queue
Forwarding Table
Send Manager
Prefix | Next
Default | 

## Slide 33: Adding up the pieces
 | ROM | RAM
CC2420 Driver | 3149 | 272
802.15.4 Encryption | 1194 | 101
Media Access Control | 330 | 9
Media Management Control | 1348 | 20
6LoWPAN + IPv6 | 2550 | 0
Checksums | 134 | 0
SLAAC | 216 | 32
DHCPv6 Client | 212 | 3
DHCPv6 Proxy | 104 | 2
ICMPv6 | 522 | 0
Unicast Forwarder | 1158 | 451
Multicast Forwarder | 352 | 4
Message Buffers | 0 | 2048
Router | 2050 | 106
UDP | 450 | 6
TCP | 1674 | 50
(including runtime)
* Production implementation on TI msp430/cc2420
24038 | ROM
3598 | RAM

## Slide 34: and Power and reliability …
Data Rate Sensitivity
(Router)
Data Rate Sensitivity
(Edge)
Deployment Duty Cycle
Deployment Reliability

## Slide 35: What has Changed with ROLL ?
Three routing requirements case studies
  Buildings [RFC 5867], Industrial [RFC 5673], Urban [RFC 5548], and home [RFC 5826]
  Narrow the domain, establish constraints
IETF Routing Protocol Survey
  Useful study, unpublished for political reasons
Three Initial Proposals
  HYDRO: simple merger of well-established techniques (CTP, TSMP, …)
  TD: repurpose of MANEMO proposal
  Backtrack
Design Team to produce unification: RPL
  1+ year, inter-related suite of design choices

## Slide 36: Elements of RPL
Retains carefully-formed, low-complexity muti-path routing
  DAG constructed and maintained via discovery and use of links
  Roots route to/from “powered Internet”
  Multiple ‘upward’ default routes
  Source-based downward routing via reversal
    State-free: routing table at root
    State-full: tables may be in any node
Imposes some structure on DAG
  Collection of single-rooted DAGs (DODAG)
  Local-repair within constraints
  Roots may initiate global repair through seq # advance
  Avoids count-to-infinity via split-horizon emulation

## Slide 37: Elements (cont)
Arbitrary point-to-point via up/down
Multiple RPL instances over common physical topology
Elaborate metric container mechanism (OF)
  Support multi-objective, constraint-based routing
  OF0 essentially shortest path (with threshold)
  MRHOF: generalization of ETX (estimated transmission cost)
Proposed lower-stretch P2P via instance formation

## Slide 38: Many Important Details
Header format specifics and trade-offs
ICMPv6 ND (RA etc.) replaced with RPL ND
  DIS, DIO, DAO
Routing Security framework from the start
Limited Tolerance for Routing Inconsistency
Source routing as compact hop-by-hop option
  6MAN
Not limited to 802.15.4 or LoWPAN
  PLC
…

## Slide 39: Rough Consensus and Running Code
IETF Standard requires multiple independent interoperable implementations
  Two major open-source ones already (next)
  Many commercial and research ones of varying quality
Standards bodies in transformation
  ZIGBEE has become compliance body
  802.15.4 | 6LoWPAN |RPL ipv6 | TCP/UDP | … ??
  IETF CORE developing compact http over UDP
  IEEE 802.15.4e/g wrapping up low power MAC
Lots of vested interest positioning & cruft

## Slide 40: Open InterOp …
MAC Parameter
alignment
Beyond Interoperability – Pushing the Performance of Sensor Network IP Stacks, Sensys 2011

## Slide 41: Opportunities and Open Problems
Quantitative Analysis and Design of WSNs in context of layered IPv6 architecture
  Objective function trade-offs, utility, table management algorithms, …
Classic issues in new context
  Transport protocol, compression, cross-layer optimization, …
Ideas set aside for lack of knowledge
  Piecewise source routing, reactive backtracking, …
“Let chaos Reign, then Rein in the Chaos”

## Slide 42: The “Killer App” for WSNs
Energy and the environmental impact of extraction, use, and disposal
THE problem of the Industrial Age
We need to find Information Age solutions to THE Industrial Age Problem
=> Fundamental transformation in the architecture of the electric grid

## Slide 43: Traditional Load-Following Grid
Baseline + Dispatchable Tiers
Oblivious Loads
Transmission
Generation
Demand
Distribution

## Slide 44: Towards an ‘Aware’ Energy Infrastructure
Baseline + Dispatchable Tiers
Oblivious Loads
Communication
Non-Dispatchable
Sources
Communication
Aware Interactive Loads
Transmission
Generation
Demand
Distribution

## Slide 45: Aware Co-operative Grid
Monitor, Model, Mitigate
  Deep instrumentation
  Waste elimination
  Efficient Operation
Shifting, Scheduling, Adaptation
Forecasting
Tracking
Market
Availability
Pricing
Planning

## Slide 46: The “Macroscope”
Observe complex interactions over time and space
Slope (Spatial Analyst)
Aspect (Spatial Analyst)
Daily Average Temperature(Geostatistical Analyst)
Elevation (Calculated from Contour Map)
Aerial Photograph (10.16cm/pixels)

## Slide 47: Where to Start?
Buildings
  72% of electrical consumption (US),
  40-50% of total consumption,
  42% of GHG footprint
  US commercial building consumption doubled 1980-2000, 1.5x more by 2025 [NREL]
Where Coal is used
Prime target of opportunity for renewable supplies
Renewable energy consumption
Electricity source

## Slide 48: Our Buildings
Lighting
Servers
PDUs, CRACs
HVAC
IT and Plug Load

## Slide 49: Energy Transparent Building
Whole Bldg
MCL equip
MCL infra
MCL vac
servers
DOP HVAC
Central vent
office HVAC
inst Lab 199
HVAC
Plug loads
Lighting
Parking Lot

## Slide 50: sMAP: Uniform Access to Diverse Physical Information
Electrical
Weather
Geographical
Water
Environmental
Structural
Actuator
Occupancy
sMAP
Modeling
Visualization
Continuous Commissioning
Control
Personal Feedback
Debugging
Storage
Location
Authentication
Actuation
Applications
Physical Information
REST API
HTTP/TCP
…
JSON Objects

## Slide 51: IP everywhere / Real World Web
Internet
Cell phone
sMAP Gateway
sMAP
Modbus
RS-485
sMAP
sMAP Gateway
EBHTTP / IPv6 / 6LowPAN Wireless Mesh Network
sMAP
sMAP
sMAP
sMAP
Edge Router
Temperature/PAR/TSR
Vibration / Humidity
AC plug meter
Light switch
Dent circuit meter
Proxy Server
EBHTTP Translation
California ISO
sMAP Gateway
sMAP Resources
Applications
Google PowerMeter
Weather
sMAP
Every Building
Database
Notes: Proxies can translate compressed JSON/HTTP to standard form,

## Slide 52: DOE Misc. and Electronic Loads
LBNL Bldg 90
611 of 1200 loads

## Slide 53: DOE/UCB/Siemens Auto Demand Response
www.openbms.org
Sutardja Dai Hall
Chart: Power (kW)
Lights & Plugs | 60.8671
Servers & Cooling | 67.5452
Nano Fab | 370.1091
HVAC | 232.9176
Other | 85.563

## Slide 54: BACNet => sMAP
Sensors,
Actuators
Controllers
Modem
Siemens P2
over RS-485
Apogee
Server
Remote
Login
BACnet/IP
Gateway
sMAP
Internet
Sutardja Dai Hall
Notes: sMAP – homogeneous interface, higher level JSON encoding, extensible schema, human & machine readable
BACnet – fixed format, binary encoding, tunneled over IP low level

## Slide 55: Personalized Automated Lighting Control
Three controllable ballasts per fixture
~5 zones per floor
BACnet
sMAP
MySQL
Python
Django
Python
Control
Process
HTTP
Gateway
Notes: Application of smap stack

## Slide 56: 6,000+ Points in 1 Modern Building
1358 control settings
  Set points, Relays (lights, pumps, etc), Schedules
2291 meters/sensors
  Power (building, floor, lights, chiller, pumps, etc)
    Current, voltage, apparent, real, reactive, peak
  Temp (rooms, chilled water, hot water)
  Air volume
  Alarms, Errors
2165 control outputs
  Dampers, valves, min/max flow, fan speed, PID parameters
72 other
US: 4+ million Commercial, 110+ million Residential

## Slide 57: Real Energy Savings
Chart: SDH 4th Floor Lighting Energy Usage
|  | Before | 13-May | 20-May | 27-May | 3-Jun | 10-Jun | 17-Jun | 24-Jun | 1-Jul | 8-Jul | 15-Jul
Colab Savings | 0 | 0 | 0.58 | 0.68 | 0.69 | 0.63 | 0.53 | 0.65 | 0.68 | 0.75 | 0.71 | 0.61
Floor kW | 3.47 | 3.47 | 1.83 | 1.47 | 1.44 | 1.86 | 1.97 | 1.64 | 1.65 | 1.2 | 1.37 | 1.78
Collab kW | 2.84 | 2.84 | 1.19 | 0.9 | 0.87 | 1.04 | 1.34 | 1 | 0.9 | 0.71 | 0.84 | 1.09

## Slide 58: Re-Flash the HVAC …
Whole Bldg
inst Lab 199
HVAC
LoCal + ActionWebs

## Slide 59: Learning-based Model Predictive Control
Mathematical model from Newton’s law of cooling
Model identified using semi-parametric regression
dT/dt = -krT - kcu(t) + kww(t)) + q(t)
change in temperature
over time
time constant
of room
AC cooling
weather
heating from occupants
and equipment
Temperature:
Experimental (blue)
Simulated (red)
Heating from occupants
and equipment
(Aswani, Master, Taneja, Culler, Tomlin, Proc. of IEEE, 2011)

## Slide 60: Learning-Based Model Predictive Control
Experimental LBMPC: 12.6kWh Consumed
Temperature
Control Action
Simulated Hysteresis Control: 29.7kWh Consumed (estimated)
Temperature
Control Action
(Aswani, Master, Taneja, Culler, Tomlin, 2011)
  LBMPC adjusts for internal dynamics, avoids over-cooling, trades off duty cycle and switching frequency

## Slide 61: Cyber / Physical Buildings
BMS
Cyber
Physical
Building
Light
Transport
Process Loads
Occupant Demand
Legacy Instrumentation & Control Interfaces
Pervasive Sensing
Activity/Usage
Streams
BIM
BITS
PIB
Activity Models
Multi-Objective Model-Driven Control
Building Integrated
Operating System
External
HVAC
Electrical
Fault, Attack, Anomaly Detect &Management
Control Plan and Schedule
Physical Models
Human-Building Interface

## Slide 62: Conclusions
The Internet is Every Thing is Here
15 years of deep innovation and research
  Critical WSN breakthroughs
  Key IPv6 developments
Worldwide community of students, faculty, and industry
Engagement of International organizations
Fundamentally a new Scientific Instrument
Focus it on the World’s most important problem
  Energy, productivity, and the environment

## Slide 63: Thank You