## Slide 1: Improving Packet Delivery Performance of Publish/Subscribe Protocols in Wireless Sensor Networks Sensors 2013, Volume 13, Issue 1
Presenter: Le Wang

## Slide 2: Outline
1. Motivation and overview
2. Background
  Polling Model and Publish/Subscribe Model
  Publication Discipline
  MQTT-S and CoQP
3. Simulation Environment
4. Evaluation
  Single Hop
    PDR
    Discarded Publication Ratio (DPR)
    Retransmitted Publication Ratio
    Duplicated Publications Ratio
  Multiple Hop
5. Summary

## Slide 3: Motivation
MQTT-S and CoAP:
  Two application protocols for Wireless Sensor Networks (WSN)
  Based on UDP
  Provide reliability mechanism in Application layer
Reliability Mechanism:
  Defines a fixed Retransmission TimeOut (RTO).
  Problems? Too long or too short?
  Result in a lower Packet Delivery Ratio (PDR).
Propose an adaptive RTO:
  Consists in using a Smooth Round-Trip Time (SRTT)
  Multiplied by a constant parameter K

## Slide 4: Background
Polling Model:
  Applications send queries to sensor nodes to retrieve information.
  Problem?
  When an event of interest occurs, in order to react in real-time, the sensor nodes have to be queried continuously.
    Waste of resources such as energy, processing and bandwidth.

## Slide 5: Background
Publish/Subscribe Model
  Entities:
    Publisher: generate events
    Subscriber: express interest in events
  Subscription:
    Register interest in the event
  Advantages:
    Decouple in time: publishers and scubscribers do not need to be actively participating in the interaction at the same time
    Decouple in space: publishers and subscribers do not need to know each other
    Publishers and subscribers can produce or consume events in an asynchronous way.

## Slide 6: Publication Discipline
Activation: when there is a pending confirmation of a publication message, and a new publication is generated
MQTT-S publication discipline:
  Discard the new publication message
CoAP publication discipline:
  Discard the old publication message
An inappropriate fixed RTO will result in a higher probability of a new publication message being generated while the RTO is active. Therefore, the publication discipline will discard the publication message (Old or New).

## Slide 7: MQTT-S
Extension of the Message Queuing Telemetry Transport (MQTT) Optimized for WSN.
Components:
  Broker node:
    responsible for managing subscriptions as well as storing and sending publications to corresponding WSN subscriber nodes.
  Publisher nodes:
    generate event
  Subscriber nodes:
    express interest in events
  Relay nodes:
    for multi-hop scenario.

## Slide 8: MQTT-S
Reliability:
  QoS Level 0 (QoS0)
    Offers a best-effort delivery service, no retransmission or Acknowledgements.
  QoS Level 1 (QoS1)
    Allows the retransmission of messages until Acked
    Does not prevent duplicate reception
  QoS Level 2 (QoS2)
    Ensures the reception of message
    Ensures to deliver only once to the destination by four message handshake.
  Parameters for QoS1 and QoS2:
    Fixed RTO: 10-15 seconds.
    Retransmission number: 3-5

## Slide 9: MQTT-S
Publication Discipline:
  “stop and wait” mechanism for the transmissions of publication messages with QoS1 and QoS2.
  A publisher node has to wait for the termination of its publication message flow with the broker node before it can start a new one.
  If more than one publications are generated, publication discipline is needed.
  Activity 1: Queue the new publication messages
    Drawback: cost more source
  Activity 2: Drop the new publication messages
    Always attempts to retransmit the old publication message till receive the ACK.
    Called ‘Persistent mode’ discipline

## Slide 10: CoAP
Characteristics:
  RESTful (Representational State Transfer)
  Resources are identified by Universal Resource Identifiers (URI)
  UDP based
Model:
  Client/server interaction model
    Request messages initiate a transaction with a server, which may send a response to the client with a matching transaction ID
    Polling based: not suitable for requiring information in real-time in order to react when an event of interest occurs.
  Publish/subscribe interaction model
    A.k.a: Observer Model
    A publisher node can send publications to a subscriber node (observer) about a event that the subscriber is interested in receiving .

## Slide 11: CoAP
  Publish/subscribe interaction model
A subscriber constantly to observe the events by registering its interest in the event (GET request to the publisher node).
Subscription Action:
  Publisher node establishes an observation relationship between the subscriber and the event.
  The publisher notifies each subscriber node that has an observation relationship with the event.
Observer Model:
  High scalability
  Use caches and proxy nodes that multiplex the interest of multiple subscribers in the same event into a single association

## Slide 12: CoAP
Reliability:
  Non-Confirmable (NON) message:
    Correspond to MQTT-S QoS 0
    No ACK to messages
  Confirmable (CON) message:
    Correspond to MQTT-S QoS 1
    ACK messages received
    Fixed RTO
      Random number between and ACK TIMEOUT constant and an ACK TIMEOUT multiplied by ACK-RANDOM-FACTOR
      UnACKed messages within RTO are retransmitted
      RTO is doubled (Exponential back-off mechanism)
    MAX_RETRANSMIT: Maximum retransmission numbers

## Slide 13: CoAP
Publication Discipline:
  “stop and wait” mechanism for the transmission of CON messages. Same with MQTT-S.
  Publication discipline is also needed to handle publication messages generated while the publication message flow is in progress (RTO is active)
Activity:
  Stop the retransmission of old publication message
  Transmit the new publication message with the number of attempts remaining from the old publication message.

## Slide 14: MQTT-S and CoAP
Fixed RTO:
  Too short: give rise to spurious retransmissions, waste bandwidth, energy and computation.
  Too long: lead to slow or late reaction to the loss of packets, increase delay ,decrease PDR.
  Suitable for deployments when RTT is close to the defined RTO value.
  Not suitable for scalability and flexibility features by the publish/subscribe model on WSN.
Adaptive RTO:
  Compute smoothed RTT (SRTT)
    SRTT = (1 - a) x SRTT + a x RTT
  Compute RTO
    RTO = SRTT x K

## Slide 15: Summary of Publication Discipline
Publication discipline has a direct impact on the number of discarded publication messages.
Publisher nodes discard greater number of publication msgs than broker node, because publisher is in charge of publication message generation.
Situation when not receiving ACK:
  Not receive publication message, require retransmission from publisher
  Received publication message, ACK is lost. Result in duplicate publication.
Limitations:
  Goodness of MQTT=S/CoAP publication discipline is beyond the scope
  Decrease in the number of discarded publications also depend on the publication generation rate in addition to adaptive RTO, which is beyond the control of an adaptive RTO.

## Slide 16: Simulation Environment
OMNet
Goal: monitor and control acritical parameters in a warehouse through a WSN deployment.
Devices:
  Publisher nodes
    measure the critical parameters in the warehouse
    One publisher node receives publication messages in a best-effort mode for monitoring process, i.e., MQTT-S QoS 0 / CoAP NON
    Another publisher node receives publication messages in reliable mode for controlling critical parameters, i.e., MQTT-S QoS 1 / CoAP CON
  Broker node:
    Receive periodic signal from publisher nodes
    Refer to the central node in MQTT-S or proxy node for CoAP

## Slide 17: Simulation Environment
Single Hop
  Subscribers and publisher nodes are place at the same distance from the broker to achieve fairness among nodes.
Multiple Hop:
  Publication messages originated in publisher nodes located from more than one hop away are received through the broker node to which the subscriber nodes are connected.
  Broker node subscribes on behalf of its subscriber nodes to another broker node that the publisher node with information of interest connected to.

## Slide 18: Simulation Environment
Other parameters
A confidence interval with probability of 95%
  A given parameter lies within the interval with a probability of 95%

## Slide 19: Performance Metrics
Packet Delivery Ratio (PDR):
  To evaluate the performance of the reliability mechanism of MQTT-S and CoAP, i.e., QoS x, CON/NON.
  PDR =
  Duplicated publication messages are not take into account
Discarded Publications Ratio (DPR):
  To evaluate the impact of the publication discipline in the PDR.
  If DRP increases, PDR will decrease
  DPR =

## Slide 20: Performance Metrics
Retransmitted Publications Ratio:
  To evaluate the effect of the RTO value.
  Good RTO could reduce spurious retransmission.
  RPR =
  Duplicated publication messages are not take into account
Duplicated Publications Ratio:
  Duplicated Publications Ratio =
  In broker and subscriber node with QoS1 (MQTT-S)
  In subscriber node with CON (CoAP)

## Slide 21: SMQTT-S: Subscriber PDR VS # of Publisher Nodes
# of publisher nodes increases, PDR decreases
K increases, PDR increases because spurious retransmissions are reduced
QoS 0 with K =3 has the highest PDR without MAC ACK; QoS 0 with K=2 has the highest PDR with MAC ACK
PDR of QoS 1 is lower than QoS 0 because additional msgs of QoS 1 congest faster
# of Publisher Nodes
Without
MAC ACK
With
MAC ACK
Recovered by MAC ACK before MQTT-S retransmission are activated
Spurious retransmissions as MQTT-S retransmission activated before MAC ACK
Single Hop

## Slide 22: CoAP: Subscriber PDR VS # of Publisher Nodes
# of publisher nodes increases, PDR decreases
K =2 has the highest PDR with/without MAC ACK
MAC ACK is required for NON when # of publisher < 40; CON when # of publisher < 30.
# of Publisher Nodes
Without
MAC ACK
With
MAC ACK
Recovered by MAC ACK before CoAP retransmission are activated
Spurious retransmissions as CoAP retransmission activated before MAC ACK
Single Hop

## Slide 23: Single Hop
SMQTT-S: fixed RTO vs adaptive RTO
PDR with fixed RTO is lower than adaptive RTO, as fixed RTO cause the MQTT-S retransmission to be activated too late to recover the message losses.
QoS 0: PDR increase 64% (20 nodes) and 23% (100 nodes); QoS 1: PDR increase 76% (10 nodes) and 21% (100 nodes);
MAC ACK is not sufficient to recover the message losses.
QoS 0: PDR increase 38% (20 nodes) and 12% (100 nodes); QoS 1: PDR increase 40% (20 nodes) and 10% (100 nodes).
Without
MAC ACK
With
MAC ACK

## Slide 24
CoAP: fixed RTO vs adaptive RTO
Compared with Default fixed RTO
  Without MAC ACK: NON: PDR increase 34% (30 nodes) and 13% (100 nodes) ;CON: PDR increase 38% (30 nodes) and 14% (100 nodes)
  With MAC ACK: CON: PDR increase 38% (30 nodes) and 14% (100 nodes) ;CON: PDR increase 26% (30 nodes) and 4% (100 nodes)
Compared with RFC6298
  Without MAC ACK: NON: PDR increase 5% (50 nodes) and 3% (100 nodes) ;CON: PDR increase 38% (30 nodes) and 14% (100 nodes)
  With MAC ACK: CON: PDR increase 13% (30 nodes) and 1% (100 nodes) ;CON: PDR increase 26% (30 nodes) and 4% (100 nodes)
Without
MAC ACK
With
MAC ACK
Single Hop

## Slide 25: Comparison of RTT and RTO Measurements
MQTT-S
PUB’s RTO is higher than BK RTO after 60 nodes
  More publishers are competing for access to the channel, then collision increases
  The RTO therefore increases as the retransmissions are activated
Higher RTO with MAC ACK is obtained due the use of MAC ACK
# of Publisher Nodes
Without
MAC ACK
With
MAC ACK
Single Hop

## Slide 26: Comparison of RTT and RTO Measurements
CoAP
A change after 60 nodes without MAC ACK
  More publishers are competing for access to the channel, then collision increases
  RTO increases slow because the publication discipline of CoAP results in the cancellation of retransmissions.
A change after 40 nodes with MAC ACK because the MAC ACK causes the network congest faster.
# of Publisher Nodes
Without
MAC ACK
With
MAC ACK
Single Hop

## Slide 27: Discarded Publication Ratio (DPR)
MQTT-S
Publishers discard more msgs than Brokers as Publishers discard the new generated msgs and keep sending old msgs if ACK is not received.
DPR decreases as K increases, except K=4:
  The retransmission of MQTT-S is activated too late to recover publication message, hence resulting higher DPR
Without MAC ACK: K=3 when lowest DPR; With MAC ACK: K=2 when lowest DPR
Without
MAC ACK
With
MAC ACK
Single Hop

## Slide 28: Discarded Publication Ratio (DPR)
CoAP
  As K increases, lower DPR obtained, except K=2
    Why?
  Publisher nodes obtain a lower DPR without MAC ACK than with MAC ACK, as the absence of MAC ACK reduces the delay.
  i.e., when RTO is active, the probability of generating a new publication is also reduced.
Without
MAC ACK
With
MAC ACK
Single Hop

## Slide 29: Retransmitted Publication Ratio
MQTT-S
Lowest retransmitted messages is obtained with K=4 with MAC ACK due to the decrease spurious retransmissions caused by application retransmissions and MAC ACK
However, the retransmissions are activated too late for packet recovery due to a larger RTO when K=4.
Therefore, K=3 is adopted.
Without
MAC ACK
With
MAC ACK
Single Hop

## Slide 30: Retransmitted Publication Ratio
CoAP
Lowest Retransmissions when K =4, but it is not sufficient.
Based on the results from the previous experiments, K=2 is adopted.
Single Hop

## Slide 31: Comparison of MQTT-S with CoAP
Retransmitted msg ratio for CoAP is lower than MQTT-S
Because the publication discipline of CoAP always cancel the old msgs to send the new generated msgs; while MQTT-S always retransmit the old msgs.
MQTT-S
CoAP
Single Hop

## Slide 32: Duplicated Publications Ratio
MQTT-S
Duplicated msgs reduce PDR because of useless data
K increases, number of duplicated messages decreases.
K=4 with MAC ACK reaches the lowest ratio of duplicated msgs.
While K =3 for highest PDR, because MQTT-S react faster when losing msgs and consequently spurious retransmission may be produced
Single Hop

## Slide 33: Duplicated Publications Ratio
CoAP
Similar with MQTT-S. Even though K=4 get the lowest duplicat msgs, K=2 get the highest PDR.
CoAP receive fewer duplicated msgs than MQTT-S because of the publication discipline.
Single Hop

## Slide 34: Single-Hop Extended Scenario
Single Hop Extend
QoS 1

## Slide 35: Single-Hop Extended Scenario
MQTT-S
MQTT-S
CoAP
Without
MAC ACK
With
MAC ACK
Without
MAC ACK
With
MAC ACK
Single Hop Extend
NON
CON

## Slide 36: Single-Hop Extended Scenario
MQTT-S: K=3 reach highest PDR; CoAP: K=2 reach highest PDR;
PDR is lower than in the single-hop scenario because
  The second broker increases the network load and results in packet losses
  Msgs between the broker nodes are sent in QoS 1, which results in more congestion
  Network load with 70 nodes is similar to 100 nodes in single hop scenario, because the second broker node increase traffic. Therefore, the result are showed up to 70 publisher nodes.
MQTT-S: QoS 0 gets higher PDR with MAC ACK; QoS 1 gets highest PDR without MAC ACK. MAC ACK is required when node # < 40;
CoAP: Highest PDR is obtained without MAC ACK;
NON: MAC ACK is required when node # < 40; CON: MAC ACK is required when node # < 30;
Single Hop Extend

## Slide 37: Single-Hop Extended Scenario
Retransmission Publication Ratio decreases as K increases.
  K=4 gets the lower retransmission publication ratio with MAC ACK
  Still adopt K=3 for MQTT-S, K=2 for CoAP, because of the highest PDR.
K increases, energy consumption decreases.
With use of the adaptive RTO of MQTT-S and CoAP consume up to 8% more energy than fixed RTO, which creates a trade-off between energy consumption and the PDR.
Max PDR by CoAP is better than MQTT-S because of the publication discipline. If PDR is the goal, choose CoAP!
Single Hop Extend

## Slide 38: Multi-Hop Scenario
Msgs from a publisher node are routed to the broker node through multiple nodes;
The received msgs by the broker node are routed to the subscriber nodes.

## Slide 39: MQTT-S: PDR vs # of nodes
MQTT-S
The network load with 40 nodes is similar to 100 nodes in single-hop scenario, therefore only obtain the results up to 40 nodes.
2. K=3.5 with MAC ACK gets the highest PDR. The increase in RTT and packet losses, therefore MAC ACK is necessary to recover packets losses.
Multi-Hop Scenario

## Slide 40: CoAP: PDR vs # of nodes
K=2.5 gets the highest PDR without MAC ACK. Because CoAP can react properly without MAC ACK with K=2.5.
The MAC ACK leads to an increase of the message delay.
CoAP
Multi-Hop Scenario

## Slide 41: Summary
Evaluate three scenarios: single-hop, single-hop extended and multi-hop scenarios with parameters of fixed RTO, adaptive RTO, MAC ACK.
Result: the adaptive RTO provides an increase in PDR.
An adaptive RTO method is more suitable in order to react properly to changing network conditions.
MAC ACK is not suitable for the lowest K value, as it may bring high congestion and decrease PDR.
Non-persistent mode CoAP leads to a higher PDR than persistent mode MQTT-S due to the publication disciplines.
Future work: adapt the K value dynamically to the network conditions: duplicated publication ratio, DPR and retransmitted publication ratio.

## Slide 42
Thank You!