## Slide 1: Mapping and Localization with RFID Technology
Matthai Philipose, Kenneth P Fishkin,
Dieter Fox, Dirk Hahnel, Wolfram Burgard
Presenter: Aniket Shah

## Slide 2: Outline
Introduction
Related Work
Probabilistic Sensor Model
Mapping
Localization
Experimental Results
Conclusion

## Slide 3: Introduction
RFID - Radio Frequency Identification; One of the methods of AIDC
Listen to broadcasts from receiver, reply with unique identifier
Paper discusses using RFID technology to enhance localization
Mobile robot equipped with laser scanner and RFID antennas used for experiment
Sensor model to detect tag position (approximate) wrt any one antenna and repeated with antennae on mobile robot
[Fig. 1]
Notes: AIDC - Automatic Identification and Data Capture; includes barcodes, biometrics, OCR, etc

## Slide 4: Introduction
Laser range data provides for map information
Monte Carlo localization used for robot pose estimation
RFID tags help reduce time and number of samples required for global localization
Paper discusses using sensor model for RFID receivers with FastSLAM to localize RFID tags
Suggests the use of these tas to detect positions of robots and people

## Slide 5
Monte Carlo localization
Input - Belief (sample), actuation and sensor data
Update motion and sensor data
Resample and calculate beliefs based on probability

## Slide 6: Related Work
RFID sensors have entered the field of mobile robotics
Low-cost passive tags with long range help in navigation, localization, mapping etc
Active beacons by Kantor and Singh to provide information based on tag response time
Tsukiyama’s system does not deal with uncertainties
SLAM techniques cannot be directly applied for range or bearing or both

## Slide 7: Probabilistic Sensor Model
Localization of tags based on a recursive update rule
x = tag pose, z1:t = data gathered in time t, p(zt | x) =likelihood of observation of zt given x
Considerations while designing observation model:
  false negative readings
  false positive readings
[Eq. 1]
Notes: false negative- no tag when it should be there
false positive- tag which is actually not in range or tag from wrong antenna

## Slide 8: Probabilistic Sensor Model
Reasons for considerations:
  Orientation of tag wrt receiver influences signal energy
  Less energy might not power the chip inside the tag leading to a no-response
  Shape and size of detection range depend on environment
Observation model must cover such situations and ensure minimal errors in localization
Observation model determined by counting frequency of detections of tag wrt antennae on robot
Distance varied between tag and robot to get the map
Notes: environment factors - metals near tags, concrete walls create disturbance, detection due to reflections

## Slide 9
[Fig. 3]
[Fig. 4]
Notes: Fig. 3 - Detection Field for left(pink) and right(yellow) antenna
Fig. 4 - Simplified sensor model for single antenna, arc with range of 95 deg in dir (0.9); circle for close detection(0.7); rest (0.5)

## Slide 10: Mapping
First application of model is to localize tags
Two steps to learn positions:
  Learn geometric structure of environment using laser range sensor
  Estimate tag position based on robot path
Geometrical structure found using FastSLAM algorithm
Use map and maximum likelihood path of robot to locate tags
Apply the recursive Bayesian filtering scheme of Eq. 1
Notes: FastSLAM algo - scan matching combined with particle filtering; scan matching converts laser readings to odometry; lower variance in the corrected odometry reduces the number of necessary resampling steps and this way decreases the particle depletion problem

## Slide 11: Mapping
Pose belief of tag represented by a set of 1000 random positions uniformly distributed in a 25 m2 are around robot’s current pose
Area independent of antenna
Initialization done at first detection of tag by robot
Posterior probability assigned to each tag position corresponding to true pose of tag
Posterior updated on each detection

## Slide 12: Localization
Compute likelihood of observation ‘y’ during localization knowing the posterior distributions of tag positions and given robot/person at position ‘l’
r(x,l) = position of tag relative to robot given pose ‘l’ of robot and location of tag sample ‘x’, p(y | r(x,l)) = sensor model description
[Eq. 2]

## Slide 13: Localization
recursive Bayesian filtering scheme:
α = normalization constant, p(lt |ut-1, l’t-1) = probability of object to be at lt give it executed movement ut-1 at position l’t-1
Notes: Bayesian filtering done to estimate robot/person pose

## Slide 14: Localization
In Monte Carlo localization, belief of robot is a set of random samples
Each sample consists of state vector which is pose of robot and weight factor ‘w’
Weight factor provides importance of particle
Beliefs updated on two alternating steps:
  In prediction step, new sample for each sample based on weight and model probability of robot’s dynamics since previous update
  In correction step, new observation is integrated into sample set by bootstrap resampling
For RFID sensors, samples placed on in potential detection range of sensor
Notes: bootstrap resampling - each sample weighed according to observation likelihood

## Slide 15: Experimental Results
Implementation and Testing done using Pioneer 2 robot with SICK LMS laser range-finder and Alien Technology’s 915 MHz RFID reader with two circularly polarized antennas
[Fig. 2]

## Slide 16
[Fig. 6]
[Fig. 7]
Notes: Fig. 6 - 100 tags used similar to the ones shown in Fig. 1 middle
Fig. 5 - Map of Intel Research Lab Seattle using FastSLAM

## Slide 17: Experimental Results
Mapping RFID tags
  Trajectory estimation by FastSLAM to determine posterior of toag location
  On first detection, initialize random points around robot and use uniform distribution for belief
  On tag detection, update posterior probability based on likelihood of observation
  Normalize belief over all samples
[Fig. 7]
Notes: Fig. 7 - Evolution of posterior about localization of tag over time; width of circle represents probability of position; beliefs shown after 6, 17, 65 and 200 measurements

## Slide 18: Experimental Results
Mapping RFID tags
  Representation can handle ambiguities in which location of tag can’t be determined uniquely
  Algorithm can accurately localize tags
  There is noise and a several false detections
  Learn position of multiple tags in environments
[Fig. 10]

## Slide 19: Experimental Results
Localization with RFID tags
  Robot steered through environment and Monte Carlo localization applied to globally estimate position
  Person localization done by ignoring odometry data and changing motion model in Monte Carlo localization
  Motion model of robot replaced by Gaussian distribution centered around current pose of robot to approximate motion of person
[Fig. 9]

## Slide 20: Experimental Results
Improving Global Localization with RFID tags
  RFID technology can be used to improve global localization even when highly accurate sensors are used
  Use of RFID sensors reduce the number of samples required
  Motion model of robot replaced by Gaussian distribution centered around current pose of robot to approximate motion of person
[Fig. 11]
[Fig. 12]

## Slide 21: Conclusion
Generated maps of RFID tags with mobile robots
Sensor model to compute likelihood of tag detections
Use of posteriors to localize robot/people
Showed that maps can be used to localize robots without odometry data
Reduce computational demands for localization by using RFID technology with laset scanners

## Slide 22: Opinion
Good paper providing proof of concept with good experimental results
Well documented; makes it easier to re-perform and compare results
Could have explained certain algorithms and math in detail
As a panelist, I would accept this paper

## Slide 23: Questions?