## Slide 1: Routing Primer
Internet of Things
Fall 2015

## Slide 2: Routing Outline
Overview of Point-to-Point Routing (WAN)
Routing Algorithm Classification
Distance Vector Routing
Link State Routing
RIP
OSPF
BGP

## Slide 3: Metropolitan Area Network (MAN)
R
R
R
R
S
S
S
s
s
s
s
s
s
s
s
s
s
R
s
R
Backbone
To the Internet or wide area network
Organization Servers
Gateway
Departmental Server
Leon-Garcia & Widjaja:
Communication Networks

## Slide 4: Wide Area Network (WAN)
Interdomain level
Intradomain level
LAN level
Autonomous system
or domain
Border routers
Border routers
Internet service provider
Leon-Garcia & Widjaja:
Communication Networks

## Slide 5: Modern Internet Backbone
National service provider A
National service provider B
National service provider C
NAP
NAP
National Internet Service Providers
Network Access
Point
Leon-Garcia & Widjaja:
Communication Networks

## Slide 6: Network Layer
transport segment from sending to receiving host.
on sending side, encapsulates segments into datagram packets.
on receiving side, delivers segments to transport layer.
network layer protocols in every host, router.
router examines header fields in all IP datagrams passing through it.
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
K & R

## Slide 7: Two Key Network Layer Functions
forwarding: move packets from router’s input to appropriate router output.
routing: determine route taken by packets from source to destination.
analogy:
routing: process of planning trip from source to destination
forwarding: process of getting through single interchange

## Slide 8: Interplay between Routing and Forwarding
1
2
3
0111
value in arriving
packet’s header
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
K & R
Routing creates the tables.
Forwarding uses the tables.

## Slide 9: Router Node Forwarding
packet
node 15
17
Outgoing Link
Router Link Buffer
Server
packet
Incoming Link
Routing table
lookup
134 17

## Slide 10: The Internet Network Layer
forwarding
table
Host, router network layer functions:
Routing protocols
path selection
RIP, OSPF, BGP
IP protocol
addressing conventions
datagram format
packet handling conventions
ICMP protocol
error reporting
router “signaling”
Transport Layer: TCP, UDP
Data Link Layer
Physical Layer
Network
Layer

## Slide 11: Routing Algorithm Classification
Internet of Things

## Slide 12: Routing
Routing algorithm:: that part of the Network Layer responsible for deciding on which output line to transmit an incoming packet.
Remember: For virtual circuit subnets the routing decision is made ONLY at set up.
Algorithm properties:: correctness, simplicity, robustness, stability, fairness, optimality, and scalability.

## Slide 13
Figure 3.28 Network represented as a graph.
Routing is Graph Theory Problem
edges have costs

## Slide 14: Routing Classification
Adaptive Routing
based on current measurements
of traffic and/or topology.
1. centralized
2. isolated
3. distributed
Non-Adaptive Routing
routing computed in advance and off-line
1. flooding
2. static routing using shortest path algorithms

## Slide 15: Flooding
Pure flooding :: every incoming packet to a node is sent out on every outgoing line.
  Obvious adjustment – do not send out on arriving link (assuming full-duplex links).
  The routing algorithm can use a hop counter (e.g., TTL) to dampen the flooding.
  Selective flooding :: only send on those lines going “approximately” in the right direction.

## Slide 16: Centralized Routing
RCC
A
Z
W
B

## Slide 17: Internetwork Routing [Halsall]
Adaptive Routing
Centralized
Distributed
Intradomain routing
Interdomain routing
Distance Vector routing
Link State routing
[IGP]
[EGP]
[BGP,IDRP]
[OSPF,IS-IS,PNNI]
[RIP]
[RCC]
Interior
Gateway Protocols
Exterior
Gateway Protocols
Isolated

## Slide 18: Adaptive Routing Design
Design Issues:
How much overhead is incurred due to gathering the routing information and sending routing packets?
What is the time frame (i.e, the frequency) for sending routing packets in support of adaptive routing?
What is the complexity of the routing strategy?

## Slide 19: Adaptive Routing
Basic functions:
1. Measurement of pertinent network data {e.g. the cost metric}.
2. Forwarding of information to where the routing computation will be done.
3. Compute the routing tables.
4. Convert the routing table information into a routing decision and then dispatch the data packet.

## Slide 20: Shortest Path Routing
1. Bellman-Ford Algorithm [Distance Vector]
2. Dijkstra’s Algorithm [Link State]
What does it mean to be the shortest (or optimal) route?
We need a cost metric (edges in graph):
a. Minimize the number of hops along the path.
b. Minimize the mean packet delay.
c. Maximize the network throughput.

## Slide 21: Distance Vector Routing {Tanenbaum & Perlman version}
Internet of Things

## Slide 22: Distance Vector Routing
Historically known as the old ARPANET routing algorithm {or known as Bellman-Ford (BF) algorithm}.
BF Basic idea: each router maintains a Distance Vector table containing the distance between itself and ALL possible destination nodes.
Distances,based on a chosen metric, are computed using information from the neighbors’ distance vectors.
Distance Metric: usually hops or delay

## Slide 23: Distance Vector Routing
Information kept by DV router
each router has an ID
associated with each link connected to a router, there is a link cost (static or dynamic).
Distance Vector Table Initialization
Distance to itself = 0
Distance to ALL other routers = infinity number

## Slide 24: Distance Vector Algorithm [Perlman]
1. A router transmits its distance vector to each of its neighbors in a routing packet.
2. Each router receives and saves the most recently received distance vector from each of its neighbors.
3. A router recalculates its distance vector when:
  It receives a distance vector from a neighbor containing different information than before.
  It discovers that a link to a neighbor has gone down (i.e., a topology change).
The DV calculation is based on minimizing the cost to each destination.

## Slide 25: Distance Vector Example
Tanenbaum
Figure 5-9.(a) A subnet. (b) Input from A, I, H, K, and the new routing table for J.

## Slide 26: Distance Vector Routing {Kurose & Ross version}
Internet of Things

## Slide 27: Distance Vector Algorithm
Bellman-Ford Equation (dynamic programming)
Define
dx(y) := cost of least-cost path from x to y
Then
dx(y) = min {c(x,v) + dv (y)}
where min is taken over all neighbors v of x.
v

## Slide 28: Bellman-Ford Example
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
Clearly, dv(z) = 5, dx(z) = 3, dw(z) = 3
du(z) = min { c(u,v) + dv(z),
c(u,x) + dx(z),
c(u,w) + dw(z) }
= min {2 + 5,
1 + 3,
5 + 3} = 4
The node that achieves minimum is next
hop in shortest path ➜ forwarding table.
Namely, packets from u destined for z are
forwarded out link between u and x.
B-F equation says:

## Slide 29: Distance Vector Algorithm
Dx(y) = estimate of least cost from x to y
Node x knows cost to each neighbor v: c(x,v)
Node x maintains distance vector
Dx = [Dx(y): y є N ]
Node x also maintains its neighbors’ distance vectors
  For each neighbor v, x maintains Dv = [Dv(y): y є N ]

## Slide 30: Distance Vector Algorithm
DV Basic idea:
From time-to-time, each node sends its own distance vector estimate to neighbors.
Asynchronous
When a node x receives a new DV estimate from any neighbor v, it saves v’s distance vector and it updates its own DV using B-F equation:
Dx(y) ← minv{c(x,v) + Dv(y)} for each node y ∊ N
Under minor, natural conditions, the estimate Dx(y) converges to the actual least cost dx(y).

## Slide 31: Distance Vector Algorithm
Iterative, asynchronous: each local iteration caused by:
local link cost change
DV update message from neighbor
Distributed:
each node notifies neighbors only when its DV changes
  neighbors then notify their neighbors if necessary.
wait for (change in local link cost or msg from neighbor)
recompute estimates
if DV to any destination has changed, notify neighbors
Each node:

## Slide 32
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0
from
cost to
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
∞
∞
7
1
0
cost to
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
time
x
z
1
2
7
y
node x table
node y table
node z table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
3
2
∞
∞

## Slide 33
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
∞
∞
7
1
0
cost to
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
2 0 1
7 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
time
x
z
1
2
7
y
node x table
node y table
node z table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
∞
∞
∞

## Slide 34: Distance Vector: Link Cost Changes
Link cost changes:
node detects local link cost change.
updates routing info, recalculates distance vector.
if DV changes, it notifies neighbors .
At time t0, y detects the link-cost change, updates its DV, and informs its neighbors.
“good
news
travels
fast”
At time t1, z receives the update from y and updates its table.
It computes a new least cost to x and sends its neighbors its DV.
At time t2, y receives z’s update and updates its distance table.
y’s least costs do not change and hence y does not send any
message to z.
x
z
1
4
50
y
1

## Slide 35
Link cost changes:
good news travels fast
bad news travels slow - “count to
infinity” problem!
44 iterations before algorithm
stabilizes: see P&D page 248!
Does this solve count to infinity problem?
x
z
1
4
50
y
60
Distance Vector: Link Cost Changes
Possible solutions:
Keep ‘infinity ‘ small {depends on graph diameter}.
Split Horizon: node does not send those routes learned from a neighbor back to that neighbor.
Split Horizon with Poison Reverse:
  If z routes through y to get to x, z tells y its (z’s) distance to x is infinite (so y won’t route to x via z).

## Slide 36: Link State Algorithm
1. Each router is responsible for meeting its neighbors and learning their names.
2. Each router constructs a link state packet (LSP) which consists of a list of names and cost to reach each of its neighbors.
3. The LSP is transmitted to ALL other routers. Each router stores the most recently generated LSP from each other router.
4. Each router uses complete information on the network topology to compute the shortest path route to each destination node.

## Slide 37: Figure 4.18 Reliable LSP Flooding
P&D slide
Reliable Flooding

## Slide 38
Reliable Flooding
The process of making sure all the nodes participating in the routing protocol get a copy of the link-state information from all the other nodes.
LSP contains:
  Sending router’s node ID
  List of connected neighbors with the associated link cost to each neighbor
  Sequence number
  Time-to-live (TTL) {an aging mechanism}

## Slide 39
First two items enable route calculation.
Last two items make process reliable
  ACKs and checking for duplicates is needed.
Periodic Hello packets used to determine the demise of a neighbor.
The sequence numbers are not expected to wrap around.
  this field needs to be large (64 bits) !!
Reliable Flooding

## Slide 40: A Link-State Routing Algorithm
Dijkstra’s algorithm
net topology, link costs known to all nodes
  accomplished via “link state broadcast”.
  all nodes have same info.
computes least cost paths from one node (‘source”) to all other nodes
  gives forwarding table for that node.
iterative: after k iterations, know least cost path to k destinations.
Notation:
c(x,y): link cost from node x to y; = ∞ if not direct neighbors.
D(v): current value of cost of path from source to destination v
p(v): predecessor node along path from source to v
N': set of nodes whose least cost path is definitively known.
K & R

## Slide 41: Dijsktra’s Shortest Path Algorithm
1 Initialization:
2 N' = {u}
3 for all nodes v
4 if v adjacent to u
5 then D(v) = c(u,v)
6 else D(v) = ∞
7
8 Loop
9 find w not in N' such that D(w) is a minimum
10 add w to N'
11 update D(v) for all v adjacent to w and not in N' :
12 D(v) = min( D(v), D(w) + c(w,v) )
13 /* new cost to v is either old cost to v or known
14 shortest path cost to w plus cost from w to v */
15 until all nodes in N'
[K&R]

## Slide 42: Dijkstra’s Algorithm: Example
Step
0
1
2
3
4
5
N'
u
ux
uxy
uxyv
uxyvw
uxyvwz
D(v),p(v)
2,u
2,u
2,u
D(w),p(w)
5,u
4,x
3,y
3,y
D(x),p(x)
1,u
D(y),p(y)
∞
2,x
D(z),p(z)
∞
∞
4,y
4,y
4,y
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5

## Slide 43: Dijkstra’s Algorithm: Example (2)
u
y
x
w
v
z
Resulting shortest-path tree from u:
v
x
y
w
z
(u,v)
(u,x)
(u,x)
(u,x)
(u,x)
destination
link
Resulting forwarding table in u:

## Slide 44: Dijkstra’s Algorithm, Discussion
Algorithm complexity: n nodes
each iteration: need to check all nodes, w, not in N
n(n+1)/2 comparisons: O(n2)
more efficient implementations possible: O(nlogn)
Oscillations possible:
e.g., link cost = amount of carried traffic
A
D
C
B
1
1+e
e
0
e
1
1
0
0
A
D
C
B
2+e
0
0
0
1+e
1
A
D
C
B
0
2+e
1+e
1
0
0
A
D
C
B
2+e
0
e
0
1+e
1
initially
… recompute
routing
… recompute
… recompute

## Slide 45: Intra-AS Routing
also known as Interior Gateway Protocols (IGP)
most common Intra-AS routing protocols:
  RIP: Routing Information Protocol
  OSPF: Open Shortest Path First
  IGRP: Interior Gateway Routing Protocol (Cisco proprietary)

## Slide 46: Routing Information Protocol (RIP)
RIP had widespread use because it was distributed with BSD Unix in “routed”, a router management daemon in 1982.
RIP - most used Distance Vector protocol.
RFC1058 in June 1988
Runs over UDP.
Metric = hop count
BIG problem is max. hop count =16
 RIP limited to running on small networks (or AS’s that have a small diameter)!!

## Slide 47: Routing Information Protocol (RIP)
Sends DV packets every 30 seconds (or faster) as Response Messages (also called advertisements).
each advertisement: list of up to 25 destination subnets within AS.
Upgraded to RIPv2
D
C
B
A
u
v
w
x
y
z
destination hops
u 1
v 2
w 2
x 3
y 3
z 2
From router A to subnets:

## Slide 48: Figure 4.17 RIP Packet Format
(network_address,
distance)
pairs
P&D slide
RIP Packets

## Slide 49: RIPv2
Allows routing on a subnet (subnet masks)
Has an authentication mechanism
Tries to deal with multicast
Uses route tags
Has the ability for router to announce routes on behalf of another router.

## Slide 50
Figure 3.31 RIPv2 Packet Format
RIPv2 Packets
subnet masks

## Slide 51: OSPF (Open Shortest Path First)
“open” :: publicly available (due to IETF)
uses Link State algorithm
  LS packet dissemination
  topology map at each node
  route computation uses Dijkstra’s algorithm.
OSPF advertisement carries one entry per neighbor router.
advertisements disseminated to entire AS (via flooding*).
  carried in OSPF messages directly over IP (rather than TCP or UDP).
* However hierarchy (partitioning domains into areas) reduces flooding impact.

## Slide 52: OSPF “Advanced” Features (not in RIP)
security: all OSPF messages authenticated (to prevent malicious intrusion).
multiple same-cost paths allowed (only one path in RIP).
For each link, multiple cost metrics for different TOS (e.g., satellite link cost set “low” for best effort; high for real time).
integrated uni- and multicast support:
  Multicast OSPF (MOSPF) uses same topology data base as OSPF.
hierarchical OSPF used in large domains.

## Slide 53
Figure 4.2 A domain divided into areas
Partitioning Domains

## Slide 54: Hierarchical OSPF

## Slide 55: Hierarchical OSPF
Two-Level Hierarchy: local area, backbone.
  Link-State Advertisements (LSAs) only in area
  each node has detailed area topology; only knows direction (shortest path) to nets in other areas.
area border routers: “summarize” distances to nets in own area, advertise to other Area Border routers.
backbone routers: run OSPF routing limited to backbone.
boundary routers: connect to other AS’s.

## Slide 56: OSPF LSA Types
1. Router link advertisement [Hello message]
2. Network link advertisement
3. Network summary link advertisement
4. AS border router’s summary link advertisement
5. AS external link advertisement

## Slide 57: OSPF
Figure 5-65.The relation between AS’s, backbones, and areas in OSPF
Tanenbaum

## Slide 58: Internet Inter-AS routing: BGP
BGP (Border Gateway Protocol): the de facto standard
BGP provides each AS a means to:
  Obtain subnet reachability information from neighboring ASs.
  Propagate reachability information to all AS-internal routers.
  Determine “good” routes to subnets based on reachability information and policy.
allows subnet to advertise its existence to rest of Internet: “I am here!”

## Slide 59: Routing Primer Summary
Routers forward and route over WANs
  Produce look up tables in routers
Routing Classification:
  Adaptive or non-adaptive
  Interdomain and Intradomain
Distance Vector Routing (DV)
  Perlman version
  Tanenbaum example
  K&R version

## Slide 60: Routing Primer Summary
Link State Routing (LS)
  Uses reliable flooding; Dijkstra’s SP algorithm
RIP
  Old ARPA routing; unicast DV routing
OSPF
  Two-Level Hierarchical LS routing
  Five LSA types for router communication
BGP
  Interdomain routing using reachability