## Slide 1: QoS Performance Analysis for CSMA/CA in IEEE802.15.5 Yon Lan, Bo Zhang and Zhicheng Chen Journal of Networks July 2014
Presenter: Bob Kinicki
Internet of Things
Fall 2015

## Slide 2: Introduction
Authors argue that slotted CSMA/CA is particularly suited for WSNs where traffic is discrete or non-cyclical.
Focus is on beacon-enabled mode for IEEE802.15.4.
QoS is used constantly in this paper but the authors’ simulated application is mathematically-based with no real intuitive notion of QoS discussed.

## Slide 3: IEEE 802.15.4 Frame Format
Low Bandwidth (250 kbps), low power (1 mW) radio
Moderately spread spectrum (QPSK) provides robustness
Simple MAC allows for general use
  Many TinyOS-based protocols (MintRoute, LQI, BVR, …), TinyAODV, Zigbee, SP100.11, Wireless HART, …
  6LoWPAN => IP
Choice among many semiconductor suppliers
Small packets used to keep packet error rate low and permit media sharing.
preamble
SFD
Len
FCF
DSN
Dst16
Src16
D pan
Dst EUID 64
S pan
Src EUID 64
Fchk
Network Header
Application Data
Max 127 bytes
Culler slide

## Slide 4: Outline
Introduction
Beacon-Enabled IEEE802.15.4 and Superframe Structure
Simulation Methodology
Analysis of Simulation Results
Conclusion
Critique

## Slide 5: Beacon-Enabled IEEE802.15.4
In beacon-enabled mode, communication behavior is constrained by superframe structure which is synchronized when coordinator periodically sends beacon frames.
Each sensor node’s communication process happens in the allocated slot time.

## Slide 6: Figure 1: 802.15.4 Superframe

## Slide 7: Beacon Interval (BI) and Superframe Duration (SD)
BI is defined by BO (Beacon Order).
SD is defined by SO (Superframe Order).

## Slide 8: Duty Cycle (DC)
Duty cycle of beacon-enabled 802.15.4 is defined as:
Example: BO-SO = 2
DC = 2-2 = ¼ = 25%

## Slide 9: Sleep Time (ST)
For each BI, the inactive period is the node sleeping time (ST) which can be calculated as:
Hence ST is affected by the value of BO and duty cycle (i.e., BO-SO)

## Slide 10: Three “What if” observations
1. BO fixed; BO-SO grows:
- ST grows and DC decreases
- E down, D up, O down
2. BO-SO fixed; BO grows:
- ST grows
- E down, D up, O down
3. BO fixed; as BO-SO increases from 0 to 14, change in ST decreases.

## Slide 11: Simulation Settings
10 m x 10 m simulated area, 2.4 GHz, 250 kbps, 600 sec. duration using OPNET
Sensors deployed randomly to create star-topology. {This is very unclear!}
Power set at 1 mW, QPSK used.
No explanation of application traffic model:

## Slide 12: Figure 2: OPNET Simulation

## Slide 13: Figure 3: 10 Node Simulation
Small
duty cycle
Large
delay

## Slide 14: Figure 4: 30 Node Simulation
Larger
delay

## Slide 15: Figure 5: 50 Node Simulation

## Slide 16: Simulations Varying BO
Authors want to study first “what if”:
- BO fixed; BO-SO varies
Fix the number of devices at 14. {Appears to minimize slot collisions!}
400 seconds simulated time.
Use Table II for traffic sources.

## Slide 17: Table II
Why this traffic?

## Slide 18: Figure 6: Energy vs BO
Best
performance

## Slide 19: Figure 7: Output Load vs BO

## Slide 20: Figure 8: Delay vs BO
Best
performance

## Slide 21: Conclusions
Basically authors argue this presentation lets one see the tradeoffs in setting for beacon-enabled, slotted CSMA/CA for IEEE802.15.4

## Slide 22: Critique
No justification or explanation of traffic sources.
They use QoS inappropriately – end-to-end delay never defined.
No discussion of traffic routes.
No sense of slotted collisions and no formal assignment to slots.
Why only star-topology?