## Slide 1: Introduction to Physical Layer
Computer Networks
Term B10

## Slide 2: Physical Layer Outline
Definitions
Multiplexing
Transmission Media
End System Choices
Residential Configurations

## Slide 3: Physical Layer Definitions
The time required to transmit a character depends on both the encoding method and the signaling speed (i.e., the modulation rate - the number of times/sec the signal changes its voltage).
baud (D) - the number of changes per second.
bandwidth (H) - the range of frequencies that is passed by a channel. The transmitted signal is constrained by the transmitter and the nature of the transmission medium in cycles/sec (hertz).
channel capacity (C) – the rate at which data can be transmitted over a given channel under given conditions.{This is also referred to as data rate (R).}

## Slide 4: Modulation Rate
DCC 6th Ed.
Stallings
modulation rate
is doubled

## Slide 5: Analog and Digital Signaling
signals:: electric or electromagnetic encoding of data.
signaling:: is the act of propagating the signal along a suitable medium.
  Analog signal – a continuously varying electromagnetic wave that may be propagated over a variety of medium depending on the spectrum (e.g., wire, twisted pair, coaxial cable, fiber optic cable and atmosphere or space propagation).

## Slide 6: Analog and Digital Signaling
digital signal – a sequence of voltage pulses that may be transmitted over a wire medium.
Note – analog signals to represent analog data and digital signals to represent digital data are not the only possibilities.
There is where modems and codecs come into the picture.

## Slide 7: Analog vs Digital (three contexts)
DCC 6th Ed.
Stallings
modem
codec

## Slide 8: Multiplexing
MUX
MUX
(a)
(b)
Trunk
group
A
A
A
A
B
B
B
B
C
C
C
C
Leon-Garcia & Widjaja:
Communication Networks
Multiplexing {general definition} ::
Sharing a resource over time.

## Slide 9: Frequency Division Multiplexing (FDM) vs Time Division Multiplexing (TDM)
FDM
frequency
time
TDM
frequency
time
4 users
Example:
K & R
Notes: Two simple multiple access control techniques.
Each mobile’s share of the bandwidth is divided into portions for the uplink and the downlink. Also, possibly, out of band signaling.
As we will see, used in AMPS, GSM, IS-54/136

## Slide 10: Frequency Division Multiplexing
Figure 2-31. (a) The original bandwidths. (b) The bandwidths raised in frequency. (c) The multiplexed channel.
Tanenbaum

## Slide 11: T1 - TDM Link
TDM: each host gets same slot in revolving TDM frame
Figure 2-33.T1 Carrier (1.544Mbps)
Tanenbaum
TDM:: each host gets a fixed slot in revolving TDM frame

## Slide 12: Concentrator [Statistical Multiplexing]

## Slide 13: Packet Switching: Statistical Multiplexing
Sequence of A & B packets does NOT have fixed pattern, bandwidth shared on demand  statistical multiplexing.
.
A
B
C
100 Mb/s
Ethernet
1.5 Mb/s
D
E
statistical multiplexing
queue of packets
waiting for output
link

## Slide 14: Wavelength Division Multiplexing
Wavelength division multiplexing.
Figure 2-32.
Tanenbaum

## Slide 15: Physical Media: Twisted Pair
Bit: propagates between transmitter/receiver pairs.
physical link: what lies between transmitter & receiver.
guided media:
  signals propagate in solid media: copper, fiber, coax.
unguided media:
  signals propagate freely, e.g., radio.
Unshielded Twisted Pair (UTP)
two insulated copper wires
  Category 3: traditional phone wires, 10 Mbps Ethernet
  Category 5 : 100Mbps Ethernet
Category 5e is now standard!!

## Slide 16: Physical Media: Coaxial Cable and Optical Fiber
Coaxial cable:
two concentric copper conductors
bidirectional
baseband:
  single channel on cable
  legacy Ethernet
broadband:
  multiple channels on cable
  HFC
Fiber optic cable:
glass fiber carrying light pulses, each pulse a bit
high-speed operation:
  point-to-point transmission (e.g., 10’s-100’s Gps)
low error rate: repeaters spaced far apart ; immune to electromagnetic noise.

## Slide 17: Physical Media: Radio Signals
signal carried in electromagnetic spectrum.
no physical “wire”
bidirectional
propagation environment effects:
  reflection
  obstruction by objects
  interference
Radio link types:
terrestrial microwave
  e.g. up to 45 Mbps channels
LAN (e.g., Wifi)
  11Mbps, 54 Mbps
wide-area (e.g., cellular)
  3G cellular: ~ 1 Mbps
satellite
  Kbps to 45Mbps channel (or multiple smaller channels)
  270 msec end-end delay
  geosynchronous versus low altitude

## Slide 18: Dial-up Modem
telephone
network
Internet
home dial-up
modem
ISP modem
(e.g., AOL)
home
PC
central office
Uses existing telephony infrastructure.
Home is connected to central office (analog signals).
up to 56Kbps direct access to router (often less)
Can’t surf and phone at same time: not “always on”.

## Slide 19: Digital Subscriber Line (ADSL)
telephone
network
DSL
modem
home
PC
home
phone
Internet
DSLAM
Existing phone line: 0-4KHz phone; 4-50KHz upstream data; 50KHz-1MHz downstream data
splitter
central
office
  Uses existing telephone infrastructure.
  up to 1 Mbps upstream (today typically < 256 kbps)
  up to 8 Mbps downstream (today typically < 1 Mbps)
  dedicated physical line to telephone central office
Asymmetric DSL

## Slide 20: Residential Access: Cable Modems
Does not use telephone infrastructure
  Instead uses cable TV infrastructure.
HFC: hybrid fiber coax
  asymmetric: up to 30Mbps downstream, 2 Mbps upstream
network of cable and fiber attaches homes to ISP router:
  homes share access to router
  unlike DSL, which has dedicated access.

## Slide 21: Residential Access: Cable Modems
Diagram: http://www.cabledatacomnews.com/cmic/diagram.html

## Slide 22: Cable Network Architecture: Overview
home
cable headend
cable distribution
network (simplified)
Typically 500 to 5,000 homes

## Slide 23: Cable Network Architecture: Overview
home
cable headend
cable distribution
network
server(s)

## Slide 24: Cable Network Architecture: Overview
home
cable headend
cable distribution
network (simplified)

## Slide 25: Cable Network Architecture: Overview
home
cable headend
cable distribution
network
Channels
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
D
A
T
A
D
A
T
A
C
O
N
T
R
O
L
1
2
3
4
5
6
7
8
9
FDM

## Slide 26: Fiber to the Home
OLT
central office
optical
splitter
ONT
optical fiber
optical fibers
Internet
Optical links from central office to the home
Two competing optical technologies:
  Passive Optical network (PON)
  Active Optical Network (AON)
Higher Internet rates. Fiber also carries television and phone services.
ONT
ONT

## Slide 27: Ethernet Internet Access
100 Mbps
100 Mbps
100 Mbps
1 Gbps
server
Ethernet
switch
Institutional
router
To Institution’s ISP
Typically used in companies, universities, etc
  10 Mbs, 100Mbps, 1Gbps, 10Gbps Ethernet
  Today, end systems typically connect into Ethernet switch.

## Slide 28: Wireless Access Networks
Shared wireless access network connects end system to router
  via base station aka “access point”.
Wireless LANs:
  802.11b/g/n (WiFi): 11, 54, 200 Mbps
Wider-area Wireless Access
  provided by telco operator
  ~1Mbps over cellular system (EVDO, HSDPA) 3G and 4G coming
  next up (?): WiMAX (10’s Mbps) over wide area
base
station
mobile
hosts
router

## Slide 29: Residential Networks
Typical Residential Network Components:
DSL or cable modem
router/firewall/NAT
Ethernet
wireless access point (AP)
wireless
access
point
wireless
laptops
router/
firewall
cable
modem
to/from
cable
headend
Ethernet

## Slide 30: Physical Layer Summary
Definitions (analog versus digital)
Multiplexing (FDM, TDM, statistical)
Transmission Media (UTP, Coax, Fiber, Radio, Satellite)
End System Choices (Dial-Up, ADSL, Cable,Ethernet, Wireless AP, Fiber-to-the Home)
Residential Configurations