## Slide 1: Cellular and Mobile Wireless Networks (part 2)
Advanced Computer Networks

## Slide 2: Cellular/Mobile Wireless Outline
Cellular Architecture
Cellular Standards
  GSM, 2G, 2.5G, 3G and 4G LTE
Mobile Definitions
  Agents, addresses, correspondent
Mobile Architecture
  Registering
  Indirect Routing
  Direct Routing

## Slide 3
Mobile
Switching
Center
Public telephone
network, and
Internet
Mobile
Switching
Center
Cellular Network Architecture
connects cells to wide area net
manages call setup
handles mobility
MSC
covers geographical region
base station (BS) analogous to 802.11 AP
mobile users attach to network through BS
air-interface: physical and link layer protocol between mobile and BS
cell
wired network

## Slide 4: Cellular Networks: The First Hop
Two techniques for sharing mobile-to-BS radio spectrum:
combined FDM/TDM: divide spectrum in frequency channels, divide each channel into time slots.
CDMA: Code Division Multiple Access
Global System for Mobile Communications (GSM):
  200 kHz frequency bands
  Each band supports 8 TDM calls.
  Speech encoded at 12.2 and 13 kbps.
frequency
bands
time slots

## Slide 5: Cellular Standards: Brief Survey
2G Systems: voice channels/digital technology
IS-136 TDMA: combined FDM/TDM (North America)
GSM (Global System for Mobile Communications): combined FDM/TDM
  most widely deployed **
IS-95 CDMA: Code Division Multiple Access
IS-136
GSM
IS-95
GPRS
EDGE
CDMA-2000
UMTS
TDMA/FDMA
Don’t drown in a bowl
of alphabet soup: use this
for reference only

## Slide 6
BSC
BTS
Base transceiver station (BTS)
Base station controller (BSC)
Mobile Switching Center (MSC)
Mobile subscribers
Base station system (BSS)
Legend
2G Network Architecture
MSC
Public
telephone
network
Gateway
MSC
G
2G: Voice Connections to the
Telephone Company

## Slide 7: Cellular Standards: Brief Survey
2.5G systems: voice and data channels
{For those who could not wait for 3G service}
Provide 2G extensions:
General Packet Radio Service (GPRS)
  evolved from GSM.
  data sent dynamically on multiple channels (if available).
  Data rates up to 115 Kbps.
Enhanced Data Rates for Global Evolution (EDGE)
  also evolved from GSM, using enhanced modulation
  data rates up to 384 Kbps.
CDMA-2000 (phase 1)
  data rates up to 144 Kbps.
  evolved from IS-95.
push came from Iphone users

## Slide 8
2.5G Network Architecture
BSC
MSC
SGSN
Public
telephone
network
Gateway
MSC
G
Serving GPRS Support Node (SGSN)
Gateway GPRS Support Node (GGSN)
Public
Internet
GGSN
G
2.5G Voice-Data Network
Key insight: new cellular data
network operates in parallel
(except at edge) with existing
cellular voice network.
voice network is unchanged in core.
data network operates in parallel.

## Slide 9
3G (Voice+Data) Network Architecture
radio
network
controller
MSC
SGSN
Public
telephone
network
Gateway
MSC
G
Serving GPRS Support Node (SGSN)
Gateway GPRS Support Node (GGSN)
Public
Internet
GGSN
G
Key insight: new cellular data
network operates in parallel
(except at edge) with existing
cellular voice network
voice network unchanged in core
data network operates in parallel

## Slide 10
radio
network
controller
MSC
SGSN
Public
telephone
network
Gateway
MSC
G
Public
Internet
GGSN
G
radio access network
Universal Terrestrial Radio
Access Network (UTRAN)
core network
General Packet Radio Service
(GPRS) Core Network
public
Internet
radio interface
(WCDMA, HSPA)
3G (Voice+Data) Network Architecture

## Slide 11: 3G Cellular - Brief Overview
3G systems: voice/data with digital technology
- higher data rates than 2.5G
Universal Mobile Telecommunications Service (UMTS)
  Leaves the existing 2.5G system in place.
  data service: High Speed Uplink/Downlink Packet Access (HSDPA/HSUPA) up to 14 Mbps.
CDMA-2000: CDMA in TDMA slots
  data service: 1xEVolution Data Optimized (1xEVDO) up to 14 Mbps
    1.67 ms slots
    Wireless AT sends DRC back to BS to adjust sending rate
    Proportional Fair Scheduler
    Uses ‘turbo code’ FEC on multiple slots with ‘early completion’.
Many K&R details later in chapter not covered!!

## Slide 12: 3GPP LTE (Long Term Evolution)
4G LTE == 3GPP LTE
Uses OFDM on downlink in cellular space. Uplink is SC-FDMA (Singular Carrier).
Has a CP (cyclic prefix) to avoid symbol distortion over a ‘slot’.
LTE frames (10 msec) are divided into 10 1msec subframes which in turn are divided into 2 two slots (0.5 msec).
Slots consist of 6 or 7 OFDM symbols.

## Slide 13: 3GPP LTE (Long Term Evolution)
OFDMA allocates a PRB (Physical Resource Block) to users. A PRB consists of 12 consecutive subcarriers (15 kHz bandwidth) for one slot.
PRB is then (6 or 7) symbols x 12 subcarriers.
Instead of PHY preambles (802.11), reference symbols are embedded in the PRB.
LTE also employs MIMO.

## Slide 14: What is Mobility?
Spectrum of mobility, from the network layer
perspective:
no mobility
high mobility
User only moves within
the same wireless
access network.
User passes through multiple access networks while maintaining ongoing connections (like cell phone).
User moves between access networks, disconnecting while between networks.

## Slide 15: Human Analogy: How to Contact a Mobile Friend ?
Search all phone books?
Call her parents or her friends?
Expect her to let you know where he/she now lives?
I wonder where Alice moved to?
Consider a friend frequently changing residence addresses. How do you find her?

## Slide 16: Mobile Network Architecture
Home network: permanent “home” of mobile
(e.g., 128.119.40/24)
Permanent address: address in home network, can always be used to reach mobile.
e.g., 128.119.40.186
Home agent: entity that will perform mobility functions on behalf of mobile, when mobile is remote.
wide area network
Correspondent: wants to communicate with mobile node.

## Slide 17: More Mobility Vocabulary
Care-of-address: address in visited network.
(e.g., 79.129.13.2)
wide area network
Visited network: network in which mobile currently resides (e.g., 79.129.13/24)
Permanent address: remains constant (e.g., 128.119.40.186)
Foreign agent: entity in visited network that performs mobility functions on behalf of mobile.
Correspondent

## Slide 18: Mobility Approaches
Let routing handle it: Routers advertise permanent address of mobile-nodes-in-residence via usual routing table exchange.
  routing tables indicate where each mobile node is located. {use OSPF intradomain & interdomain routing info}
  no changes to end-systems.
Let end-systems handle it:
  indirect routing: communication from correspondent to mobile node goes through home agent, then forwarded to remote network.
  direct routing: correspondent gets foreign address of mobile node, sends directly to mobile node.

## Slide 19: Mobility Approaches
Let routing handle it: Routers advertise permanent address of mobile-nodes-in-residence via usual routing table exchange.
  routing tables indicate where each mobile node is located.
  no changes to end-systems
Let end-systems handle it:
  indirect routing: communication from correspondent to mobile node goes through home agent, then forwarded to remote network.
  direct routing: correspondent gets foreign address of mobile node, sends directly to mobile node.
not
scalable
to millions of
mobiles

## Slide 20: Mobility ‘Registration’
End result:
Foreign agent knows about mobile node.
Home agent knows location of mobile node.
wide area network
Home network
Visited network
1
Mobile node contacts foreign agent upon entering visited network.
2
Foreign agent contacts home agent home: “This mobile node is resident in my network”.

## Slide 21: Mobility via Indirect Routing
wide area network
Home
network
Visited
network
3
2
4
1
Correspondent addresses packets using home address of mobile node.
Home agent intercepts packets, forwards to foreign agent.
Foreign agent receives packets, forwards to mobile node.
Mobile node replies directly to correspondent.

## Slide 22: Indirect Routing
Mobile uses two addresses:
  permanent address: used by correspondent (Hence, mobile location is transparent to correspondent.)
  care-of-address: used by home agent to forward datagrams to mobile node via foreign agent.
Foreign agent functions may be done by mobile node itself (e.g., use DHCP).
Triangle routing: correspondent-home-network-mobile
  inefficient when the
  correspondent and mobile
  are in the same network.

## Slide 23: Indirect Routing Moving between Networks
Suppose the mobile node moves to another network:
  registers with new foreign agent.
  new foreign agent registers with home agent.
  home agent updates COA for mobile node.
  packets continue to be forwarded to mobile node
  (but with new care-of-address).
Mobility involving multiple foreign networks is transparent.
  On-going connections can be maintained!
  However, potential for datagram loss when disconnection/reattachment time is not short.

## Slide 24: Mobility via Direct Routing
wide area network
Home
network
Visited
network
4
2
5
1
Correspondent requests and receives foreign address of mobile node.
Correspondent forwards to foreign agent.
Foreign agent receives packets, forwards to mobile node.
Mobile node replies directly to correspondent.
3
C A
Correspondent
agent

## Slide 25: Mobility via Direct Routing
Overcomes the triangle routing problem.
Non-transparent to correspondent: Correspondent must get care-of-address from home agent.
What if mobile node changes visited network?

## Slide 26: Accommodating Mobility with Direct Routing
wide area network
1
Foreign net visited
at session start
Anchor
foreign
agent
2
4
New foreign
agent
3
5
Correspondent
agent
Correspondent
New
foreign
network
Anchor foreign agent: FA in first visited network.
Data always routed first to Anchor FA.
When mobile node moves: new FA arranges to have data forwarded from old FA (chaining).

## Slide 27: Cellular/Mobile Wireless Summary
Cellular Architecture
  FDM/TDM, CDMA
Cellular Standards
  2G, GSM
    BSS, BTS, BSC, MSC
  2.5G
    GPRS, EDGE, CDMA-2000
  3G
    UTMS, CDMA-2000 (EVDO)
  4G LTE
    OFDM, MIMO

## Slide 28: Cellular/Mobile Wireless Summary
Mobile Definitions
  Home and foreign agents, permanent and care-of-addresses, correspondent, home and foreign networks.
Mobile Architecture
  Move routing to edge, use agents.
  Registering with agents
  Indirect Routing
    Triangular routing
  Direct Routing
    Anchor foreign agent