## Slide 1: Wireless Networks
Advanced Computer Networks

## Slide 2: Wireless Networks Outline
Terminology, WLAN types, IEEE Standards
IEEE 802.11a/b/g/n
802.11 AP Management Functions
  Association, scanning
802.11 MAC Sub-Layer
  DCF
    CSMA/CA
    MACAW

## Slide 3: Wireless Networks Outline
802.11 MAC Sub-Layer (cont.)
  RTS/CTS
  PCF
    Beacons, DIFS, SIFS
  Frame Details
    PLCP preamble and header
    Address fields
  Dynamic Rate Adaptation
  Frame Fragmentation

## Slide 4: LAN, WLAN and WSN Terminology
802.3::
Ethernet CSMA/CD
802.11a/b/g/n::
WiFi CSMA/CA
802.15.4::
ZigBee 802.11-based
  lower data rates, lower power
Bluetooth::
TDMA
- wireless Personal Area Networks (PANs) that provide secure, globally unlicensed short-range radio communication.
  Clusters with max of 8: cluster head + 7 nodes
WSNs

## Slide 5: Elements of a Wireless Network
network
infrastructure
wireless hosts
laptop, PDA, IP phone
run applications
may be stationary (non-mobile) or mobile
  wireless does not always mean mobility

## Slide 6: Elements of a Wireless Network
network
infrastructure
base station
typically connected to wired network
relay - responsible for sending packets between wired network and wireless host(s) in its “area”
  e.g., cell towers, 802.11 access points

## Slide 7: Wireless Local Area Networks (WLANs)
The proliferation of laptop computers and other mobile devices (PDAs and cell phones) created an obvious application level demand for wireless local area networking.
Companies jumped in, quickly developing incompatible wireless products in the 1990’s.
Industry decided to entrust standardization to IEEE committee that dealt with wired LANs
– namely, the IEEE 802 committee!!

## Slide 8: IEEE 802 Standards Working Groups
Figure 1-38. The important ones are marked with *. The ones marked with  are hibernating. The one marked with † gave up.
802.15.4 ZigBee
Tanenbaum

## Slide 9: IEEE 802.11
The following IEEE 802.11 standards exist or are in development to support the creation of technologies for wireless local area networking:
802.11a - 54 Mbps standard, 5 GHz signaling (ratified 1999)
802.11b - 11 Mbps standard, 2.4 GHz signaling (1999)
802.11c - operation of bridge connections (moved to 802.1D)
802.11d - worldwide compliance with regulations for use of wireless signal spectrum (2001)
802.11e - Quality of Service (QoS) support (not yet ratified)
802.11f - Inter-Access Point Protocol recommendation for communication between access points to support roaming clients (2003)
802.11g - 54 Mbps standard, 2.4 GHz signaling (2003)
802.11h - enhanced version of 802.11a to support European regulatory requirements (2003)
802.11i- security improvements for the 802.11 family (2004)
802.11j - enhancements to 5 GHz signaling to support Japan regulatory requirements (2004)
802.11k - WLAN system management (in progress)
About.com

## Slide 10: IEEE 802.11
The following IEEE 802.11 standards exist or are in development to support the creation of technologies for wireless local area networking:
802.11m - maintenance of 802.11 family documentation
802.11n - OFDM version at 248 Mbps; MIMO version 600 Mbps ??
** formally voted into the standard in September 2009!
802.11p- Wireless Access for the Vehicular Environment
802.11r - fast roaming support via Basic Service Set transitions
802.11s - ESS mesh networking for access points
802.11t - Wireless Performance Prediction - recommendation for testing standards and metrics
802.11u - internetworking with 3G / cellular and other forms of external networks
802.11v - wireless network management / device configuration
802.11w - Protected Management Frames security enhancement
802.11x- skipped (generic name for the 802.11 family)
802.11y - Contention Based Protocol for interference avoidance
About.com

## Slide 11: Wireless Link Standards
Indoor
10-30m
Outdoor
50-200m
Mid-range
outdoor
200m – 4 Km
Long-range
outdoor
5Km – 20 Km
.056
.384
1
4
5-11
54
IS-95, CDMA, GSM
2G
UMTS/WCDMA, CDMA2000
3G
802.15
802.11b
802.11a,g
UMTS/WCDMA-HSPDA, CDMA2000-1xEVDO
3G cellular
enhanced
802.16 (WiMAX)
802.11a,g point-to-point
200
802.11n
Data rate (Mbps)
data

## Slide 12: Wireless Link Characteristics
Differences from wired link…
decreased signal strength: radio signal attenuates as it propagates through matter (path loss).
interference from other sources: standardized wireless network frequencies (e.g., 2.4 GHz) shared by other devices (e.g., phone); devices (motors) interfere as well.
multipath propagation: radio signal reflects off objects ground, arriving ad destination at slightly different times.
…. makes communication across (even a point to point) wireless link much more difficult.

## Slide 13: Classification of Wireless Networks
Base Station:: all communication through an Access Point (AP) {note hub topology}. Other nodes can be fixed or mobile.
Infrastructure Wireless:: AP is connected to the wired Internet.
Ad Hoc Wireless:: wireless nodes communicate directly with one another.
MANETs (Mobile Ad Hoc Networks) :: ad hoc nodes are mobile.

## Slide 14: Wireless LANs
Figure 1-36.(a) Wireless networking with a base station. (b) Ad hoc networking.
Tanenbaum

## Slide 15: Infrastructure Wireless LAN
DCC 9th Ed.
Stallings
Notes: Stallings DCC9e Figure 17.3 suggests the differences between a wireless LAN that supports LAN extension and nomadic access requirements and an ad hoc wireless LAN. In the former case, the wireless LAN forms a stationary infrastructure consisting of one or more cells with a control module for each cell. Within a cell, there may be a number of stationary end systems. Nomadic stations can move from one cell to another. In contrast, there is no infrastructure for an ad hoc network. Rather, a peer collection of stations within range of each other may dynamically configure themselves into a temporary network.

## Slide 16: Wireless Network Taxonomy
single hop
multiple hops
infrastructure
(e.g., APs)
no
infrastructure
host connects to
base station (WiFi,
WiMAX, cellular)
which connects to
larger Internet
no base station, no
connection to larger
Internet (Bluetooth,
ad hoc nets)
host may have to
relay through several
wireless nodes to
connect to larger
Internet: mesh net
no base station, no
connection to larger
Internet. May have to
relay to reach other
a given wireless node
MANET, VANET

## Slide 17: The 802.11 Protocol Stack
Note – ordinary 802.11 products are no longer being manufactured.
Figure 4-25. Part of the 802.11 protocol stack.
Tanenbaum
802.11n
OFDM SDM

## Slide 18: Wireless Physical Layer
Physical layer conforms to OSI (five options)
  1997: 802.11 infrared, FHSS, DSSS {FHSS and DSSS run in the 2.4GHz band}
  1999: 802.11a OFDM and 802.11b HR-DSSS
  2001: 802.11g OFDM
  2009: 802.11n OFDM and MIMO
802.11 Infrared
  Two capacities: 1 Mbps or 2 Mbps.
  Range is 10 to 20 meters and cannot penetrate walls.
  Does not work outdoors.
802.11 FHSS (Frequence Hopping Spread Spectrum)
  The main issue is multipath fading.
  [P&D] The idea behind spread spectrum is to spread the signal over a wider frequency to minimize the interference from other devices.
  79 non-overlapping channels, each 1 Mhz wide at low end of 2.4 GHz ISM band.
  The same pseudo-random number generator used by all stations to start the hopping process.
  Dwell time: min. time on channel before hopping (400msec).

## Slide 19: Media Access Control
Notes: The 802.11 working group considered two types of proposals for a MAC algorithm: distributed access protocols, which, like Ethernet, distribute the decision to transmit over all the nodes using a carrier sense mechanism; and centralized access protocols, which involve regulation of transmission by a centralized decision maker. A distributed access protocol makes sense for an ad hoc network of peer workstations (typically an IBSS) and may also be attractive in other wireless LAN configurations that consist primarily of bursty traffic. A centralized access protocol is natural for configurations in which a number of wireless stations are interconnected with each other and some sort of base station that attaches to a backbone wired LAN; it is especially useful if some of the data is time sensitive or high priority.
The end result for 802.11 is a MAC algorithm called DFWMAC (distributed foundation wireless MAC) that provides a distributed access control mechanism with an optional centralized control built on top of that. Stallings DCC9e Figure 17.5 illustrates the architecture. The lower sublayer of the MAC layer is the distributed coordination function (DCF). DCF uses a contention algorithm to provide access to all traffic. Ordinary asynchronous traffic directly uses DCF. The point coordination function (PCF) is a centralized MAC algorithm used to provide contention-free service. PCF is built on top of DCF and exploits features of DCF to assure access for its users.

## Slide 20: Wireless Physical Layer
802.11 DSSS (Direct Sequence Spread Spectrum)
  The main idea is to represent each bit in the frame by multiple bits in the transmitted signal (i.e., it sends the XOR of that bit and n random bits).
  Spreads signal over entire spectrum using pseudo-random sequence (similar to CDMA see Kurose & Ross Chap 6).
  Each bit transmitted using an 11-bit chipping Barker sequence, PSK at 1Mbaud.
  This yields a capacity of 1 or 2 Mbps.
Figure 2.37 Example 4-bit chipping sequence
P&D slide
unique code
per sender

## Slide 21: Code Division Multiple Access (CDMA)
Used in several wireless broadcast channels (cellular, satellite, etc) standards.
A unique “code” assigned to each user; i.e., code set partitioning.
All users share the same frequency, but each user has its own chipping sequence (i.e., code) to encode data.
encoded signal = (original data) X (chipping sequence)
decoding: inner-product of encoded signal and chipping sequence
Allows multiple users to “coexist” and transmit simultaneously with minimal interference (if codes are “orthogonal”).

## Slide 22: CDMA Encode/Decode
slot 1
slot 0
d1 = -1
1
1
1
1
1
-
1
-
1
-
1
-
Zi,m= di.cm
d0 = 1
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
slot 0
channel
output
slot 1
channel
output
channel output Zi,m
sender
code
data
bits
slot 1
slot 0
d1 = -1
d0 = 1
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
slot 0
channel
output
slot 1
channel
output
receiver
code
received
input
Di = S Zi,m.cm
m=1
M
M
Bit width

## Slide 23: CDMA: Two-Sender Interference

## Slide 24: Wireless Physical Layer
802.11a OFDM (Orthogonal Frequency Divisional Multiplexing)
  Compatible with European HiperLan2.
  54 Mbps in wider 5.5 GHz band  transmission range is limited.
  Uses 52 FDM channels (48 for data; 4 for synchronization).
  Encoding is complex ( PSM up to 18 Mbps and QAM above this capacity).
  E.g., at 54 Mbps 216 data bits encoded into into 288-bit symbols.
  More difficulty penetrating walls.

## Slide 25: Wireless Physical Layer
802.11b HR-DSSS (High Rate Direct Sequence Spread Spectrum)
  11a and 11b shows a split in the standards committee.
  11b approved and hit the market before 11a.
  Up to 11 Mbps in 2.4 GHz band using 11 million chips/sec.
  Note in this bandwidth all these protocols have to deal with interference from microwave ovens, cordless phones and garage door openers.
  Range is 7 times greater than 11a.
  11b and 11a are incompatible!!

## Slide 26: Wireless Physical Layer
802.11g OFDM(Orthogonal Frequency Division Multiplexing)
  An attempt to combine the best of both 802.11a and 802.11b.
  Supports bandwidths up to 54 Mbps.
  Uses 2.4 GHz frequency for greater range.
  Is backward compatible with 802.11b.

## Slide 27: Data Rate vs Distance (m)
Notes: The IEEE 802.11 standards do not include a specification of speed versus distance objectives. Different vendors will give different values, depending on environment. Stallings DCC9e Table 17.5, based on [LAYL04] gives estimated values for a typical office environment.

## Slide 28: Wireless Physical Layer
802.11n OFDM version at 248 Mbps
Physical Layer Changes:
  Multiple-Input-Multiple-Output (MIMO)
  maximum of 600 Mbps with the use of four spatial streams at a channel width of 40 MHz.
  Spatial Division Multiplexing (SDM)
MAC Layer Changes:
  Frame aggregation into single block for transmission

## Slide 29: IEEE 802.11 MAC Frame Format
29
Notes: Stallings DCC9e Figure 17.8 shows the 802.11 frame format. This general format is used for all data and control frames, but not all fields are used in all contexts. The fields are:
Frame Control: Indicates the type of frame (control, management, or data) and provides control information. Control information includes whether the frame is to or from a DS, fragmentation information, and privacy information.
Duration/Connection ID: If used as a duration field, indicates the time (in microseconds) the channel will be allocated for successful transmission of a MAC frame. In some control frames, this field contains an association, or connection, identifier.
Addresses: The number and meaning of the 48-bit address fields depend on context. The transmitter address and receiver address are the MAC addresses of stations joined to the BSS that are transmitting and receiving frames over the wireless LAN. The service set ID (SSID) identifies the wireless LAN over which a frame is transmitted. For an IBSS, the SSID is a random number generated at the time the network is formed. For a wireless LAN that is part of a larger configuration the SSID identifies the BSS over which the frame is transmitted; specifically, the SSID is the MAC-level address of the AP for this BSS (Stallings DCC9e Figure 17.4). Finally the source address and destination address are the MAC addresses of stations, wireless or otherwise, that are the ultimate source and destination of this frame. The source address may be identical to the transmitter address and the destination address may be identical to the receiver address.
Sequence Control: Contains a 4-bit fragment number subfield, used for fragmentation and reassembly, and a 12-bit sequence number used to number frames sent between a given transmitter and receiver.
Frame Body: Contains an MSDU or a fragment of an MSDU. The MSDU is a LLC protocol data unit or MAC control information.
Frame Check Sequence: A 32-bit cyclic redundancy check.

## Slide 30: 802.11 LAN Architecture
wireless host communicates with base station
  base station = access point (AP)
Basic Service Set (BSS) (aka “cell”) in infrastructure mode contains:
  wireless hosts
  access point (AP): base station
  ad hoc mode: hosts only
BSS 1
BSS 2
Internet
hub, switch
or router
AP
AP

## Slide 31: 802.11 Management Functions
Channel Selection
Scanning
Station (user) Authentication and Association
Beacon Management
Power Management Mode
Beacon
Beacon
Returned
Probe
Sent
Adv-Nets
Keating

## Slide 32: Channels and AP Association
802.11b: 2.4GHz-2.485GHz spectrum divided into 11 channels (overlapping frequencies).
  AP admin chooses frequency for AP.
  Interference is possible: The channel can be same as that chosen by a neighbor AP!
Wireless nodes must associate with an AP.
  Node scans channels, listening for beacon frames containing AP’s name (SSID) and MAC address.
  Node makes choice for AP association {default is best RSSI}.
  may perform authentication [K&R Chapter 8].
  will typically run DHCP to get IP address in AP’s subnet.

## Slide 33: 802.11 Overlapping Channels
802.11b/g transmission occurs on one of 11 overlapping channels in the 2.4GHz North American ISM band.
2.412
2.417
2.422
2.432
2.442
2.452
2.462
2.472
2.484
2.427
2.437
2.447
2.457
2.467
2
3
4
5
1
7
8
9
10
6
11
12
13
14
Adv-Nets
Keating

## Slide 34: 802.11: Passive/Active Scanning
AP 2
AP 1
H1
BBS 2
BBS 1
1
2
2
3
4
Active Scanning
Probe Request frame broadcast from H1
Probes response frame sent from APs
Association Request frame sent: H1 to selected AP
Association Response frame sent: H1 to selected AP
AP 2
AP 1
H1
BBS 2
BBS 1
1
2
3
1
Passive Scanning
beacon frames sent from APs
association Request frame sent: H1 to selected AP
association Response frame sent: H1 to selected AP

## Slide 35: 802.11 MAC Layer Protocol
In 802.11 wireless LANs, “seizing the channel” does not exist as in 802.3 wired Ethernet.
Two additional problems:
  Hidden Terminal Problem
  Exposed Station Problem
To deal with these two problems 802.11 supports two modes of operation:
  DCF (Distributed Coordination Function)
  PCF (Point Coordination Function).
All implementations must support DCF, but PCF is optional.

## Slide 36: Figure 4-26.(a)The hidden terminal problem. (b) The exposed station problem.
802.11 Problems
Tanenbaum

## Slide 37: The Hidden Terminal Problem
Wireless stations have transmission ranges and not all stations are within radio range of each other.
Simple CSMA will not work!
C transmits to B.
If A “senses” the channel, it will not hear C’s transmission and falsely conclude that A can begin a transmission to B.

## Slide 38: The Exposed Station Problem
This is the inverse problem.
B wants to send to C and listens to the channel.
When B hears A’s transmission, B falsely assumes that it cannot send to C.

## Slide 39: Distribute Coordination Function (DCF)
CSMA/CA (CSMA with Collision Avoidance) uses one of two modes of operation:
virtual carrier sensing
physical carrier sensing
The two methods are supported by:
1. MACAW (Multiple Access with Collision Avoidance for Wireless) with virtual carrier sensing.
2. 1-persistent physical carrier sensing.

## Slide 40: Wireless LAN Protocols [Tan pp.269-270]
MACA protocol reduces hidden and exposed terminal problems:
Sender broadcasts a Request-to-Send (RTS) and the intended receiver sends a Clear-to-Send (CTS).
Upon receipt of a CTS, the sender begins transmission of the frame.
RTS,CTS helps determine who else is in range or busy (Collision Avoidance).
  - Can a collision still occur?

## Slide 41: Wireless LAN Protocols
Figure 4-12. (a) A sending an RTS to B.
(b) B responding with a CTS to A.
MACAW added ACKs, Carrier Sense, and BEB done per stream and not per station.
Tanenbaum

## Slide 42: Virtual Channel Sensing in CSMA/CA
Figure 4-27. The use of virtual channel sensing using CSMA/CA.
C (in range of A) receives the RTS and based on information in RTS creates a virtual channel busy NAV (Network Allocation Vector).
D (in range of B) receives the CTS and creates a shorter NAV.
Tanenbaum

## Slide 43: Collision Avoidance: RTS-CTS Exchange
AP
A
B
time
RTS(A)
RTS(B)
RTS(A)
CTS(A)
CTS(A)
DATA (A)
ACK(A)
ACK(A)
reservation collision
NAV
defer

## Slide 44: Virtual Channel Sensing in CSMA/CA
What is the advantage of RTS/CTS?
RTS is 20 bytes, and CTS is 14 bytes.
MPDU can be 2300 bytes.
“virtual” implies source station sets the duration field in data frame or in RTS and CTS frames.
Stations then adjust their NAV accordingly!

## Slide 45: 1-Persistent Physical Carrier Sensing
The station senses the channel when it wants to send.
If idle, the station transmits.
  A station does not sense the channel while transmitting.
If the channel is busy, the station defers until idle and then transmits (1-persistent).
Upon collision (no ACK received), wait a random time using binary exponential backoff (BEB).

## Slide 46: IEEE 802.11 MAC Protocol: CSMA/CA
802.11 sender
1 if sense channel idle for DIFS then
  Transmit entire frame (no CD).
2 if sense channel busy then
  Choose a random backoff time.
  When channel is busy, counter is frozen.
  Timer counts down while channel idle and
  transmit when timer expires.
  if no ACK, increase random backoff interval, repeat 2.
802.11 receiver
- if frame received OK
return ACK after SIFS.
sender
receiver
DIFS
data
SIFS
ACK

## Slide 47: Point Coordinated Function (PCF)
PCF uses a base station to poll other stations to see if they have frames to send.
No collisions occur.
Base station sends beacon frame periodically.
Base station can tell another station to sleep to save on batteries and base stations holds frames for sleeping station.
Subsequently, BS awakens sleeping node via beacon frame.

## Slide 48: DCF and PCF Co-Existence
Distributed and centralized control can co-exist using InterFrame Spacing.
SIFS (Short IFS):: the time waited between packets in an ongoing dialog (RTS,CTS,data, ACK, next frame)
PIFS (PCF IFS):: when no SIFS response, base station can issue beacon or poll.
DIFS (DCF IFS):: when no PIFS, any station can attempt to acquire the channel.
EIFS (Extended IFS):: lowest priority interval used to report bad or unknown frame.

## Slide 49: Inter-frame Spacing in 802.11
Figure 4-29. Interframe Spacing in 802.11.
Tanenbaum

## Slide 50: Basic CSMA/CA
[N. Kim]
possible
collision !!

## Slide 51: 802.11 Physical Layer
[N. Kim]
‘Adjust transmission rate on the fly’

## Slide 52: 802.11 Frames - Addresses
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
2
2
6
6
6
2
6
0 - 2312
4
seq
control
Address 2: MAC address
of wireless host or AP
transmitting this frame
Address 1: MAC address
of wireless host or AP
to receive this frame
Address 3: MAC address
of router interface to which AP is attached
Address 4: used only in ad hoc mode

## Slide 53
Internet
router
AP
H1
R1
AP MAC addr H1 MAC addr R1 MAC addr
address 1
address 2
address 3
802.11 frame
R1 MAC addr H1 MAC addr
dest. address
source address
802.3 frame
802.11 Frame - Addresses

## Slide 54
Type
From
AP
Subtype
To
AP
More
frag
WEP
More
data
Power
mgt
Retry
Rsvd
Protocol
version
2
2
4
1
1
1
1
1
1
1
1
duration of reserved
transmission time (RTS/CTS)
frame seq # (for RDT)
frame type
(RTS, CTS, ACK, data)
802.11 Frame Addresses (more)
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
2
2
6
6
6
2
6
0 - 2312
4
seq
control

## Slide 55
hub or
switch
AP 2
AP 1
H1
BBS 2
BBS 1
802.11: Mobility within Same Subnet
router
H1 remains in same IP subnet: IP address can remain same.
Switch: Which AP is associated with H1?
  Uses self-learning (Ch. 5)
  Switch will see frame from H1 and “remember” which switch port can be used to reach H1.

## Slide 56: Wireless Network Details
All APs (or base stations) will periodically send a beacon frame (10 to 100 times a second).
Beacon frames are also used by DCF to synchronize and handle nodes that want to sleep.
  Node sets Power management bit to indicate going to sleep and timer wakes node up for next beacon.
  The AP will buffer frames intended for a sleeping wireless client and wakeup for reception with beacon frame.
AP downstream/upstream traffic performance is asymmetric.
Wireless communication quality between two nodes can be asymmetric due to multipath fading.{Characterization paper shows this!}

## Slide 57: Wireless Network Details
802.11b, g and n use dynamic rate adaptation based on frame loss (algorithms internal to wireless card at the AP)
  e.g. for 802.11b choices are: 11, 5.5, 2 and 1 Mbps
Standard 802.11 retries:
  7 retries for RTS and CTS
  4 retries for Data and ACK frames
RTS/CTS may be turned off by default [Research has shown that RTS/CTS degrades performance when hidden terminal is not an issue].

## Slide 58: Node Contention
58
58
[N. Kim]
without RTS/CTS

## Slide 59: Wireless Link Characteristics
SNR: signal-to-noise ratio
larger SNR – easier to extract signal from noise.
SNR versus BER tradeoffs
given a physical layer: increase power -> increase SNR-> decrease BER.
given a SNR: choose physical layer that meets BER requirement, aiming for highest throughput.
SNR may change with mobility: dynamically adapt physical layer (modulation technique, rate).
10
20
30
40
QAM256 (8 Mbps)
QAM16 (4 Mbps)
BPSK (1 Mbps)
SNR(dB)
BER
10-1
10-2
10-3
10-5
10-6
10-7
10-4

## Slide 60
Dynamic Rate Adaptation
Mobile Node Example:
1. SNR decreases, BER increases as node moves away from base station.
2. When BER becomes too high, switch to lower transmission rate but with lower BER.
Idea:: lower data rate for higher throughput.
QAM256 (8 Mbps)
QAM16 (4 Mbps)
BPSK (1 Mbps)
10
20
30
40
SNR(dB)
BER
10-1
10-2
10-3
10-5
10-6
10-7
10-4
operating point
K & R
Note - Performance Anomaly paper shows there are other issues when wireless flows contend at AP !

## Slide 61: Rate Adaptation versus Distance
61
61
[CARA paper]

## Slide 62: Figure 4-28 Fragmentation in 802.11
High wireless error rates  long packets have less probability of being successfully transmitted.
Solution: MAC layer fragmentation with stop-and-wait protocol on the fragments.
Tanenbaum

## Slide 63: Wireless Networks Summary
Terminology, WLAN types, IEEE Standards
  Infrastructure, ad hoc, MANET, Base Station, Access Point, single and multi-hop
IEEE 802.11a/b/g/n
  Differences in data rate and transmission technologies
  FHSS, DSSS, CDMA, OFDM, HR-DSSS, MIMO

## Slide 64: Wireless Networks Summary
802.11 AP Management Functions
  Association with AP, active and passive scanning, beacon frames
802.11 MAC Sub-Layer
  Overlapping channels
  Hidden terminal problem, exposed station problem
  DCF
    CSMA/CA
    MACAW

## Slide 65: Wireless Networks Summary
802.11 MAC Sub-Layer (cont.)
  RTS/CTS
  PCF
    Beacons, DIFS, SIFS, sleeping nodes
  Frame Details
    PLCP preamble and header
    3 or 4 Address fields used in 802.11
  SNR vs BER issues
  Dynamic Rate Adaptation
  Frame Fragmentation