## Slide 1: The Mote Revolution: Low Power Wireless Sensor Network Devices
University of California, Berkeley
Joseph Polastre Robert Szewczyk Cory Sharp David Culler

## Slide 2: Outline
Trends and Applications
Mote History and Evolution
Design Principles
Telos

## Slide 3: Faster, Smaller, Numerous
Moore’s Law
  “Stuff” (transistors, etc) doubling every 1-2 years
Bell’s Law
  New computing class every 10 years
year
log (people per computer)
Streaming Data to/from the Physical World

## Slide 4: Applications
Environmental Monitoring
  Habitat Monitoring
  Integrated Biology
  Structural Monitoring
Interactive and Control
  Pursuer-Evader
  Intrusion Detection
  Automation
Density & Scale
Sample Rate & Precision
Mobility
Low Latency
Disconnection & Lifetime

## Slide 5: Open Experimental Platform
Networking
Small microcontroller 8 kB code 512 B data
Simple, low-power radio 10 kbps ASK
EEPROM (32 KB)
Simple sensors
WeC 99
“Smart Rock”
Mica 1/02
NEST open exp. Platform 128 kB code, 4 kB data 40kbps OOK/ASK radio 512 kB Flash
Rene 11/00
Designed for experimentation
sensor boards
power boards
TinyOS
Services
Dot 9/01
Demonstrate scale
Spec 6/03
“Mote on a chip”
Telos 4/04
Robust
Low Power
250kbps
Easy to use
Mica2 12/02
38.4kbps radio FSK
Commercial Off The Shelf Components (COTS)
Notes: Before we jump in to the technical material, I would like to give you one more bit of context.

## Slide 6
Mote Evolution

## Slide 7: Low Power Operation
Efficient Hardware
  Integration and Isolation
    Complementary functionality (DMA, USART, etc)
  Selectable Power States (Off, Sleep, Standby)
  Operate at low voltages and low current
    Run to cut-off voltage of power source
Efficient Software
  Fine grained control of hardware
  Utilize wireless broadcast medium
  Aggregate

## Slide 8: Typical WSN Application
Periodic
  Data Collection
  Network Maintenance
  Majority of operation
Triggered Events
  Detection/Notification
  Infrequently occurs
    But… must be reported quickly and reliably
Long Lifetime
  Months to Years without changing batteries
  Power management is the key to WSN success
sleep
wakeup
processing
data acquisition
communication
Power
Time

## Slide 9: Design Principles
Key to Low Duty Cycle Operation:
  Sleep – majority of the time
  Wakeup – quickly start processing
  Active – minimize work & return to sleep

## Slide 10: Sleep
Majority of time, node is asleep
  >99%
Minimize sleep current through
  Isolating and shutting down individual circuits
  Using low power hardware
    Need RAM retention
Run auxiliary hardware components from low speed oscillators (typically 32kHz)
  Perform ADC conversions, DMA transfers, and bus operations while microcontroller core is stopped

## Slide 11: Wakeup
Overhead of switching from Sleep to Active Mode
Microcontroller
Radio (FSK)
10ns – 4ms typical
1– 10 ms typical
2.5 ms
292 ns

## Slide 12: Active
Microcontroller
  Fast processing, low active power
  Avoid external oscillators
Radio
  High data rate, low power tradeoffs
  Narrowband radios
    Low power, lower data rate, simple channel encoding, faster startup
  Wideband radios
    More robust to noise, higher power, high data rates
External Flash (stable storage)
  Data logging, network code reprogramming, aggregation
  High power consumption
  Long writes
Radio vs. Flash
  250kbps radio sending 1 byte
    Energy : 1.5mJ
    Duration : 32ms
  Atmel flash writing 1 byte
    Energy : 3mJ
    Duration : 78ms

## Slide 13: Telos Platform
A new platform for low power research
  Monitoring applications:
    Environmental
    Building
    Tracking
Long lifetime, low power, low cost
Built from application experiences and low duty cycle design principles
Robustness
  Integrated antenna
  Integrated sensors
  Soldered connections
Standards Based
  IEEE 802.15.4
  USB
  IEEE 802.15.4 ZigBee
  CC2420 radio
  Frame-based
  250kbps
  2.4GHz ISM band
TI MSP430
  Ultra low power
    1.6mA sleep
    460mA active
    1.8V operation
Open embedded platform with open source tools, operating system (TinyOS), and designs.

## Slide 14: Low Power Operation
TI MSP430 -- Advantages over previous motes
  16-bit core
  12-bit ADC
    16 conversion store registers
    Sequence and repeat sequence programmable
  < 50nA port leakage (vs. 1mA for Atmels)
  Double buffered data buses
  Interrupt priorities
  Calibrated DCO
Buffers and Transistors
  Switch on/off each sensor and component subsystem

## Slide 15: Minimize Power Consumption
Compare to MicaZ: a Mica2 mote with AVR mcu and 802.15.4 radio
Sleep
  Majority of the time
  Telos: 2.4mA
  MicaZ: 30mA
Wakeup
  As quickly as possible to process and return to sleep
  Telos: 290ns typical, 6ms max
  MicaZ: 60ms max internal oscillator, 4ms external
Active
  Get your work done and get back to sleep
  Telos: 4-8MHz 16-bit
  MicaZ: 8MHz 8-bit

## Slide 16: CC2420 Radio IEEE 802.15.4 Compliant
CC2420
  Fast data rate, robust signal
    250kbps : 2Mchip/s : DSSS
    2.4GHz : Offset QPSK : 5MHz
    16 channels in 802.15.4
    -94dBm sensitivity
  Low Voltage Operation
    1.8V minimum supply
  Software Assistance for Low Power Microcontrollers
    128byte TX/RX buffers for full packet support
    Automatic address decoding and automatic acknowledgements
    Hardware encryption/authentication
    Link quality indicator (assist software link estimation)
      samples error rate of first 8 chips of packet (8 chips/bit)

## Slide 17: Power Calculation Comparison Design for low power
Mica2 (AVR)
  0.2 ms wakeup
  30 mW sleep
  33 mW active
  21 mW radio
  19 kbps
  2.5V min
    2/3 of AA capacity
MicaZ (AVR)
  0.2 ms wakeup
  30 mW sleep
  33 mW active
  45 mW radio
  250 kbps
  2.5V min
    2/3 of AA capacity
Telos (TI MSP)
  0.006 ms wakeup
  2 mW sleep
  3 mW active
  45 mW radio
  250 kbps
  1.8V min
    8/8 of AA capacity
Supporting mesh networking with a pair of AA batteries reporting data once every 3 minutes using synchronization (<1% duty cycle)
328 days
945 days
453 days

## Slide 18: Integrated Antenna Inverted-F Microstrip Antenna and SMA Connector
Inverted-F
  Psuedo Omnidirectional
  50m range indoors
  125m range outdoors
  Optimum at 2400-2460MHz
SMA Connector
  Enabled by moving a capacitor
  > 125m range
  Optimum at 2430-2483MHz

## Slide 19: Sensors
Integrated Sensors
  Sensirion SHT11
    Humidity (3.5%)
    Temperature (0.5oC)
    Digital sensor
  Hamamatsu S1087
    Photosynthetically active light
    Silicon diode
  Hamamatsu S1337-BQ
    Total solar light
    Silicon diode
Expansion
  6 ADC channels
  4 digital I/O
  Existing sensor boards
    Magnetometer
    Ultrasound
    Accelerometer
    4 PIR sensors
    Microphone
    Buzzer
dot
mag
ultrasound
acoustic

## Slide 20: Conclusions
New design approach derived from our experience with resource constrained wireless sensor networks
  Active mode needs to run quickly to completion
  Wakeup time is crucial for low power operation
    Wakeup time and sleep current set the minimal energy consumption for an application
  Sleep most of the time
Tradeoffs between complexity/robustness and low power radios
Careful integration of hardware and peripherals